#	linux_dev.doc
#
#	Created: Thu Jul  9 15:55:42 1992
#	Last modified: Thu Jul  9 16:18:18 1992
#
#	@ arl // 1992


	How does one add device to Linux?
	=================================

	1)	You should have device driver ;-)

	2)	The device driver should have <device_name>_init
		function, here's for example "lp" device:

			long
			lp_init( long kmem_start )
			{
				chrdev_fops[6] = &lp_fops;

				<init code here>
			}

	3)	As you see "lp" device number is fixed to 6 ;-)

	4)	You should have file operations struct for your
		device, and for the "lp" device it is:

			static struct fileoperations lp_fops	=
			{
				lp_seek,
				lp_read,
				lp_write,
				NULL,		/* lp_readdir */
				NULL,		/* lp_select */
				NULL,		/* lp_ioctl */
				lp_open,
				lp_release
			};

		You should have the functions mentioned at the
		table.

	5)	kernel/chr_drv/mem.c contains function chr_dev_init
		where you should add your character device
		<device_name>_init.

		kernel/blk_drv/ll_rw_blk.c contains function
		blk_dev_init where you shoud add your block device
		<device_name>_init or to init/main.c function
		start_kernel if your block driver might contain
		the root device.


	Drawbacks
	=========

	1)	The device numbers are fixed

		There are absolute numbers on the kernel or
		device driver code.

	2)	The system does not have configure table

		You have to edit source files for adding or
		deleting a device driver from the kernel.

		It's extremely hard to find out what's going on ...