[ PROTOCOLS:NBSOSI-AGREEMENTS.DOC ]                              [ 8/88 ]

Computer Science and Technology
NBS Special Publication 500-150

Stable Implementation Agreements for Open Systems Interconnection Protocols
Version 1 Edition 3
December 1987

Based on the Proceedings of the NBS Workshop for Implementors of OSI

U.S. Department of Commerce
C. William Verity, Secretary

National Bureau of Standards
Ernest Ambler, Director
Issued January 1988




                            Table of Contents

1. GENERAL INFORMATION . . . . . . . . . . . . . . . . . . . . . . .    1
   1.1  PURPOSE OF THIS DOCUMENT . . . . . . . . . . . . . . . . . .    1
   1.2  PURPOSE OF THE WORKSHOP  . . . . . . . . . . . . . . . . . .    1
   1.3  WORKSHOP ORGANIZATION  . . . . . . . . . . . . . . . . . . .    2

2. SUB NETWORKS  . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   2.1  INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . . .    1
   2.2  SCOPE AND FIELD OF APPLICATION . . . . . . . . . . . . . . .    1
   2.3  STATUS . . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   2.4  ERRATA . . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   2.5  LOCAL AREA NETWORKS  . . . . . . . . . . . . . . . . . . . .    1
        2.5.1     IEEE 802.2 LOGICAL LINK CONTROL  . . . . . . . . .    1
        2.5.2     IEEE 802.3 CSMA/CD ACCESS METHOD . . . . . . . . .    2
        2.5.3     IEEE 802.4 TOKEN BUS ACCESS METHOD . . . . . . . .    3
        2.5.4     IEEE 802.5 TOKEN RING ACCESS METHOD  . . . . . . .    3
   2.6  WIDE AREA NETWORKS . . . . . . . . . . . . . . . . . . . . .    5
        2.6.1     CCITT RECOMMENDATION X.25  . . . . . . . . . . . .    5

3. NETWORK LAYER . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   3.1  INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . . .    1
   3.2  SCOPE AND FIELD OF APPLICATION . . . . . . . . . . . . . . .    1
   3.3  STATUS . . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   3.4  ERRATA . . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   3.5  CONNECTIONLESS-MODE NETWORK SERVICE (CLNS) . . . . . . . . .    1
        3.5.1     Provision of CLNS over Local . . . . . . . . . . .    1
        3.5.2     Provision of CLNS over X.25 Subnetworks  . . . . .    1
        3.5.3     Agreements on Protocols  . . . . . . . . . . . . .    2
             3.5.3.1   ISO 8473  . . . . . . . . . . . . . . . . . .    2
             3.5.3.2   Subnetwork Dependent Convergence Function . .    3
   3.6  CONNECTION-MODE NETWORK SERVICE (CONS) . . . . . . . . . . .    3
        3.6.1     Mandatory Method of Providing CONS . . . . . . . .    3
        3.6.2     Additional Option:  Provision of CONS over X.25 1980
                  Subnetworks  . . . . . . . . . . . . . . . . . . .    3
        3.6.3     Agreements on Protocols  . . . . . . . . . . . . .    4
             3.6.3.1   ISO 8878  . . . . . . . . . . . . . . . . . .    4
             3.6.3.2   Subnetwork Dependent Convergence Protocol (ISO
                       8878/Annex A) . . . . . . . . . . . . . . . .    4
   3.7  ADDRESSING . . . . . . . . . . . . . . . . . . . . . . . . .    4
   3.8  ROUTING  . . . . . . . . . . . . . . . . . . . . . . . . . .    5
        3.8.1     Static Routing . . . . . . . . . . . . . . . . . .    5
        3.8.2     End System to Intermediate System  . . . . . . . .    5
   3.9  MIGRATION CONSIDERATIONS . . . . . . . . . . . . . . . . . .    6
        3.9.1     X.25-1980  . . . . . . . . . . . . . . . . . . . .    6
   3.10 CONFORMANCE  . . . . . . . . . . . . . . . . . . . . . . . .    7

4. TRANSPORT . . . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   4.1  INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . . .    1
   4.2  SCOPE AND FIELD OF APPLICATION . . . . . . . . . . . . . . .    1
   4.3  STATUS . . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   4.4  ERRATA . . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   4.5  TRANSPORT CLASS 4  . . . . . . . . . . . . . . . . . . . . .    1
        4.5.1     Transport Class  . . . . . . . . . . . . . . . . .    1
        4.5.2     Protocol Agreements  . . . . . . . . . . . . . . .    1
             4.5.2.1   Rules for Negotiation . . . . . . . . . . . .    1
             4.5.2.2   Transport Class 4 Service Access Points or
                       Selectors . . . . . . . . . . . . . . . . . .    3
             4.5.2.3   Retransmission Timer  . . . . . . . . . . . .    3
             4.5.2.4   Keep-Alive Function . . . . . . . . . . . . .    4
   4.6  TRANSPORT CLASS 0  . . . . . . . . . . . . . . . . . . . . .    6
        4.6.1     Transport Class 0 Overview . . . . . . . . . . . .    6
        4.6.2     Protocol Agreements  . . . . . . . . . . . . . . .    6
             4.6.2.1   Transport Class 0 Service Access Points . . .    7
        4.6.3     Rules for Negotiation  . . . . . . . . . . . . . .    7

5. UPPER LAYERS  . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   5.1  INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . . .    1
        5.1.1     References . . . . . . . . . . . . . . . . . . . .    1
   5.2  SCOPE AND FIELD OF APPLICATION . . . . . . . . . . . . . . .    1
   5.3  STATUS . . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   5.4  ERRATA . . . . . . . . . . . . . . . . . . . . . . . . . . .    2
        5.4.1     ISO Defect Reports . . . . . . . . . . . . . . . .    2
        5.4.2     Session Defects  . . . . . . . . . . . . . . . . .    2
   5.5  ASSOCIATION CONTROL SERVICE ELEMENT  . . . . . . . . . . . .    2
        5.5.1     Introduction . . . . . . . . . . . . . . . . . . .    2
        5.5.2     Services . . . . . . . . . . . . . . . . . . . . .    3
             5.5.2.1   ACSE Services . . . . . . . . . . . . . . . .    3
             5.5.2.2   Use of Presentation Layer Services  . . . . .    3
        5.5.3     Protocol agreements  . . . . . . . . . . . . . . .    3
             5.5.3.1   Application Context . . . . . . . . . . . . .    3
             5.5.3.2   Section Deleted . . . . . . . . . . . . . . .    4
             5.5.3.3   AE Title  . . . . . . . . . . . . . . . . . .    4
   5.6  PRESENTATION . . . . . . . . . . . . . . . . . . . . . . . .    4
        5.6.1     Introduction . . . . . . . . . . . . . . . . . . .    4
        5.6.2     Services . . . . . . . . . . . . . . . . . . . . .    5
             5.6.2.1   Presentation Services . . . . . . . . . . . .    5
             5.6.2.2   Use of Session Layer Services . . . . . . . .    6
        5.6.3     Protocol Agreements  . . . . . . . . . . . . . . .    6
             5.6.3.1   Transfer Syntaxes . . . . . . . . . . . . . .    6
             5.6.3.2   Abstract Syntaxes . . . . . . . . . . . . . .    6
             5.6.3.3   Presentation Context Identifier . . . . . . .    6
             5.6.3.4   Mode-selector Position in SET . . . . . . . .    7
             5.6.3.5   Default Context . . . . . . . . . . . . . . .    7
             5.6.3.6   P-Selectors . . . . . . . . . . . . . . . . .    7
             5.6.3.7   Provider Abort Parameters . . . . . . . . . .    7
             5.6.3.8   Provider Aborts and Session Version . . . . .    7
             5.6.3.9   CPC-type  . . . . . . . . . . . . . . . . . .    7
             5.6.3.10  Presentation-context-definition-result-list .    8
             5.6.3.11  RS-PPDU . . . . . . . . . . . . . . . . . . .    8
        5.6.4     Presentation ASN.1 Encoding Rules  . . . . . . . .    8
             5.6.4.1   Invalid Encoding  . . . . . . . . . . . . . .    8
             5.6.4.2   Protocol-version, Presentation-requirements .    8
             5.6.4.3   Presentation-selector . . . . . . . . . . . .    8
   5.7  SESSION  . . . . . . . . . . . . . . . . . . . . . . . . . .    8
        5.7.1     Introduction . . . . . . . . . . . . . . . . . . .    8
        5.7.2     Services . . . . . . . . . . . . . . . . . . . . .    9
             5.7.2.1   Session Services  . . . . . . . . . . . . . .    9
             5.7.2.2   Use of Transport Services . . . . . . . . . .    9
        5.7.3     Protocol Agreements  . . . . . . . . . . . . . . .    9
             5.7.3.1   Concatenation . . . . . . . . . . . . . . . .    9
             5.7.3.2   Segmenting  . . . . . . . . . . . . . . . . .   10
             5.7.3.3   Reuse of Transport Connection . . . . . . . .   10
             5.7.3.4   Use of Transport Expedited Data . . . . . . .   10
             5.7.3.5   Use of Session Version Number . . . . . . . .   10
             5.7.3.6   Receipt of Invalid SPDUs  . . . . . . . . . .   11
             5.7.3.7   Invalid SPM Intersections . . . . . . . . . .   11
             5.7.3.8   S-Selectors . . . . . . . . . . . . . . . . .   11
   5.8  UNIVERSAL ASN.1 ENCODING RULES . . . . . . . . . . . . . . .   11
        5.8.1     Tags . . . . . . . . . . . . . . . . . . . . . . .   12
        5.8.2     Definite length  . . . . . . . . . . . . . . . . .   12
        5.8.3     EXTERNAL Type  . . . . . . . . . . . . . . . . . .   12
   5.9  CONFORMANCE  . . . . . . . . . . . . . . . . . . . . . . . .   12
        5.9.1     Specific ASE Requirements for ACSE Presentation and
                  Session  . . . . . . . . . . . . . . . . . . . . .   12
             5.9.1.1   FTAM  . . . . . . . . . . . . . . . . . . . .   13
                  5.9.1.1.1 Phase 2  . . . . . . . . . . . . . . . .   13
             5.9.1.2   MHS . . . . . . . . . . . . . . . . . . . . .   15
                  5.9.1.2.1 Phase 1  . . . . . . . . . . . . . . . .   15
             5.9.1.3   DS  . . . . . . . . . . . . . . . . . . . . .   16
                  5.9.1.3.1 Phase 1  . . . . . . . . . . . . . . . .   16
   5.10 APPENDIX A:  RECOMMENDED PRACTICES . . . . . . . . . . . . .   17

6. ISO FILE TRANSFER, ACCESS AND MANAGEMENT PHASE 2  . . . . . . . .    1
   6.1  INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . . .    1
   6.2  SCOPE AND FIELD OF APPLICATION . . . . . . . . . . . . . . .    1
   6.3  STATUS . . . . . . . . . . . . . . . . . . . . . . . . . . .    2
   6.4  ERRATA . . . . . . . . . . . . . . . . . . . . . . . . . . .    3
   6.5  ASSUMPTIONS  . . . . . . . . . . . . . . . . . . . . . . . .    4
   6.6  PRESENTATION AGREEMENTS  . . . . . . . . . . . . . . . . . .    5
   6.7  SERVICE CLASS AGREEMENTS . . . . . . . . . . . . . . . . . .    6
   6.8  FUNCTIONAL UNIT AGREEMENTS . . . . . . . . . . . . . . . . .    6
   6.9  FILE ATTRIBUTE AGREEMENTS  . . . . . . . . . . . . . . . . .    6
        6.9.1     Mandatory Group  . . . . . . . . . . . . . . . . .    7
        6.9.2     Optional Groups  . . . . . . . . . . . . . . . . .    7
   6.10 DOCUMENT TYPE AGREEMENTS . . . . . . . . . . . . . . . . . .    8
        6.10.1    Character Sets . . . . . . . . . . . . . . . . . .   11
             6.10.1.1  IA5 Character Set . . . . . . . . . . . . . .   12
             6.10.1.2  8859-1 Character Set  . . . . . . . . . . . .   14
        6.10.2    Document Type Negotiation Rules  . . . . . . . . .   14
             6.10.2.1  Connection Establishment  . . . . . . . . . .   14
             6.10.2.2  File Creation . . . . . . . . . . . . . . . .   14
             6.10.2.3  File Opening  . . . . . . . . . . . . . . . .   14
        6.10.3    Relationship Between DUs, DEs and Document Types .   15
   6.11 F-CANCEL ACTION  . . . . . . . . . . . . . . . . . . . . . .   16
   6.12 IMPLEMENTATION INFORMATION AGREEMENTS  . . . . . . . . . . .   16
   6.13 DIAGNOSTIC AGREEMENTS  . . . . . . . . . . . . . . . . . . .   16
   6.14 CONCURRENCY  . . . . . . . . . . . . . . . . . . . . . . . .   18
   6.15 REQUESTED ACCESS . . . . . . . . . . . . . . . . . . . . . .   18
   6.16 SECURITY . . . . . . . . . . . . . . . . . . . . . . . . . .   19
        6.16.1    Initiator Identity and Filestore Password    . . .   19
        6.16.2    Access Passwords   . . . . . . . . . . . . . . . .   19
        6.16.3    Implementation Responsibilities  . . . . . . . . .   19
   6.17 REQUIREMENT FOR CONFORMANT IMPLEMENTATIONS . . . . . . . . .   19
        6.17.1    Interoperable Configurations . . . . . . . . . . .   20
        6.17.2    Relationship to ISO 8571--The FTAM Standard  . . .   21
        6.17.3    Requirements for Document Type Support . . . . . .   21
        6.17.4    Initiators . . . . . . . . . . . . . . . . . . . .   22
        6.17.5    Responders . . . . . . . . . . . . . . . . . . . .   23
        6.17.6    Senders  . . . . . . . . . . . . . . . . . . . . .   24
             6.17.6.1  Initiator Senders . . . . . . . . . . . . . .   25
             6.17.6.2  Responder Senders . . . . . . . . . . . . . .   25
        6.17.7    Receivers  . . . . . . . . . . . . . . . . . . . .   25
             6.17.7.1  Initiator Receivers . . . . . . . . . . . . .   26
             6.17.7.2  Responder Receivers . . . . . . . . . . . . .   26
        6.17.8    Minimum Ranges . . . . . . . . . . . . . . . . . .   26
        6.17.9    Use of Lower Layer Services  . . . . . . . . . . .   29
   6.18 IMPLEMENTATION PROFILES  . . . . . . . . . . . . . . . . . .   29
        6.18.1    General Requirements for the Defined Implementation
                  Profiles . . . . . . . . . . . . . . . . . . . . .   30
        6.18.2    Intentionally Left Empty . . . . . . . . . . . . .   30
        6.18.3    Document Type Requirements for the Defined
                  Implementation Profiles  . . . . . . . . . . . . .   30
        6.18.4    Parameters for the Defined Implementation Profiles   31
        6.18.5    Parameter Ranges for the Defined Implementation
                  Profiles . . . . . . . . . . . . . . . . . . . . .   32
        6.18.6    File Attribute Support for Implementations . . . .   32
   6.19 PROVISION OF SPECIFIC FUNCTION . . . . . . . . . . . . . . .   35
        6.19.1    Implementation Profile T1:  Simple File Transfer .   35
        6.19.2    Implementation Profile T2:  Positional File Transfer  35
        6.19.3    Implementation Profile T3:  Full File Transfer . .   36
        6.19.4    Implementation Profile A1: Simple File Access  . .   37
        6.19.5    Implementation Profile A2:  Full File Access . . .   37
        6.19.6    Implementation Profile M1:  Management . . . . . .   38
   6.20 HARMONIZATION  . . . . . . . . . . . . . . . . . . . . . . .   38
   6.21 APPENDIX A:    FTAM DOCUMENT TYPES . . . . . . . . . . . . .   39


7. CCITT 1984 X.400 BASED MESSAGE HANDLING SYSTEM  . . . . . . . . .    1
   7.1  INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . . .    1
   7.2  SCOPE  . . . . . . . . . . . . . . . . . . . . . . . . . . .    2
   7.3  STATUS . . . . . . . . . . . . . . . . . . . . . . . . . . .    3
   7.4  ERRATA . . . . . . . . . . . . . . . . . . . . . . . . . . .    3
   7.5  PRMD to PRMD . . . . . . . . . . . . . . . . . . . . . . . .    3
        7.5.1     Introduction . . . . . . . . . . . . . . . . . . .    3
        7.5.2     Service Elements and Optional User Facilities  . .    4
             7.5.2.1   Classification of Support for Services  . . .    4
                  7.5.2.1.1 Support (S)  . . . . . . . . . . . . . .    5
                  7.5.2.1.2 Non Support (N)  . . . . . . . . . . . .    5
                  7.5.2.1.3 Not Used (N/U) . . . . . . . . . . . . .    6
                  7.5.2.1.4 Not Applicable (N/A) . . . . . . . . . .    6
             7.5.2.2   Summary of Supported Services . . . . . . . .    6
             7.5.2.3   MT Service Elements and Optional User
                  Facilities . . . . . . . . . . . . . . . . . . . .    6
             7.5.2.4   IPM Service Elements and Optional User
                  Facilities . . . . . . . . . . . . . . . . . . . .    8
        7.5.3     X.400 Protocol Definitions . . . . . . . . . . . .    9
             7.5.3.1   Protocol Classification . . . . . . . . . . .   10
             7.5.3.2   General Statements on Pragmatic Constraints .   10
             7.5.3.3   MPDU Size . . . . . . . . . . . . . . . . . .   11
             7.5.3.4   P1 Protocol Elements  . . . . . . . . . . . .   11
                  7.5.3.4.1 P1 Envelope Protocol Elements  . . . . .   11
             7.5.3.5   ORName Protocol Elements  . . . . . . . . . .   16
             7.5.3.6   P2 Protocol Profile (Based on [X.420])  . . .   18
                  7.5.3.6.1 P2 Protocol - Heading  . . . . . . . . .   19
                  7.5.3.6.2 P2 Protocol - BodyParts  . . . . . . . .   21
                  7.5.3.6.3 P2 BodyPart Protocol Elements  . . . . .   23
        7.5.4     Reliable Transfer Server (RTS) . . . . . . . . . .   25
             7.5.4.1   Implementation Strategy . . . . . . . . . . .   25
             7.5.4.2   RTS option selection  . . . . . . . . . . . .   25
             7.5.4.3   RTS Protocol Options and Clarifications . . .   26
             7.5.4.4   RTS Protocol Limitations  . . . . . . . . . .   29
        7.5.5     Use of Session Services  . . . . . . . . . . . . .   31
        7.5.6     Data Transfer Syntax . . . . . . . . . . . . . . .   31
   7.6  PRMD to ADMD and ADMD to ADMD  . . . . . . . . . . . . . . .   31
        7.6.1     Introduction . . . . . . . . . . . . . . . . . . .   31
        7.6.2     Additional ADMD Functionality  . . . . . . . . . .   33
             7.6.2.1   Relay Responsibilities of an ADMD . . . . . .   33
             7.6.2.2   P1 Protocol Classification Changes  . . . . .   34
             7.6.2.3   O/R Names . . . . . . . . . . . . . . . . . .   34
             7.6.2.4   P1 ADMD Name  . . . . . . . . . . . . . . . .   35
        7.6.3     Interworking with Integrated UAs . . . . . . . . .   35
        7.6.4     Differences with Other Profiles  . . . . . . . . .   35
             7.6.4.1   TTC Profile . . . . . . . . . . . . . . . . .   35
             7.6.4.2   CEPT Profile  . . . . . . . . . . . . . . . .   36
        7.6.5     Connection of PRMDs to Multiple ADMDs  . . . . . .   36
        7.6.6     Connection of an ADMD to a Routing PRMD  . . . . .   36
        7.6.7     Management Domain Names  . . . . . . . . . . . . .   37
        7.6.8     Envelope Validation Errors . . . . . . . . . . . .   37
        7.6.9     Quality of Service . . . . . . . . . . . . . . . .   38
             7.6.9.1   Domain Availability . . . . . . . . . . . . .   38
                  7.6.9.1.1 ADMD Availability  . . . . . . . . . . .   38
                  7.6.9.1.2 PRMD Availability  . . . . . . . . . . .   38
             7.6.9.2   Delivery Times  . . . . . . . . . . . . . . .   38
        7.6.10    Billing Information  . . . . . . . . . . . . . . .   39
        7.6.11    Transparency . . . . . . . . . . . . . . . . . . .   39
        7.6.12    RTS Password Management  . . . . . . . . . . . . .   40
        7.6.13    For Further Study  . . . . . . . . . . . . . . . .   40
   7.7  INTER and INTRA PRMD CONNECTIONS . . . . . . . . . . . . . .   40
        7.7.1     Introduction . . . . . . . . . . . . . . . . . . .   40
        7.7.2     The Relaying PRMD  . . . . . . . . . . . . . . . .   41
             7.7.2.1   Relay Responsibilities of a PRMD  . . . . . .   41
             7.7.2.2   Interaction with an ADMD  . . . . . . . . . .   41
        7.7.3     Intra PRMD Connections . . . . . . . . . . . . . .   42
             7.7.3.1   Relay Responsibilities of an MTA  . . . . . .   42
             7.7.3.2   Loop Suppression within a PRMD  . . . . . . .   43
             7.7.3.3   Routing Within a PRMD . . . . . . . . . . . .   44
                  7.7.3.3.1 Class Designations . . . . . . . . . . .   44
                  7.7.3.3.2 Specification of MTA Classes . . . . . .   46
                  7.7.3.3.3 Consequences of Using Certain Classes of
                       MTAs  . . . . . . . . . . . . . . . . . . . .   46
             7.7.3.4   Uniqueness of MPDUidentifiers Within a PRMD .   47
        7.7.4     Service Elements and Optional User Facilities  . .   47
        7.7.5     X.400 Protocol Definitions . . . . . . . . . . . .   48
             7.7.5.1   Protocol Classification . . . . . . . . . . .   48
             7.7.5.2   P1 Protocol Elements  . . . . . . . . . . . .   48
             7.7.5.3   Reliable Transfer Server (RTS)  . . . . . . .   51
   7.8  ERROR HANDLING . . . . . . . . . . . . . . . . . . . . . . .   51
        7.8.1     MPDU Encoding  . . . . . . . . . . . . . . . . . .   52
        7.8.2     Contents . . . . . . . . . . . . . . . . . . . . .   52
        7.8.3     Envelope . . . . . . . . . . . . . . . . . . . . .   52
             7.8.3.1   Pragmatic Constraint Violations . . . . . . .   52
             7.8.3.2   Protocol Violations . . . . . . . . . . . . .   52
             7.8.3.3   O/R Names . . . . . . . . . . . . . . . . . .   52
             7.8.3.4   TraceInformation  . . . . . . . . . . . . . .   53
             7.8.3.5   InternalTraceInfo . . . . . . . . . . . . . .   54
             7.8.3.6   Unsupported X.400 Protocol Elements . . . . .   54
                  7.8.3.6.1 deferredDelivery . . . . . . . . . . . .   54
                  7.8.3.6.2 PerDomainBilateralInfo . . . . . . . . .   55
                  7.8.3.6.3 ExplicitConversion . . . . . . . . . . .   55
                  7.8.3.6.4 alternateRecipientAllowed  . . . . . . .   55
                  7.8.3.6.5 contentReturnRequest . . . . . . . . . .   55
             7.8.3.7   Unexpected Values for INTEGER Protocol Elements  55
                  7.8.3.7.1 Priority . . . . . . . . . . . . . . . .   55
                  7.8.3.7.2 ExplicitConversion . . . . . . . . . . .   56
                  7.8.3.7.3 ContentType  . . . . . . . . . . . . . .   56
             7.8.3.8   Additional Elements . . . . . . . . . . . . .   56
        7.8.4     Reports  . . . . . . . . . . . . . . . . . . . . .   56
   7.9  MHS USE OF DIRECTORY SERVICES  . . . . . . . . . . . . . . .   56
        7.9.1     Directory Service Elements . . . . . . . . . . . .   56
        7.9.2     Use of Names and Addresses . . . . . . . . . . . .   57
   7.10 CONFORMANCE  . . . . . . . . . . . . . . . . . . . . . . . .   58
        7.10.1    Introduction . . . . . . . . . . . . . . . . . . .   58
        7.10.2    Definition of Conformance  . . . . . . . . . . . .   58
        7.10.3    Conformance Requirements . . . . . . . . . . . . .   60
             7.10.3.1  Introduction  . . . . . . . . . . . . . . . .   60
             7.10.3.2  Initial Conformance . . . . . . . . . . . . .   60
                  7.10.3.2.1     Interworking  . . . . . . . . . . .   61
                  7.10.3.2.2     Service . . . . . . . . . . . . . .   61
   7.11 APPENDIX A:    INTERPRETATION OF X.400 SERVICE ELEMENTS  . .   62
   7.12 APPENDIX B:    RECOMMENDED X.400 PRACTICES . . . . . . . . .   66
        7.12.1    RECOMMENDED PRACTICES IN P2  . . . . . . . . . . .   66
        7.12.2    RECOMMENDED PRACTICES IN RTS . . . . . . . . . . .   66
        7.12.3    RECOMMENDED PRACTICES FOR ORName . . . . . . . . .   67
        7.12.4    POSTAL ADDRESSING  . . . . . . . . . . . . . . . .   70
        7.12.5    EDI use of X.400 . . . . . . . . . . . . . . . . .   71
             7.12.5.1  Introduction and Scope  . . . . . . . . . . .   71
             7.12.5.2  Model . . . . . . . . . . . . . . . . . . . .   71
             7.12.5.3  Protocol Elements Supported for EDI . . . . .   73
             7.12.5.4  Addressing and Routing  . . . . . . . . . . .   73
        7.12.6    USA Body Parts . . . . . . . . . . . . . . . . . .   74
   7.13 APPENDIX C:    RENDITION OF IA5Text AND T61String CHARACTERS   75
        7.13.1    GENERATING AND IMAGING IA5Text . . . . . . . . . .   75
        7.13.2    GENERATING AND IMAGING T61String . . . . . . . . .   75
   7.14 APPENDIX D:    DIFFERENCES IN INTERPRETATION DISCOVERED
                       THROUGH TESTING OF THE MHS FOR THE CeBit 87
                       DEMONSTRATION . . . . . . . . . . . . . . . .   76
        7.14.1    ENCODING OF RTS USER DATA  . . . . . . . . . . . .   76
        7.14.2    EXTRA SESSION FUNCTIONAL UNITS . . . . . . . . . .   76
        7.14.3    MIXED CASE IN THE MTA NAME . . . . . . . . . . . .   77
        7.14.4    X.410 ACTIVITY IDENTIFIER  . . . . . . . . . . . .   77
        7.14.5    ENCODING OF PER RECIPIENT FLAG AND PER MESSAGE FLAG  77
        7.14.6    ENCODING OF EMPTY BITSTRINGS . . . . . . . . . . .   78
        7.14.7    ADDITIONAL OCTETS FOR BITSTRINGS . . . . . . . . .   78
        7.14.8    APPLICATION PROTOCOL IDENTIFIER  . . . . . . . . .   78
        7.14.9    INITIAL SERIAL NUMBER IN S-CONNECT . . . . . . . .   78
        7.14.10   CONNECTION DATA ON RTS RECOVERY  . . . . . . . . .   78
        7.14.11   ACTIVITY RESUME  . . . . . . . . . . . . . . . . .   78
        7.14.12   OLD ACTIVITY IDENTIFIER  . . . . . . . . . . . . .   79
        7.14.13   NEGOTIATION DOWN TO TRANSPORT CLASS 0  . . . . . .   79
   7.15 APPENDIX E:    WORLDWIDE X.400 CONFORMANCE PROFILE MATRIX  .   80
   7.16 APPENDIX F:    INTERWORKING WARNINGS . . . . . . . . . . . .   91


8. DIRECTORY SERVICES PROTOCOLS  . . . . . . . . . . . . . . . . . .    1
   8.1  INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . . .    1
   8.2  SCOPE AND FIELD OF APPLICATION . . . . . . . . . . . . . . .    2
   8.3  STATUS     . . . . . . . . . . . . . . . . . . . . . . . . .    3
   8.4  USE OF DIRECTORIES . . . . . . . . . . . . . . . . . . . . .    3
   8.5  DIRECTORY ASEs, APPLICATION CONTEXTS, AND PORTS  . . . . . .    4
   8.6  SCHEMAS  . . . . . . . . . . . . . . . . . . . . . . . . . .    5
        8.6.1     Maintenance of Structures and Naming Rules . . . .    5
        8.6.2     Maintenance of object classes and subclasses . . .    6
        8.6.3     Maintenance of Attribute Types . . . . . . . . . .    6
        8.6.4     Maintenance of Attribute Syntaxes  . . . . . . . .    6
   8.7  CLASSIFICATION OF SUPPORT FOR ATTRIBUTE TYPES  . . . . . . .    6
        8.7.1     Mandatory Support  . . . . . . . . . . . . . . . .    7
        8.7.2     Optional Support . . . . . . . . . . . . . . . . .    7
   8.8  INTORDUCTION TO PRAGMETIC CONSTRAINTS  . . . . . . . . . . .    8
   8.9  GENERAL CONSTRAINTS  . . . . . . . . . . . . . . . . . . . .    8
        8.9.1     Character Sets . . . . . . . . . . . . . . . . . .    8
        8.9.2     APDU Size Considerations . . . . . . . . . . . . .    8
        8.9.3     Service Control (SC) Considerations  . . . . . . .    9
        8.9.4     Priority Service Control . . . . . . . . . . . . .    9
   8.10 CONSTRAINTS ON OPERATIONS  . . . . . . . . . . . . . . . . .   10
        8.10.1    Filters  . . . . . . . . . . . . . . . . . . . . .   10
        8.10.2    Errors . . . . . . . . . . . . . . . . . . . . . .   10
   8.11 CONSTRAINTS ON ATTRIBUTE TYPES . . . . . . . . . . . . . . .   10
        8.11.1    Attribute Values . . . . . . . . . . . . . . . . .   10
   8.12 CONFORMANCE  . . . . . . . . . . . . . . . . . . . . . . . .   15
        8.12.1    DUA Conformance  . . . . . . . . . . . . . . . . .   15
        8.12.2    DSA Conformance  . . . . . . . . . . . . . . . . .   16
        8.12.3    Directory Systems Conformance Classes  . . . . . .   17
        8.12.4    Authentication Conformance . . . . . . . . . . . .   17
        8.12.5    Authentication Conformance Classes . . . . . . . .   18
   8.13 DISTRIBUTED OPERATIONS . . . . . . . . . . . . . . . . . . .   18
        8.13.1    Referrals and Chaining . . . . . . . . . . . . . .   19
   8.14 UNDERLYING SERVICES  . . . . . . . . . . . . . . . . . . . .   19
        8.14.1    ROSE . . . . . . . . . . . . . . . . . . . . . . .   19
        8.14.2    Session  . . . . . . . . . . . . . . . . . . . . .   19
   8.15 ACCESS CONTROL . . . . . . . . . . . . . . . . . . . . . . .   19
   8.16 AUTHENTICATION . . . . . . . . . . . . . . . . . . . . . . .   19
   8.17 TEST CONSIDERATIONS  . . . . . . . . . . . . . . . . . . . .   20
        8.17.1    Major elements of Architecture . . . . . . . . . .   20
        8.17.2    Search Operation . . . . . . . . . . . . . . . . .   21
   8.18 ERRORS . . . . . . . . . . . . . . . . . . . . . . . . . . .   21
        8.18.1    Permanent vs. Temporary Service Errors . . . . . .   21
   8.19 APPENDIX A     Definitions . . . . . . . . . . . . . . . . .   22
   8.20 APPENDIX B     Attributes and Object Classes . . . . . . . .   23
   8.21 APPENDIX C     The Use of ROSE . . . . . . . . . . . . . . .   28
   8.22 APPENDIX D     Guidelines  . . . . . . . . . . . . . . . . .   29
   8.23 APPENDIX E     Glossary  . . . . . . . . . . . . . . . . . .   30

9. SECURITY  . . . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   9.1  Definitions  . . . . . . . . . . . . . . . . . . . . . . . .    1
   9.2  Matrix of Security Services and OSI Layers . . . . . . . . .    2

10.     OBJECT IDENTIFIER: STRUCTURE AND ALLOCATION  . . . . . . . .    1
   10.1 Specific ASE Requirements for ACSE Presentation and Session     5
        10.1.1    FTAM . . . . . . . . . . . . . . . . . . . . . . .    5
             10.1.1.1  Phase 2 . . . . . . . . . . . . . . . . . . .    5
        10.1.2    MHS  . . . . . . . . . . . . . . . . . . . . . . .    8
             10.1.2.1  Phase 1 . . . . . . . . . . . . . . . . . . .    8
        10.1.3    DS . . . . . . . . . . . . . . . . . . . . . . . .    9
             10.1.3.1  Phase 1 . . . . . . . . . . . . . . . . . . .    9

11.     REFERENCES . . . . . . . . . . . . . . . . . . . . . . . . .    1
   11.1 CCITT  . . . . . . . . . . . . . . . . . . . . . . . . . . .    1
   11.2 ISO  . . . . . . . . . . . . . . . . . . . . . . . . . . . .    2
   11.3 IEEE . . . . . . . . . . . . . . . . . . . . . . . . . . . .    8
   11.4 NBS  . . . . . . . . . . . . . . . . . . . . . . . . . . . .    9
   11.5 MAP  . . . . . . . . . . . . . . . . . . . . . . . . . . . .   10
   11.6 TOP  . . . . . . . . . . . . . . . . . . . . . . . . . . . .   10
   11.7 CEN/CENELEC  . . . . . . . . . . . . . . . . . . . . . . . .   10
   11.8 SPAG . . . . . . . . . . . . . . . . . . . . . . . . . . . .   10

                            List of Figures

Figure 2.1  LSAP bit pattern   . . . . . . . . . . . . . . . . . . .    1
Figure 2.2  I-Field Format . . . . . . . . . . . . . . . . . . . . .    4

Figure 4.1  AK exchange on idleconnection  . . . . . . . . . . . . .    6

Figure 6.1  Model of file transfer/access  . . . . . . . . . . . . .    2
Figure 7.1  The layered structure of this implementation agreement .    1
Figure 7.2  This agreement applies to the interface between:  (A) PRMD  
          and PRMD; (B) PRMD and ADMD; (C) ADMD and ADMD; and  (D)    
          MTA and MTA  . . . . . . . . . . . . . . . . . . . . . . .    3
Figure 7.3  Interconnection of private domains . . . . . . . . . . .    4
Figure 7.4  X.409 Definition of Privately Defined BodyParts  . . . .   22
Figure 7.5  An ADMD may (b) or may not (a) serve as a relay  . . . .   33
Figure 7.6  Relaying PRMD  . . . . . . . . . . . . . . . . . . . . .   41
Figure 7.7  Intra PRMD connections . . . . . . . . . . . . . . . . .   42
Figure 7.8  MD C must know of A to route the message . . . . . . . .   42
Figure 7.9  Definition of InternalTraceInfo  . . . . . . . . . . . .   43
Figure 7.10 Defined Actions in MTASuppliedInfo . . . . . . . . . . .   44
Figure 7.11 Example of a confirguration to be avoided  . . . . . . .   47


Figure 8.1  Structure of this Implementation Agreement . . . . . . .    1
Figure 8.2  Centralized Directory Model  . . . . . . . . . . . . . .    2
Figure 8.3  Distributed Directory Model  . . . . . . . . . . . . . .    3
Figure 8.4  Access to the Directory  . . . . . . . . . . . . . . . .    5
Figure 8.5  APDU Exchange  . . . . . . . . . . . . . . . . . . . . .    8
Figure 8.6  Logical DSA Application Environment  . . . . . . . . . .    9

                            List of Tables

Table 5.1  Session States  . . . . . . . . . . . . . . . . . . . . .   18
Table 5.2  Incoming Events . . . . . . . . . . . . . . . . . . . . .   19

Table 6.1  Parameters for FTAM-1, -2, -3 . . . . . . . . . . . . . .    8
Table 6.2  Parameters for NBS-6, NBS-7, NBS-8  . . . . . . . . . . .   10
Table 6.3  FTAM primitive data types . . . . . . . . . . . . . . . .   11
Table 6.4  IRV Graphic Character Allocations . . . . . . . . . . . .   13
Table 6.5  Interoperable configurations  . . . . . . . . . . . . . .   21
Table 6.6  Required minimal parameter support  . . . . . . . . . . .   27
Table 6.7  Implementation profile support requirements . . . . . . .   34
Table 6.8  Implementation Profiles (NBS) and Profiles (SPAG/CEN-CLC)   38
Table 6.9  Information objects in NBS-6  . . . . . . . . . . . . . .   41
Table 6.10 Information objects in NBS-7  . . . . . . . . . . . . . .   46
Table 6.11 Information objects in NBS-8  . . . . . . . . . . . . . .   50
Table 6.12 Datatypes for keys  . . . . . . . . . . . . . . . . . . .   52
Table 6.12 Information objects in NBS-9  . . . . . . . . . . . . . .   56
Table 6.14 Basic constraints for NBS Ordered flat  . . . . . . . . .   60
Table 6.15 Identity constraints in NBS Ordered flat  . . . . . . . .   61

Table 7.1   Basic MT service elements . . . . . . . . . . . . . . .    6
Table 7.2   MT optional user facilities provided to the UA-selectable on
          a per-message basis  . . . . . . . . . . . . . . . . . . .    7
Table 7.3  MT optional user facilities provided to the UA agreed for  
          any contractual period of time . . . . . . . . . . . . . .    7
Table 7.4   Basic IPM service elements . . . . . . . . . . . . . . .    8
Table 7.5  IPM optional facilities agreed for a contractual period of  
          time . . . . . . . . . . . . . . . . . . . . . . . . . . .    8
Table 7.6   IPM optional user facilities selectable on a per-message    
          basis  . . . . . . . . . . . . . . . . . . . . . . . . . .    9
Table 7.7   Protocol Classifications . . . . . . . . . . . . . . . .   10
Table 7.8   P1 protocol elements . . . . . . . . . . . . . . . . . .   12
Table 7.9   ORName protocol elements . . . . . . . . . . . . . . . .   17
Table 7.10  P2 heading protocol elements . . . . . . . . . . . . . .   19
Table 7.11  P2 BodyParts . . . . . . . . . . . . . . . . . . . . . .   23
Table 7.12  Checkpoint window size of IP . . . . . . . . . . . . . .   29
Table 7.13  RTS protocol elements  . . . . . . . . . . . . . . . . .   30
Table 7.14  P1 Protocol Classification Changes for a Delivering ADMD   34
Table 7.15  Delivery Time Targets  . . . . . . . . . . . . . . . . .   38
Table 7.16  Forced Nondelivery Times . . . . . . . . . . . . . . . .   39
Table 7.17  Conformant MTA Classifications . . . . . . . . . . . . .   45
Table 7.18  P1 Protocol Elements . . . . . . . . . . . . . . . . . .   49
Table 7B.1  Printable string to ASCII mapping  . . . . . . . . . . .   69
Table 7E.1  Protocol element comparison of RTS . . . . . . . . . . .   81
Table 7E.2  Protocol element comparison of P1  . . . . . . . . . . .   83
Table 7E.3  Protocol element comparison of P2  . . . . . . . . . . .   88

Table 8.1  Pragmatic Constraints for Selected Attributes.  . . . . .   12

Table 9.1  OSI Layers Desirable for Placing Security . . . . . . . .    3

 
1. GENERAL INFORMATION

   1.1  PURPOSE OF THIS DOCUMENT

   This document records stable implementation agreements of OSI
   protocols among the organizations participating in the NBS Workshop
   for Implementors of OSI.  Stable in the context of this document
   means that:

        1)   The agreements are based on final standards
             (e.g., ISO-IS or CCITT Recommendations) or
             nearly final (e.g., ISO-DIS) with no
             significant changes expected, and,

        2)   The agreements have been approved by the NBS
             Workshop Plenary for progression from the "On-
             Going" agreements document to the draft stable
             agreements document and after a period of
             review have been passed to these final stable
             agreements.  The only changes allowed will be
             clarifications, errata and the correction of
             omissions discovered in their implementation.

   For these reasons, the agreements are considered advanced enough for
   use in product and test suite development, as well as for procurement
   references.

   Future releases of these Stable Agreements will add and/or extend
   functionality offered by this version.  When required, new versions
   will be introduced on a yearly basis.  It is the NBS Workshop intent
   that new versions of this Stable Agreements document will be
   compatible with the present version.  If this proves impractical, the
   agreements will attempt to provide mechanisms and guidelines which
   maximize interoperability.


   1.2  PURPOSE OF THE WORKSHOP

   In February, 1983, at the request of industry, NBS organized the NBS
   Workshop for Implementors of OSI to bring together future users and
   potential suppliers of OSI protocols.  The workshop accepts as input
   the specifications of emerging standards for protocols and produces as
   output agreements on the implementation and testing particulars of
   these protocols.  This process is expected to expedite the development
   of OSI protocols and promote interoperability of independently
   manufactured data communications equipment.

   1.3  WORKSHOP ORGANIZATION

   The Workshop organizes its work through Special Interest Groups
   (SIGs) that prepare technical documentation.  An executive committee
   of SIG chairpersons led by the overall Workshop chairperson
   administers the workshop.  NBS invites highly qualified technical
   leaders from participating organizations to assume leadership roles in
   the SIGs.  The SIGs are encouraged to coordinate with standards
   organizations and user groups, and to seek widespread technical
   consensus on implementation agreements through international
   discussions and liaison activities.

   The Workshop meets four times a year at the National Bureau of
   Standards in Gaithersburg, Maryland where each SIG is required to
   convene its meeting.  In addition, a plenary assembly of all workshop
   delegates is convened for consideration of SIG motions and other
   workshop business.  SIGs are also encouraged to hold interim meetings
   at varied locations around the world.

   The Workshop is an open public forum.  Registration materials,
   documents, and workshop schedules are available from:

                  
                  National Bureau of Standards
                  NBS Workshop for Implementors of OSI
                  Building 225, Room B-217
                  Gaithersburg, Maryland 20899

2. SUB NETWORKS

   2.1  INTRODUCTION

   This chapter provides agreements about subnetwork services used in
   providing the OSI Network Layer.


   2.2  SCOPE AND FIELD OF APPLICATION

   These agreements cover subnetwork types including local area networks,
   packet switched networks, circuit switched networks, ISDN, and others.


   2.3  STATUS

   This version was completed on December 18, 1987.

   Ongoing work for other agreements and for future versions of these
   agreements is contained in the "On-Going" agreements document,
   including provisions for ISDN.


   2.4  ERRATA


   2.5  LOCAL AREA NETWORKS

        2.5.1     IEEE 802.2 LOGICAL LINK CONTROL

        The following decisions have been reached with respect to this
        protocol.

        l.   Link Service Access Point (LSAP)

             The IEEE 802 committee has assigned the code below to
             address systems using any ISO network layer protocol.  Note
             that bit zero is transmitted first.

             The most significant bit is bit 7, thus this bit pattern
             represents hexadecimal FE.

                        0   l   2   3   4   5   6   7 
                      ZDDDBDDDBDDDBDDDBDDDBDDDBDDDBDDD?
                      3 0 3 l 3 l 3 l 3 l 3 l 3 l 3 1 3
                      @DDDADDDADDDADDDADDDADDDADDDADDDY

                      Figure 2.1  LSAP bit pattern 


        2.   Type and Class

             Only the connectionless type l, class l IEEE 802 link
             service will be used.


        2.5.2     IEEE 802.3 CSMA/CD ACCESS METHOD


        The following implementation agreements have been reached with
        respect to the IEEE 802.3 CSMA/CD Access Method and Physical
        Layer Specifications: for 10 BASE 5:

             o    The address length shall be 48 bits


        The following implementation agreements have been reached with
        respect to 10 BROAD 36 Networks:

                  1.   Single Cable Networks

                       -    The translator frequency shall be 192.25 Mhz
                       -    The channel allocations are

                       Reverse Channels              Forward Channels

                       T12, T13, T14                 L, M, N
                       T13, T14, 2'                  M, N, O
                       T14, 2', 3'                   N, O, P
                       2', 3', 4'                    O, P, Q
                       3', 4', 4A'                   P, Q, R
                       4', 4A', 5'                   Q, R, S

                  2.   Dual Cable Networks

                       For nontranslated dual cable networks forward and
                       reverse frequencies are the same.  Permissible
                       channel allocations are:

                                 T12, T13, T14
                                 T13, T14, 2'
                                 T14, 2', 3'
                                 2', 3', 4'
                                 3', 4', 4A'
                                 4', 4A', 5'
                                 L, M, N
                                 M, N, O
                                 N, O, P
                                 O, P, Q
                                 Q, R, S

                  3.   When both IEEE 802.4 and IEEE 802.3 10 BROAD 36
                       networks coexist on the broadband cable system the
                       preferred channel allocations are:

                                      Reverse             Forward

                  IEEE 802.3          T12, T13, T14       L, M, N

                  IEEE 802.4          6', FM1'            T, U

                  channels            3', 4'              P, Q
                  reserved for        4A', 5'             R, S
                  future use



        2.5.3     IEEE 802.4 TOKEN BUS ACCESS METHOD

        The following options are agreed to with respect to Draft J of
        token bus:  

             o    Data Rate:

                  -    10 Mb (Broadband)
                  -    5 Mb (carrierband)

             o    Addressing: 48 bit

             o    The lmeOption, Priority Mechanism, shall be implemented

             o    Broadband Channel Assignments

   
                  Forward                       Reverse
                       P                             3'
                       Q                             4'
                       R                             4A'
                       S                             5'
                       T                             6'
                       U                             FM1'


        2.5.4     IEEE 802.5 TOKEN RING ACCESS METHOD

        The following implementation agreements have been reached with
        respect to the IEEE Standard 802.5, Token Passing Ring Access
        Method and Physical Layer specification.

             o    The data signalling rate shall be 4 Mbit/s

             o    The address length shall be 48 bits

             o    The message priority (PM) of the AMP data unit shall be
                  7

             o    The ALL_STATIONS_THIS_RING_ADDRESS shall be
                  X'COOOFFFFFFFF'

             o    The TRR value shall be 4 milliseconds

             o    The THT value shall be 8.9 milliseconds

             o    The TQP value shall be 20 milliseconds

             o    The TVX value shall be 10 milliseconds

             o    The TNT value shall be 2.6 milliseconds

             o    The TAM value shall be 7 seconds

             o    The TSM value shall be 15 seconds

             o    The MAC Information field (I-field) shall be defined as
                  follows:

             ZDDDDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDDDD?
             3 Starting Sequence 3    I-Field       3  End Sequence  3
             @DDDDDDDDDDDDDDDDDDDADDDDDDDDDDDDDDDDDDADDDDDDDDDDDDDDDDY

                       and the:

                  1)   Starting Sequence includes: SD, AC, FC, DA, SA
                  2)   Ending Sequence includes: FCS, ED, FS


                       Figure 2.2  I-Field Format


             o    With the above timer and MAC I-field definitions, the
                  following limits are defined:

                  -    Protocol limits the I-field to a maximum of 4425
                       bytes.

                  -    All stations shall support I-fields that have a
                       minimum of one byte and a maximum of at least 2000
                       bytes.


   2.6  WIDE AREA NETWORKS


        2.6.1     CCITT RECOMMENDATION X.25

        The procedures required to describe the DTE/DTE interface and the
        DTE side of the DTE/DCE interface, for systems attached to
        subnetworks providing an X.25 interface shall be as defined in
        ISO 7776 and ISO 8208.

3. NETWORK LAYER


   3.1  INTRODUCTION

   This chapter presents agreements for providing the OSI network
   service.  Also contained here are agreements on network layer
   addressing and routing.


   3.2  SCOPE AND FIELD OF APPLICATION

   These agreements cover both connectionless-mode and connection-mode
   network services.


   3.3  STATUS

   This version of the agreements was completed on December 18, 1987.

   Ongoing work for other agreements and for future versions of these
   agreements is contained in the "On-Going" agreements document,
   including provisions for ISDN, and including specific aspects of using
   the X.25 PLP over LANs.


   3.4  ERRATA


   3.5  CONNECTIONLESS-MODE NETWORK SERVICE (CLNS)


        3.5.1     Provision of CLNS over Local Area Networks (LANS)

        When providing CLNS over a LAN subnetwork, the following shall
        apply:

             1.   The definition of CLNS shall be as specified in ISO
                  8348/AD1.

             2.   The protocol used to provide CLNS shall be ISO 8473
                  with agreements as specified in 3.5.3.1.


        3.5.2     Provision of CLNS over X.25 Subnetworks

        When providing CLNS over X.25 subnetworks, the following shall
        apply:

             1.   The definition of CLNS shall be as specified in ISO
                  8348/AD1.

             2.   The protocol used to provide CLNS shall be ISO 8473
                  with agreements as specified in 3.5.3.1.

             3.   The necessary subnetwork dependant convergence function
                  shall be as defined in ISO 8473 for operation over X.25
                  subnetworks, with agreements as specified in 3.5.3.2.

             4.   The X.25 PLP shall be as defined in ISO 8208.



        3.5.3     Agreements on Protocols


             3.5.3.1   ISO 8473

             1. Subsets of the protocol:

                  o    Implementations will not transmit PDUs encoded
                       using the inactive subset. Received PDUs encoded
                       using the inactive subset will be discarded.

                  o    The non-segmenting subset will not be used. 
                       Implementations will not generate data PDUs
                       without a segmentation part.  However,
                       implementations will receive and correctly process
                       PDUs which do not contain the segmentation part.

             2. Mandatory Functions:

                  o    The lifetime parameter shall be used as specified
                       in section 6.4 of ISO 8473.  The parameter shall
                       have an initial value of at least three times the
                       network span or  three times the maximum transit
                       delay (in units of 500 milliseconds), whichever is
                       greater.

                  o    The reassembly timer for an initial PDU at the
                       reassembly point shall be no greater than the
                       largest value of all lifetime parameters contained
                       in all derived PDUs.

             3. Optional Functions:

                  o    The Security parameter is not defined by these
                       Agreements.  Implementations shall not transmit
                       the parameter except where defined by bilateral
                       agreements.

                  o    Partial and complete source Routing will not be
                       supported.

                  o    Partial record of Route will be supported by
                       Intermediate systems.

                  o    ISO 8473 will be followed with respect to QOS.


             3.5.3.2   Subnetwork Dependent Convergence Function

             1.   When 8473 SNDC functions are used over X.25
                  subnetworks, the default throughput class shall be used
                  if this facility is available.


   3.6  CONNECTION-MODE NETWORK SERVICE (CONS)

   The following agreements concern provision of the connection-mode
   Network Service.


        3.6.1     Mandatory Method of Providing CONS

        When providing CONS using X.25 1984, the following shall apply:

        o    The definition of the CONS is as specified in ISO 8348,
             Network Service Definition.

        o    The mapping of the elements of the CONS to the elements of
             the X.25 Packet Level Protocol (PLP) is as specified in ISO
             8878, Use of X.25 to Provide the Connection-mode Network
             Service.

        o    The general procedures and formats of the X.25 PLP are as
             specified in ISO 8208, X.25 Packet Level Protocol for Data
             Terminal Equipment.


        3.6.2     Additional Option:  Provision of CONS over X.25 1980
                  Subnetworks

        When providing CONS over an X.25 1980 subnetwork, the following
        shall apply:

             o    The definition of the CONS is as specified in ISO 8348,
                  Network Service Definition.

             o    The subnetwork dependant convergence protocol required
                  to provide CONS shall be as specified in ISO 8878 Annex
                  A, and referred to as the Alternative Procedures for
                  Network Connection Establishment and Release, with
                  agreements as defined in 3.6.3.2.


        3.6.3     Agreements on Protocols


             3.6.3.1   ISO 8878

             o    The Receipt Confirmation service will not be provided,
                  so the corresponding protocol elements need not be
                  implemented.

             o    The Expedited Data service will not be provided, so the
                  corresponding protocol elements need not be
                  implemented.

             o    Where the ISO 8208 diagnostic codes are not provided,
                  all  Cause/Diagnostic code combinations can be mapped
                  to the Originator/Reason code of "Undefined".


             3.6.3.2   Subnetwork Dependent Convergence Protocol (ISO
                       8878/Annex A)

             o    The Receipt Confirmation service will not be provided,
                  so the corresponding protocol elements need not be
                  implemented.

             o    The Expedited Data service will not be provided, so the
                  corresponding protocol elements need not be
                  implemented.

   3.7  ADDRESSING

   Address formats supported will conform to ISO 8348 DAD2.

        o    NSAP address formats will have a hierarchical structure.
             This will reduce the size of routing tables.

        o    If used in the Domain Specific Part (DSP), an NSAP selector
             shall be the least significant component in the hierarchy.
             The NSAP selector shall not be used to preform routing; it
             is simply intended to identify the network service user at
             the destination end system.  For those implementations
             using an NSAP selector, there shall be one and only one
             selector for each NSAP within the end system.  All NSAP
             addresses identifying a given NSAP will use the same NSAP
             selector value.


   3.8  ROUTING


        3.8.1     Static Routing

        End systems and intermediate systems supporting static routing
        will provide a local mechanism to update and, if necessary, to
        create the local routing table.  Updating and consistency
        checking will be performed by human operators.  The algorithms
        and data structures used for static routing are not specified in
        these agreements.  Implementors are free to perform these
        functions in the manner which is most appropriate to their system
        environment.


        3.8.2     End System to Intermediate System

        Dynamic routing between end systems and intermediate systems is
        performed using the protocol described in ISO 9542, End System to
        Intermediate System Routing Exchange Protocol for use in
        conjunction with ISO 8473.  The following agreements apply to the
        use of this protocol over LANs and point-to-point links.

             1.   Implementations must support any valid NSAP format. For
                  the purposes of the protocol, NSAP addresses are
                  treated simply as octet strings.

             2.   Implementations must support both Configuration
                  Information and Route Redirection Information.  No
                  subsets are permitted.

             3.   All timer values must be settable using local system
                  management.

             4.   Use of checksums must be settable using local system
                  management. Under normal use, checksums will be
                  disabled.

             5.   The QOS, Security and Priority parameters should not be
                  used for routing.  For conformance, Intermediate
                  systems must transmit these parameters in RD PDUs if
                  they are present in the data PDU which generated the
                  redirect.  However, End systems must ignore them in
                  received RD PDUs.

             6.   Both ES and IS implementations must support the
                  'optimization' described in Clause A.3 of ISO 9542 for
                  system initialization.  Its use must be selectable
                  using local system management.

             7.   This protocol employs the same LSAP as ISO 8473.

             8.   The encoding of the BSNPA address follows the syntax
                  rules for the data link being used.  On a LAN, for
                  example, it is a 48-bit MAC address.

             9.   The multicast addresses corresponding to "All
                  Intermediate Systems on the network" (All_ISN) and "All
                  End Systems on the network" (All_ESN) shall default to
                  the following:

                            All_ISN = 0900 2B00 0004
                            All_ESN = 0900 2B00 0005

             10.  The ES-IS protocol should be primarily responsible for
                  updating the Network Layer Routing Information Base
                  (RIB).  In addition, a management mechanism capable of
                  adding and deleting "static" entries into the RIB is
                  recommended.  When using the management mechanism to
                  add an entry, there should be no holding timer, and the
                  entry should be write protected from alteration by the
                  ES-IS protocol.

             Note:     This function enables route table entries to be
                       made which are static in nature.  The use of
                       static entries is not intended for normal
                       operations, but rather is provided for test and
                       debug as well as for interoperation with other OSI
                       implementations which do not support the ES-IS
                       protocol.


   3.9  MIGRATION CONSIDERATIONS

   This section considers problems arising from evolving OSI standards
   and implementations based on earlier versions of OSI standards.


        3.9.1     X.25-1980

        Until there is widespread availability of 1984 X.25 service, it
        will be necessary for X.400 systems to use those existing packet-
        switched public data networks which offer only pre-1984 X.25
        service.  While 1980 X.25 does not provide the CONS as defined by
        ISO 8348, there is no implication of non-conformance to these
        Agreements resulting there from for systems using 1980 X.25 to
        interchange data at the Network Layer, provided they conform in
        all other respects.

        This is an exception to the Agreements for providing the OSI
        Network Service, granted temporarily for practical reasons.  This
        exception will be removed when it is deemed to be no longer
        necessary, in the judgement of the Workshop.  While this
        provision is in effect, it provides an alternative method of
        using 1980 X.25 to the provisions of 3.6.2

   3.10 CONFORMANCE


4. TRANSPORT

   4.1  INTRODUCTION

   These agreements support the integration of LANs, packet networks, and
   other WANs with the smallest possible set of mandatory protocol sets,
   in accordance with the other agreements already reached.  Nothing here
   shall preclude vendors from implementing protocol suites in addition
   to the ones described in this document.

   4.2  SCOPE AND FIELD OF APPLICATION

   Two connection-oriented transport classed have been identified for
   implementation: classes 0 and 4.  Transport class 4 is endorsed for
   use over CLNS and CONS.  Transport class 0 is endorsed for use over
   CONS.

   4.3  STATUS

   Completed March 1987.

   4.4  ERRATA

   4.5  TRANSPORT CLASS 4

        4.5.1     Transport Class 4 Overview

        Transport class 4 is mandatory for communication between systems
        using the OSI CLNS and may also be used for systems using the OSI
        CONS (i.e., a private MHS, etc.).
        
        4.5.2     Protocol Agreements

        The full protocol will be available including expedited data and
        negotiation at connection establishment.  A disconnect request
        shall be issued in response to a connect request when the maximum
        number of transport connections is reached or exceeded.

             4.5.2.1   Rules for Negotiation

             o    In general, the ISO rules for negotiation will be used,
                  specifics follow.

             o    All implementations will send the l6/3l window
                  size/sequence space in the CR TPDU.  Implementations
                  must all provide the l6/3l ISO option.  Implementations
                  must be able to accept the 4/7 in a CR TPDU.

             o    The ISO maximum TPDU size is negotiable between l28 and
                  8K octets, always negotiated downward.  The ISO rules
                  are to be followed, allowing any valid size in the CR
                  TPDU.  TPDU size negotiation is a local implementation
                  issue.  Each vendor will decide how it is implemented
                  in their end system.

             o    The security parameter is optional and user defined in
                  the ISO specification.  Implementations should not send
                  the security parameter in the CR TPDU; if received the
                  parameter should be ignored.

             o    The use of checksums shall be as specified in ISO 8073
                  section 6.5.4., i.e., checksum shall be used unless
                  both transports explicitly agree negotiate to its non-
                  use.  Requesting its non-use is an implementation
                  choice.  All implementations must be able to operate
                  with checksums.
        

             o    Use of acknowledgement time parameter is optional in
                  ISO 8073.  If an implementation is operating any policy
                  which delays the transmission of AK TPDUs, the maximum
                  amount of time by which a single AK TPDU may be delayed
                  shall be indicated to the peer transport service
                  provider using the acknowledgement time parameter.  The
                  value transmitted should be expressed in units of
                  milliseconds and rounded up to the nearest whole
                  millisecond.

             o    Throughput, priority, and transit delay are optional in
                  the ISO specification.  Do not send in the CR TPDU;
                  ignore in the CC TPDU.

             o    User data in the CR TPDU and the CC TPDU are optional. 
                  No implementation should send; all implementations must
                  be prepared to receive.

             o    An unknown parameter in any received CR TPDU shall be
                  ignored.

             o    Known parameters with invalid values in a CR TPDU shall
                  be handled as follows:

             Parameter                     Action

             TSAP id                       Send DR TPDU
             TPDU size                     ignore parm, use default
             Version                       ignore parm, usedefault
             Protection (Security)         implementation dependent
             Checksum                      discard CR TPDU
             Additional Options            Protocol Error
             Alternate Protocol Classes    Protocol Error
             Acknowledge Time              ignore parm
             Throughput                    ignore parm
             Residual Error Rate           ignore parm
             Priority                      ignore parm
             Transit Delay                 ignore parm


             4.5.2.2   TRANSPORT CLASS 4 SERVICE ACCESS POINTS OR
                       SELECTORS

             The TSAP selector field in the CR and CC TPDUs shall be
             encoded as a variable length field and will be interpreted
             as an octet string.  The length of the string cannot exceed
             32 octets.


             4.5.2.3   Retransmission Timer

             It is recommended that the value used for the retransmission
             timer be based upon the round-trip delay experienced on a
             transport connection.  The implementation should maintain,
             and continually update, an estimate of the round-trip delay
             for the TC.  From this estimate, a value for the
             retransmission timer is calculated each time it is started. 
             An example technique for maintaining the estimate and
             calculating the retransmission timer is described below.  
             The value of the retransmission timer may be calculated
             according to the following formula:

                                 tT1 <DDD kE + AR 

             In this formula, E is the current estimate of the round-trip
             delay on the transport connection, AR  is the value of the
             acknowledgement time parameter received from the remote
             transport service provider during connection establishment,
             and k is some locally administered factor.

             A value for k should be chosen to keep the retransmission
             timer sufficiently small such that lost TPDUs will be
             detected quickly, but not so small that false alarms are
             generated causing unnecessary retransmission.

             The value of E may be calculated using an exponentially
             weighted average based upon regular sampling of the interval
             between transmitting a TPDU and receiving the corresponding
             acknowledgement.  Samples are taken by recording the time of
             day when a TPDU requiring acknowledgement is transmitted and
             calculating the difference between this and the time of day
             when the corresponding acknowledgement is received.  New
             samples are incorporated with the existing average according
             to the following formula.

                                 E <DDD E + (1 - `)(S - E)

             In this formula, S is the new sample and ` is a parameter
             which can be set to some value between 0 and 1.  The value
             chosen for ` determines the relative weighting placed upon
             the current estimate and the new sample. A large value of `
             weights the old estimate more heavily causing it to respond
             only slowly to variations in the round-trip delay.

             A small value weights the new sample more heavily causing a
             quick response to variations. (Note that setting ` to 1 will
             effectively disable the algorithm and result in a constant
             value for E, being that of the initial seed.)

             If ` is set to 1-2-n for some value of n, the update can be
             reduced to a subtract and shift as shown below.

                                 E <DDD E + 2-n (S - E)

             When sampling, if an AK TPDU is received which acknowledges
             multiple DT TPDUs, only a single sample should be taken
             being the round-trip delay experienced by the most recently
             transmitted DT TPDU.  This attempts to minimize in the
             sample any delay caused by the remote transport service
             provider withholding AK TPDUs.


             4.5.2.4   Keep-Alive Function

             The Class 4 protocol detects a failed transport connection
             by use of an 'inactivity timer'.  This timer is reset each
             time a TPDU is received on a connection.  If the timer ever
             expires, the connection is terminated.

             The Class 4 protocol maintains an idle connection by
             periodically transmitting an AK TPDU upon expiration of the
             'window timer'. Thus, in a simple implementation, the
             interval of one transport entity's window timer must be less
             than that of its peer's inactivity timer, and vice versa. 
             The following agreements permit communicating transport
             entities to maintain an idle connection without shared
             information about timer values.

                  o    In accordance with ISO 8073, clause 12.2.3.9.a,
                       all  implementations must respond to the receipt
                       of a duplicate AK TPDU not containing FCC by
                       transmitting an AK TPDU containing the 'flow
                       control confirmation' parameter.


                  o    Implementations must always transmit duplicate AK
                       TPDUs without FCC on expiration of the local
                       window timer (see ISO 8073, clause 12.2.3.8.1). 
                       Receipt of this TPDU by the remote transport
                       entity will cause it to respond with an AK TPDU
                       containing the 'flow control confirmation'
                       parameter.  When this is received by the local
                       transport entity, it will reset its inactivity
                       timer.  See figure 4.1.

                  o    It is a local matter for an implementation to set
                       the intervals of its timers to appropriate
                       relative values. Specifically:

                  o    The window timer must be greater than the
                       round-trip delay.  See section 4.1.4.

                  o    The inactivity timer must be greater than two
                       times the window timer; and should normally be an
                       even greater multiple if the transport connection
                       is to be resilient to the loss of an AK TPDU.

             A duplicate AK TPDU (See Figure 4.1) is one which contains
             the same values for YR-TU-NR, credit, and subsequence number
             as the previous AK TPDU transmitted.  A duplicate AK TPDU
             does not acknowledge any new data, nor does it change the
             credit window.


               I                  W
               3                  3             3                 3
               3                  3             3                 3
               3              DDDDEDDDD         3    duplicate    3
               3          expire  3             3       AK        3
               3                  3             3                 3
           DDDDEDDDD              3             3     AK + FCC    3
        reset  3                  3             3                 3
               3                  3             3                 3
               3                  3             3                 3
               3              DDDDEDDDD         3    duplicate    3
               3          expire  3             3       AK        3
               3                  3             3                 3
               3                  3             3                 3
           DDDDEDDDD              3             3     AK + FCC    3
        reset  3                  3             3                 3
               3                  3             3                 3
               3                  3             3                 3
               3              DDDDEDDDD         3                 3
               3          expire  3             3                 3
               3                  3             3                 3
               3                  3             3                 3


                Figure 4.1  AK exchange on idleconnection


   4.6  TRANSPORT CLASS 0

        4.6.1     Transport Class 0 Overview

        Transport class 0 over X.25 is mandatory (see X.400) for use in
        communicating with public MHS systems operating in accordance
        with the CCITT X.400 series recommendations.  The purpose of the
        agreements concerning transport class 0 is to allow connection to
        these public services.  Transport class 0 over X.25 can also be
        used in communicating between PRMDs (this choice is prevalent
        outside North America).

        4.6.2     Protocol Agreements

        Transport Class 0 agreements follow:

             o    The Error (ER) TPDU may be used at any time and upon
                  receipt requires that the recipient disconnect the
                  network connection, and by extension the transport
                  connection.

             o    The allowed values for the maximum TPDU size are as
                  specified in ISO 8073.  They are:  128, 256, 512, 1024,
                  and 2048.

             o    The class 0 protocol does not support multiplexing.  At
                  any instant, one transport corresponds to one network
                  connection.

             o    It is recommended that the optional timers TS1 and TS2,
                  if implemented, be settable by local system management.
                  Values in the order of minutes should be supported.

             o    An unlimited TSDU length must be supported.  


             4.6.2.1   TRANSPORT CLASS 0 SERVICE ACCESS POINTS

             For communicating with public MHS systems, Section 5 of
             X.410 specifies the use and format of TSAP identifiers.

        4.6.3     Rules for Negotiation

        The ISO rules for negotiations will be used.

5. UPPER LAYERS


   5.1  INTRODUCTION

   In this portion of the Implementors' Agreements, the NBS Upper Layers
   SIG is primarily concerned with providing implementation agreements
   for ACSE, and the Presentation and Session layers, so that systems
   implemented according to these agreements can successfully
   interoperate.


        5.1.1     References

        All documents referenced in the Upper Layers section of these
        agreements can be found in the REFERENCES section of this NBS
        Implementors' Agreements document. 



   5.2  SCOPE AND FIELD OF APPLICATION

   This section does not detail particular conformance statements for
   ACSE, Presentation, and Session, since what is to be implemented in
   each case depends on which Application Service Elements (ASE's) and
   which functional units within each ASE are used with an Application
   Process.  Each ASE's SIG must specify which functional units of each
   layer it requires.  However, the scope of each layer is based on the
   total indicated requirements of all ASE's for which there is an active
   NBS SIG.  The implementation agreements are not specified beyond that
   scope.

   It is not the intent of this document to specify or reproduce
   standards, but when a referenced standard is unclear or has known
   defects, an attempt will be made to remedy the problem herein.  Any
   attempted clarification should be considered as a possible
   interpretation; the ISO standard still takes precedence if there is
   any conflict.  The situation with respect to defects in a standard is
   somewhat different; a reported defect may be technically resolved by
   the appropriate international technical committee with likely approval
   by the voting members pending for several months.  Since relevant
   defects can't be ignored in an implementation, this document will
   recommend using defect resolutions which have the tentative approval
   of the appropriate standards committees.

   5.3  STATUS

   This document is the first stable version of the NBS UL SIG.


   5.4  ERRATA


        5.4.1     ISO Defect Reports

        This section lists the defect reports from ISO which are
        currently recognized to be valid for the purposes of NBS
        conformance.


        5.4.2     Session Defects

        These defects are listed for the benefit of X.400
        implementations.

        The following 8326 defect reports  have been incorporated into
        version 1 of Session:

             004, 006, 007, 009, 011, 012, 013, 014, 015, 016, 017, 020.

        The following 8327 defect reports  have been incorporated into
        version 1 of Session:

             001, 003, 004, 005, 006, 007, 008, 009, 010, 012, 017, 018,
             019, 026, 027, 030, 034, 035.



   5.5  ASSOCIATION CONTROL SERVICE ELEMENT


        5.5.1     Introduction

        This section details the implementation requirements for the
        Association Control Service Element (ACSE) of the Application
        layer.  It is the intent of this section to follow the ISO ACSE
        standards.  Where those specifications are inadequate, this
        section should provide the necessary information.


        5.5.2     Services


             5.5.2.1   ACSE Services

             The following ACSE service primitives are within the
             possible scope of an NBS conformant system:

                  1.  A_ASSOCIATE request
                  2.  A_ASSOCIATE indication
                  3.  A_ASSOCIATE response 
                  4.  A_ASSOCIATE confirm 
                  5.  A_RELEASE request 
                  6.  A_RELEASE indication 
                  7.  A_RELEASE response 
                  8.  A_RELEASE confirm 
                  9.  A_ABORT request 
                  10. A_ABORT indication 
                  11. A_P_ABORT indication 


             5.5.2.2   Use of Presentation Layer Services

             ACSE services will make use of Presentation layer services
             in the manner defined in the ACSE Protocol specification.


        5.5.3     Protocol agreements

        Implementations shall be based on the ACSE Service definition and
        the ACSE Protocol specification.


             5.5.3.1   Application Context

             Specific Application Contexts and their names will be
             supplied and defined by  an appropriate NBS SIG.  Other
             application contexts may be defined and specified as
             dictated by particular application requirements.

             Optional names and specifications are outlined by each
             application  SIG under the heading "Specific ASE
             Requirements for ACSE, Presentation, and Session".  The use
             of these names implies adherence to the relevant NBS
             implementors' agreements for a particular application  SIG.

             The utility of  an NBS defined name (which is an OBJECT
             IDENTIFIER) is left up to the application.  An NBS name may
             or may not be used in the ACSE APDU.  The consequence of the
             name is left up to the application entities and any a priori
             agreements that they have.  In other words, it is up to the
             application whether this parameter is ignored or validated
             for correctness.  (Note that the consequence of this name
             must also be dictated by the particular conformance test). 

             The UL  SIG recognizes that this parameter needs further
             definition by the appropriate standards bodies.  Therefore,
             the use of this parameter for association negotiation is not
             recommended at this time.


             5.5.3.2   Section Deleted


             5.5.3.3   AE Title

             A value is defined for the AE Title only to satisfy the FTAM
             requirement for exchanging fields of this type.

             This value does not identify an Application Entity and
             carries no semantics.  The AE title maps onto the AP title
             and the AE qualifier.  If the AE title is used, then both QP
             title (an OBJECT IDENTIFIER) and AE qualifier (an INTEGER)
             must be sent.

             The value for the AP titles is {1 3 999 1 ftam-nil-ap-title
             (7)} at this time.  Values for the AE qualifier are outside
             the scope of these agreements.


   5.6  PRESENTATION


        5.6.1     Introduction

        This section details the implementation requirements for the
        Presentation layer.  It is the intent of this section to follow
        the ISO Presentation Standards.  Where those specifications are
        inadequate, this section should provide the necessary
        information.

        The task of the Presentation layer is to carry out the
        negotiation of transfer syntaxes and to provide for the
        transformation to and from transfer syntaxes.  The transformation
        to and from a particular transfer syntax is a local
        implementation issue and is not discussed within this section. 
        This section is concerned with the protocol agreements, and thus
        is entirely devoted to the issues involved with the negotiation
        of transfer syntaxes and the responsibilities of the
        Presentation protocol.


        5.6.2     Services


             5.6.2.1   Presentation Services

             The following functional units are within the possible scope
             of an NBS conformant system:

                  Presentation Kernel - This functional 
                  unit supports the basic Presentation
                  services required to establish a
                  Presentation connection, transfer
                  normal data, and release a
                  Presentation connection.  This is a
                  non-negotiable functional unit.

                  The Context Management and Context
                  Restoration functional units are not
                  within the scope of an NBS
                  conformant system and need not be
                  supported.

             The requirement that the Presentation kernel functional unit
             be implemented does not imply that any of the Session
             functional units for expedited data, typed data, and
             capability data and the corresponding Presentation service
             primitives are required to be implemented.  Any service not
             supported by the Session layer is also not supported by the
             Presentation layer; see the section on Session Functional
             Units for the possible Session functional units.  The
             services provided by the Presentation layer are limited by
             the services provided by the Session layer as defined in the
             Session service definition ISO/IS 8326 and the Session
             protocol definition ISO/IS 8327.


             5.6.2.2   Use of Session Layer Services

             Presentation layer services shall make use of Session layer
             services in the manner defined in the Presentation Protocol
             Specification.


        5.6.3     Protocol Agreements

        Implementations shall be based on the Presentation Service
        Definition, ISO 8822  and the Presentation Protocol Definition,
        ISO 8823.


             5.6.3.1   Transfer Syntaxes

                  o    The following transfer syntax must be supported
                       for all mandatory abstract syntaxes: the basic
                       encoding rules for ASN.1.  This syntax is derived
                       by applying the basic encoding rules for ASN.1 to
                       the abstract syntax (see the Basic Encoding Rules
                       for ASN.1, ISO 8825).

                  o    The number of transfer syntaxes proposed is
                       dependent upon the recognized transfer syntaxes
                       which are available to support the particular
                       abstract syntaxes used by an Application Entity.


             5.6.3.2   Abstract Syntaxes

                  o    Several abstract syntax names may map onto a
                       single transfer syntax name.  

                  o    The ACSE abstract syntax shall always be present
                       in the defined context set.



             5.6.3.3   Presentation Context Identifier

                  o    The presentation context identifier value shall be
                       encoded in no more than 2 octets.

                  o    Implementations must be able to handle a minimum
                       of 2 presentation contexts per connection.


             5.6.3.4   Mode-selector Position in SET

             Whenever the Mode-selector value within either a CP-PPDU or
             CPA-PPDU is normal-mode (1), it shall occur as the first
             element within the SET.



             5.6.3.5   Default Context

             If the Presentation expedited data service is required, the
             default context must be explicitly present in the P-CONNECT
             PPDU at Presentation connect time.


             5.6.3.6   P-Selectors

             Local P-selectors shall be a maximum of 4 octets.  This
             applies only to P-selectors in PPDUs whose receipt by an
             NBS-conformant system normally results in either a P-CONNECT
             indication or a P-CONNECT confirmation being issued.


             5.6.3.7   Provider Abort Parameters

             No conformance requirements are implied by the use of either
             the Abort-reason or the Event-identifier component of the
             ARP-PPDU.  The decision to include these parameters is left
             up to the implementation issuing the abort.


             5.6.3.8   Provider Aborts and Session Version

             The Presentation Provider Abort PPDU (ARP-PPDU) shall be
             present regardless of the Session version in effect for a
             given association.  This precludes the use of indefinite
             length encoding of an ARP-PPDU when Session version 1 is in
             effect.


             5.6.3.9   CPC-type

             NBS conformant implementations shall not use any CPC-type
             values in the SS-user data parameter of the S-CONNECT
             request unless more than one transfer syntax is proposed. 
             Each CPC-type represents a unique transfer syntax.  Note:
             currently only 1 transfer syntax is recognized.


             5.6.3.10  Presentation-context-definition-result-list

             No semantics are implied by the absence of this optional
             component of the CPR-PPDU.  This component is required if
             the Provider-reason is absent in the CPR-PPDU.  If the
             Provider-reason is present, then the Presentation-context-
             definition-result-list is optional.


             5.6.3.11  RS-PPDU

             The Presentation-context-identifier-list shall not be
             present when only the kernel functional unit is in effect.


        5.6.4     Presentation ASN.1 Encoding Rules


             5.6.4.1   Invalid Encoding

             If a received PPDU contains any improperly encoded data
             values (including data values embedded within the User Data
             field of a PPDU) and an abort is issued, then either a P-U-
             ABORT or a P-P-ABORT shall be issued.


             5.6.4.2   Protocol-version, Presentation-requirements

             Protocol-version and Presentation-requirements shall be
             encoded in their primitive forms, if present.


             5.6.4.3   Presentation-selector

             Any type defined as a Presentation-selector shall be encoded
             in its primitive form, if present.



   5.7  SESSION
 

        5.7.1     Introduction

        This section details the implementation requirements for the
        Session layer.  It is the intent of this section to follow the
        ISO Session Standards to the fullest extent possible.  Where
        those specifications are inadequate, this section should provide
        the necessary information.
 

        5.7.2     Services


             5.7.2.1   Session Services

             The following functional units are within the possible scope
             of an NBS conformant system:

                  Kernel 

                  Duplex

                  Expedited Data

                  Resynchronize 

                  Exceptions

                  Activity Management

                  Half-duplex

                  Minor Synchronize

                  Major Synchronize

                  Typed Data


             5.7.2.2   Use of Transport Services

             The use of Transport layer services by the Session layer
             functional units listed in the previous section is as
             specified in the Transport Protocol Specification, ISO/IS
             8073.
 

        5.7.3     Protocol Agreements

        Implementations shall be based on the Session service definition
        ISO/IS 8326 and the Session protocol definition ISO/IS 8327.
 

             5.7.3.1   Concatenation

             When a category 0 SPDU is concatenated with a category 2
             SPDU, the category 0 SPDU shall contain neither the Token
             Item field nor User Data.  If either a Token Item field or
             User Data is received in such a concatenated incoming SPDU,
             the receiving Session Protocol Machine has the option of
             either properly processing the fields or issuing a provider
             abort on the connection.

             Extended concatenation is not required and can be refused
             using the normal negotiation mechanisms of the Session
             protocol.


             5.7.3.2   Segmenting

             Session Segmenting is not required and can be refused using
             the normal negotiation mechanisms of the session protocol. 


             5.7.3.3   Reuse of Transport Connection

             Reuse of a transport connection is not required and can be
             refused.


             5.7.3.4   Use of Transport Expedited Data

             The use of transport expedited service is as stated in the
             session protocol specification: if available, transport
             expedited service must be used. 


             5.7.3.5   Use of Session Version Number

             Session versions 1 and 2 are recognized.  Each relevant NBS 
             SIG chooses the version or versions of Session which it
             requires for a particular implementation phase, and these
             choices are documented in section 5.9.1.  

             Session version 2 specifies the use of unlimited user data
             during connection establishment as dictated by the DAD 2 to
             ISO 8327 to Incorporate Unlimited User Data.

             All Session version 1 implementations must be able to
             negotiate version 1 operation when responding to a CONNECT
             (CN) SPDU proposing both version 1 and version 2.

             In addition, all Session version 1 implementations, upon
             receipt of a CONNECT (CN) SPDU proposing only version 2,
             should respond with a REFUSE (RF) SPDU containing a Reason
             Code indicating that the proposed version is not supported. 
             Until pending defect reports are adopted, implementations
             may disconnect.

             If Session versions 1 and 2 are both proposed in the CONNECT
             (CN) SPDU, then the maximum length of the User Data
             parameter value in the CONNECT (CN) SPDU shall be 512 octets
             and a PGI field of 193 shall be associated with this
             parameter.  This implies that an implementation supporting
             both Session versions 1 and 2 can establish a connection
             with an implementation supporting only version 1.

             If only Session version 2 is proposed in the CONNECT (CN)
             SPDU, then the maximum length of the Session User Data
             parameter value of the S-CONNECT service request shall be
             10,240 octets.  This restriction implies that the OVERFLOW
             ACCEPT (OA) SPDU and CONNECT DATA OVERFLOW (CDO) SPDU are
             not used.  If the length of the User Data parameter value is
             no greater than 512 octets, then an associated PGI field of
             193 shall be used, otherwise a PGI field of 194 shall be
             used.

             When Session version 2 is negotiated, then in all SPDUs the
             maximum length of the User Data parameter value with an
             associated PGI field of 193 shall be 10,240 octets.  NBS
             conformant Session version 2 implementations need only
             support the maximum data lengths specified in the Specific
             ASE Requirements section.
   
 
             5.7.3.6   Receipt of Invalid SPDUs

             Upon receipt of an invalid SPDU, the SPM shall take any
             action in A.4.3 of the Session protocol definition ISO/IS
             8327 except action d.
 

             5.7.3.7   Invalid SPM Intersections

             If the conditions described in A.4.1.2 of the Session
             protocol definition ISO/IS 8327 are satisfied, the SPM shall
             always take the actions described by A.4.1.2 a.

             Note:     This implies that no S-P-EXCEPTION-REPORT
                       indications will be generated nor EXCEPTION REPORT
                       SPDUs sent due to invalid intersections of the
                       Session state table resulting from received SPDUs.


             5.7.3.8   S-Selectors

             S-selectors shall be a maximum of 16 octets.  



   5.8  Universal ASN.1 Encoding Rules


        5.8.1     Tags

        The maximum value of an ASN.1 basic encoding tag that need be
        handled by an NBS-conformant implementation shall be 16,383. 
        This is the maximum unsigned number that can be represented in 14
        bits, therefore, the maximum encoding of a tag occupies 3 octets.


        5.8.2     Definite length

        The maximum value of an ASN.1 length octets component that need
        be handled by an NBS-conformant implementation shall be
        4,294,967,295.  This is the maximum unsigned integer that can be
        represented in 32 bits, therefore, the maximum encoding of a
        length octets component will occupy 5 octets.  Also, note this
        restriction does not apply to indefinite length encoding.


        5.8.3     EXTERNAL Type

        It is assumed that "presentation layer negotiation of encoding
        rules" is always in effect, and therefore clause 32.5 of the
        Specification of ASN.1, ISO 8824 never applies.



   5.9  CONFORMANCE

   In order for an implementation to be in conformance with the NBS
   implementors' agreements, the following rules shall be adhered to:

   o    A conformant implementation must  meet all of the requirements of
        this specification.  All documents referenced in the Upper Layers
        section shall be used as the supporting documents for all
        implementations of ACSE, Presentation, or Session.  The full
        references for these documents are in the REFERENCES section.

   o    NBS conformant implementations shall be ISO conformant.  PICS may
        contain limitations on length or value aspects of a protocol. 
        PICS of NBS conformant systems shall not contain restrictions
        more severe than those in these implementation agreements.  Note:
        an implementation may abort a connection if the constraints
        specified in these agreements are violated.

   o    Guidelines for implementation of standards' defects will be as
        per the resolution of such defects by the appropriate ISO
        standards committee.


        5.9.1     Specific ASE Requirements for ACSE Presentation and
                  Session

        The following list for each ASE the corresponding NBS SIGs
        requirements of and restrictions on ACSE, Presentation, and
        Session.

        All listed requirements and restrictions shall be included in an
        NBS conformant system and shall be implemented in accordance with
        these NBS Implementor's agreements.

        All OBJECT IDENTIFIERS are specified in terms of their associated
        ObjectDescriptor's.  See the chapter on OBJECT IDENTIFIERs for
        the values of the associated OBJECT IDENTIFIERs.


             5.9.1.1   FTAM

                  5.9.1.1.1 Phase 2

                       ACSE Requirements:
                            all

                            Application Contexts:
                                 o    "ISO FTAM" - implies the use of the
                                      ACSE and the FTAM ASE.

                            Abstract Syntaxes:
                                 o    "ISO 8650-ACSE1"

                                      Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single ASN.1 type"

                       Presentation Requirements:

                            Presentation Functional Units:
                                 o    kernel

                            Presentation Contexts:
                                 o    At least 3 Presentation Contexts
                                      must be supported.

                            Abstract Syntaxes:

                                 Abstract Syntaxes for conformant
                                 Implementations

                                 o    "FTAM-PCI"

                                      Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single ASN.1 type:

                                 o    "FTAM unstructured binary abstract
                                      syntax"
                  
                                       Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single ASN.1 type"

                                 Abstract Syntaxes Depending on
                                 Implementation Profile

                                 o    "FTAM-FADU"
                                      Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single ASN.1 type"


                                 o    "FTAM unstructured text abstract
                                      syntax"

                                      Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single ASN.1 type"

                                 o    "NBS abstract syntax AS1"

                                      Associated Transfer Syntax:
                                           o    "Basic Encoding  of a
                                                single ASN.1 type"

                                 o    "NBS file directory entry abstract
                                      syntax"

                                      Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single Asn.1 type"


                       Session Requirements:

                            Session Functional Units:
                                 o    kernel
                                 o    duplex

                            Version Number: 2

                            Maximum size of User Data parameter field:
                            10,240


                       Session Options:

                            Session Functional Units:
                                 o    resynchronize
                                           only a Resynchronize Type
                                           value of "abandon"

                                 o    minor synchronize
                                           Note:     The minor
                                                     synchronize
                                                     functional unit is
                                                     required whenever
                                                     the resynchronize
                                                     functional unit is
                                                     available.

             5.9.1.2   MHS


                  5.9.1.2.1 Phase 1

                       Session Requirements:

                            Session Functional Units:
                                 o    kernel
                                 o    half-duplex
                                 o    exceptions
                                 o    activity management
                                 o    minor synchronize

                            Version Number: 1

                            Maximum size of User Data parameter field:
                            512

                            Session Notes:
                                 o    Restricted use is made by the RTS
                                      of the session services implied by
                                      the functional units selected. 
                                      Specifically,

                                      .    No use is made of S-TOKEN-
                                           GIVE, and
                                      .    S-PLEASE-TOKENS only asks for
                                           the data token.

                                 o    In the S-CONNECT SPDU, the Initial
                                      Serial Number should not be
                                      present.

                                 o    The format of the Connection
                                      Identifier in the S-CONNECT SPDU is
                                      described in Version 5 of the
                                      X.400-Series Implementors' Guide.

             5.9.1.3   DS


                  5.9.1.3.1 Phase 1


                       ACSE Requirements:
                            all

                            Application Context:

                            Abstract Syntaxes:
                                 o    "ISO 8650-ACSE1"
                                           Associated Transfer Syntax:
                                                o    "Basic Encoding of a
                                                     single ASN.1 type"

                                 o    "Directory Services"
                                           Associated Transfer Syntax:
                                                o    "Basic Encoding of a
                                                     single ASN.1 type"

                       Presentation Requirements:

                            Presentation Functional Units:
                                 o    kernel

                            Presentation Contexts:
                                 o    At least 2 Presentation Contexts
                                      must be supported.

                       Session Requirements:

                            Session Functional Units:
                                 o    kernel
                                 o    duplex

                            Version Number: 2 

                            Maximum size of User Data parameter field:
                            10,240

5.10   APPENDIX A:  RECOMMENDED PRACTICES


Reflect Parameter Values

   The optional "Reflect Parameter Values" parameter in the provider
   ABORT SPDU shall be encoded so as to represent the Session connection
   state, the incoming event and the first invalid SPDU field exactly at
   the moment a protocol error was detected.

   The first octet encodes the Session state as a number relative to 0 as
   detailed in Table 1.

   The second octet encodes the incoming event as a number relative to 0
   as detailed in Table 2.

   The third octet contains the SI, PGI, or PI Code of any SI field, PGI
   unit or PI unit in error.

   NOTE:  The remaining 6 octets are undefined herein.

                       Table 1 - Session States


State     rel.#   Description

  1        0      Idle, no transport connection 
  1B       1      Wait for T-connect confirm 
  1C       2      Idle, transport connected 
  2A       3      Wait for the ACCEPT SPDU 
  3        4      Wait for the DISCONNECT SPDU 
  8        5      Wait for the S-CONNECT response 
  9        6      Wait for the S-RELEASE response 
 16        7      Wait for the T-DISCONNECT indication 
713        8      Data Transfer state
  1A       9      Wait for the ABORT ACCEPT SPDU
  4A      10      Wait for the MAJOR SYNC ACK SPDU or PREPARE
                  SPDU 
  4B      11      Wait for the ACTIVITY END ACK SPDU or PREPARE
                  SPDU 
  5A      12      Wait for the RESYNCHRONIZE ACK SPDU or PREPARE
                  SPDU
  5B      13      Wait for the ACTIVITY INTERRUPT SPDU or PREPARE
                  SPDU
  5C      14      Wait for the ACTIVITY DISCARD ACK SPDU or
                  PREPARE
                  SPDU 
  6       15      Wait for the RESYNCHRONIZE SPDU or PREPARE
                  SPDU 
 10A      16      Wait for the S-SYNC-MAJOR response 
 10B      17      Wait for the S-ACTIVITY-END response 
 11A      18      Wait for the S-RESYNCHRONIZE response 
 11B      19      Wait for the S-ACTIVITY-INTERRUPT response 
 11C      20      Wait for the S-ACTIVITY-DISCARD response 
 15A      21      After PREPARE, wait for the MAJOR SYNC ACK SPDU or the
                  ACTIVITY END ACK 
 15B      22      After PREPARE, wait for the RESYNCHRONIZE SPDU or the
                  ACTIVITY DISCARD SPDU
 15C      23      After PREPARE, wait for the RESYNCHRONIZE ACK SPDU, or
                  the ACTIVITY INTERRUPT ACK SPDU or the ACTIVITY
                  DISCARD ACK SPDU 
 18       24      Wait for GIVE TOKENS ACK SPDU 
 19       25      Wait for a recovery request or SPDU 
 20       26      Wait for a recovery SPDU or request 
 21       27      Wait for the CAPABILITY DATA ACK SPDU 
 22       28      Wait for the S-CAPABILITY-DATA response 
  1D      29      Wait for the CONNECT DATA OVERFLOW SPDU
  2B      30      Wait for the OVERFLOW ACCEPT SPDU
 15D      31      After PREPARE, wait for the ABORT SPDU

                       Table 2 - Incoming Events

 
Event            Rel.# Description 

SCONreq           0    S-CONNECT request 
SCONrsp+          1    S-CONNECT accept response 
SCONrsp-          2    S-CONNECT reject response 
SDTreq            3    S-DATA request 
SRELreq           4    S-RELEASE request 
SRELrsp+          5    S-RELEASE accept response 
SUABreq           6    S-U-ABORT request 
TCONcnf           7    T-CONNECT confirmation 
TCONind           8    T-CONNECT indication 
TDISind           9    T-DISCONNECT indication 
TIM              10    Time out 
AA               11    ABORT ACCEPT 
AB-nr            12    ABORT - no reuse 
AC               13    ACCEPT 
CN               14    CONNECT 
DN               15    DISCONNECT 
DT               16    DATA TRANSFER 
FN-nr            17    FINISH - no reuse 
RF-nr            18    REFUSE - no reuse 
SACTDreq         19    S-ACTIVITY-DISCARD request 
SACTDrsp         20    S-ACTIVITY-DISCARD response 
SACTEreq         21    S-ACTIVITY-END request 
SACTErsp         22    S-ACTIVITY-END response 
SACTIreq         23    S-ACTIVITY-INTERRUPT request 
SACTIrsp         24    S-ACTIVITY-INTERRUPT response 
SACTRreq         25    S-ACTIVITY-RESUME request 
SACTSreq         26    S-ACTIVITY-START request 
SCDreq           27    S-CAPABILITY-DATA request 
SCDrsp           28    S-CAPABILITY-DATA response 
SCGreq           29    S-CONTROL-GIVE request 
SEXreq           30    S-EXPEDITED-DATA request 
SGTreq           31    S-TOKEN-GIVE request 
SPTreq           32    S-TOKEN-PLEASE request 
SRELrsp-         33    S-RELEASE response reject 
SRSYNreq(a)      34    S-RESYNCHRONIZE request abandon 
SRSYNreq(r)      35    S-RESYNCHRONIZE request restart 
SRSYNreq(s)      36    S-RESYNCHRONIZE request set 
SRSYNrsp         37    S-RESYNCHRONIZE response  
SSYNMreq         38    S-SYNC-MAJOR request  
SSYNMrsp         39    S-SYNC-MAJOR response  
SSYNmreq         40    S-SYNC-MINOR request  
SSYNmrsp         41    S-SYNC-MINOR response  
STDreq           42    S-TYPED-DATA request
SUERreq          43    S-U-EXCEPTION-REPORT request  
AB-r             44    ABORT - reuse SPDU 

                          Table 2 - continued


Event            Rel.# Description 

AD               45    ACTIVITY DISCARD SPDU 
ADA              46    ACTIVITY DISCARD ACK SPDU 
AE               47    ACTIVITY END SPDU 
AEA              48    ACTIVITY END ACK SPDU 
AI               49    ACTIVITY INTERRUPT SPDU 
AIA              50    ACTIVITY INTERRUPT ACK SPDU 
AR               51    ACTIVITY RESUME SPDU 
AS               52    ACTIVITY START SPDU 
CD               53    CAPABILITY DATA SPDU 
CDA              54    CAPABILITY DATA ACK SPDU 
ED               55    EXCEPTION DATA SPDU 
ER               56    EXCEPTION REPORT SPDU 
EX               57    EXPEDITED DATA SPDU 
FN-r             58    FINISH - reuse SPDU 
GT               59    GIVE TOKENS SPDU 
GTA              60    GIVE TOKENS ACK SPDU 
GTC              61    GIVE TOKENS CONFIRM SPDU 
MAA              62    MAJOR SYNC ACK SPDU 
MAP              63    MAJOR SYNC POINT SPDU 
MIA              64    MAJOR SYNC ACK SPDU 
MIP              65    MINOR SYNC POINT SPDU 
NF               66    NOT FINISHED SPDU 
PR-MAA           67    PREPARE (MAJOR SYNC ACK) SPDU 
PR-RA            68    PREPARE (RESYNCHRONIZE ACK) SPDU
PR-RS            69    PREPARE (RESYNCHRONIZE) SPDU 
PT               70    PLEASE TOKENS SPDU with Token Item
                       Parameter
RA               71    RESYNCHRONIZE ACK SPDU 
RF-r             72    REFUSE - reuse SPDU 
RS-a             73    RESYNCHRONIZE - abandon SPDU 
RS-r             74    RESYNCHRONIZE - restart SPDU 
RS-s             75    RESYNCHRONIZE - set SPDU 
TD               76    TYPED DATA SPDU
CDO              77    CONNECT DATA OVERFLOW SPDU
OA               78    OVERFLOW ACCEPT SPDU
PR-AB            79    PREPARE (ABORT) SPDU
6. ISO FILE TRANSFER, ACCESS AND MANAGEMENT PHASE 2

   6.1  INTRODUCTION

   This section defines Implementors' Agreements based on ISO File
   Transfer, Access and Management (FTAM), as defined in ISO 8571. This
   International Standard has four parts.  Part 1 of the IS gives general
   concepts, Part 2 defines the Virtual Filestore (VFS), Part 3 defines
   the File Service, and Part 4 defines the File Protocol.

   FTAM, as described in the IS, is based on the following ISO documents: 
   ACSE Service and Protocol (ISO 8649, ISO 8650), Presentation Service
   and Protocol (ISO 8822, ISO 8823), ASN.1 Abstract Syntax Notation and
   Basic Encoding Rules (ISO 8824, ISO 8825), and Session Service and
   Protocol (ISO 8326, ISO 8327).  These services and protocols are
   defined architecturally in the OSI Reference Model (ISO 7498).  These
   Agreements provide detailed guidance for the implementor, and
   eliminate ambiguities in interpretations.

   The general agreements reached with respect to the ISO File Transfer,
   Access and Management Protocol (FTAM) are that the Phase 2 FTAM
   specification (this section) is based on the International Standard
   (IS).


   6.2  SCOPE AND FIELD OF APPLICATION

   These FTAM Phase 2 Agreements cover transfer of and access to files
   between the Filestores of two end systems, including the management of
   a Virtual Filestore.  One end system acts in the Initiator role and
   initiates the file transfer/access, while the other end system acts in
   the Responder role and provides access to the file in the Virtual
   Filestore.  This paper describes Agreements for the actions and
   attributes of the Virtual Filestore, and the service provided by the
   file service provider to file service users, together with the
   necessary communications between the Initiator and Responder.


                                        ZDDDDDDDDDDDDDD?
                                        3   Virtual    3
                                        3  Filestore   3
                                        3      2       3
                                        @DDDDDDRDDDDDDDY
                                               :
                                               :
ZDDDDDDDDDDDDDD?    ZDDDDDDDDDDDDDD?    ZDDDDDDPDDDDDDD?    ZDDDDDDDDDDDDDD?
3    Real      3    3     End      3    3     End      3    3     Real     3
3  Filestore   CDDDD4   System 1   FMMMM5   System 2   CDDDD4   Filestore  3
3      1       3    3- Initiator - 3    3- Responder - 3    3       2      3
@DDDDDDDDDDDDDDY    @DDDDDDDDDDDDDDY    @DDDDDDDDDDDDDDY    @DDDDDDDDDDDDDDY


                   Figure 6.1  Model of file transfer/access


        Note: Agreements apply on the double lines of Figure 1.
        The mapping between the Virtual Filestore and the Real Filestore
        together with the local data management system is not part of
        these Agreements.

   These Agreements define General Agreements is in section 6.5 through
   6.16, minimum functionality (Conformant Implementations) in section
   6.17, and functionality for several Implementation Profiles which are
   tailored to different classes of user requirements in sections 6.18
   and 6.19.
   

   6.3  STATUS

   This version of the FTAM Implementation Agreements was completed
   December 18, 1987.  No further enhancements will be made to this
   version.  See the next section, ERRATA.

   Note: These Agreements were updated from the previous March 1987 DIS
   based Agreements.

 
     6.4  ERRATA
ZDDDDDDDDDDDBDDDDDDDDDBDDDDDDDDDDDBDDDDDDDDDDDBDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3CP no      3Type     3ref. doc   3section    3Comment                                        3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 2/88-1  3technical3NBS 500-15036.10.2.2,  3Check of already established presentation      3
3           3         3           36.10.2.3   3context for a document type not at CREATE time 3
3           3         3           3           3but at OPEN time                               3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 2/88-2  3editorial3NBS 500-15036, App. A, 3Appendix A, Part 4 of Object Identifiers       3
3           3         3           3Part 4     3removed                                        3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 2/88-3  3editorial3NBS 500-15036.5        3Clarification that current AET definition      3
3           3         3           3new bullet 3carries no semantics and other values are      3
3           3         3           37          3outside scope.                                 3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 2/88-4  3technical3NBS 500-15035.9        3Clarification for UL specs that ABORT possible 3
3           3         3           3           3if UL constraints are violated                 3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 2/88-5  3editorial3NBS 500-15036, App. A  3Replace 'organ-code' by 'organization-code' for3
3           3         3           3           3all NBS Object Identifiers                     3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 2/88-6  3editorial3NBS 500-15036.5        3Clarification that <shared ASE information>    3
3           3         3           3new bullet 3and <application context name> agreements are  3
3           3         3           38,9        3general agreements                             3
3           3         3           36.18.3     3                                               3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 2/88-7  3editorial3NBS 500-15036.18.2     3Move 6.18.2 to new Section 6.17.9              3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 2/88-8  3editorial3NBS 500-1503Table 6.4  3Rendition of currency sign in table 6.4        3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 2/88-9  3editorial3NBS 500-15036.2, 6.17  3Clarification of meaning of General Agreements,3
3           3         3           3           3Conformance and Implementation Profiles        3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 2/88-10 3editorial3NBS 500-15036.5        3Definition of 's', 'os' for a parameter.       3
3           3         3           3new bullet 3Clarification of support level for <initiator  3
3           3         3           310, 6.18.3 3identity>, <filestore password>, <access       3
3           3         3           3bullet 5   3password> parameter                            3
3           3         3           36.16.1     3                                               3
3           3         3           36.16.2     3                                               3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 5/88-1  3editorial3NBS 500-1503Table 6.7  3Clarification fo support of T&M service class  3
3           3         3           3Note 4     3                                               3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 5/88-2  3editorial3NBS 500-15036.18.3     3Remove <charging> value zero                   3
3           3         3           3bullet 6   3                                               3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 5/88-3  3editorial3NBS 500-1503Table 6.9  3Updated definition of Datatype 2               3
CDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3CP 5/88-4  3editorial3NBS 500-15036.5, new   3More clarification to CP 2/88, use of AETitle  3
3           3         3           3bullet 7   3values                                         3
@DDDDDDDDDDDADDDDDDDDDADDDDDDDDDDDADDDDDDDDDDDADDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
   6.5  ASSUMPTIONS

   1.   FTAM protocol machines must be able to parse and process at a
        minimum 7K octets of FTAM PCI and FTAM user data (including
        grouped FPDUs) as they would be encoded with the ASN.1 Basic
        Encoding Rules.  It is recommended, however, that  Presentation
        user data not be restricted in size.

   2.   In order to maximize interoperability, it is important that the
        implementations of FTAM service providers do not unnecessarily
        restrict the service user's ability to generate arbitrary file
        service requests.  Otherwise, they may not be able to work with
        FTAM Responders whose operation is constrained by their mapping
        of the FTAM Virtual Filestore to their local filestore.  For
        example, error procedures should only be invoked when an error
        actually occurs, not at the point of the specification of
        options which might result in an error.

   3.   Implementations must be able to parse all valid optional
        parameters if they are present in the PDU.  Only those optional
        parameters specified as supported in these Agreements are
        required to be implemented.  If these parameters are not present,
        a default value is assigned locally.  A Responder should not
        refuse a request solely because a parameter that is optional in
        the FTAM standard, but is supported in these Agreements, is not
        present.

   4.   Consideration of any standardized service interface is not
        covered by these Agreements.

   5.   These Agreements define no restrictions for the values used for
        the <communication quality of service> parameter in <F-
        INITIALIZE>.

   6.   FTAM is defined in phases.  The Phase 1 FTAM implementation
        specification is based on the second ISO Draft Proposal, dated
        April 1985, and the ISO Draft Proposal 8824 and 8825.

        The Phase 2 FTAM specification (this section) is based on the 
        International Standard (IS).  THERE IS NO BACKWARD COMPATIBILITY
        WITH NBS FTAM PHASE 1.  Backward compatibility is impossible,
        since Phase 1 uses Session services directly, while Phase 2 uses
        ACSE and Presentation services.  Furthermore, there are
        differences in Filestore, PDU Abstract Syntax, FADU Abstract
        Syntax, and Transfer Syntax.  There also are differences in the
        transparency mechanisms and service class negotiations.

        The <implementation information> parameter of <F-INITIALIZE> FPDU
        as defined in ISO 8571-4, 20.3 is used to pass 'user version'
        information with respect to different FTAM phases of the NBS
        Implementors Agreements or with respect to FTAM profiles of other
        bodies (see section 6.13 6.12 of this document).  It is the goal
        of these Agreements to use the 'user version' mechanism to
        provide at least one level of backward compatibility for all
        future NBS FTAM Phases, facilitating backward compatibility for
        future FTAM products, assuming different new versions of the
        respective IS's also enable backward compatibility.

   7.   Section 5.5.3 5.5.3.3 defines a value (that carries no semantics)
        for the AETitle that can be used by FTAM ASEs for communication. 
        Other values for the AETitle are outside the scope of these
        Agreements.

        For the Called-AETitle, Calling-AETtitle and Responding AETitle
        the association shall not be rejected/aborted if the value
        specified in 5.5.3.3 is sent or if any of the parameters are not
        sent.  The association may be rejected/aborted if a value other
        than specified in 5.5.3.3 is sent.

        Use of values outside the scope of these Agreements is
        discouraged until agreed upon semantics have been associated with
        AETitles.

   8.   Use of <shared ASE information> parameter and <charging>
        parameter is not defined within the scope of the Agreements.

   9.   Use of <application context name> parameter is not defined within
        the scope of these Agreements.  This parameter does not prohibit
        the establishment of an FTAM association.

   10.  These Agreements use the term 'supported' for a parameter to mean
        that the syntax and semantics of that parameter shall be
        implemented.  However, it is not a requirement that the parameter
        be used in all instances of communication, unless stated
        otherwise.

        Also these Agreements use the term 'optionally supported' for a
        parameter to mean that it is left to the implementation whether
        the semantics of that parameter are implemented or not.


   6.6  PRESENTATION AGREEMENTS

   The following Abstract Syntaxes are recognized in these agreements:

        "FTAM FADU"
        "FTAM PCI"
        "FTAM unstructured text abstract syntax"
        "FTAM unstructured binary abstract syntax"
        "NBS abstract syntax AS1"
        "NBS file directory entry abstract syntax"
   
   The following Transfer Syntax is supported:

        "Basic Encoding of a single ASN.1 type"
   (See Appendix A, Part 3)


   6.7  SERVICE CLASS AGREEMENTS

   Implementation Agreements have been reached for the following service
   classes.

        o    File Transfer
        o    File Access
        o    File Management
        o    File Transfer and Management
        o    Unconstrained


   6.8  FUNCTIONAL UNIT AGREEMENTS

   Implementation agreements have been reached for the following
   functional units.

        o    Kernel
        o    Read
        o    Write
        o    File Access
        o    Limited File Management
        o    Enhanced File Management
        o    Grouping

   Implementation of the Recovery, Restart Data Transfer, and FADU
   Locking functional units is not specified.


   6.9  FILE ATTRIBUTE AGREEMENTS

   Implementation of the Kernel Group of file attributes is defined.  If
   the optional Storage Group and Security Group are implemented, aspects
   of their implementation are defined.  Implementation of the Private
   Group is not specified.

   Responses to an attribute value request shall always include one of
   the following (as specified in ISO 8571-2, clause 9.4):

   o    An actual file attribute value.

   o    A value indicating that no value is available, optionally with a
        diagnostic.

   o    No value and an error code, optionally with a diagnostic
        indicating that the attribute is not supported.


        6.9.1     Mandatory Group

        Only the Kernel Group of attributes is required.  A value for
        <filename>, <permitted actions>, and <contents type> will always
        be available.

        A minimum range is required for <filename> values as specified in
        ISO 8571-2.  No maximum length or format restrictions apply.  A
        system that does not support <filename> values with a sequence of
        more than one Graphic String or extended <filename>
        characteristics may reject a request involving such a <filename>. 
        All systems must be able to interpret a <filename> value with a
        sequence of one Graphic String.  Requests using such a single
        component <filename> value with a sequence of one Graphic String
        are responded to using a single component <filename> value. 
        Responses to requests involving <filename> values having two or
        more Graphic Strings are not defined here but may be interpreted
        via bilateral or other external agreements.  Use of <filename>
        values with a sequence of more than one Graphic String is
        discouraged.

        Apart from the minimum conformance requirements specified in ISO
        8571-2, file names have to be specified in the naming convention
        of the responding FTAM implementation.  It is a local
        implementation matter of the FTAM Responder, whether or not an
        additional name mapping onto the real FIlestore's file name
        convention is supported.

        In order to enable interworking with all FTAM Responders' virtual
        Filestores, it is recommended that FTAM Initiators impose no
        restrictions on the attribute range supported for file names
        beyond those specified in ISO 8571-2.

        For the purpose of interworking according to these Agreements the
        <contents type> attribute is limited to the <document type name>
        format.  The <constraint set name, abstract syntax name> form is
        outside the scope of these Agreements.  It should always be
        parsed correctly when received, but may result in an error.

        6.9.2     Optional Groups

        If the optional Security Group of file attributes is implemented,
        an actual value must be available for the <access control>
        attribute.

        The <access control> attribute is a SET OF <access control
        element>.  The minimum requirement in these Agreements is the
        support of one <access control element>, according to the base
        standard.  The terms <concurrency access>, <identity>, and
        <passwords> are each optionally supported.  Details of their use
        shall be specified in the PICS.  Use of the <location> term is
        not specified in these Agreements.

        Implementation of the Private Group is not specified.


   6.10 DOCUMENT TYPE AGREEMENTS

   These document types are defined.

        FTAM-1    "ISO FTAM unstructured text"
        FTAM-2    "ISO FTAM sequential text"
        FTAM-3    "ISO FTAM unstructured binary"
        NBS-6     "NBS-6 FTAM sequential file"
        NBS-7     "NBS-7 FTAM random access file"
        NBS-8     "NBS-8 FTAM indexed file"
        NBS-9     "NBS-9 FTAM file directory file"

   Detailed document type definitions are given in Appendix 6A and in ISO
   8571-2, Annex B.

   Note: Document types NBS-1 to NBS-5 are not defined in these
   Agreements.  The numbering starts with NBS-6 because of the original
   DIS version of these Agreements.

   An implementation claiming conformance to these Agreements which also
   supports any or all of the document types FTAM-1, FTAM-2, and FTAM-3
   as defined in ISO 8571-2, Annex B, must minimally support the
   combinations of parameter values as specified in Table 6.1.


                Table 6.1  Parameters for FTAM-1, -2, -3
                                                                         
ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3            Universal             Maximum              String          3
3            Class Number          String Length6       Significance    3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                       3
3 FTAM-1     General String 1(27)    134 or less       'not-significant'3
3            IA5String 2(22)                                            3
3                                                                       3
3 FTAM-2     Graphic String 3,4(25)  134 or less5      'not-significant'3
3                                                                       3
3                                                                       3
3 FTAM-3     <not applicable>        512 or less       'not-significant43
3                                                                       3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY


   Notes:
   1.   The minimum level of support for General String is the IA5 G0
        character set and the 8859-1 G0 and G1 character sets, and IA5 C0
        set.

   2.   The support for IA5 String is the IA5 G0 character set and the
        IA5 C0 set.

   3.   The minimum level of support for Graphic String is the IA5 G0
        character set and the 8859-1 G0 and G1 sets.

   4.   This is the default when the parameter is not specified.

   5.   The implementation need not support Data Units whose total
        character count exceeds 134.

   6.   As per Table 6.3.

   For the use of FTAM-2 only the FADU identities of 'begin', 'end',
   'first', and 'next' are required for conformant implementations.

   For the document types NBS-6, NBS-7 and NBS-8 parameters are used for
   which the Agreements apply as specified in Table 6.2.
                       Table 6.2  Parameters for NBS-6, NBS-7, NBS-8

ZDDDDDDDDDDDDDDBDDDDDDDDDDDDDBDDDDDDDDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDDDDD?
3 Parameter    3 PrimType    3     String-length     3   Length-1      3   Length-2      3
CDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDDDDD4
3              3             3                       3                 3                 3
3 int          3 INTEGER     3 Number of octets      3                 3                 3
3              3             3 required to represent,3                 3                 3
3              3             3 in 2's complement     3                 3                 3
3              3             3 format, the largest   3                 3                 3
3              3             3 integer to be passed  3                 3                 3
3              3             3                       3                 3                 3
3 bit          3 BIT STRING  3 Number of bits in     3                 3                 3
3              3             3 string                3                 3                 3
3              3             3 (non-varying)         3                 3                 3
3              3             3                       3                 3                 3
3 ia5          3 IA5String   3 Max number of         3                 3                 3
3              3             3 characters in string  3                 3                 3
3              3             3                       3                 3                 3
3 graphic      3 Graphic     3 Max number of         3                 3                 3
3              3 String      3 characters in string  3                 3                 3
3              3             3                       3                 3                 3
3              3             3                       3                 3                 3
3 general      3 General     3 Max number of         3                 3                 3
3              3 String      3 characters in string  3                 3                 3
3              3             3                       3                 3                 3
3              3             3                       3                 3                 3
3 octet        3 OCTET STRING3 Max numbers of octets 3                 3                 3
3              3             3 in string             3                 3                 3
3              3             3                       3                 3                 3
3 private-     3 Floating    3                       3 The minimum     3 Number of bits  3
3 class-number 3 Point       3                       3 number of bits  3 required to     3
3              3 Number      3                       3 required to be  3 represent the   3
3              3             3                       3 maintained in   3 largest unbiased3
3              3             3                       3 the mantissa for3 integer exponent3
3              3             3                       3 relative        3 in 2's          3
3              3             3                       3 precision       3 complement      3
3              3             3                       3                 3                 3
3              3             3                       3                 3                 3
3              3             3                       3                 3                 3
3              3             3                       3                 3                 3
3 univer-      3 UTCTime     3 <not applicable>      3                 3                 3
3 time         3             3                       3                 3                 3
3              3             3                       3                 3                 3
3 gen-time     3 Generalized 3 <not applicable>      3                 3                 3
3              3 Time        3                       3                 3                 3
3              3             3                       3                 3                 3
3 boolean      3 BOOLEAN     3 <not applicable>      3                 3                 3
3              3             3                       3                 3                 3
3 null         3 NULL        3 <not applicable>      3                 3                 3
3              3             3                       3                 3                 3
@DDDDDDDDDDDDDDADDDDDDDDDDDDDADDDDDDDDDDDDDDDDDDDDDDDADDDDDDDDDDDDDDDDDADDDDDDDDDDDDDDDDDY

   Note: The string length parameter specifies the actual number of
   characters from the referenced character set.  It does not include any
   escape sequences or overhead from the encoding.

   The primitive data types and minimal size ranges that an
   implementation must accept for storage are given in Table 6.3.
        

                  Table 6.3  FTAM primitive data types

          ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
          3Primitive Data Type          Minimum Range (Octets)3
          3                                                   3
          3ASN.1   INTEGER                       1 - 2        3
          3ASN.1   BIT STRING                    0 - 1        3
          3ASN.1   IA5String                     0 - 134      3
          3ASN.1   GeneralString                 0 - 134      3
          3ASN.1   GraphicString                 0 - 134      3
          3ASN.1   OCTET STRING                  0 - 512      3
          3ASN.1   BOOLEAN                                    3
          3ASN.1   NULL                                       3
          3ASN.1   GeneralizedTime                            3
          3ASN.1   UniversalTime                              3
          3NBS-AS1 FloatingPointNumber  mantissa 1-23 bits    3
          3                             exponent 0-8  bits    3
          @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

   Notes:
   1.   The primitive data types and their maximum ranges for a specific
        file as described by the parameters above are maintained in the
        <contents type> file attribute.  The <contents type> file
        attribute value is established at the file's creation and cannot
        be changed via FTAM for the life of the file.  This implies that
        the data element types and ranges and data unit formats are fixed
        for all accessors of that file as long as the file exists.

   2.   The syntax for floating point numbers is part of the definition
        of NBS abstract syntax AS1 in Annex 6A Part 3.  It is derived
        from existing standards IEC 559 and IEEE 754.


        6.10.1    Character Sets

        Implementation of a character set in FTAM is understood as:

             o    a transfer syntax is defined for the character set

             o    document types are defined using the character set in
                  their abstract syntactic definition

             o    documents of those types are stored in the Virtual File
                  Store as defined in the character set specification. 
                  They are written into the VFS and read from the VFS as
                  defined by the abstract syntax and the transfer syntax
                  for the document type.  It is not in the scope of FTAM
                  Agreements to specify the local representation of those
                  documents in the Real Filestore, nor to specify
                  rendition of graphic characters or control characters
                  on character imaging devices.  These renditions are
                  possible agreements between applications using FTAM for
                  their communication.

        The character sets IA5 and ISO 8859-1 shall always be
        implemented.


             6.10.1.1  IA5 Character Set

             The International Reference Version (IRV) of IA5 is
             available for use when there is no requirement to use a
             national or an application-oriented version.  In information
             interchange, the IRV is assumed unless a particular
             agreement exists between sender and receiver of the data. 
             The graphic characters allocated to the IRV are as specified
             in Table 6.4.

              Table 6.4. IRV Graphic Character Allocations

    ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
    3 Graphic          Name                   Coded Representation 3
    CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
    3                                                              3
    3    #             Number sign                     2/3         3
    3                                                              3
    3    o             Currency sign                   2/4         3
    3                                                              3
    3    @             Commercial at                   4/0         3
    3                                                              3
    3    [             Left square bracket             5/11        3
    3                                                              3
    3    \             Reverse solidus                 5/12        3
    3                                                              3
    3    ]             Right square bracket            5/13        3
    3                                                              3
    3    ^             Circumflex accent               5/14        3
    3                                                              3
    3    '             Grave accent                    6/0         3
    3                                                              3
    3    {             Left curly bracket              7/11        3
    3                                                              3
    3    3             Vertical line                   7/12        3
    3                                                              3
    3    }             Right curly bracket             7/13        3
    3                                                              3
    3    ~             Tilde, overline                 7/14        3
    3                                                              3
    @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

   It should be noted that no substitution is allowed when using the IRV
   and that the facility of combined vertical and horizontal movements of
   the active position does not apply to any format effectors.

   It is permitted to use composite graphic characters and there is no
   limit to their number.  Because of this freedom, their processing and
   imaging may cause difficulties at the receiving end.  Therefore
   agreement between sender and receiver of the data is recommended if
   composite characters are used.

   Note:     Attention is drawn to the fact that different national
             character sets exist.

   (See ISO 646 or CCITT Recommendation T.50 for more information)


             6.10.1.2  8859-1 Character Set

             The Latin Alphabet No.1 (ISO 8859-1) is used to specify the
             printable characters of G0 and G1.  C0 control characters
             and their associated rules are taken from the IA5
             definition.

        6.10.2    Document Type Negotiation Rules


             6.10.2.1  Connection Establishment

             In connection establishment the <contents type list>
             parameter is used only to establish presentation contexts. 
             Both the <document type name> form and the <abstract syntax
             name> form are supported.


             6.10.2.2  File Creation

             An <F-CREATE request> FPDU must contain a <document type
             name> value in its <initial attributes> parameter.  

             If the specified document type requires parameterization,
             then these parameters must be supplied, otherwise the <F-
             CREATE request> may be rejected.

             Notes:
                  1.   It is understood that <permitted actions> sub-
                       field of <initial attributes> parameter will
                       always be used at <F-CREATE request>.  The value
                       may be changed by the Responder.

                  2.   If the <document type name> used requires DU
                       syntax parameters and one of the parameters
                       specifies 'FloatingPointNumber' as a primitive
                       data type, the request may be rejected, in case
                       the optional type 'FloatingPointNumber' is not
                       supported by the Responder.


             6.10.2.3  File Opening

             The <document type name> form (with appropriate parameters
             as specified in 8871-2, clause 12.3) shall always be used
             when proposing a <contents type>; as an alternative the
             'ContentsTypeUnknown' value may be used in the <F-OPEN
             request>.  An <F-OPEN response> shall use the <document type
             name> option (with appropriate parameters) in the <contents
             type> field.

             This allows the receiving entity to use the <document type
             name> attributed to the file instead of receiving a
             <constraint set name> and <abstract syntax name> pair, which
             does not reflect the file information contained in the FTAM
             and NBS document types.

             This document type name is either a value from the set of
             base document type names as negotiated upon connection
             establishment or a document type name, for which an
             appropriate presentation context was established.

             Notes:
             1.   An <F-OPEN response> without a <document type name>
                  (but carrying the <constraint set name> and <abstract
                  syntax name> form) may cause the Initiator to issue an
                  <F-CLOSE request>.

             2.   If the <document type name> used requires DU syntax
                  parameters and one of the parameters specifies
                  'FloatingPointNumber' as a primitive data type, the
                  request may be rejected, in case the optional type
                  'FloatingPointNumber' is not supported by the
                  Responder.

        6.10.3    Relationship Between DUs, DEs and Document Types

        "Abstract Syntax" is used to refer to the syntactic information
        which is architecturally passed between the Application and
        Presentation Layers.  The Abstract Syntax defines Data Element
        (DE) types which are not necessarily ASN.1 primitive types.  A
        Data Element (DE) is the smallest piece of data whose identity is
        necessarily preserved by the Presentation Service.  Data types
        may be made up of other data types.  Data Elements are not
        defined in terms of other Data Elements.

        A Data Unit (DU) is a sequence of one or more Data Elements.
        Architecturally, entire, single DEs are passed into and out of
        the application process.  In a real implementation, DUs may be
        passed.

        To maintain DU boundaries during transfer, file structuring
        information must be passed (ISO8571-FADU definition in ISO 8571-
        2, clause 7.5).  A Data Element is referred to as a File-
        Contents- Data-Element in the ISO8571-FADU definition.

        Document types refer to aspects of local processing and storage. 
        They describe:

             o    structural relationship between DUs,
             o    structure of DUs, called DU syntax, and
             o    DE types found in the file.

        Because document types pertain to local processing and storage,
        the DU syntax makes assertions about the syntax and the size of
        DUs (records) in storage.  Parameters on the document types
        provide this information about the syntax and size of the DUs.


   6.11 F-CANCEL ACTION

   When an F-CANCEL is sent or received, the following occurs:

        o    no more data is sent,
        o    checkpoint numbers are removed, and
        o    state of the file is implementation dependent.

   Note:     When mapping F-CANCEL on P-RESYNCHRONIZE (abandon) it is
             required that P-SYNC-MINOR be used after F-READ/F-WRITE (see
             ISO 8571-4 clauses 13, 14).


   6.12 IMPLEMENTATION INFORMATION AGREEMENTS

   o    The <implementation information> parameter of <F-INITIALIZE>
        FPDU is not required by these Agreements.

   o    It may be used to pass user version information as a series of
        values, separated by ';'.

   o    The following will indicate conformance to the NBS Phase 2
        Agreements:  NBS-Phase2.

        Note:     The list of possible values may be enlarged for future
                  FTAM phases or FTAM profiles of other bodies.

   o    This parameter is for information only; it is not used for
        negotiation.

        The establishment of an FTAM regime should not be rejected only
        because of an unknown <implementation information> value.

   6.13 DIAGNOSTIC AGREEMENTS

   o    The <diagnostic> parameter is supported; a value in the
        <response> PDU is needed when the <action result> or <state
        result> is not zero.  (The nature of these agreements is to
        provide <diagnostic> information when any result parameter is not
        'success'.)

   o    General catch-all diagnostic action is discouraged.

   o    The <further details> subfield is supported.  It will be encoded
        as GraphicString, but is restricted to IA5 (IRV, graphic
        characters) and ISO 8859-1 only.

   o    Use of F-P-ABORT for other than protocol errors and catastrophic
        situations is discouraged.

   o    When returning an error status in a file management related
        diagnostic (i.e., <F-READ-ATTRIBUTE response> or <F-
        CHANGE-ATTRIBUTE response>), identify the erroneous attribute by
        using the first two characters of <further details> to hold a
        2-digit number (encoded as IA5String) from the <F-READ-ATTRIBUTE
        request> attributes abstract syntax definition (ISO 8571-4,
        clause 20.3).

             00   Filename
             01   Permitted Actions
             02   Contents Type
             03   Storage Account
             04   Date and Time of Creation
             05   Date and Time of Last Modification
             06   Date and Time of Last Read Access
             07   Date and Time of Last Attribute Modification
             08   Identity of Creator
             09   Identity of Last Modifier
             10   Identity of Last Reader
             11   Identity of Last Attribute Modifier
             12   File Availability
             13   File Size
             14   Future Filesize
             15   Access Control
             16   Legal Qualifications
             17   Private Use

        The set of file management diagnostics, found in ISO 8571-3 Annex
        A, must be supported.

   o    In the case where a specific parameter can in no way be
        accommodated then the request fails and a <diagnostic> indicating
        one such parameter should be returned by the responder.  In the
        case where a negotiable parameter cannot be accommodated with
        exactly the value requested but is negotiated to a different
        value (as defined in the standard) then the request formally
        succeeds but informative <diagnostics> indicating those
        parameters negotiated should be returned.

   o    In order to provide for robust applications using FTAM, well
        defined and precise diagnostics are required to be returned by
        responding implementations whenever an action cannot be carried
        out precisely as requested with respect to non-negotiable
        parameters.  All such applicable diagnostics will be returned in
        those cases.  An action is carried out precisely as requested
        with  respect to a parameter when the value of that parameter on
        the <request> FPDU is equal to the value in effect during or
        subsequent to the action, depending on whether the action is
        regime control.

        Diagnostics exist to signal 'parameter not supported' and
        Responder implementations shall issue all appropriate
        diagnostics.  The <further details> subfield of the <diagnostic>
        parameter shall specify the parameter which is not implemented. 

   6.14 CONCURRENCY

   The <concurrency control> used by default on actions requested by an
   <F-SELECT indication> or <F-CREATE indication> service are:

             'shared'       for read and read attribute

             'exclusive'    for all other actions

   The default for actions not requested is specified as 'not required'
   as per ISO 8571-3.

   Note: A local implementation may choose to be more restrictive in
   order to assure file consistency for concurrent accessors.

   FADU locking is not required.

   6.15 REQUESTED ACCESS

   The <requested access> parameter on <F-SELECT> or <F-CREATE> is used
   to specify the actions which the Initiator may perform during the file
   selection.  The value of the <requested access> parameter is compared
   by the Responder to the <access control> and <permitted actions> file
   attributes and concurrency controls (including those requested by the
   Initiator) currently in place on the file.  If the value of the
   <requested access> parameter is not consistent with either <access
   control>, <permitted actions>, or concurrency controls in place, then
   the <F-SELECT> or <F-CREATE> must be rejected.

   <requested access> is consistent with <access control> if, for each
   action requested, that action either requires no password, or the
   required password has been specified on the <F-SELECT request> or <F-
   CREATE request>.

   <requested access> is consistent with <permitted actions> if, for each
   action requested, that action is allowed by the <permitted actions>
   file attribute.

   <requested access> is consistent with <concurrency control> requested
   on the <F-SELECT> or <F-CREATE> if, for each action requested, that
   action has not been specified as 'not required' or 'no access' in the
   <concurrency control> parameter.

   <requested access> is consistent with concurrency controls in place on
   the file if for each action requested no other accessor of the file
   has set the concurrency control for that action to either 'exclusive'
   or 'no access'.

   6.16 SECURITY

        6.16.1    Initiator Identity and Filestore Password  

        The <initiator identity> and <filestore password> parameters for
        an implementation acting as an Initiator are supported.  These
        parameters are optional for an implementation acting as a
        Responder.

        

        The syntax of <initiator identity> and <filestore password> is
        system-dependent.  <initiator identity> and <filestore password>
        will represent account information on the local system, which
        may be different from the <account> parameter.

        6.16.2    Access Passwords 

        The <access passwords> and <create password> parameters for an
        implementation acting as an Initiator are supported if the
        Security Group of attributes is supported.  These parameters for
        an implementation acting as a Responder are optionally supported
        if the Security Group is supported.

        


        6.16.3    Implementation Responsibilities

        It is the responsibility of each local system to provide security
        for its own real filestore.  Encryption of passwords will not be
        done by FTAM.

        A user of the file service must be known by the Responder.
        "Known" is defined by the local Filestore, and is dependent on
        the level of security provided by the local Filestore.


   6.17 REQUIREMENT FOR CONFORMANT IMPLEMENTATIONS

   This section gives the criteria to be satisfied by every
   implementation of FTAM that conforms to these Agreements.

   Conformance to these Agreements is stated in terms of the different
   roles occupied by FTAM implementations.  The interoperability of
   certain configurations of these roles motivates this approach.
   Interoperable configurations of these roles are given in section
   6.17.1.

   The only function provided by every conformant implementation is the
   transfer of unstructured binary files in their entirety.  It must be
   recognized that such simple transfer, while commonly understood and
   generally important, will not support all applications of FTAM.
   Section 6.18 defines Implementation Profiles of FTAM services and
   protocol that can provide other specific functions.  Those other
   functions exploit the access and management capabilities of FTAM. The
   unconstrained service class (with appropriately chosen functional
   units) can be used to provide the functions of any of the
   Implementation Profiles.  Users of FTAM must consider carefully what
   functions they require.  They must examine all the Implementation
   Profiles and select according to their needs.

   Implementation conforming to these Agreements require adherence to the
   General Agreements in sections 6.5 through 6.16 of these Agreements.


        6.17.1    Interoperable Configurations

        Any implementation conforming to this specification must be able
        to act in at least one of the following role combinations:

        1.   initiator and receiver,

        2.   initiator and sender,

        3.   responder and sender,

        4.   responder and receiver.

        Minimal implementations of combination 1 will interoperate with
        minimal implementations of combination 3.  Minimal
        implementations of combination 2 will interoperate with minimal
        implementations of combination 4.

        Any implementations of roles l and 3 will be able to interoperate
        at the intersection of their capabilities (which will be at least
        the minimal capabilities described in sections 6.17.3 to 6.17.8). 
        Any implementations of roles 2 and 4 will be able to interoperate
        at the intersection of their capabilities (which will be at least
        the minimal capabilities described in sections 6.17.3 to 6.17.8).

        These role combinations and this interoperability are shown in
        Table 6.5 below.

                 Table 6.5  Interoperable configurations

    ZDDDDDDDDDDDDDDDDDDDDDDDRDDDDDDDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDDDDDDDDDDD?
    3                       :      Initiator       3      Responder        3
    3                       GDDDDDDDDDBDDDDDDDDDDDDEDDDDDDDDDBDDDDDDDDDDDDD4
    3                       :  sender 3  receiver  3  sender 3  receiver   3
    3MMMMMMMMMMMQMMMMMMMMMMMNMMMMMMMMMXMMMMMMMMMMMMXMMMMMMMMMXMMMMMMMMMMMMM3
    3           3 sender    :         3            3         3      x      3
    3 Initiator CDDDDDDDDDDDWDDDDDDDDDEDDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDD3
    3           3 receiver  :         3            3    x    3             3
    CDDDDDDDDDDDEDDDDDDDDDDDWDDDDDDDDDEDDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDD4
    3           3 sender    :         3     x      3         3             3
    3 Responder CDDDDDDDDDDDWDDDDDDDDDEDDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDD4
    3           3 receiver  :    x    3            3         3             3
    3           3           :         3            3         3             3
    @DDDDDDDDDDDADDDDDDDDDDDPDDDDDDDDDADDDDDDDDDDDDADDDDDDDDDADDDDDDDDDDDDDY


        6.17.2    Relationship to ISO 8571--The FTAM Standard

        Any implementation in conformance to ISO 8571 (as defined in ISO
        8571-4, clause 22 (Conformance)), in addition to the
        implementation of the minimal protocols and roles enumerated in
        sections 6.17.3 to 6.17.8, is considered to be in conformance
        with these Agreements.  Any implementation violating any of the
        conformance statements in ISO 8571-4 is considered to be in
        violation of these Agreements.


        6.17.3    Requirements for Document Type Support

        The document type FTAM-3 shall be supported for purposes of
        transfer and storage.  The details regarding support for FTAM-3
        in the FTAM dialogue are given in section 6.10.

        Support of document types other than FTAM-3 is not required for
        conformant implementations.  Support for document types described
        in these Agreements also entails support for:

             o    the semantics given in their description and further
                  qualified in 6.10
   
             o    the preferred transfer syntax "Basic Encoding of a
                  single ASN.1 type"


        6.17.4    Initiators

        Every implementation of an FTAM Initiator shall support:

             o    the kernel protocol and its mandatory parameters with
                  minimum ranges [Minimum required ranges are specified
                  in section 6.17.8.],

             o    the grouping protocol and the <threshold> parameter
                  with a value of at least 2 for use in the file transfer
                  class,

             o    at least one of the read or write protocols [Specific
                  conformance for reading and writing is defined in
                  sections 6.17.6 and 6.17.7.],

        and support the applicable procedures defined in ISO 8571-4
        clauses 8.1 (FTAM regime establishment), 8.2 (FTAM regime
        termination), 8.3 (File selection), 8.4 (File deselection), 8.9
        (File open), 8.10 (File close), 8.11 (Begin group), 8.12 (End
        group), and 10 (File general actions).  To support the above
        protocols and procedures the implementation shall always support
        the kernel functional unit and additionally shall be able to:

             o    request the grouping and at least one of the read or
                  write functional units,

             o    request the file transfer class with the <service
                  class> parameter, 

             o    request the document type FTAM-3 using the <document
                  type name> form of the <contents type> parameter,

             o    request the <FTAM quality of service> parameter with
                  value 0 and accept in all cases the returned value 0,
                  and

             o    request a <communication quality of service> consistent
                  with the transport definition in these Agreements

        as part of the Filestore initialization procedures in ISO 8571-4
        clause 8.1, FTAM regime establishment.

        Initiators must be able to operate under all circumstances if the
        above minimum values are successfully negotiated and returned on
        an <F-INITIALIZE response> PDU.  Initiators must be able to
        operate with any downward negotiation of requested parameter
        values as described in the standard.

        Should the supporting services break down, such that FTAM
        communication is impossible, the FTAM protocol machine shall
        notify the user with an <F-P-ABORT indication> and <diagnostic>
        value with identifier 1011, as well as any known <further
        details>.

        Note: Interworking may not be possible between Initiators not
        supporting attributes of the Storage Group and Security Group,
        and Responders requiring these attributes to be used.


        6.17.5    Responders

        Every implementation of an FTAM Responder shall support:

             o    the kernel protocol and its mandatory parameters with
                  minimum ranges [Minimum required ranges are specified
                  in section 6.17.8.],

             o    the grouping protocol and the <threshold> parameter
                  with a value of at least 2 for use in the file transfer
                  class,

             o    at least one of the read or write protocols [Specific
                  conformance for reading and writing is defined in
                  sections 6.17.6 and 6.17.7],

        and support the applicable procedures, defined in ISO 8571-4
        clauses 9.1 (FTAM regime establishment), 9.2 (FTAM regime
        termination), 9.3 (File selection), 9.4 (File deselection), 9.9
        (File open), 9.10 (File close), 9.11 (Begin group), 9.12 (End
        group), and 10 (File general actions).  To support the above
        protocols and procedures the implementation shall always support
        the kernel functional unit and additionally shall be able to:

             o    accept requests for the grouping and at least one of
                  the read or write functional units,

             o    accept requests for the file transfer class with the
                  <service class> parameter,
   
             o    accept the document type FTAM-3 using the <document
                  type name> form of the <contents type> parameter, 

             o    accept requests for an <FTAM quality of service>
                  parameter with any value but may respond with the value
                  0, and

             o    accept requests for a <communication quality of
                  service> consistent with the transport definition in
                  these agreements

        as part of the filestore initialization procedures in ISO 8571-4
        clause 9.1, FTAM regime establishment.

        Responders must be able to operate under all circumstances if the
        above minimum values are requested on an <F-INITIALIZE request>
        PDU. Responders must not negotiate upward in the sense described
        in the standard.

        Responders must complete each action requested and supported in a
        manner consistent with its description in ISO 8571-2 clauses 10
        (Actions on complete files) and 11 (Actions for file access), and
        must interpret each supported attribute in a manner consistent
        with its definition in ISO 8571-2 clause 12 (File attributes).

        Under circumstances where actions cannot be carried out either as
        requested or consistently with ISO 8571-2 clause 10 (Actions on
        complete files) and 12 (Actions for file access), the Responder
        must return at least one diagnostic indicating:

             o    if the failure was due to either a protocol or
                  Filestore failure, and then:

                  --   precisely which action failed,
                  --   at least one of the parameters that could not be
                       accommodated  with the diagnostic type indicating
                       at least the degree of failure, as given by the
                       action and state result parameter, or

             o    that the failure was due to unforeseen system shutdown.

        Should the supporting services break down, such that FTAM
        communication is impossible, the FTAM protocol machine shall
        notify the user with an <F-P-ABORT indication> and <diagnostic>
        with identifier 1011, as well as inform the user of any known
        <further details>.


        6.17.6    Senders

        Every implementation of an FTAM sender shall support the read
        functional unit as Responder or the write functional unit as
        Initiator, and support the applicable procedures defined in ISO
        8571-4 clauses 11 (State of the bulk data transfer activity), 12
        (Bulk data transfer protocol data units), 15 (Bulk data transfer
        sending entity actions), 17.1 (Discarding), and 17.2 (Cancel).

        To support those procedures the implementation shall be able to
        send files of the document type FTAM-3 and shall be able to send
        them as user data in PPDUs in blocks of up to 7168 octets.


             6.17.6.1  Initiator Senders

             Every implementation of an FTAM sender which is also an FTAM
             Initiator shall support:

                  o    the write functional unit and protocol, and

                  o    for the document type FTAM-3 the following bulk
                       data transfer specification parameters:

                                 FADU operation      replace
                                 FADU identity       first

             and support the applicable procedures, defined in ISO 8571-4
             clause 13 (Bulk data transfer initiating entity actions).


             6.17.6.2  Responder Senders

             Every implementation of an FTAM sender which is also an FTAM
             Responder shall support:

                  o    the read functional unit and protocol, and

                  o    for the document type FTAM-3 the following bulk
                       data transfer specification parameters:

                                 FADU identity       first
                                 Access context      UA

             and support the applicable procedures, defined in ISO 8571-4
             clause 14 (Bulk data transfer responding entity actions).


        6.17.7    Receivers

        Every implementation of an FTAM receiver shall support the read
        functional unit as Initiator or the write functional unit as
        Responder, and support the applicable procedures, defined in ISO
        8571-4 clauses 11 (State of the bulk data transfer activity), 12
        (Bulk data transfer protocol data units), 16 (Bulk  data transfer
        receiving entity actions), 17.1 (Discarding), and 17.2 (Cancel).

        To support those procedures the implementation shall be able to
        receive files of the document type FTAM-3 and shall be able to
        receive them as user data in PPDUs in blocks of at least 7168
        octets.


             6.17.7.1  Initiator Receivers

             Every implementation of an FTAM receiver which is also an
             FTAM Initiator shall support:

                  o    the read functional unit and protocol, and

                  o    for the document type FTAM-3 the following bulk
                       data transfer specification parameters:

                                 FADU identity       first
                                 Access context      UA

             and support the applicable procedures, defined in ISO 8571-4
             clause 13 (Bulk data transfer initiating entity actions).


             6.17.7.2  Responder Receivers

             Every implementation of an FTAM receiver which is also an
             FTAM Responder shall support:

                  o    the write functional unit and protocol, and

                  o    for the document type FTAM-3 the following bulk
                       data transfer specification parameters:

                                 FADU operation      replace
                                 FADU identity       first

             and support the applicable procedures, defined in ISO 8571-4
             clause 14 (Bulk data transfer responding entity actions).


        6.17.8    Minimum Ranges

        Any implementation of any conformant FTAM configuration shall be
        able to receive and meaningfully process all mandatory parameters
        for all functional units supported as well as the <diagnostic>
        parameter within at least the minimum ranges of values given in
        Table 6.6.  A conforming implementation may support a wider range
        of values for any parameter.


              Table 6.6  Required minimal parameter support

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3      Parameter                               Minimum Range                 3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3general               diagnostic  Values as specified in ISO 8571-3 Annex A 3
3                                  (Diagnostic parameter values) Tables 44,  3
3                                  45 and 46 which correspond directly to    3
3                                  mandatory parameters.                     3
3                   action result  All values.                               3
3                    state result  All values.                               3
3                                                                            3
3F_INITIALIZE                                                                3
3                                                                            3
3               functional units1  'read' (for initiator/receivers and       3
3                                  responder/senders) and 'grouping'         3
3                                  or                                        3
3                                  'write' (for initiator/senders and        3
3                                  responder/receivers) and 'grouping'       3
3presentation context management2   'Not required.'                          3
3                      all others  As specified in sections 6.17.4 and       3
3                                   6.17.5 above.                            3
3                                                                            3
3                                                                            3
3F_SELECT                                                                    3
3                      attributes  Only <filename> is used with a minimum    3
3                                  supportable length of 8 characters.  Any  3
3                                  other attribute supported for other       3
3                                  services must have minimum supported      3
3                                  lengths as in ISO 8571-2 clause 15        3
3                                  (Minimum attribute ranges) Table 2.       3
3                                                                            3
3               requested access   'read' for initiator/receivers            3
3                                  'read' for responder/senders              3
3                                  'replace' for initiator/senders           3
3                                  'replace' for responder/receivers         3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                      (Continued on next page.)
           Table 6.6  Required minimal parameter support, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3      Parameter                               Minimum Range                 3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3F_OPEN                                                                      3
3                  processing mode  'read' for initiator/receivers           3
3                                   'read' for responder/senders             3
3                                   'replace' for initiator/senders          3
3                                   'replace' for responder/receivers        3
3                                                                            3
3                  contents type   'FTAM-3'                                  3
3                                                                            3
3F_READ                                                                      3
3                  FADU identity   'first'                                   3
3                  access context  'UA'                                      3
3F_WRITE                                                                     3
3                  FADU operation  'read' for initiator/receivers            3
3                                  'read' for responder/senders              3
3                                  'replace' for initiator/senders           3
3                                  'replace' for responder/receivers         3
3                                                                            3
3                  FADU identity   'first'                                   3
3                                                                            3
3F_BEGIN_GROUP                                                               3
3                                                                            3
3                      threshold3  For file transfer (a minimal required     3
3                                  function) 2.                              3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY


        For any other supported parameters, minimum ranges are taken from
        the minimum ranges for the attribute corresponding to each as in
        ISO 8571-2 Table 4.

DDDDDDDDDDDDDDD
Notes:
        1.   The parameters, functional units, and presentation context
             management are not ordered, so "minimum value" cannot be
             formally defined.  The above values are those required for
             conformance to these Agreements but no value conformant to
             ISO 8571 for use in other applications is regarded to be in
             violation of these Agreements.

        2.   Other functional units (and service classes) for defined
             implementations may also be valid provided that they are
             implemented in accordance with these Agreements,
             specifically section 6.17.8.

        3.   Every implementation must support the <threshold> value 2 to
             provide the basic required function of file transfer; any
             other value in other applications is acceptable.


        6.17.9    Use of Lower Layer Services

             o    Support for the Presentation Context Management
                  functional unit is not required.

             o    Implementations will support the Session, Presentation,
                  and ACSE requirements as stated in section 5.

   Note:  Implementation of the Session Resynchronize  and the  Minor
   Synchronize functional units is highly recommended, since the F-
   CANCEL service may be less effective when mapped to S-DATA.


   6.18 IMPLEMENTATION PROFILES

   This section defines Implementation Profiles for the specific
   functions of:
                  
        o    File Transfer
        o    File Access
        o    File Management.

   Those definitions are expressed in terms of:

        o    Document Types
        o    Attributes
        o    Service Classes (both service elements and their
             parameters).

   This by no means defines all possible Implementation Profiles.

   The following Implementation Profiles are defined:

        T1:  Simple File Transfer
        T2:  Positional File Transfer
        T3:  Full File Transfer
        A1:  Simple File Access
        A2:  Full File Access
        M1:  Management.

   Implementation Agreements have been reached for the following service
   classes.  Note that any given implementation may support more than one
   service class.
   
        o    File Transfer
        o    File Access
        o    File Management
        o    Unconstrained
        o    File Transfer and Management

   Support of an Implementation Profile requires adherence to:  

   1.   corresponding definition in  8571-3 clause 8 and any related
        procedures in 8571-4 clause 8-17, 

   2.   requirements given in sections 6.5-6.18 of these Agreements, and 

   3.   requirements for parameter and attribute support as defined in
        section 6.17.8.

        6.18.1    General Requirements for the Defined Implementation
                  Profiles


        o    Implementations will be able to act either as Initiator or
             Responder or both.

        o    Implementations must support diagnostics as described in
             section 6.13 of these Agreements.

        o    Implementations that support the file access service class
             will support access to sequential files.  Support of
             sequential files entails hierarchy of depth and arc length
             equal to 1.  Other hierarchy depth and arc lengths are not
             precluded by these agreements.


        6.18.2    Intentionally Left Empty


        6.18.3    Document Type Requirements for the Defined
                  Implementation Profiles

        Implementations conformant to Implementation Profiles defined in
        Table 6.7 will support the following document types with the
        caveats and procedures given.  Those document types are defined
        in Appendix 6A and section 6.10 of these Agreements, and in ISO
        8571-2.

             o    FTAM-1

             o    FTAM-2

             o    FTAM-3

             o    NBS-6

             o    NBS-7

                  Note:     Support of this document type entails the
                            naming of FADUs by  their position in
                            preorder traversal.

                  Caveat:   Other methods of naming FADUs depend on the
                            system, application, and specific file, and
                            as such are not described here.
             o    NBS-8

             o    NBS-9

        Support for any document type requires the ability to transfer
        and store the abstract syntax given in its definition.  These
        Agreements do not specify techniques or formats for storage.

        Caveat:   Specific abstract syntaxes for the parameterized
                  document types NBS-6,7,8 are not specified in these
                  Agreements.

        Any document type supported must be identifiable by its document
        type name as given in ISO 8571-2 and in Appendix 6A of these
        Agreements and, where defined, the parameterization scheme given
        in section 6.10 of these Agreements.

        For conformance to NBS-9 a Responder is only required to return
        the <filename> attribute, subject to local security and access
        control.  All other requested attributes need not be returned.

        Systems supporting the NBS-9 document type shall make available
        an NBS-9 document called 'DIRLIS'.  This document can be used to
        obtain a listing of files and their associated attributes from a
        remote Filestore.

        File security issues related to NBS-9 are subject to the security
        agreements outlined in section 6.16.


        6.18.4    Parameters for the Defined Implementation Profiles

             o

             o

             o    Implementations will support the <contents type list>
                  parameter on the  <F-INITIALIZE> service element.  The
                  initiating service must supply a value for this
                  parameter.

             o    Implementations will support the <diagnostic> parameter
                  as stated in section 6.13 of these Agreements.

             o    The <initiator identity> parameter is supported.    Use
                  must be consistent with section 6.16 of these
                  Agreements.

             o    Implementations are not precluded from using other
                  parameters for security and/or accounting.  Responders
                  must state the semantics applying to <account> and
                  <charging> parameters.  The Responder's minimum
                  implementation is to accept but ignore the <account>.
                  and to return a <charging> value of zero.


        6.18.5    Parameter Ranges for the Defined Implementation
                  Profiles

        Parameter ranges for Implementations Profiles are as stated for
        primitive data types in section 6.10 of these agreements.


        6.18.6    File Attribute Support for Implementations

        Implementations of the Implementation Profiles will support file
        attributes or attribute groups in the following ways.

        o    mandatory 
                       This feature is mandatory in the ISO 8571-2
                       standard and shall therefore be implemented by all
                       implementations claiming conformance to these
                       Agreements.

        o    supported 
                       This feature shall be implemented by all
                       implementations claiming conformance to these
                       Agreements (for attributes, this implies that at
                       least the minimum range of attribute values, as
                       defined in ISO 8571-2 clause 15, shall be
                       supported).  Conformant implementations shall also
                       be able to interwork with other implementations
                       that do not support this feature by negotiating
                       out the corresponding features.

        o    optionally supported
                       Implementations claiming conformance to these
                       Agreements may or may not implement this feature
                       (for attributes, this implies that at least either
                       the minimum range of attribute values, as defined
                       in ISO 8571-2 clause 15, shall be supported or
                       that the 'no value available' result shall be
                       supplied).  If an attribute group with a support
                       level of 'optionally supported' is chosen to be
                       supported, then all the attributes of this group
                       that are classified as 'mandatory' or 'supported'
                       shall be supported.

        o    not supported
                       This feature is outside the scope of these
                       Agreements.


Kernel Group                                         mandatory

   o Filename                                        mandatory
   o Permitted Actions                               mandatory
   o Contents Type                                   mandatory

Storage Group                                        optionally supported
   
   o Storage Account                                 optionally supported
   o Date and Time of Creation                       optionally supported
   o Date and Time of Last Modification              optionally supported 
   o Date and Time of Last Read Access               optionally supported
   o Date and Time of Last Attribute Modification    optionally supported
   o Identity of Creator                             optionally supported
   o Identity of Last Modifier                       optionally supported
   o Identity of Last Reader                         optionally supported
   o Identity of Last Attribute Modifier             optionally supported
   o File Availability                               supported
   o Filesize                                        supported
   o Future Filesize                                 optionally supported

Security Group                                       optionally supported
   
   o Access Control                                  supported
   o Legal Qualifications                            optionally supported
   
Private Group                                        not supported

          Table 6.7 Implementation profile support requirements

ZDDDDDDDDDDDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3                          3              Service Class                      3
3 Functional Unit          3    T        M         A        T&M      UNCST   3
CDDDDDDDDDDDDDDDDDDDDDDDDDDEDDDDDDDDDBDDDDDDDDDBDDDDDDDDDBDDDDDDDDDBDDDDDDDDD4
3                          3         3         3         3         3         3
3 Kernel                   3 T1,T2,T33   M1    3   A1,A2 3         3         3
3 Read     (See note 3.)   3 T1,T2,T33         3   A1,A2 3         3         3
3                          3         3         3         3         3         3
3 Write    (See note 3.)   3 T1,T2,T33         3   A1,A2 3         3         3
3                          3         3         3         3         3         3
3 Limited File Mgmnt.      3SeeNote 63   M1    3SeeNote 63   See   3   See   3
3 Enhanced File Mgmnt.     3         3   M1    3         3         3         3
3 Grouping                 3 T1,T2,T33   M1    3         3         3         3
3 File Access              3         3         3   A1,A2 3         3         3
3                          3         3         3         3         3         3
3       Document Types     3         3         3         3         3         3
3                          3         3         3         3         3         3
3 FTAM-1                   3 T1,T2,T33  [M1]   3   A1,A2 3         3         3
3 FTAM-2                   3 T2,T3   3  [M1]   3   A1,A2 3         3         3
3 FTAM-3                   3 T1,T2,T33  [M1]   3   A1,A2 3   Note  3   Note  3
3                          3         3         3         3         3         3
3 NBS-6                    3 [T2],T3 3  [M1]   3  [A1],A23    4    3    5    3
3                          3         3         3         3         3         3
3 NBS-7                    3 [T2],T3 3  [M1]   3  [A1],A23         3         3
3                          3         3         3         3         3         3
3 NBS-8                    3 T3      3  [M1]   3   A2    3         3         3
3                          3         3         3         3         3         3
3 NBS-9                    3[T1],[T2]3  [M1]   3         3         3         3
3                          3[T3]     3         3         3         3         3
@DDDDDDDDDDDDDDDDDDDDDDDDDDADDDDDDDDDADDDDDDDDDADDDDDDDDDADDDDDDDDDADDDDDDDDDY

Notes: to 6.18.3 and Table 6.7

1. The Management Implementation Profile is only to be implemented in
   conjunction  with one of the Transfer or Access Profiles.

2. Profile T2 is subset of T3.  A1 and T1 are subsets of A2 and T2,  
   respectively.

3. Profiles T1, T2, and T3 require the support of read and/or write
   functional units.

4. Support of the <File Transfer and Management> service class is
   optional.  If an implementation is capable of supporting
   Implementation Profile M1 and one of the T-Implementation Profiles,
   the Initiator may choose to request the <File Transfer and Management>
   service class.  Any implementation so doing must be prepared for the
   possibility of rejection of the request by the Responder.

   Support of the <File Transfer and Management> service class is
   optional.  The rules for including it in a request and for the
   response to it are as given in ISO 8571-3, clause 10.1.  Any
   implementation including TM in the request must be prepared for the
   possibility that it might be removed from the response.

5. The support of the <Unconstrained> service class is optional.  There
   are no constraints on this service class beyond those of ISO 8571.

6. Limited File Management is not required for the T- and A-
   Implementation Profiles, but very often it will be a user request to
   have limited file management functionality available together with
   file transfer and file access functions.  So Limited File Management
   may be added as an option to the T- and A- Implementation Profiles.

7. [] in Table 6.7 specifies that the document type is optional for the
   respective Implementation Profile.  For M1 the support level depends
   on the T- or A- Implementation Profile, in conjunction with which M1
   is implemented.


   6.19 PROVISION OF SPECIFIC FUNCTION


        6.19.1    Implementation Profile T1:  Simple File Transfer

        Implementation Profile T1 provides the function of transferring
        entire files at the external file service level for files with an
        unstructured constraint set.  This includes support of the
        document types:

             o    FTAM-1    "ISO FTAM unstructured text"
             o    FTAM-3    "ISO FTAM unstructured binary"
             o    NBS-9     "NBS-9 file directory file"        (optional)

        This Implementation Profile supports file transfer and not file
        access, that is, the ability to:

             o    read a complete file

                  and/or

             o    write (replace, extend) to a file.


        6.19.2    Implementation Profile T2:  Positional File Transfer

        Implementation Profile T2 provides the function of transferring
        files at the external file service level for files with an
        unstructured or flat constraint set.  This includes support of
        the document types:

             o    FTAM-1    "ISO FTAM unstructured text"
             o    FTAM-2    "ISO FTAM sequential text"
             o    FTAM-3    "ISO FTAM unstructured binary"
             o    NBS-6     "NBS-6 FTAM sequential file"       (optional)
             o    NBS-7     "NBS-7 FTAM random access file"    (optional)
             o    NBS-9     "NBS-9 file directory file"        (optional)

        This Implementation Profile supports file transfer and not file
        access, that is, the ability to:

             o    read a complete file or a single FADU which is
                  identified by position
   
                  and/or
   
             o    write (replace, extend, insert depending on constraint
                  set and document type) to a file or an FADU.

        This Implementation Profile is upwardly compatible to T1 for the
        transfer of unstructured files.


        6.19.3    Implementation Profile T3:  Full File Transfer

        Implementation Profile T3 provides the function of transferring
        files at the external file service level for files with an
        unstructured, flat or general hierarchical constraint set.  This
        includes support of the document types:

             o    FTAM-1    "ISO FTAM unstructured text"
             o    FTAM-2    "ISO FTAM sequential text"
             o    FTAM-3    "ISO FTAM unstructured binary"
             o    NBS-6     "NBS-6 FTAM sequential file"
             o    NBS-7     "NBS-7 FTAM random access file"
             o    NBS-8     "NBS-8 FTAM indexed file"
             o    NBS-9     "NBS-9 file directory file"        (optional)

        This Implementation Profile supports file transfer and not file
        access, that is, the ability to:

             o    read a complete file or a single FADU which is
                  identified by key or by position
   
                  and/or

             o    write (replace, extend, insert depending on constraint
                  set and document type) to a file or an FADU.

        This Implementation Profile is upwardly compatible to T1 for the
        transfer of unstructured files.


        6.19.4    Implementation Profile A1: Simple File Access

        Implementation Profile A1 provides the function of transfer of
        and access to files with unstructured or flat constraint sets at
        the external file service level.  This includes support of the
        document types:

             o    FTAM-1    "ISO FTAM unstructured text"
             o    FTAM-2    "ISO FTAM sequential text"
             o    FTAM-3    "ISO FTAM unstructured binary"
             o    NBS-6     "NBS-6 FTAM sequential file"       (optional)
             o    NBS-7     "NBS-7 FTAM random access file"    (optional)


        This Implementation Profile supports file transfer and file
        access, that is the ability to:

             o    read a complete file or FADUs which are identified by
                  position,

             o    write (replace, extend, insert depending on constraint
                  set and document type) to a file or an FADU,

             o    locate and erase within files.



        6.19.5    Implementation Profile A2:  Full File Access

        Implementation Profile A2 provides the function of transfer of
        and access to files with unstructured or flat constraint sets at
        the external file service level.  This includes support of the
        document types:

             o    FTAM-1    "ISO FTAM unstructured text"
             o    FTAM-2    "ISO FTAM sequential text"
             o    FTAM-3    "ISO FTAM unstructured binary"
             o    NBS-6     "NBS-6 FTAM sequential file"
             o    NBS-7     "NBS-7 FTAM random access file"
             o    NBS-8     "NBS-8 FTAM indexed file"

        This Implementation Profile supports file transfer and file
        access, that is, the ability to:

             o    read from a complete file, or from a series of FADUs
                  which are identified by key or by position,

             o    write (replace, extend, insert depending on constraint
                  set and document type) to a file or an FADU,

             o    locate and erase within files.



        6.19.6    Implementation Profile M1:  Management

        Implementation Profile M1 provides the function for an Initiator
        to manage the files within the Virtual Filestore, to which access
        is provided by the Responder.  Management includes the services
        of:

             o    creating a file
             o    deleting a file
             o    reading attributes of a file
             o    changing attributes of a file.


   6.20 HARMONIZATION

   The Implementation Profiles for File Transfer, File Access and
   Management correspond to the Profiles of SPAG (Standards Promotion and
   Application Group) in Europe, so that interworking will be possible. 
   Those Profiles are described in the 'Guide to the Use of Standards'
   (GUS); they are the basis for the Functional Standards as defined by
   CEN/CENELEC (Comite Europeenne de Normalization).

   Table 6.8 Implementation Profiles (NBS) and Profiles (SPAG/CEN-CLC)

           ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
           3  Implementation Profile         SPAG/CEN-CLC        3
           CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDDDDDDDDDDD4
           3                             3                       3
           3         T1                  3          A/111        3
           3         T2                  3          A/112        3
           3         T3                  3          A/113        3
           3         A1                  3          A/122        3
           3         A2                  3          A/123        3
           3         M1                  3          A/13         3
           @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDADDDDDDDDDDDDDDDDDDDDDDDY

6.21   APPENDIX A:    FTAM DOCUMENT TYPES


 Part 1:  Document Types
 Part 2:  Constraint Sets
 Part 3:  Abstract Syntaxes
 Part 4:  Intentionally Left Empty

Part 1:  Document Types

NBS-6 Sequential file document type

1. Entry Number:   NBS-6

2. Information objects
                    Table 6.9 Information objects in NBS-6
                      
ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDRDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3 document type name            : {iso identified-organization icd (9999)     3
3                               : organization-code  (1) document             3
3                               : type (5) sequential (6)}                    3
3                               :           "NBS-6 FTAM sequential file"      3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 abstract syntax names:        : {iso identified-organization icd (9999)     3
3 a) name for asname1           : organization-code  (1) abstract-            3
3                               : syntax (2) nbs-as1 (1)}                     3
3                               :           "NBS abstract syntax AS1"         3
3 b) name for asname2           : {iso standard 8571 abstract-syntax(2) ftam- 3
3                               :  fadu (2)}                                  3
3                               :                 "FTAM FADU"                 3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 transfer syntax names:        : {joint-iso-ccitt asn1 (1) basic-encoding (1)3
3                               : }   "Basic Encoding of a single ASN.1 type" 3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMJMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3parameter syntax:                                                            3
3  PARAMETERS ::= SEQUENCE OF CHOICE {Parameter0, Parameter1, Parameter2}     3
3  Parameter0 ::= universal-class-number-0 [0] INTEGER {univer-time (23),     3
3                                                       gen-time (24),        3
3                                                       boolean (1),          3
3                                                       null (5) }            3
3 Parameter1  ::= [1] SEQUENCE  {                                             3
3                 universal-class-number-1 INTEGER { int       (2),           3
3                                                    bit       (3),           3
3                                                    ia5      (22),           3
3                                                    graphic  (25),           3
3                                                    general  (27),           3
3                                                    octet     (4)},          3
3                 string-length INTEGER }                                     3
3 Parameter2  ::= [2] SEQUENCE {                                              3
3                 private-class-number INTEGER {float (0)},                   3
3                 length-1     INTEGER,                                       3
3                 length-2     INTEGER }                                      3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMKMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 file model                    : {iso standard 8571 file-model (3)           3
3                               :  hierarchical (1)}                          3
3                               :  "FTAM hierarchical file model"             3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 constraint set                : {iso standard 8571 constraint-set (4)       3
3                               :  sequential-flat (2)}                       3
3                               :  "FTAM sequential flat constraint set"      3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMJMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 file contents:                                                              3
3                Datatype1 ::= PrimType -- as defined in Annex 6 A, Part 3    3
3                Datatype2 ::= CHOICE   { Node-Descriptor-Data-Element,       3
3                                         Enter-Subtree-Data-Element , Exit-  3
3                                         Subtree-Data-Element}               3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

3. Scope and field of application

   The document type defines the contents of a file for storage, for
   transfer and access by FTAM.

   Note: Storage refers to apparent storage within the Virtual Filestore.

4. References

   ISO 8571, Information Processing Systems - Open Systems
   Interconnection - File Transfer, Access and Management

5. Definitions

   This definition makes use of the terms data element, data unit and
   file access data unit as defined in ISO 8571-1.

6. Abbreviations

   FTAM File Transfer, Access and Management

7. Document semantics

   The document consists of zero, one or more file access data units,
   each of which consists of zero, one or more data elements.  The order
   of each of these elements is significant.

   The document structure takes any of the forms allowed by the FTAM 
   hierarchical file model as constrained by the sequential flat
   constraint set (see Table 6.9)  These definitions appear in ISO 8571-
   2.  As additional constraints FADU identity will be limited to
   'begin', 'end', 'first' and 'next'.

   For a specific file the number of data elements in a data unit is
   given by the parameters.  Each data element is a data type from the
   set of primitive data types defined in the Annex 6.A, Part 3 of this
   document.  Each data unit contains the same data element types in the
   same order as all other data units.  These types are determined by the
   parameters 0 through 2.

   Note: The string length values are the actual number of characters
   from the specified character set, they do not include any escape
   sequences or overhead from the encoding.

8. Abstract syntactic structure

   The abstract syntactic structure of the document is a hierarchically
   structured file as defined in the ASN.1 module ISO8571-FADU in ISO
   8571, in which each of the file access data units has the abstract
   syntactic structure of NBS-AS1 as defined by the parameters.

9. Definition of transfer

9.1     Datatype definitions

        The file consists of data values which are of either

             a)   Datatype1 defined in Table 6.9, where the PrimType in
                  the datatype is given by the NBS-AS1 definition; or

             b)   Datatype2 defined in Table 6.9, the ASN.1 datatype
                  declared as "Data-Element" in the ASN.1 module ISO8571-
                  FADU.

9.2     Presentation data values

        The document is transferred as a series of presentation data
        values, each of which is either

             a)   one value of the ASN.1 datatype "Datatype1", carrying
                  one of the data elements from the document.  All values
                  are transmitted in the same (but any ) presentation
                  context defined to support the abstract syntax name
                  "asname1" or

             b)   a value of "Datatype2".  All values are transmitted in
                  the same (but any) presentation context defined to
                  support the abstract syntax name "asname2".

        Notes:

        1.   Specific carrier standards may impose additional constraints
             on the presentation context to be used, where the above
             permits a choice
        2.   Any document type defined in this entry either makes no use
             of Datatype2, or starts with a Datatype2 transmission.

        Boundaries between presentation data values in the same
        presentation context, and boundaries between P-DATA primitives,
        are chosen locally by the sending entity at the time of
        transmission, and carry no semantics of the document type. 
        Receivers which support this document type shall accept a
        document with any of the permitted transfer options (e.g.
        document type parameters and transfer syntaxes).

9.3     Sequence of presentation data values

        The sequence of presentation data values of type a) and the
        sequence of presentation data values of types a) and b) is the
        same as the sequence of data elements within a Data Unit, and
        Data Units in the hierarchical structure, when flattened
        according to the definition of the hierarchical file model in ISO
        8571-2.

10.     Transfer syntax

        An implementation supporting this document type shall support the
        transfer syntax generation rules named in Table 6.9 for all
        presentation data values transferred.  An implementation may
        optionally support other named transfer syntaxes.

11.     ASE specific specifications for FTAM

11.1    Simplification and relaxation

11.1.1  Structural simplification

        This simplification loses information.

        The document type NBS-6 may be simplified to the document type
        FTAM-3 (allowed only when reading the file).  The octet
        representation of the transferred data is unpredictable.  It will
        usually correspond to the data values as stored in the local Real
        Filestore of the Responder.

11.2    Access context selection

        A document of type NBS-6 may be accessed in any one of the access
        contexts defined in the sequential flat constraint set.  The
        presentation data units transferred in each case are those
        derived from the structuring elements defined for that access
        context in ISO 8571-2.

11.3    The INSERT operation

        When the <INSERT> operation is applied at the end of file the
        transferred material shall be the series of FADUs which would be
        generated by reading any NBS-6 document with the same parameter
        values in access context FA.
NBS-7 Random access file

1. Entry number:   NBS-7

2. Information objects
                    Table 6.10 Information objects in NBS-7

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDRDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3 document type name            : {iso identified-organization icd (9999)     3
3                               : organization-code  (1) document             3
3                               : type (5) random-file (7)}                   3
3                               :              "NBS-7 FTAM random access file"3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 abstract syntax names:        : {iso identified-organization icd (9999)     3
3 a) name for asname1           : organization-code  (1) abstract-            3
3                               : syntax (2) nbs-as1 (1)}                     3
3                               :         "NBS abstract syntax AS1"           3
3 b) name for asname2           : {iso standard 8571 abstract-syntax(2) ftam- 3
3                               :  fadu (2)}          "FTAM FADU"             3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 transfer syntax names:        : {joint-iso-ccitt asn1 (1) basic-encoding (1)3
3                               : }    "Basic Encoding of a single ASN.1 type"3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMJMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3parameter syntax:                                                            3
3  PARAMETERS ::= SEQUENCE OF CHOICE {Parameter0, Parameter1, Parameter2}     3
3  Parameter0 ::= universal-class-number-0 [0] INTEGER {univer-time (23),     3
3                                                       gen-time (24),        3
3                                                       boolean (1),          3
3                                                       null (5) }            3
3 Parameter1  ::= [1] SEQUENCE  {                                             3
3                 universal-class-number-1 INTEGER { int       (2),           3
3                                                    bit       (3),           3
3                                                    ia5      (22),           3
3                                                    graphic  (25),           3
3                                                    general  (27),           3
3                                                    octet     (4)},          3
3                 string-length INTEGER }                                     3
3 Parameter2  ::= [2] SEQUENCE {                                              3
3                 private-class-number INTEGER {float (0)},                   3
3                 length-1     INTEGER,                                       3
3                 length-2     INTEGER }                                      3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMKMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 file model                    : {iso standard 8571 file-model (3)           3
3                               :  hierarchical (1)}                          3
3                               :  "FTAM hierarchical file model"             3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 constraint set                : {iso identified-organization icd (9999)     3
3                               : organization-code (1) constraint-set (4) nbs3
3                               : -ordered flat (2)}                          3
3                               :     "NBS ordered flat constraint set"       3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMJMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 file contents:                                                              3
3                Datatype1 ::= PrimType -- as defined in Annex 6 A, Part 3    3
3                Datatype2 ::= CHOICE   { Node-Descriptor-Data-Element,       3
3                                         Enter-Subtree-Data-Element }        3
3                                         Exit-Subtree-Data-Element }         3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

3. Scope and field of application

   The document type defines the contents of a file for storage, for
   transfer and access by FTAM.

   Note: Storage refers to apparent storage within the Virtual Filestore.

4. References

   ISO 8571, Information Processing Systems - Open Systems
   Interconnection -File Transfer, Access and Management

5. Definitions

   This definition makes use of the terms data element, data unit and
   file access data unit as defined in ISO 8571-1.

6. Abbreviations

   FTAM File Transfer, Access and Management

7. Document semantics

   The document consists of zero, one or more file access data units,
   each of which consists of zero, one or more data elements.  The order
   of each of these elements is significant.

   The document structure takes any of the forms allowed by the FTAM 
   hierarchical file model as constrained by the NBS-ordered-flat
   constraint set (see Table 6.10).  These definitions appear in Appendix
   6 A, Part 2 of this document.

   For a specific file the number of data elements in a data unit is
   given by the parameters.  Each data element is a data type from the
   set of primitive data types defined in the Annex 6.A, Part 3 of this
   document.  Each data unit contains the same data element types in the
   same order as all other data units.  These types are determined by the
   parameters 0 through 2.

   Note: The string length values are the actual number of characters
   from the specified character set, they do not include any escape
   sequences or overhead from the encoding.

8. Abstract syntactic structure

   The abstract syntactic structure of the document is a hierarchically
   structured file as defined in the ASN.1 module ISO8571-FADU in ISO
   8571, in which each of the file access data units has the abstract
   syntactic structure of NBS-AS1 as defined by the parameters.



9. Definition of transfer

9.1     Datatype definitions

        The file consists of data values which are of either

             a)   Datatype1 defined in Table 6.10, where the PrimType in
                  the datatype is given by the NBS-AS1 definition; or

             b)   Datatype2 defined in Table 6.10, the ASN.1 datatype
                  declared as "Data-Element" in the ASN.1 module ISO8571-
                  FADU.

9.2     Presentation data values

        The document is transferred as a series of presentation data
        values, each of which is either

             a)   one value of the ASN.1 datatype "Datatype1", carrying
                  one of the data elements from the document.  All values
                  are transmitted in the same (but any ) presentation
                  context defined to support the abstract syntax name
                  "asname1" or

             b)   a value of " Datatype2".  All values are transmitted in
                  the same (but any) presentation context defined to
                  support the abstract syntax name " asname2".

        Notes:

        1.   Specific carrier standards may impose additional constraints
             on the presentation context to be used, where the above
             permits a choice
        2.   Any document type defined in this entry either makes no use
             of Datatype2, or starts with a Datatype2 transmission.

        Boundaries between presentation data values in the same
        presentation context, and boundaries between P-DATA primitives,
        are chosen locally by the sending entity at the time of
        transmission, and carry no semantics of the document type. 
        Receivers which support this document type shall accept a
        document with any of the permitted transfer options (e.g.
        document type parameters and transfer syntaxes).

9.3     Sequence of presentation data values

        The sequence of presentation data values of type a) and the
        sequence of presentation data values of types a) and b) is the
        same as the sequence of data elements within a Data Unit, and
        Data Units in the hierarchical structure, when flattened
        according to the definition of the hierarchical file model in ISO
        8571-2.

10.     Transfer syntax

        An implementation supporting this document type shall support the
        transfer syntax generation rules named in Table 6.10 for all
        presentation data values transferred.  Implementation may
        optionally support other named transfer syntaxes.

11.     ASE specific specifications for FTAM

11.1    Simplification and relaxation

11.1.1  Structural simplification

        This simplification loses information.

        The document type NBS-7 may be accessed as a document type FTAM-3 
        (allowed only when reading the file) by specifying document type
        FTAM-3 in the <contents type> parameter in <F-OPEN request>, and
        limiting access context to UA on F-READ.

        The octet representation of the transferred data is
        unpredictable.  It will usually correspond to the data values as
        stored in the local Real Filestore of the Responder.

        A document of type NBS-7 can be accessed as a document of type
        NBS-6 (allowed only when reading the file) by specifying document
        type NBS-6 with appropriate data type parameters in the <contents
        type> parameter on the <F-OPEN request>.
        
11.2    Access context selection

        A document of type NBS-7 may be accessed in any one of the access
        contexts defined in the NBS-ordered-flat constraint set.  The
        presentation data units transferred in each case are those
        derived from the structuring elements defined for that access
        context in ISO 8571-2.

11.3    The INSERT operation

        When the <INSERT> operation is applied at the end of file the
        transferred material shall be the series of FADUs which would be
        generated by reading any NBS-7 document with the same parameter
        values in access context FA.

NBS-8 Indexed sequential file
1. Entry Number:  NBS-8
2. Information objects

                    Table 6.11 Information objects in NBS-8
                      
ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDRDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3 document type name            : {iso identified-organization icd (9999)     3
3                               : organization-code  (1) document             3
3                               : type (5) indexed-file (8)}                  3
3                               :                   "NBS-8 FTAM indexed file" 3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 abstract syntax names:        : {iso identified-organization icd (9999)     3
3 a) name for asname1           : organization-code  (1) abstract-            3
3                               : syntax (2) nbs-as1 (1)}                     3
3                               :           "NBS abstract syntax AS1"         3
3 b) name for asname2           : {iso standard 8571 abstract-syntax(2) ftam- 3
3                               :  fadu (2)}                                  3
3                               :                    "FTAM FADU"              3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 transfer syntax names:        : {joint-iso-ccitt asn1 (1) basic-encoding (1)3
3                               : }                                           3
3                               :   "Basic Encoding of a single ASN.1 type"   3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMJMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3parameter syntax:                                                            3
3  PARAMETERS ::= SEQUENCE           {DataTypes, KeyType, KeyPosition}        3
3                                                                             3
3  DataTypes  ::= SEQUENCE OF CHOICE {Parameter0, Parameter1, Parameter2}     3
3                                                                             3
3  KeyType    ::= CHOICE {Parameter0, Parameter1, Parameter2}                 3
3                                                                             3
3             --  Parameter0, Parameter1, Parameter2, as defined for the      3
3             --  document types NBS-6, NBS-7                                 3
3                                                                             3
3  KeyPosition::= position INTEGER                                            3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMKMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 file model                    : {iso standard 8571 file-model (3)           3
3                               :  hierarchical (1)}                          3
3                               :  "FTAM hierarchical file model"             3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 constraint set                : {iso standard 8571 constraint-set (4)       3
3                               :  ordered-flat (3) }                         3
3                               :  "FTAM ordered flat constraint set"         3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMJMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 file contents:                                                              3
3                Datatype1 ::= PrimType -- as defined in Annex 6 A, Part 3    3
3                Datatype2 ::= CHOICE   { Node-Descriptor-Data-Element,       3
3                                         Enter-Subtree-Data-Element }        3
3                                         Exit-Subtree-Data-Element }         3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY


3. Scope and field of application 

   The document type defines the contents of a file for storage, for
   transfer and access using FTAM.

   Note: Storage refers to apparent storage within the Virtual Filestore.

4. References

   ISO 8571, Information Processing Systems - Open Systems
   Interconnection -File Transfer, Access and Management

5. Definitions

   This definition makes use of the terms data element, data unit and
   file access data unit as defined in ISO 8571-1.

6. Abbreviations

   FTAM File Transfer, Access and Management

7. Document semantics

   The document consists of zero, one or more file access data units,
   each of which consists of zero, one or more data elements.  The order
   of each of these elements is significant.

   The document structure takes any of the forms allowed by the FTAM 
   hierarchical file model as constrained by the FTAM ordered flat
   constraint set (see Table 6.11).  These definitions appear in ISO
   8571-2.

   The following additional requirements are specified for the use of the
   ordered flat constraint set:

        o    The FADU identities 'first', 'last', and 'traversal number'
             are not required for conformant implementations

        o    The identities 'next' and 'previous' are allowed for all
             FADUs 


   Each data element is a data type from the set of primitive data types
   defined in Appendix 6A, Part 3 of this document.  Each data unit
   contains the same data element types in the same order as all other
   data units.  These types and their respective maximum lengths are
   defined by the <DataTypes> parameter.

   Note: The length values refer to the number of characters from the
   applicable type, not to the number of octets in the encoding, nor to
   the line length in any rendition of the document, where these are
   different.

   Each data unit in the file has a key associated with it.  The key of
   each data unit is of the same data type as the key of all other data
   units in the file and is a single data element from the set of
   primitive data types defined in Appendix 6A, Part 3.

   The type and length of the key are defined by the <KeyType> parameter.

   The primitive data types and minimum size ranges of each unit which an
   implementation must accept as a key value are given in the following
   Table 6.12.


                                Table 6.12  Datatypes for keys

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3     Key Type                Minimum Range (octets)        Order                          3
3                                                                                          3
3    ASN.1 INTEGER            (1-2)                         increasing numeric value       3
3    ANS.1 IA5String          (0-16)                        lexical order                  3
3    ASN.1 GraphicString      (0-16)                        lexical order                  3
3    ANS.1 GeneralString      (0-16)                        lexical order                  3
3    ANS.1 OCTET STRING       (0-16)                        increasing value               3
3    ASN.1 GeneralizedTime                                  increasing time value          3
3    ASN.1 UniversalTime                                    increasing time value          3
3    NBS-AS1 FloatingPointNumber                            increasing numeric value       3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
 
 
   The position of the key in the data unit is specified by the
   <position> parameter.
   position = 0 implies the key is not part of the data
   position > 0 specifies the actual data element in the data unit.

8. Abstract syntactic structure

   The abstract syntactic structure of the document is a hierarchically
   structured file as defined in the ASN.1 module ISO8571-FADU in ISO
   8571, in which each of the file access data units has the abstract
   syntactic structure of NBS-AS1 as defined by the parameters.

9. Definition of transfer

9.1     Datatype definitions

        The file consists of data values which are of either

        a)   Datatype1 defined in Table 6.11, where the PrimType in the
             datatype is given by the NBS-AS1 definition; or

        b)   Datatype2 defined in Table 6.11, the ASN.1 datatype declared
             as "Data-Element" in the ASN.1 module ISO8571-FADU.

9.2     Presentation data values

        The document is transferred as a series of presentation data
        values, each of which is either

        a)   one value of the ASN.1 datatype "Datatype1", carrying one of
             the data elements from the document.  All values are
             transmitted in the same (but any) presentation context
             defined to support the abstract syntax name "asname1" or

        b)   a value of "Datatype2".  All values are transmitted in the
             same (but any) presentation context defined to support the
             abstract syntax name "asname2".

        Notes:

        1.   Specific carrier standards may impose additional constraints
             on the presentation context to be used, where the above
             permits a choice
        2.   Any document type defined in this entry either makes no use
             of Datatype2, or starts with a Datatype2 transmission.

        Boundaries between presentation data values in the same
        presentation context, and boundaries between P-DATA primitives,
        are chosen locally by the sending entity at the time of
        transmission, and carry no semantics of the document type. 
        Receivers which support this document type shall accept a
        document with any of the permitted transfer options (e.g.
        document type parameters and transfer syntaxes).

9.3     Sequence of presentation data values

        The sequence of presentation data values of type a) and the
        sequence of presentation data values of types a) and b) is the
        same as the sequence of data elements within a Data Unit, and
        Data Units in the hierarchical structure, when flattened
        according to the definition of the hierarchical file model in ISO
        8571-2.

10.     Transfer syntax

        An implementation supporting this document type shall support the
        transfer syntax generation rules named in Table 6.11 for all
        presentation data values transferred.  Implementation may
        optionally support other named transfer syntaxes.

11.     ASE specific specifications for FTAM

11.1    Simplification and relaxation

11.1.1  Structural simplification

        This simplification loses information.

        The document type NBS-8 may be accessed as a document type FTAM-3 
        (allowed only when reading the file) by specifying document type
        FTAM-3 in the <contents type> parameter in <F-OPEN request>, and
        limiting access context to UA on F-READ.

        The octet representation of the transferred data is
        unpredictable.  It will usually correspond to the data values as
        stored in the local Real Filestore of the Responder.

        A document of type NBS-8 can be accessed as a document of type
        NBS-6 (allowed only when reading the file) by specifying document
        type NBS-6 with appropriate data type parameters in the <contents
        type> parameter on the <F-OPEN request>.  The traversal order of
        the FADUs must be maintained.

        Note: The traversal order is as reading the file as NBS-8 in key
        order.

11.2    Access context selection

        A document of type NBS-8 may be accessed in any one of the access
        contexts defined in the FTAM ordered flat constraint set.  The
        presentation data units transferred in each case are those
        derived from the structuring elements defined for that access
        context in ISO 8571-2.

11.3    The INSERT operation

        When the <INSERT> operation is applied the transferred material
        shall be the series of FADU which would be generated by reading
        any NBS-8 document with the same parameter values in access
        context FA.

        The insertion of a new FADU after an already existing FADU will
        be indicated via a diagnostic on TRANSFER-END.

11.4    The EXTEND operation

        This operation is excluded for the use with this document type.
NBS-9 File directory file

1. Entry Number:   NBS-9

2. Information objects

                 Table 6.12 Information objects in NBS-9

ZDDDDDDDDDDDDDDDDDDDDDDDDRDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3 document type name     : {iso identified-organization icd (9999)      3
3                        : organization-code  (1) document              3
3                        : type (5) file directory (9)}                 3
3                        :       "NBS-9 FTAM file directory file"       3
FMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 abstract syntax names: : {iso identified-organization icd (9999)      3
3                        : organization-code  (1) abstract              3
3                        : syntax (2) nbs-as2 (2)}                      3
3                        :  "NBS file directory entry abstract syntax"  3
FMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 transfer syntax names: : {joint-iso-ccitt asn1 (1) basic-encoding (1)}3
3                        : "Basic Encoding of a single ASN.1 type"      3
FMMMMMMMMMMMMMMMMMMMMMMMMJMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 parameter syntax                                                      3
3                                                                       3
3 PARAMETERS ::= attribute-names [0] IMPLICIT BIT STRING {              3
3                                                                       3
3             -- Kernel group                                           3
3                                                                       3
3                  read_filename (0),                                   3
3                  read_permitted-actions (1),                          3
3                  read_contents-type (2),                              3
3                                                                       3
3             -- Storage group                                          3
3                                                                       3
3                  read_storage-account (3),                            3
3                  read_date-and-time-of-creation (4),                  3
3                  read_date-and-time-of-last-modification (5),         3
3                  read_date-and-time-of-last-read-access (6),          3
3                  read_date-and-time-of-last-attribute-modification(7),3
3                  read_identity-of-creator (8),                        3
3                  read_identity-of-last-modifier (9),                  3
3                  read_identity-of-last-reader (10),                   3
3                  read_identity-of-last-attribute-modifier (11),       3
3                  read_file-availability (12),                         3
3                  read_filesize (13),                                  3
3                  read_future-filesize (14),                           3
3                                                                       3
3             -- Security group                                         3
3                                                                       3
3                  read_access-control (15),                            3
3                  read_legal-qualifications (16),                      3
3                                                                       3
3             -- Private group                                          3
3                                                                       3
3                  read_private-use (17) }                              3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                (Continued on next page.)
                 Table 6.12 Information objects in NBS-9 continued.
                  
ZDDDDDDDDDDDDDDDDDDDDDDDDRDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3 file model             : {iso standard 8571 file-model (3)            3
3                        :  hierarchical (1)} FTAM hierarchical file    3
3                        :  "FTAM hierarchical file model"              3
FMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 constraint-set         : {iso standard 8571 constraint-set (4)        3
3                        :  unstructured (1)} FTAM unstructured         3
3                        : "FTAM unstructured constraint set"           3
FMMMMMMMMMMMMMMMMMMMMMMMMJMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 File contents:                                                        3
3                                                                       3
3                Datatype1 ::= FileDirectoryEntry                       3
3                              --As defined by NBS-AS2 in Appendix A,   3
3                              --Part 3 of this document                3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

3. Scope and field of Application

   This document defines the contents of a file for transfer (not for
   storage) using FTAM.

4. References

   ISO 8571, Information Processing Systems - Open Systems
   Interconnection -File Transfer, Access and Management.

5. Definitions

   This definition makes use of the terms data element, data unit and
   file access data unit as defined in ISO 8571-1

6. Abbreviations

   FTAM File Transfer, Access and Management.

7. Document Semantics

   The document consists of one file access data unit, which consists
   only of zero, one or more data elements of type <FileDirectoryEntry>
   (defined in NBS-AS2).

   The document structure takes any of the forms allowed by the FTAM
   hierarchical file model as constrained by the unstructured constraint
   set.  These definitions appear in ISO 8571-1.

   The parameter of the document type is used on <F-OPEN request> to
   specify the desired attributes of each of the files on the Filestore,
   when reading the document.


8. Abstract syntactic structure

   The abstract syntactic structure of the document is a series of file
   directory entries, each of which is defined by the
   <FileDirectoryEntry> definition in NBS-AS2.

   Additional constraints are defined for this document type:  File
   access actions are restricted to Read.  File-directory files may be
   Selected, Opened, Read, Closed, and Deselected.  They may not be
   Created or Deleted.  They may not be Written or Modified (except as a
   side effect of actions performed on individual files contained within
   a file directory).

9. Definition of transfer

9.1     Datatype definition

        The file consists of zero or more values of Datatype1 defined in
        Table 6.13.

9.2     Presentation data values

        The document is transferred as a series of presentation data
        values.  Each presentation data value shall consist of one value
        of the ASN.1 data type "Datatype1", carrying one of the file
        directory entries from the document.

        All values are transmitted in the same (but any) presentation
        context established to support the abstract syntax name "asname1"
        declared in Table 6.13.

9.3     Sequence of presentation data values

        The sequence of presentation data values is the same as the
        sequence of file directory entries within the Data Unit in the
        file.

10.     Transfer syntax

        An implementation supporting this document type shall support the
        transfer syntax generation rules named in Table 6.13 for all
        presentation data values transferred.  Implementations shall
        optionally support other named transfer syntaxes.

11.     ASE specific specifications for FTAM

11.1    Simplification and relaxation

        Relaxation is allowed to any bitstring combination of the
        document type parameter.

                       Part 2:  Constraint Sets 

NBS Ordered flat constraint set

1. Field of application

   The NBS-ordered flat constraint set applies to files which are
   structured into a sequence of individual FADUs and to which access may
   be made on an FADU basis by position in the sequence.

2. Basic constraints
            Table 6.14 Basic constraints for NBS Ordered flat
                                                                         
ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDRDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3 Constraint set descriptor    : "NBS ordered flat constraint set"      3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 Constraint set identifier    : {iso identified-organization icd (9999)3
3                              : organization-code  (1)                 3
3                              : constraint-set (4) nbs-ordered-flat(1)}3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 Node name                    : None                                   3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 File access actions          : Locate, Read, Insert, Erase, Replace   3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 Qualified action             : None                                   3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 Available access contexts    : HA, FA, UA                             3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 Creation state               : Root node without an associated data   3
3                              : unit                                   3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 Location after open          : Root node                              3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 Beginning of file            : Root node                              3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 End of file                  : No node selected; 'previous' gives last3 
3                              : node in traversal sequence,'current'and3
3                              :'next'give an error.                    3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 Read whole file              : Read in access context FA or UA with   3
3                              : FADU identity of 'begin'.              3
FMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMNMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM5
3 Write whole file (append)    : Transfer the series of leaf FADUs which3
3                              : would be generated by reading the whole3
3                              : file in access context FA; perform the 3
3                              : transfer with an FADU identity of 'end'3
3                              : and a file access action of 'insert'.  3
3                              :                                        3
3 Write whole file (replace)   : Transfer the series of leaf FADUs which3
3                              : would be generated by reading the whole3
3                              : file in access-context HA; perform the 3
3                              : transfer with FADU identity 'begin' and3
3                              : file action of 'replace'.              3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDPDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY


3. Structural constraints

   The root node shall not have an associated data unit; all children of
   the root node shall be leaf nodes and may have an associated data
   unit; all arcs from the root node shall be of length one.

4. Action constraints

   Insert: The <Insert> action is allowed only at the end of file.  If
   the FADU identity is 'end' the new node is inserted following all
   existing nodes in the file.  If the FADU identity is 'traversal
   number', the number must be at least one greater than the traversal
   number of the last existing node.  Any nodes between the last existing
   node and the new node are empty, i.e. nodes without data.  If the FADU
   identity is a 'traversal number' not greater than that of the last
   existing node, an error will occur.

   Erase: The Erase action is only allowed at the root node to empty the
   file, with FADU identity of 'begin'.  The result is a solitary root
   node without an associated data unit.

   Note: It is the intention when using this constraint set to allow for
   emptying an FADU, i.e. leaving an FADU with a DU of data length 0 (or
   without a DU); afterwards data may be reinserted into this hole.  In
   order to empty an FADU, the <Replace> operation may be used with new
   data of length zero (or with an FADU whose <data exists> bit is set to
   'false' and no DU).  Refilling the hole is accomplished by a
   <Replace> operation with the new DU (or with the new FADU, whose <data
   exists> bit is set to 'true' and the new DU).

5. Identity constraints

   The FADU identity associated with the file action shall be one of the
   identities 'begin', 'end', 'first', 'last', 'current', 'next',
   'previous' or a 'traversal number' greater than or equal to one.  The
   actions with which these identities can be used are given in the
   following table.

              Table 6.15 Identity constraints in NBS Ordered flat
                                                     
   ZDDDDDDDDBDDDDDDDBDDDDDBDDDDDBDDDDDDBDDDDDDDBDDDDDDBDDDDDDDDBDDDDDDDDDD?
   3 Action 3 Begin 3 End 3First3 Last 3Current3 Next 3Previous3Traversal 3
   CDDDDDDDDEDDDDDDDEDDDDDEDDDDDEDDDDDDEDDDDDDDEDDDDDDEDDDDDDDDEDDDDDDDDDD4
   3        3       3     3     3      3       3      3        3          3
   3 Locate 3 valid 3valid3valid3 valid3 valid 3 valid3 valid  3  valid   3
   3        3       3     3     3      3       3      3        3          3
   3 Read   3 whole 3     3leaf 3 leaf 3 leaf  3 leaf 3 leaf   3  leaf    3
   3        3       3     3     3      3       3      3        3          3
   3 Insert 3       3valid3     3      3       3      3        3  leaf    3
   3        3       3     3     3      3       3      3        3          3
   3 Erase  3 whole 3     3     3      3       3      3        3          3
   3        3       3     3     3      3       3      3        3          3
   3 Replace3 whole 3     3leaf 3 leaf 3 leaf  3 leaf 3 leaf   3  leaf    3
   3        3       3     3     3      3       3      3        3          3
   @DDDDDDDDADDDDDDDADDDDDADDDDDADDDDDDADDDDDDDADDDDDDADDDDDDDDADDDDDDDDDDY

                      Part 3:  Abstract Syntaxes 

Abstract Syntax NBS-AS1

Abstract syntax name:  {iso identified-organization icd (9999)
                       organization-code  (1) abstract-syntax (2) nbs-as1
                       (1)}
                       "NBS abstract syntax AS1"

This is an abstract syntax for the set of presentation data values, each
of which is a value of the ASN.1 type NBS-AS1.PrimType

NBS-AS1 DEFINITIONS ::=
BEGIN
PrimType ::= CHOICE {  INTEGER,
                       BIT STRING,
                       BOOLEAN,
                       IA5String,
                       GraphicString,
                       GeneralString,
                       OCTET STRING,
                       UTCTime,
                       GeneralizedTime,
                       NULL,
                       FloatingPointNumber }

                       --   The support for IA5String is the IA5 G0
                       --   character set and the IA5 C0 set
                       --   The minimum level of support for
                       --   GraphicString is the IA5 G0 character set and
                            the 8859-1 G0 and G1 sets
                       --   The minimum level of support for
                            GeneralString is the IA5 G0 character set and
                            the 8859-1 G0 and G1 character sets, and IA5
                            C0 set.

FloatingPointNumber ::=     [PRIVATE 0]    CHOICE {
                                 finite [0] IMPLICIT SEQUENCE
                                      {    Sign,
                                           mantissa BIT STRING,
                                      --   first bit must be 1
                                           exponent INTEGER},
                                 infinity [1] IMPLICIT Sign,
                                 signalling-nan [2] IMPLICIT NaN,
                                 quiet-nan [3] IMPLICIT NaN,
                                 zero [4] IMPLICIT NULL }

Sign    ::= INTEGER { positive (0), negative (1) }
NaN     ::= INTEGER
END

For this abstract syntax the following transfer syntax can be used
   {joint-iso-ccitt asn1 (1) basic-encoding (1)}
   "Basic Encoding of a single ASN.1 type"

Notes:  1.   The mantissa is a number in the range (1/2 <mantissa<1).
        2.   The value is equal to mantissa * 2 exponent.
        3.   The first bit in the mantissa is most significant.
        4.   See IEEE 754 for definitions of terminology, such as NaN.
        5.   A minimum length range (in bits) is required for the
             components of <FloatingPointNumber>, as follows: mantissa 1-
             23 bits, and exponent 0-8 bits.



Abstract Syntax NBS-AS2

Abstract syntax name:       { iso identified-organization icd (9999)
                            organization-code  (1) abstract-syntax (2)
                            nbs-as2 (2) }

                            "NBS file directory entry abstract syntax"

This is an abstract syntax for the set of presentation data values, each
of which is a value of the ASN.1 Type NBS-AS2.FileDirectoryEntry.

   NBS-AS2 DEFINITIONS ::=

   BEGIN

   FileDirectoryEntry  ::=[PRIVATE 2] Read-Attributes

   Read-Attributes     ::=ISO8571-FTAM.Read-Attributes

   END

For this abstract syntax the following transfer syntax will be used

   {    joint-iso-ccitt asn1 (1) basic-encoding (1) }

   "Basic Encoding of a single ASN.1 type"


Abstract Syntax "FTAM unstructured text abstract syntax"

This abstract syntax is defined as DataType1 (File Contents) in Table 19
of ISO 8571-2, Annex B.


Abstract Syntax "FTAM unstructured binary abstract syntax"

This abstract syntax is defined as DataType1 (File Contents) in Table 21
of ISO 8571-2, Annex B.
Part 4: Intentionally Left Empty

7. CCITT 1984 X.400 BASED MESSAGE HANDLING SYSTEM

   7.1  INTRODUCTION

   This is an implementation agreement developed by the Implementor's
   Workshop sponsored by the U.S. National Bureau of Standards to promote
   the useful exchange of data between devices manufactured by different
   vendors.  This agreement is based on, and employs protocols developed
   in accord with, the OSI Reference Model.  While this agreement
   introduces no new protocols, it eliminates ambiguities in
   interpretations.

   This is an implementation agreement for a Message Handling System
   (MHS) based on the X.400-series of Recommendations (1984) and Version
   5 of the X.400 Series Implementor's Guide from the CCITT.  It is
   recommended that product vendors consult later versions of this guide. 
   Figure 7.1 displays the layered structure of this agreement.

   This agreement can be used over any Transport protocol class.  In
   particular, this MHS agreement can be used over the Transport protocol
   class 0 used over CCITT X.25, described in section 4.6 of this
   document.  In addition, this MHS agreement can be used over the
   Transport profiles used in support of MAP (Manufacturing Automation
   Protocol) or TOP (Technical and Office Protocols).  Note that the MAP
   or TOP environment must support the reduced Basic Activity Subset
   (BAS) as defined in X.410.

   The UAs and MTAs require access to directory and routing services.  A
   Directory Service is to be provided for each (vendor-specific) domain. 
   Except insofar as they must be capable of providing addressing and
   routing described hereunder, these services and associated protocols
   are not described by this agreement.

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3                                                                       3
3     User Agent Layer                        CCITT X.420               3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                       3
3     Message Transfer Agent Layer            CCITT X.411               3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                       3
3     Reliable Transfer Service Layer         CCITT X.410               3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                       3
3     Presentation Layer                      CCITT X.410 sec. 4.2      3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                       3
3     Session Layer                           See Section 5.1.1         3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

   Figure 7.1  The layered structure of this implementation agreement


   7.2  SCOPE

   This agreement applies to Private Management Domains (PRMDs) and
   Administration Management Domains (ADMDs).  Four boundary interfaces
   are specified:

        (A)  PRMD to PRMD;
        (B)  PRMD to ADMD;
        (C)  ADMD to ADMD.
        (D)  MTA to MTA (within a PRMD, e.g., for MTAs from different
             vendors.)

   In case A, the PRMDs do not make use of MHS services provided by an
   ADMD.  In cases B and C, UAs associated with an ADMD can be the source
   or destination for messages.  Furthermore, in cases A and B, a PRMD
   can serve as a relay between MDs, and in cases B and C an ADMD can
   serve as a relay between MDs.  Figure 7.2 illustrates the interfaces
   to which the agreement applies.

   X.400 protocols other than the Message Transfer Protocol (P1) and the
   Interpersonal Messaging Protocol (P2) are beyond the scope of this
   agreement.  Issues arising from the use of other protocols or relating
   to P1 components in support of other protocols are outside the scope
   of this document.  This agreement describes the minimum level of
   services provided at each interface shown in Figure 7.2.  Provision
   for the use of the remaining services defined in the X.400 Series of
   Recommendations is outside the scope of this document.

   With the exception of intra domain connections, this agreement does
   not cover message exchange between communicating entities within a
   domain even if these entities communicate via P1 or P2.  Bilateral
   agreements between domains may be implemented in addition to the
   requirements stated in this document.  Conformance to this agreement
   requires the ability to exchange messages without use of bilateral
   agreements.

 PRMD = Private Management Domain
 ADMD = Administration Management Domain              ZDDDDD?
                                                      3PRMD 3
                                                      @DDBDDY
ZDDDDDDDDDDDDDD?                  |                   ---3----A
3         PRMD 3                  |                   ZDDADD?
3 ZDDDDDDD?    CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4PRMD 3
3 3 MTA A 3    3                  |                   @DDBDDY
3 @DDDBDDDY    3   |              A                   ---3----B
3  ---3---D    3   |                                  ZDDADD?
3 ZDDDADDD?    CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4ADMD 3
3 3 MTA B 3    3   |                                  @DDBDDY
3 @DDDDDDDY    3   |                                  ---3----C
@DDDDDDDDDDDDDDY   B                                  ZDDADD?
                                                      3ADMD 3
                                                      @DDDDDY


   Figure 7.2     This agreement applies to the interface between:  (A)
                  PRMD and PRMD; (B) PRMD and ADMD; (C) ADMD and ADMD;
                  and  (D)  MTA and MTA


   7.3  STATUS

   This version of the X.400 based Message Handling System implementation
   agreements was completed on December 17, 1987.  No further
   enhancements will be made to this version.  See the next
   section--Errata.


   7.4  ERRATA


   7.5  PRMD to PRMD

        7.5.1     Introduction

        This section is limited in scope to issues arising from the direct
        connection (interface A in Figure 7.2) of two PRMDs.  "Direct" means
        that no ADMD or relaying PRMD provides MHS services to facilitate
        message interchange.  "Direct" does not exclude those instances for
        which Administrations happen to be ADMDs but are not providing X.400
        services, that is, they are used only to provide lower layer services
        such as X.25.  Figure 7.3 schematically represents the scope of this
        section.

        These issues relate to the use of the UAL (User Agent Layer) and MTL
        (Message Transfer Layer) services, protocol elements, recommended
        practices and constraints.  In particular, this section addresses the
        P1 and P2 protocols and their related services in a direct connection
        environment.  This section describes the minimum level of services
        provided by a PRMD.  Provision for the use of the remaining services
        defined in the X.400 Series of Recommendations is beyond the scope of
        this section.


ZDDDDDDDDDDDDDDDDDDDD?                                 ZDDDDDDDDDDDDDDDDDDDDD?
3  Private Domain X  3                                 3  Private Domain Y   3
3                    3                                 3                     3
3                    3                                 3                     3
3                    3                                 3                     3
3                    3                                 3                     3
3      ZDDDDD?       3                                 3     ZDDDDDD?        3
3   ZD>3 UA  3<DDDDDDEDDDDDDDDDDDDD P2 DDDDDDDDDDDDDDDDEDDDD>3  UA  3<D?     3
3   3  CDDDDD4       3                                 3     CDDDDDD4  3     3
3   3  3 MTA 3<DDDDDDEDDDDDDDDDDDDD P1 DDDDDDDDDDDDDDDDEDDDD>3  MTA 3  3     3
3   3  @DDDDDY       3                                 3     @DDDDDDY  3     3
3   3    /3\         3                                 3        /3\    3     3
3         3          3                                 3         3     3     3
3  000000000000000   3                                 3  00000000000000     3
3  0the00000000000   3                                 3  0the0000000000     3
3  0remainder of00   3                                 3  0remainder of0     3
3  0Domain X000000   3                                 3  0Domain Y00000     3
3  0NETWORK0000000   3                                 3  0NETWORK000000     3
3  000000000000000   3                                 3  00000000000000     3
@DDDDDDDDDDDDDDDDDDDDY                                 @DDDDDDDDDDDDDDDDDDDDDY


                Figure 7.3  Interconnection of private domains


        7.5.2     Service Elements and Optional User Facilities

        This section identifies those service elements and optional user
        facilities that must be provided in support of P1 and P2.

             7.5.2.1   Classification of Support for Services

             The classification of UA and MT-Service elements is used to
             define characteristics of equipment.  Equipment can claim
             SUPPORT or NON-SUPPORT of a Service; in the case of
             UA-service elements, a separate classification is given for
             Origination and Reception.

             The service provider is defined as the entity providing the
             service, in this case, the MTL or the UAL.  The service user
             is either the MHS user or the UAL.  The classification of
             provider and user relates to the sublayer for which the
             service element is defined.

                  7.5.2.1.1 Support (S)

                  a)   Support means:

                       o    The service provider makes the service
                            element available to the service user.

                       o    The service user gives adequate support to
                            the MHS to invoke the service element or
                            makes information associated with the service
                            element available.

                  b)   Support for Origination means that:

                       o    The service provider makes the service
                            element available to the service user for
                            invocation.

                       o    The service user gives adequate support to
                            the end user of the MHS to invoke the service
                            element.

                  c)   Support for Reception means that:

                       o    The service provider makes information
                            associated with the service element available
                            to the service user.

                  Note: A UA- or MT-service element can carry
                  information from originator to recipient only if:

                       o    the service element is available to the
                            originator,
                       o    the service element is available to the
                            recipient, and
                       o    all intermediate steps carry the information.

                  7.5.2.1.2 Non Support (N)

                  This means that the service provider is not required to
                  make the service element available to the service user. 
                  However, the service provider should not regard the
                  occurrence of the corresponding protocol elements as an
                  error and should be able to relay such elements. 
                  Implementations making a profile available should
                  indicate deviations (additions or deletions) with
                  respect to the requirement in the profile.

                  7.5.2.1.3 Not Used (N/U)

                  This means that although the Recommendation allows this
                  service element, this profile does not use it.

                  7.5.2.1.4 Not Applicable (N/A)

                  This means that this service element does not apply in
                  this particular case (for originator or recipient).

             7.5.2.2   Summary of Supported Services

             a)   Within a PRMD, a User Agent must support all P2 BASIC
                  IPM Services (X.400) and all P2 ESSENTIAL IPM Optional
                  user facilities (X.401) subject to the qualifiers
                  listed in Appendix 7A.

             b)   Within a PRMD, a MTA must support all BASIC MT Services
                  (X.400) and all ESSENTIAL MT optional user facilities
                  (X.401) subject to the qualifiers listed in Appendix
                  7A.

             c)   No support is required of the additional optional user
                  facilities of X.401.

             7.5.2.3   MT Service Elements and Optional User Facilities

             Tables 7.1 through 7.3 show the message transfer (MT)
             service elements and optional user facilities.


                   Table 7.1 Basic MT service elements
 ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
 3                                            Support (S) or  3
 3     Service Elements                       Non-support (N) 3
 3                                                            3
 CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
 3 Access Management                                  N/U1    3
 3 Content Type Indication                            S       3
 3 Converted Indication                               S       3
 3 Delivery Time Stamp Indication                     S       3
 3 Message Identification                             S       3
 3 Non-delivery Notification                          S       3
 3 Original Encoded Information Types Indication      S       3
 3 Registered Encoded Information Types               N/U1    3
 3 Submission Time Stamp Indication                   S       3
 @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
 
 DDDDDDDDDDDDDDDD

1    Not applicable to co-resident UA and MTA.



Table 7.2    MT optional user facilities provided to the UA-selectable on a
             per-message basis

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3                                                                            3
3                                                   Support (S) or           3
3  MT Optional User Facilities      Categorization  Non-support (N)          3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                            3
3 Alternate Recipient Allowed               E              S                 3
3 Conversion Prohibition                    E              S                 3
3 Deferred Delivery                         E              N2                3
3 Deferred Delivery Cancellation            E              N2                3
3 Delivery Notification                     E              S                 3
3 Disclosure of Other Recipients            E              N3                3
3 Explicit Conversion                       A              N                 3
3 Grade of Delivery Selection               E              S                 3
3 Multi-destination Delivery                E              S                 3
3 Prevention of Non-delivery Notification   A              N                 3
3 Probe                                     E              N4                3
3 Return of Contents                        A              N                 3
3                                                                            3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY


Table 7.3    MT optional user facilities provided to the UA agreed for
             any contractual period of time

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3                                               Support (S) or  3
3 MT Optional User Facilities   Categorization   Non-Support (N)3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                               3
3Alternate Recipient Assignment         A               N       3
3Hold for Delivery                      A               N/U     3
3Implicit Conversion                    A               N       3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
 
 DDDDDDDDDDDDD

E: Essential optional user facility.
A: Additional optional user facility.
2  A local facility subject to qualifiers in Appendix 7A.
3  Support not required for an originating MT user; support must be
   provided for recipient MT users.
4  Subject to qualifiers in Appendix 7A.



             7.5.2.4   IPM Service Elements and Optional User Facilities

             Tables 7.4 through 7.5 show the IPM service elements and
             optional user facilities.


                  Table 7.4 Basic IPM service elements

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3                                                               3
3                                    Origination   Reception    3
3        Service  Elements              by UAs        by UAs    3
3                                                               3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3Access Management                        N/U5           N/U5   3
3Content Type Indication                  S              S      3
3Converted Indication                     N/A            S      3
3Delivery Time Stamp Indication           N/A            S      3
3Message Identification                   S              S      3
3Non-delivery Notification                S              N/A    3
3Original Encoded Information             S              S      3
3   Types Indication                                            3
3Registered Encoded Information Types     N/A            N/A5   3
3Submission Time Stamp Indication         S              S      3
3IP-message Identification                S              S      3
3Typed Body                               S              S      3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

5    Does not apply to co-resident UA and MTA.


Table 7.5    IPM optional facilities agreed for a contractual period of
             time

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3                                                              3
3                                               Support (S) or 3
3     Service Elements       Categorization     Non-Support (N)3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3Alternate Recipient Assignment      A                N        3
3Hold for Delivery                   A                N        3
3Implicit Conversion                 A                N        3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

                                    
Table 7.6  IPM optional user facilities selectable on a per-message basis

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3                                                             3
3                                       Origination  Reception3
3 IPM Optional User Facilities             by UAs      by UAs 3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3Alternate Recipient Allowed               A (N)         A (N)3
3Authorizing  Users Indication             A (N)         E (S)3
3Auto-forwarded Indication                 A (N)         E (S)3
3Blind Copy Recipient Indication           A (N)         E (S)3
3Body Part Encryption Indication           A (N)         E (S)3
3Conversion Prohibition                    E (S)         E (S)3
3Cross-referencing Indication              A (N)         E (S)3
3Deferred Delivery                         E (N)6        N/A  3
3Deferred Delivery Cancellation            A (N/U)6      N/A  3
3Delivery Notification                     E (S)         N/A  3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3Disclosure of Other Recipients            A (N)         E (S)3
3Expiry Date Indication                    A (N)         E (S)3
3Explicit Conversion                       A (N)         N/A  3
3Forwarded IP-message Indication           A (N)         E (S)3
3Grade of Delivery Selection               E (S)         E (S)3
3Importance Indication                     A (N)         E (S)3
3Multi-destination Delivery                E (S)         N/A  3
3Multi-part Body                           A (N)         E (S)3
3Non-receipt Notification                  A (N)         A (N)3
3Obsoleting Indication                     A (N)         E (S)3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3Originator Indication                     E (S)         E (S)3
3Prevention of Non-delivery Notification   A (N)         N/A  3
3Primary and Copy Recipients Indication    E (S)         E (S)3
3Probe                                     A (N)         N/A  3
3Receipt Notification                      A (N)         A (N)3
3Reply Request Indication                  A (N)         E (S)3
3Replying IP-message Indication            E (S)         E (S)3
3Return of Contents                        A (N)         N/A  3
3Sensitivity Indication                    A (N)         E (S)3
3Subject Indication                        E (S)         E (S)3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

DDDDDDDDDDD

6    A local facility subject to qualifiers in Appendix 7A.

        7.5.3     X.400 Protocol Definitions

        This section reflects the agreements of the NBS/OSI Workshop
        regarding P1 and P2 protocol elements.

             7.5.3.1   Protocol Classification

             The protocol classifications are defined below in table
             7.7:
                                                                       
ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD? 
3   1)  UNSUPPORTED = X                                                     3 
3       These elements may be generated, but no specific processing should  3
3       be expected in a relaying or delivering domain.  A relaying domain  3
3       must at least relay the semantics of the element.  The absence of   3
3       these elements should not be assumed, in a relaying or delivering   3
3       domain, to convey any significance.                                 3
3                                                                           3
3   2)  SUPPORTED = H                                                       3
3       These elements may be generated.  However, implementations are not  3
3       required to be able to generate these elements.  Appropriate        3
3       actions shall be taken in a relaying or delivering domain.          3
3                                                                           3
3   3)  GENERATABLE = G                                                     3
3       Implementations must be able to generate and handle these protocol  3
3       elements, although they are not necessarily present in all          3
3       messages generated by implementations of this profile.              3
3       Appropriate actions shall be taken in a relaying or delivering      3
3       domain.                                                             3
3                                                                           3
3   4)  REQUIRED = R                                                        3
3       Implementations of this profile must always generate this protocol  3
3       element.  However, its absence cannot be regarded as a protocol     3
3       violation as other MHS implementations may not require this         3
3       protocol element.  Appropriate actions shall be taken in a          3
3       relaying or delivering domain.                                      3
3                                                                           3
3   5)  MANDATORY = M                                                       3
3       This must occur in each message as per X.411 or X.420 as            3
3       appropriate; absence is a protocol violation.  Appropriate actions  3
3       shall be taken in a relaying or delivering domain.                  3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

                      Table 7.7  Protocol Classifications


             7.5.3.2   General Statements on Pragmatic Constraints

             a)   Where a protocol element is defined as a choice of
                  Numeric String and Printable String (i.e.,
                  Administration Domain Name and Private Domain
                  Identifier), then a numeric value encoded as a
                  printable string is equivalent to the same value
                  encoded as a numeric string.  This does not apply to
                  the Country Name protocol element.

             b)   The maximum number of recipients in a single MPDU is
                  32K - 1 (that is, 32767).  However, no individual
                  limits on the number of occurrences (recipients) are
                  placed on the following protocol elements: Authorizing
                  Users, Primary Recipients, Copy Recipients, Blind Copy
                  Recipients, Obsoletes and Cross References. 
                  Additionally, there is no limit on the number of Reply
                  to Users.  This is a local matter for the originating
                  system.

             c)   Use of strings.  A Printable String is defined in terms
                  of the number of characters, which is the same number
                  of octets.  For T.61 strings the number of octets is
                  twice the number of characters specified.

             d)   The ability to generate maximum size elements is not
                  required, with the exception of the component fields in
                  the Standard Attribute List, in which case it is
                  required.


             7.5.3.3   MPDU Size

             The following agreements govern the size of MPDUs:

             o    All MTAEs must support at least one MPDU of at least
                  two megabyte.

             o    The size of the largest MPDU supported by a UAE is a
                  local matter.


             7.5.3.4   P1 Protocol Elements

                  7.5.3.4.1 P1 Envelope Protocol Elements

                  Table 7.8 contains Protocol Elements and their
                  classes.

                       Table 7.8   P1 protocol elements

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Element                          Class         Restrictions and Comments    3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3MPDU                                                                        3
3   UserMPDU                        G                                        3
3   DeliveryReportMPDU              G                                        3
3                                                                            3
3   ProbeMPDU                       H                                        3
3                                                                            3
3UserMDPU                                                                    3
3   UMPDUEnvelope                   M                                        3
3   UMPDUContent                    M                                        3
3                                                                            3
3UMPDUEnvelope                                                               3
3   MPDUIdentifier                  M                                        3
3   originator ORname               M                                        3
3   originalEncodedInformationTypes G                                        3
3                                         If this field is absent, then the  3
3                                         Encoded Information Type is        3
3                                         "unspecified".                     3
3   ContentType                     M                                        3
3   UAContentID                     H     Maximum length = 16 characters.    3
3   Priority                        G                                        3
3   PerMessageFlag                  G     Maximum length = 2 octets.         3
3   deferredDelivery                X                                        3
3   PerDomainBilateralInfo          X     No limit on number of occurrences. 3
3   RecipientInfo                   M     Maximum number = 32K - 1 occurr-   3
3                                         ences. More severe limitations are 3
3                                         by bilateral agreement.            3
3   TraceInformation                M                                        3
3UMPDUContent                       M                                        3
3                                                                            3
3MPDUIdentifier                                                              3
3   GlobalDomainIdentifier          M                                        3
3   IA5String                       M     Maximum length = 32 characters,    3
3                                         graphical subset only.  Refer to   3
3                                         T.50 for clarification of graphical3
3PerMessageFlag                           subset.                            3
3   discloseRecipients              H                                        3
3   conversionProhibited            G                                        3
3   alternateRecipientAllowed       H                                        3
3   contentReturnRequest            X                                        3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                      (Continued on next page.)
                  Table  7.8 P1 protocol elements, Continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Element                          Class   Restrictions and Comments          3
3                                                                            3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3PerDomainBilateralInfo                                                      3
3   CountryName                     M     Maximum length = 3 characters.     3
3   AdministrationDomainName        M     Maximum length = 16 characters.    3
3   BilateralInfo                   M     Maximum depth = 8; maximum         3
3                                         length = 1024 octets               3
3                                         (including encoding).              3
3 RecipientInfo                                                              3
3   recipient                       M                                        3
3   ExtensionIdentifier             M     Maximum value = 32K - 1 (32767).   3
3   perRecipientFlag                M     Maximum length = 2 octets.         3
3   ExplicitConversion              X                                        3
3                                                                            3
3perRecipientFlag                                                            3
3   ResponsibilityFlag              M                                        3
3   ReportRequest                   M                                        3
3   UserReportRequest               M                                        3
3                                                                            3
3TraceInformation                         Reference should be made to        3
3                                         Version 5 of the X.400 Imple-      3
3                                         mentor's Guide for information     3
3   GlobalDomainIdentifier          M     related to Trace sequencing.       3
3   DomainSuppliedInfo              M                                        3
3                                                                            3
3DomainSuppliedInfo                                                          3
3   arrival                         M                                        3
3   deferred                        X                                        3
3   action                          M                                        3 
3     0=relayed  (value)            G                                        3
3     1=rerouted (value)            H     Rerouting is not required.         3
3   converted                       H                                        3
3   previous                        H                                        3
3                                                                            3
3ORName                                   See section 7.5.3.5                3
3                                                                            3
3EncodedInformationTypes                                                     3
3   bit string                      M     Delivery can only occur if match   3
3                                         is made with Registered Encoded    3
3                                         Information Types.  Individual     3
3                                         vendors may impose limits.         3
3                                         Maximum length = 4 octets.         3
3   G3NonBasicParameters            X                                        3
3   TeletexNonBasicParameters       X                                        3
3   PresentationCapabilities        X                                        3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                      (Continued on next page.)
                   Table 7.8 P1 protocol elements, Continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3                                                                            3
3Element                         Class    Restrictions and Comments          3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                            3
3DeliveryReportMPDU                                                          3
3   DeliveryReportEnvelope          M                                        3
3   DeliveryReportContent           M                                        3
3                                                                            3
3                                                                            3
3                                                                            3
3DeliveryReportEnvelope                                                      3
3   report                          M                                        3
3   originator                      M                                        3
3   TraceInformation                M                                        3
3                                                                            3
3DeliveryReportContent                                                       3
3   original                        M                                        3
3   intermediate                    G     See comment at end of table.       3
3   UAContentID                     G                                        3
3   ReportedRecipientInfo           M     Maximum number = 32K - 1           3
3                                         occurrences.                       3
3   returned                        H     Can only be issued if specifically 3
3                                         requested in the originating       3
3                                         message.                           3
3   billingInformation              X     Maximum depth = 8; maximum         3
3                                         length = 1024 octets (including    3
3                                         encoding).                         3
3                                                                            3
3                                                                            3
3ReportedRecipientInfo                                                       3
3   recipient                       M                                        3
3   ExtensionsIdentifier            M                                        3
3   PerRecipientFlag                M                                        3
3   LastTraceInformation            M                                        3
3   intendedRecipient               H                                        3
3   SupplementaryInformation        X     Maximum length = 64 characters.    3
3                                         Value is pending verification by   3
3                                         the CCITT SG VIII or XI.           3
3                                                                            3
3                                                                            3
3                                                                            3
3                                                                            3
3LastTraceInformation                                                        3
3   arrival                         M                                        3
3   converted                       G                                        3
3   Report                          M                                        3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                       (Continued on next page.
                   Table 7.8 P1 protocol elements, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3                                                                            3
3Element                          Class   Restrictions and Comments          3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3Report                                                                      3
3   DeliveredInfo                   G     Generated if delivery is reported. 3
3   NondeliveredInfo                G     Generated if failure to deliver    3
3                                         is reported.                       3
3DeliveredInfo                                                               3
3   delivery                        M                                        3
3   typeofUA                        R     This element must be generated with3
3                                         a PRIVATE value by PRMDs.          3
3                                                                            3
3NonDeliveredInfo                                                            3
3   ReasonCode                      M                                        3
3   DiagnosticCode                  H     Whenever possible, use a meaningful3
3                                         diagnostic code.                   3
3                                                                            3
3ProbeEnvelope                                                               3
3   probe                           M                                        3
3   originator                      M                                        3
3   ContentType                     M                                        3
3   UAContentID                     H     Maximum length = 16 characters.    3
3   original                        G     If this field is absent, then the  3
3                                         Encoded Information Type is        3
3                                         "unspecified".                     3
3                                                                            3
3                                                                            3
3   TraceInformation                M                                        3
3                                                                            3
3   PerMessageFlag                  G                                        3
3                                                                            3
3   contentLength                   H                                        3
3   PerDomainBilateralInfo          X                                        3
3   RecipientInfo                   M     Maximum number = 32K - 1           3
3                                         occurrences.                       3
3GlobalDomainIdentifier                                                      3
3   CountryName                     M     Maximum length = 3 characters.     3
3   AdministrationDomainName (4)    M     Maximum length = 16 characters or  3
3                                         digits.                            3
3                                                                            3
3   PrivateDomainIdentifier         R     Maximum length = 16 characters or  3
3                                         digits.  This element must be      3
3                                         generated by PRMDs.                3
3                                                                            3
3                             End of Definitions                             3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY



Notes on Table 7.8

        Comment on intermediate TraceInformation in the
        DeliveryReportContent in table 7.8:  Audit and confirmed reports
        should not be requested  by other than the originating domain for
        two reasons.  First, the return path of the report may be
        different from the path taken by the original message, and it may
        exclude the domain that added the request for audit and confirmed
        to the message.  Second, if the return path is different from the
        path of the original message, the originating domain would
        receive intermediate trace information that it did not request.

             7.5.3.5   ORName Protocol Elements

             Only form 1 variant 1 O/R names are supported.

             Table 7.9 contains ORName protocol elements.

             These agreements interpret 1984 X.400 Section 3.4 to mean
             that the attributes in the ORName in the MPDU must identify
             exactly one UA, and that all the values for the attributes
             specified in the ORName must be identical to the values of
             the corresponding attributes associated with the recipient
             UA. Underspecified names that are unique are deliverable.

             Overspecified ORNames, ORNames with mismatching fields, and
             ambiguous names are to be non-delivered or sent to the
             alternate recipient as appropriate.

                     Table 7.9   ORName protocol elements

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Element                          Class     Restrictions and Comments        3
3                                                                            3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                            3
3ORName                                                                      3
3   StandardAttributeList           M                                        3
3   DomainDefinedAttributeList      X                                        3
3                                                                            3
3StandardAttributeList (1)                                                   3
3   CountryName                     R     As defined in X.411, Maximum       3
3                                         length = 3 characters.             3
3   AdministrationDomainName (4)    R     Maximum length = 16 characters     3
3                                         or digits.                         3
3   X121Address                     X     Maximum length = 15 digits.        3
3   TerminalID                      X     Maximum length = 24 characters.    3
3   PrivateDomainName (2)           G     Maximum length = 16 characters.    3
3   OrganizationName (2)            G     Maximum length = 64 characters.    3
3   UniqueUAIdentifier              X     Maximum length = 32 digits.        3
3   PersonalName                    G     Maximum length of values of sub-   3
3                                         elements = 64 characters.          3
3                                         Note:  The possibility that this   3
3                                                value may be reduced to 40  3
3                                                characters is for further   3
3                                                study by the CCITT.         3
3                                                                            3
3   OrganizationalUnit (3)          G     Maximum length = 32 characters per 3
3                                         occurrence.  A maximum of four     3
3                                         occurrences are allowed.           3
3                                                                            3
3DomainDefinedAttributeList (5)           Maximum = 4 occurrences.           3
3   type                            M     Maximum length = 8 characters.     3
3   value                           M     Maximum length = 128 characters.   3
3                                                                            3
3PersonalName                                                                3
3   surName                         M     Maximum length = 40 characters.    3
3   givenName                       G     Maximum length = 16 characters.    3
3   initials                        G     Maximum length =  5 characters;    3
3                                         excluding surname initial and      3
3                                         punctuation and spaces.            3
3   generationQualifier             G     Maximum length = 3 characters.     3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                      (Continued on next page.)
                Table 7.9  ORName Protocol Elements, Continued


Notes:

   1.   The following apply for comparison of the Standard Attributes of
        an O/R Name:

        a.   Lower case is interpreted as upper case (for IA5).

        b.   Multiple spaces may be interpreted as a single space.       
             Originating domains shall only transmit single              
             significant spaces.  If multiple spaces are transmitted,    
             non-delivery may occur.

   2.   At least one of these must be supplied.

   3.   These should be sent in ascending sequence, from the least
        significant <Organizational Unit>  (lowest in organization
        hierarchy) to the most significant.  Only those specified should
        be sent. (That is, an unspecified <Organizational  Unit> should
        not be sent along as a field of [null] content, nor zero length,
        etc.)

   4.   This attribute shall contain one space in all ORNames of messages
        originated in a PRMD that is not  connected to an ADMD,  and in
        ORNames of recipients reachable only through a PRMD; otherwise,
        this attribute shall contain an appropriate ADMD name.

   5.   Some existing systems which will be accessed via an X.400 service
        (whether directly connected using X.400 protocols or otherwise)
        may require the provision of addressing attributes which are not
        adequately supported by Standard Attributes as defined in these
        Agreements.  In such cases, Domain Defined Attributes are an
        acceptable means of carrying additional addressing information. 
        Failure to support the specification and relaying of DDAs may
        prevent successful interworking with such existing systems until
        such time as all systems are capable of relaying and delivery
        using only the Standard Attribute list.  Specific recommendations
        on the use of DDAs for particular applications are in the
        Recommended Practices Section 7.12, Appendix B.

             7.5.3.6   P2 Protocol Profile (Based on [X.420])

             Tables 7.10 and 7.11 classify the support for the P2
             protocol  elements required by this profile.  The tables
             give restrictions and comments in addition to X.420.

             Restriction on length is one of the types of restrictions. 
             The reaction of implementations to a violation of this
             restriction is not defined by this Profile.

                  7.5.3.6.1 P2 Protocol - Heading

                  Table 7.10 below specifies the support for protocol
                  elements in P2 Headings.

                   Table 7.10   P2 heading protocol elements

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3   Element                     Class     Restrictions and Comments          3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3UAPDU                                                                       3
3   IM-UAPDU                        G                                        3
3   SR-UAPDU                        X                                        3
3                                                                            3
3IM-UAPDU                                                                    3
3   Heading                         M                                        3
3   Body                            M                                        3
3                                                                            3
3Heading                                                                     3
3   IPMessageId                     M                                        3
3   originator                      R                                        3
3   authorizingUsers                H                                        3
3   primaryRecipients               G     At least one of primaryRecipients, 3
3   copyRecipients                  G     copyRecipients, or                 3
3                                         blindCopyRecipients must be        3
3   blindCopyRecipients             H     present.                           3
3   inReplyTo                       G                                        3
3   obsoletes                       H                                        3
3   crossReferences                 H                                        3
3   subject                         G     Maximum length = 128 T.61          3
3                                         characters (256 octets);the ability3
3                                         to generate the maximum size       3
3                                         subject is not required.           3
3   expiryDate                      H                                        3
3   replyBy                         H                                        3
3   replyToUsers                    H                                        3
3   importance                      H     Appropriate action is for further  3
3                                         study.                             3
3   sensitivity                     H     Appropriate action is for further  3
3                                         study.                             3
3   autoforwarded                   H                                        3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                      (Continued on next page.)
              Table 7.10 P2 heading protocol elements, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Element                         Class    Restrictions and Comments          3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                            3
3IPmessageId                                                                 3
3   ORName                          H                                        3
3   PrintableString                 M     Maximum length = 64 characters.    3
3ORDescriptor                                                                3
3   ORName                          H     Specify the ORName whenever it is  3
3                                         possible.  See Appendix 7B.        3
3   freeformName                    H     Maximum length = 64 characters,    3
3                                         graphical subset only (128 octets.)3
3   telephoneNumber                 H     Maximum length = 32 characters.    3
3                                         This allows for punctuation. It    3
3                                         does not take into account possible3
3                                         future use by ISDN.                3
3                                                                            3
3Recipient                                                                   3
3   ORDescriptor                    M                                        3
3   reportRequest                   X                                        3
3   replyRequest                    H                                        3
3                                                                            3
3Body                                     No limit on number of BodyParts.   3
3   BodyPart                        G     No limit on length of any BodyPart 3
3                                         or the depth of ForwardedIPMessage 3
3                                         BodyParts nested. Classification is3
3                                         subject to pending CCITT resolution3
3                                                                            3
3                                                                            3
3SR-UAPDU                                                                    3
3   nonReceipt                      H                                        3
3   receipt                         H                                        3
3   reported                        M                                        3
3   actualRecipient                 R                                        3
3   intendedRecipient               H                                        3
3   converted                       X                                        3
3NonReceiptInformation                                                       3
3   reason                          M                                        3
3   nonReceiptQualifier             H                                        3
3   comments                        H     Maximum length = 256 characters.   3
3   returned                        H     May only be issued if specifically 3
3                                         requested by originator.           3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                      (Continued on next page.)
              Table 7.10  P2 heading protocol elements, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Element                         Class    Restrictions and Comments          3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                            3
3ReceiptInformation                                                          3
3   receipt                         M                                        3
3   typeOfReceipt                   H                                        3
3   SupplementaryInformation        X     Maximum length = 64 characters.    3
3                                         Note:  This value is pending       3
3                                         verification by the CCITT SG       3
3                                         VIII or IX.                        3
3                                                                            3
3                         End of Definitions                                 3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY


                  7.5.3.6.2 P2 Protocol - BodyParts

                  a)   All BodyParts with identifiers in the range 0 up
                       to and including 16K -1 are legal and should be
                       relayed.  BodyPart identifiers corresponding to
                       X.121 Country Codes should be interpreted as
                       described in Note 2 of figure 7.4.

                       o    Implementations are required to generate and
                            image IA5Text.

                       o    Implementations should specify the other
                            BodyPart types supported.

                       o    If an implementation supports a particular
                            BodyPart type for reception, it should also
                            be able to support that BodyPart type for
                            reception if it is part of a
                            ForwardedIPMessage.

                       o    For the BodyPart types currently considered,
                            support for the protocol elements is as
                            indicated in table 7.11.

                  b)   Privately Defined BodyParts

                       This section describes an interim means for
                       identifying privately defined BodyParts.  This
                       section shall be replaced in a future version
                       taking into account CCITT recommendations with
                       equivalent functionality.
ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3        BodyPart  :: =  CHOICE {                                           3
3          [0]IMPLICIT IA5Text,                                             3
3                     [1]IMPLICIT TLX,                                      3
3                         .                                                 3
3                         .                                                 3
3                         .                                                 3
3                   [234]IMPLICIT UKBodyParts,                              3
3                         .                                                 3
3                         .                                                 3
3                         .                                                 3
3                   [310]IMPLICIT USABodyParts,                             3
3                         .                                                 3
3                         .                                                 3
3                         .                    }                            3
3                   Where UKBodyParts and USABodyParts are defined as:      3
3                                                                           3
3                     SEQUENCE {BodyPartNumber, ANY}                        3
3                                                                           3
3                     BodyPartNumber ::= INTEGER                            3
3                                                                           3
3                                                                           3
3                                                                           3
3                                                                           3
3                                                                           3
3       Note 1:  In the EncodedInformationTypes of the P1 Envelope, the     3
3                undefined bit must be set when a message contains a        3
3                privately defined BodyPart.  Each UA that expects such     3
3                BodyParts should include undefined in the set of           3
3                deliverable EncodedInformationTypes it registers with the  3
3                MTA.                                                       3
3                                                                           3
3       Note 2:  All BodyPartNumbers assigned must be interpreted relative  3
3                to the BodyPart in which they are used, which is that      3
3                tagged with the value [310] for those defined within the   3
3                United States.  The NBS assigns unique message             3
3                BodyPartNumbers for privately defined formats within the   3
3                United States.                                             3
3                                                                           3
3       Note 3:  Refer to section 7.12.6 for recommendations regarding the  3
3                implementaion of USABodyParts.                             3
3                                                                           3
3                                                                           3
3                                                                           3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

          Figure 7.4  X.409 Definition of Privately Defined BodyParts
                  7.5.3.6.3 P2 BodyPart Protocol Elements

                           Table 7.11   P2 BodyParts

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Elements                        Class    Restrictions and Comments          3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                            3
3BodyPart                                                                    3
3   IA5Text                         G                                        3
3   TLX                             X                                        3
3   Voice                           X                                        3
3   G3Fax                           X                                        3
3   TIFO                            X                                        3
3   TTX                             X                                        3
3   Videotex                        X                                        3
3   NationallyDefined               X                                        3
3   Encrypted                       X                                        3
3   ForwardedIPMessage              H                                        3
3   SFD                             X                                        3
3   TIF1                            X                                        3
3   unidentified                    X                                        3
3                                                                            3
3IA5Text                                                                     3
3   repertoire                      H                                        3
3   IA5String                       M     For rendition of IA5Text see       3
3                                         Appendix 7C.                       3
3TLX                                      For further study by CCITT.        3
3                                                                            3
3Voice                                                                       3
3   Set                                   For further study by CCITT.        3
3   BitString                       M                                        3
3                                                                            3
3G3Fax                                                                       3
3   numberOfPages                   X                                        3
3   P1.G3NonBasicParameters         X                                        3
3   SEQUENCE (OF BIT STRING)        M                                        3
3   BIT STRING                      H     See Note.                          3
3                                                                            3
3P1.G3NonBasicParameters                  Support for individual elements is 3
3                                         for further study.                 3
3                                                                            3
3TIFO                                                                        3
3   T.73Document                    M                                        3
3   T.73ProtocolElement             H     See Note.                          3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                      (Continued on next page.)
                      Table 7.11  P2 BodyParts, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Elements                       Class     Restrictions and Comments          3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                            3
3TTX                                                                         3
3   numberOfPages                   X                                        3
3   telexCompatible                 X                                        3
3   P1.TeletexNonBasicParams        X                                        3
3   SEQUENCE                        M                                        3
3   T61String                       H     See Note.                          3
3                                                                            3
3P1.TeletexNonBasicParams                                                    3
3   graphicCharacterSets            X                                        3
3   controlCharacterSets            X                                        3
3   pageFormats                     X                                        3
3   miscTerminalCapabilities        X                                        3
3   privateUse                      X                                        3
3                                                                            3
3Videotex                                                                    3
3   SET                                   For further study by CCITT.        3
3   VideotexString                  M                                        3
3                                                                            3
3NationallyDefined                                                           3
3   ANY                             M                                        3
3                                                                            3
3Encrypted                                                                   3
3   SET                                   For further study by CCITT.        3
3   BIT STRING                      M                                        3
3                                                                            3
3ForwardedIPMessage                                                          3
3   delivery                        H                                        3
3   DeliveryInformation             H                                        3
3   IM-UAPDU                        M                                        3
3                                                                            3
3DeliveryInformation                                                         3
3   P1.ContentType                  M                                        3
3   originator                      M                                        3
3   original                        M                                        3
3   P1.Priority                     G                                        3
3   DeliveryFlags                   M                                        3
3   otherRecipients                 H                                        3
3   thisRecipient                   M                                        3
3   intendedRecipient               H                                        3
3   converted                       X                                        3
3   submission                      M                                        3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                      (Continued on next page.)
                          Table  7.11  P2 BodyParts, continued
                                                                              
ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Elements                        Class      Restrictions and Comments        3
3                                                                            3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3SFD                                                                         3
3   SFD.Document                    M                                        3
3                                                                            3
3TIF1                                                                        3
3   T73 Document                    M                                        3
3   T73.ProtocolElement             H       See note.                        3
3               DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD                      3
3                                                                            3
3Note:  This element is not an addition to the definition of the BodyPart.   3
3       It is described here to show that the SEQUENCE may contain zero      3
3       elements.  A Problem Report has been submitted to the CCITT to       3
3       clarify whether this is permissible.  The NBS/OSI Workshop will      3
3       adopt the CCITT decision.                                            3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

        7.5.4     Reliable Transfer Server (RTS)

             7.5.4.1   Implementation Strategy

             Based on X.410 clause 3 and X.411 clause 3.5.

             7.5.4.2   RTS option selection

             a)   The maximum number of simultaneous associations is not
                  limited in this profile; if the capacity of a system is
                  exceeded, it should not initiate or accept additional
                  associations.

             b)   Associations are established by the MTA which has
                  messages to transfer.

             c)   Associations are released when they are not needed. 
                  Associations may also be ended prematurely due to
                  internal problems of the RTS.

             d)   For both monologue and two way alternate associations,
                  the initiator keeps the initial turn.

             e)   When establishing an RTS association, the following
                  rules apply to the use of parameters in addition to
                  those in X.410 clause 3.2.1:

                  Dialogue mode: Monologue must be supported for this
                                 profile; two-way alternate is used only
                                 if both partners agree.

                  Initial turn:  Kept by the initiator of the
                                 association.

             f)   The 'priority-mechanism' and the 'transfer-time limit'
                  are regarded as local matters.

             7.5.4.3   RTS Protocol Options and Clarifications

             Realization of the RTS protocol is subject to the following
             rules in addition to those specified in X.410 clause 4:

             a)   One RTS association corresponds to one or more
                  consecutive session connections (not concurrent ones). 
                  The first is opened with ConnectionData of type OPEN,
                  and subsequent ones are opened with type RECOVER.

             b)   Recovery of a Session connection is only by RTS
                  initiator.

             c)   Checkpoint size:

                  o    Checkpointing and No Checkpointing should be
                       supported.  Whenever possible, checkpointing
                       should be used.

                  o    The minimum checkpointSize is 1 (that is, 1024
                       octets).

             d)   Window size:

                  o    Minimal value of 1 (if checkpointing is
                       supported).

                  o    WindowSize = 1 means:  After an S-SYNCH-MINOR
                       request is sent, wait until the confirmation is
                       received before issuing an S-DATA, S-SYNCH-MINOR,
                       or S-ACTIVITY-END request.

             e)   APDUs should not be blocked into one activity.

             f)   Only one SSDU shall be transferred:

                  o    Between two adjacent minor synch points.

                  o    Between minor synch points and adjacent
                       S-ACTIVITY-START and S-ACTIVITY-END requests.

                  o    Between S-ACTIVITY-START and S-ACTIVITY-END
                       without checkpoints.

             g)   A monologue association is defined as follows:

                  o    The RTS user responsible for establishing the
                       association is called the initiator.

                  o    The initiator keeps the initial turn.

                  o    APDUs are transferred in the direction of the
                       initiator to the recipient only.

                  o    There shall be no token passing.

                  o    Only the initiator can effect an orderly release
                       of the association.

             h)   A two-way alternate association is as described in
                  X.410.

             i)   In the UserData parameter of the S-U-ABORT, the
                  ReflectedParameter will not be used in the
                  AbortInformation element.

             j)   When the S-ACTIVITY-RESUME is used to resume an
                  activity in the same session connection as the one in
                  which it started, this must happen immediately after
                  the activity has been interrupted (i.e., no intervening
                  activity can occur).  Otherwise, X.410 clause 4.3
                  paragraph 1 may be violated.

             k)   When S-ACTIVITY-RESUME is used to resume an activity
                  started in another session connection, the following
                  conditions must be met:

                  o    The current session connection is of type
                       "recover".

                  o    The value of OldSessionConnectionIdentifier in
                       S-ACTIVITY-RESUME must match the value of the
                       SessionConnectionIdentifier parameter used in the
                       S-CONNECT of the prior session connection.  This
                       value is also identical to the
                       SessionConnectionIdentifier in the ConnectionData
                       (in PConnect, in SS-UserData) for the current
                       session connection.

                  o    This must occur as the first activity of the next
                       session connection for the same RTS-association. 
                       It must be the first, otherwise X.410 clause 4.5.1
                       point 1 is violated.

             Note: It is in the same RTS-ASSOCIATION because the use of
             S-ACTIVITY-RESUME only makes sense within the scope of one
             RTS association.

             l)   If the transfer of an APDU is interrupted before the
                  confirmation of the first checkpoint, the value of the
                  SynchronizationPointSerialNumber in S-ACTIVITY-RESUME
                  should be zero, and the S-ACTIVITY-RESUME must be
                  immediately followed by an S-ACTIVITY-DISCARD.

             m)   In S-TOKEN-PLEASE, the UserData parameter shall contain
                  an integer conforming to X.409 which conveys the
                  priority.

             n)   The receiving RTS can use the value of the Reason
                  parameter in the S-U-EXCEPTION-REPORT to suggest to the
                  sending RTS that it should either interrupt or discard
                  the current activity.  S-U-Exception Reports are
                  handled as stated in Version 5 of the Implementors
                  Guide pages 12-13, paragraph E-33.

             o)   In the case of S-P-ABORT, the current activity (if any)
                  is regarded as interrupted, rather than discarded.

             p)   Table 7.12 illustrates the legal negotiation
                  possibilities allowed by X.410 clause 4.2.1 regarding
                  checkpoint size and window size.

             q)   These agreements include the provisions of version 6 of
                  the Implementors Guide identical in all respects to
                  version 5, except that the following points have been
                  added to section 3.5:

        o    for section 4.4.1 of X.410;
             "If the receiving RTS receives an S-ACTIVITY-DISCARD
             indication primitive and has already issued a TRANSFER
             indication primitive, it aborts the connection (S-U-ABORT
             request) with the "transfer completed" version code."

        o    for section 4.6.2 of X.410
             "The "transfer completed (7)" abort reason is used to
             indicate to the sending RTS that the receiving RTS could not
             discard the activity because it has already completed the
             transfer (issued a TRANSFER indication primitive)." 
             Transfer completed (7) is also added to the table of abort
             reasons in this section.

                   Table 7.12  Checkpoint window size of IP

                          ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
                          3                acceptor answer                   3 
                          CDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDDDD4
                          3      CS = 0    3    CS = m      3   CS = n       3
                          3(or unspecified)3    WS = j      3   WS = j       3
                          3 WS unspecified 3(or unspecified)3(or unspecified)3
ZDDDDDDDDDBDDDDDDDDDDDDDDDABDDDDDDDDDDDDDDDEDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDDDD4
3         3    CS = O      3               3                3                3
3         3(or unspecified)3   legal       3     legal      3      legal     3
3         3    WS = i      3               3                3                3
3initiator3(or unspecified)3               3                3                3
3proposal 3                3               3                3                3
3         CDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDDDEDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDDDD4
3         3    CS = k      3               3                3                3
3         3    WS = i      3   legal       3     legal      3   not allowed  3
3         3(or unspecified)3               3                3                3
@DDDDDDDDDADDDDDDDDDDDDDDDDADDDDDDDDDDDDDDDADDDDDDDDDDDDDDDDADDDDDDDDDDDDDDDDY

   Legend:

   o    CS means CheckpointSize
   o    WS means WindowSize
   o    i, j, k, m, and n are integer values with the following
        relations:
 

             0 s m s k < n       (values assigned to CS)
             0 < j s i           (values assigned to WS)


   o    For unspecified parameters, the default applies.  In this
        case,the numeric relations apply, that is, the default values
        substitutefor the unspecified integer.

             7.5.4.4   RTS Protocol Limitations

             The RTS Protocol Limitations for this profile are listed in
             table 7.13.

                       Table 7.13 RTS protocol elements

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Element                         Class    Restriction                        3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                            3
3PConnect                          M                                         3
3   DataTransferSyntax             M      Value = 0.                         3
3pUserData                         M                                         3
3   checkpointSize                 H                                         3
3   windowSize                     H                                         3
3   dialogueMode                   H                                         3
3   ConnectionData                 M                                         3
3   applicationProtocol            G      Value = 1.                         3
3                                  H      Value = 8883.                      3
3   ConnectionData                                                           3
3    open                          G                                         3
3    recover                       G                                         3
3                                                                            3
3   open                                                                     3
3    RTS user data                 G                                         3
3                                                                            3
3   recover                                                                  3
3    SessionConnectionIdentifier   G                                         3
3                                                                            3
3RTS user data                                                               3
3   mTAName                        G      Maximum length 32 characters       3
3                                         graphic subset of IA5 only.        3
3   password                       G      Maximum length 64 octets           3
3                                         graphic subset of IA5 only.        3
3 < null RTS User Data >           G      Generated if other validation      3
3                                         methods are used.                  3
3                                                                            3
3SessionConnectionIdentifier                                                 3
3   CallingSSUserReference         M      Maximum length 64 octets including 3
3                                         encoding = 62 octets of T.61.      3
3   CommonReference                M                                         3
3   AdditionalReferenceInformation H      Maximum length 4 octets including  3
3                                         encoding = 2 octets of T.61.       3
3                                                                            3
3PAccept                           G                                         3
3   DataTransferSyntax             M      Value = 0.                         3
3   pUserData                      M                                         3
3   checkpointSize                 H                                         3
3   windowSize                     H                                         3
3   ConnectionData                 M                                         3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                      (Continued on next page.)
                 Table 7.13  RTS protocol elements, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Element                        Class     Restriction                        3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                            3
3PRefuse                         G                                           3
3   RefuseReason                 M                                           3
3                                                                            3
3SS User Data                    G        See Note                           3
3   (in S-TOKEN-PLEASE)                                                      3
3                                                                            3
3AbortInformation                G                                           3
3   (in S-U-ABORT)                                                           3
3   AbortReason                  H                                           3
3   reflectedParameter           X        Restricted to 8 bits.              3
3                                                                            3
3                        End of Definitions                                  3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

   Note: Generated if supplied by the RTS-user.  The RTS use may specify
   a priority in the TURN-PLEASE primitive, and if so, it is carried as
   the SS-User-Data in S-TOKEN-PLEASE.


        7.5.5     Use of Session Services

        The session requirements and use of session are covered in
        section 5 of this document.

        7.5.6     Data Transfer Syntax

        This section defines Presentation Transfer Syntax and notation
        rules applicable to these agreements.  Implementations must
        conform EXACTLY as specified in X.409 with no further
        restrictions.  Appendix 7C defines rendition of IA5 Text and T61
        characters.

   7.6  PRMD to ADMD and ADMD to ADMD

        7.6.1     Introduction

        This section defines the implementation agreements that apply to
        the interface between two management domains when at least one is
        an ADMD.  A message arriving at an ADMD has either no recipient
        within that domain or one or more recipients within that domain. 
        In the former case, the ADMD serves as a relay between two or
        more domains and the actions required of that ADMD are
        independent of the nature (PRMD or ADMD) of the domains.  In the
        latter case, the ADMD is responsible for delivering messages to
        the proper recipient(s) within its jurisdiction, and may also be
        responsible for relaying the message.

        Given the two roles for an ADMD, this section describes two
        distinct sets of functional requirements for an ADMD.  The first
        is the relaying requirement that is needed to provide PRMD and
        other ADMD interworking.  The second is analogous to the PRMD's
        support to its customers through the integrated UAs.  These are
        distinct functional differences.  The services provided to the
        UAs of an ADMD are independent of the requirement that an ADMD
        provide a function for interworking with any type of Management
        Domain (MD).  Figure 7.5 illustrates the two roles played by an
        ADMD.

        This section is presented in the form of deviations from the
        agreements applicable to PRMD-to-PRMD (section 7.5).  Unless
        explicitly noted in the remainder of this section, all of the
        specifications for PRMD to PRMD apply to PRMD to ADMD and ADMD to
        ADMD.


ZDDDDDDDDDDDDDDDDDDD?                                    ZDDDDDDDDDDDDDDDDDDD?
3   PRMD or ADMD    3                                    3       ADMD        3
3   ZDDDDDDDDDD? <--3---------------P2-------------------3--> ZDDDDDDDDD?    3
3   3 IPM - UA 3    3                                    3    3IPM - UA 3    3
3   CDDDDDDDDDD4 <--3---------------P1-------------------3--> CDDDDDDDDD4    3
3   3    MTA   3    3                                    3    3   MTA   3    3
3   @DDDDDDDDDDY    3                                    3    @DDDDDDDDDY    3
@DDDDDDDDDDDDDDDDDDDY                                    @DDDDDDDDDDDDDDDDDDDY
                                   (a)
                                                                        
ZDDDDDDDDDDDDDDDDDDD?                                    ZDDDDDDDDDDDDDDDDDDD?
3   PRMD or ADMD    3                                    3   PRMD or ADMD    3
3   ZDDDDDDDDDD?    3                                    3   ZDDDDDDDDDD?    3
3   3 IPM - UA 3 <--3---------------P2-------------------3-> 3 IPM - UA 3    3
3   CDDDDDDDDDD4    3                                    3   CDDDDDDDDDD4    3
3   3   MTA    3    3                                    3   3    MTA   3    3
3   @DDDDDDDDDDY    3                                    3   @DDDDDDDDDDY    3
@DDDDDDDDDDDDDDDDDDDY                                    @DDDDDDDDDDDDDDDDDDDY
          |                                                      |
          |                                                      |
          |                                                      |
          P1                                                     P1
          |                                                      |
          |                ZDDDDDDDDDDDDDDDDDD?                  |
          |                3       ADMD       3                  |
          ---------------->3      ZDDDD?      3<------------------
                           3      3 MTA3      3                
                           3      @DDDDY      3
                           @DDDDDDDDDDDDDDDDDDY
                     
                                   (b)


          Figure 7.5  An ADMD may (b) or may not (a) serve as a relay


        7.6.2     Additional ADMD Functionality

        The following defines the additional ADMD specific functionality
        required over and above that specified in the PRMD section.

             7.6.2.1   Relay Responsibilities of an ADMD

             ADMDs will relay all content types (not just P2) unchanged
             in the absence of a request for conversion.

             7.6.2.2   P1 Protocol Classification Changes

             Table 7.14 describes the changes to the PRMD P1 Protocol
             classifications required for a delivering Administration
             domain (with respect to the original message; this means the
             domain which originates the delivery reports).

     Table 7.14  P1 Protocol Classification Changes for a Delivering ADMD

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3                                                                           3
3  Protocol Elements                 Class                                  3
3                                                                           3
3                                                                           3
3        DeliveredInfo                                                      3
3         typeOfUA                          H                               3
3                                                                           3
3        ReportedRecipientInfo                                              3
3         SupplementaryInformation          H   See Note 1.                 3
3                                                                           3
3        GlobalDomainIdentifier                                             3
3         PrivateDomainIdentifier           H                               3
3                                                                           3
3                                                                           3
3                                                                           3
3                                                                           3
3       For relaying Administration domains, the classifications are all "X"3
3                                                                           3
3       For originating Administration domains, these are all               3
3       "NOT APPLICABLE".                                                   3
3                                                                           3
3                                                                           3
3  Note 1:  Domains providing access to TELEX/TELETEX recipients, whether   3
3           directly or indirectly as a result of bilateral agreements      3
3           between domains, must ensure that this information, when        3
3           present, is accessible by the recipient of the delivery report. 3
3                                                                           3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY


             7.6.2.3   O/R Names

             O/R Names shall consist of:

             o    CountryName,
             o    AdministrationDomainName.

             as well as one of the following:

             o    PrivateDomainName,
             o    PersonalName,
             o    OrganizationName,
             o    OrganizationalUnit,
             o    UniqueUAIdentifier,
             o    X121Address.

             and permits the optional inclusion of a

             o    DomainDefinedAttributeList.

             Note: The destination PrivateDomainName or OrganizationName
             must be present if destined for a PRMD.  The ADMD relaying
             the message to that destination PRMD requires this element.

             7.6.2.4   P1 ADMD Name

             Management Domains (MDs) must specify in the ADMD name field
             of the O/R Name StandardAttributeList in P1, the name of the
             Administration domain:

             o    to which the message is being sent (in recipient names)

             o    from which the message originated (in the originator
                  name).

        7.6.3     Interworking with Integrated UAs

        If the message originates at a UA owned by an ADMD, or is
        delivered to such a UA, the O/R Name follows the same Form 1
        Variant 1 constraints as the base specifications; except that the
        ADMD name is the name of the ADMD that owns the UA and instead of
        supplying a PRMD Name, one (or more) of the following must be
        provided:

             o    OrganizationName,
             o    OrganizationalUnit,
             o    PersonalName.

        and may optionally include a

             o    DomainDefinedAttributeList.

        7.6.4     Differences with Other Profiles

             7.6.4.1   TTC Profile

             There are no outstanding issues regarding interworking
             between TTC-conformant systems and NBS-conformant systems
             with the exception of the number of recipients and the
             supported MPDU sizes.  The ExtensionIdentifier field may
             contain a maximum value of 32K-1; however, according to the
             current TTC profile, if a message with more than 256
             recipients is received, some TTC-conformant domain may
             generate a nondelivery notification.  This also applies to
             the ReportedRecipientInfo in a delivery report.  Further, a
             TTC MTA is required to handle an MPDU size of at least 32KB. 
             The NBS required MPDU size is 2MB as covered in section
             7.5.3.3.  Other differences are shown in Appendix E.  TTC is
             currently based on Version 4 of the Implementor's Guide.

             7.6.4.2   CEPT Profile

             See Appendix 7E.

        7.6.5     Connection of PRMDs to Multiple ADMDs

        Given that Management Domain names (both PRMD and ADMD) shall be
        unique within the U.S., then when an ADMD is presented a message
        for transfer from a PRMD, it will accept O/R Names (both
        originator and recipient) which have an AdministrationDomainName
        field value different than the Administration's name.  "Accept"
        implies the attempt to route/deliver the message shall be made,
        as appropriate, based upon the knowledge that MD names are
        unique.

        Whether this functionality is required by an Administration for
        conformance to this agreement is for further study.

        If a PRMD is connected to two or more ADMDs which are not
        effectively connected (either directly or via a third ADMD), full
        X.400 functionality shall not be available.  Problems occur
        especially in the areas of:

             o    Naming,
             o    Routing,
             o    Replying.

        It should be noted that a single PRMD that is connected to more
        than one ADMD can be represented by more than one combination of
        country-name, ADMD-name, and PRMD name.  For example, it may
        occur that the PRMD-name for a particular PRMD may take different
        values, depending on the ADMD-name.  Implementors should be aware
        of the consequences of these possibilities on routing.


        7.6.6     Connection of an ADMD to a Routing PRMD

        It is possible for a collection of interconnected private domains
        to establish one domain as the "gateway" to an ADMD, and hence to
        the world.

        If an ADMD is connected to such a gateway PRMD, the individual
        private domains shall be registered with the Administration. 
        Administrations need not support such connections.

        Note also that upon receipt by the ADMD of a message originating
        somewhere within the PRMD collection, that the TraceInformation
        may contain more than one element.

        The X.400 Recommendations specify that an ADMD should not attempt
        to relay a message destined for another ADMD through a PRMD, thus
        an ADMD should ensure that messages destined for another ADMD are
        not relayed through a PRMD.  It should be noted, however, that a
        relaying PRMD will relay any such message it receives.

        7.6.7     Management Domain Names

        o    All Management Domain Names (both Private and
             Administration) shall be unique within the U.S.

        o    A central naming authority shall be established to register
             domain names.

        7.6.8     Envelope Validation Errors

        For validation errors, a non-delivery notice shall be generated
        (if possible) with reason code of 'unableToTransfer' and
        diagnostic code of 'invalidParameters' (unless specified
        otherwise).

        ADMDs will validate P1 Envelopes in the following areas:

        a)   The X.409 syntax of all elements should be checked.

        b)   The pragmatic constraint limits (lengths of fields and
             number of occurrences of fields) should be checked.

        c)   Semantic validation of the following elements should be
             done:

             o    originator O/R Name,
             o    recipient O/R Name in the RecipientInfo,
             o    Priority.

        d)   Only recipient Names with the responsibility flag set should
             be validated.  The validation of O/R names is defined in
             7.8.3.3; the validation of priority is defined in 7.8.3.7.1.

             MPDU Identifier Validation

             o    Validation of the GlobalDomainIdentifier component of
                  the MPDU Identifier is performed upon reception of a
                  message (i.e., as a result of a TRANSFER.Indication).

             o    The country name should be known to the validating
                  domain, and depending on the country name, validation
                  of the ADMD name may also be possible.

             o    Additional validation of the GlobalDomainIdentifier is
                  performed against the corresponding first entry in the
                  TraceInformation.  If inconsistencies are found during
                  the comparison, a non-delivery notice with the above
                  defined reason and diagnostic codes is generated.

             o    A request will be generated to the CCITT for a more
                  meaningful diagnostic code (such as
                  'InconsistentMPDUIdentifier').

        7.6.9     Quality of Service

             7.6.9.1   Domain Availability

                  7.6.9.1.1 ADMD Availability

                  The goal is to provide 24 hour per day availability. 
                  Note that there will be periods of time when an ADMD
                  may be unavailable due to maintenance windows in its
                  supporting network or in an MTA within the domain.

                  7.6.9.1.2 PRMD Availability

                  Although the goal of PRMD availability is also 24 hours
                  per day, business reasons are likely to dictate some
                  different level of availability.  ADMDs shall require a
                  profile from the PRMD that indicates its schedule of
                  regular availability to the ADMD.

             7.6.9.2   Delivery Times

             In the absence of standardized quality of service
             parameters, the following are agreed to.  When standardized
             parameters from CCITT Study Group I become available, they
             shall be adopted.

             a)   In table 7.15 the following delivery time targets are
                  established:

                    Table 7.15  Delivery Time Targets            

           ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
           3    Delivery Class                   95% Delivered Before   3
           3                                                            3
           3   Urgent                                3/4 hour           3
           3   Normal                                  4 hours          3
           3   Non-Urgent                             24 hours          3
           @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                                   

             b)   The interval(s) between retries and the number of retry
                  attempts that an ADMD uses in attempting delivery to a
                  PRMD or integrated UA, will be locally determined
                  domain parameters.  However, the total elapsed times
                  after which delivery attempts will be stopped are shown
                  in table 7.16.  This implies that, after these times, a
                  Non-Delivery Notice will be generated.

             An Administration shall continue to attempt delivery until
             the forced nondelivery time, even if the recipient domain
             has scheduled an unavailability window.

                     Table 7.16  Forced Nondelivery Times

          ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
          3    Delivery Class                   NonDelivery Forced After   3
          3                                                                3
          3    Urgent                                 4 hours              3
          3    Normal                                24 hours              3
          3    Non-Urgent                            36 hours              3
          @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                                      

             Note:Both tables apply to the period between acceptance by
             the originating MTA in the originating Administration domain
             to the time of delivery in the destination Administration
             domain.  Transit time within PRMDs is NOT included in the
             above times.

        7.6.10    Billing Information

        a)   All aspects relating to billing, charging, tariffs,
             settlement, and in particular to the use of the
             billingInformation field in the delivery report, is subject
             to bilateral agreement, and shall not be addressed in these
             implementation agreements.

        b)   No ADMD shall require a PRMD to supply or process billing
             information.

        7.6.11    Transparency

        a)   No P1 extensions, other than the MOTIS extensions are to be
             allowed (Reference A/3211).  Should an ADMD receive a
             message containing P1 extensions, it shall generate a
             non-delivery notice (if possible) with reason code of
             unableToTransfer and diagnostic code of invalidParameters.

        If MOTIS elements are present, a relaying MTA can optionally: 

             o    Relay the message.  If the MTA does relay, it must not
                  drop any of the protocol elements.

             o    Non-Deliver the message.

        A receiving MTA can optionally:

             o    Deliver the message

             o    Non-Deliver the message.

        b)   The CCITT has been requested to establish a more meaningful
             diagnostic code (such as protocolError) for this occurrence. 
             Such a code has now been provided in the Implementors Guide.

        c)   P2 extensions shall be relayed transparently by ADMDs.

        7.6.12    RTS Password Management

        RTS password management shall be a local matter.  This includes:

             o    password length
             o    frequency of changes
             o    exchange of passwords with communicating partners
             o    loading passwords ( i.e., the timing of password
                  changes with respect to active associations).

        7.6.13    For Further Study

        Issues requiring further study are:

             o    Intra-Domain Routing
             o    Multi-Vendor Domains

   7.7  INTER and INTRA PRMD CONNECTIONS

        7.7.1     Introduction

        This section is limited in scope to issues arising from the
        indirect connection of a PRMD to another PRMD or to an ADMD, and
        to the interconnection of MTAs to form inter-PRMD connections. 
        Indirect means that the connection is made via a relaying PRMD. 
        The X.400 Recommendations describe the way that a PRMD connects
        to a ADMD and the way that an ADMD connects to another ADMD.  The
        Recommendations do not, however, describe the way that a PRMD
        connects indirectly to an ADMD or another PRMD, nor do they
        describe the way that MTAs are connected within a PRMD.  These
        configurations (shown in Figures 7.6 and 7.7) are useful, for
        example, in connecting equipment from different vendors at a
        single customer site.

        The P1 protocol and its related services for both inter and intra
        PRMD connections are addressed in this section.  In addition, a
        method for routing within a PRMD is given.  It is recognized that
        uniform methods for Administration, maintenance, and quality of
        service should be developed for such configurations, and this
        work is for further study.

        This section describes the minimum that must be provided in order
        to implement a relaying PRMD and a MTA within a PRMD.

        This section is presented in the form of deviations from
        agreements applicable to PRMD to PRMD connection (section 7.5). 
        That is, unless specifically noted in the remainder of this
        section, the agreements in section 7.5 apply to both relaying
        PRMDs and MTAs within a PRMD.

        It should be noted that the comments regarding ORNames in Section
        7.6.5 also apply to this section.

        7.7.2     The Relaying PRMD

        A PRMD that has the capability of relaying messages to another
        PRMD is called a relaying PRMD.  A PRMD implementation need not
        claim to be a relaying PRMD.  A PRMD implementation which does
        claim to be a relaying PRMD must follow the implementation
        agreements in this section.

             7.7.2.1   Relay Responsibilities of a PRMD

             The responsibilities of a relaying PRMD are the same as
             those of an ADMD (as specified in sections 7.6.8 and
             7.6.2.1).  In addition, the PRMD will simply deliver
             messages routed to it from an ADMD, even if this results in
             routing a message from the ADMD to the PRMD to another ADMD.

             7.7.2.2   Interaction with an ADMD

             In order for an ADMD to route a message to ADMD A via ADMD
             B, it must know that A is reachable through B.  Similarly,
             in order for any MD to route a message to PRMD A via a
             relaying PRMD B, it must know that A is reachable through B
             (see Figure 7.8).

                                 ZDDDDDDDD?
                                 3  ADMD  3
                                 @DDDBDDDDY
            ZDDDDDDDD?           ZDDDADDDD?            ZDDDDDDDD?
            3 PRMD A CDDDDDDDDDDD4 PRMD B CDDDDDDDDDDDD4 PRMD C 3
            @DDDDDDDDY           @DDDDDDDDY            @DDDDDDDDY

                                   Relay

                        Figure 7.6  Relaying PRMD

           ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
           3  PRMD                                       3
           3           ZDDDDDD?               ZDDDDDD?   3
           3           3MTA A 3               3 MTA D3   3
           3           @DDBDDDY               @DDBDDDY   3
           3              3                      3       3   ZDDDDDDD?
           3              3                      3       3   3  ADMD 3
           3           ZDDADDD?               ZDDADDD?   3   3       3
           3           3MTA B CDDDDDDDDDDDDDDD4 MTA CCDDDEDDD4   or  3
           3           @DDDDDDY               @DDDDDDY   3   3       3
           3                                             3   3  PRMD 3
           @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY   @DDDDDDDY

                   Figure 7.7  Intra PRMD connections


        Note 1: Section 7.6.6 specifies that ADMDs are not required to
        connect to a relaying PRMD, but they are not precluded from doing
        so.

        Note 2: TraceInformation may have more than one sequence on 
        submission of a message by a relaying PRMD to an ADMD.


         ZDDDDDDD?
         3  MD D 3
         @DDDBDDDY
       ZDDDDDADDDDDDDDD?
       3    relay      3       ZDDDDDDDDDD?        ZDDDDDDDD?
       3    MD  C with 3DDDDDDD4   relay  CDDDDDDDD4   MD A 3
       3    a message  3       3   MD B   3        @DDDDDDDDY
       3    for A      3       @DDDDDDDDDDY
       @DDDDDDDDDDDDDDDY

       Figure 7.8 MD C must know of A to route the message

        7.7.3     Intra PRMD Connections

        A PRMD is composed of MTAs which cooperate to perform the
        functions expected of a domain.  An MTA implementation need not
        claim to follow the implementation agreements of this section.

             7.7.3.1   Relay Responsibilities of an MTA

             The relaying responsibilities of an MTA are the same as
             those of an ADMD (as specified in sections 7.6.8 and
             7.6.2.1) with one exception: loop suppression within the
             domain is done using the MOTIS InternalTraceInfo protocol
             element.  The MTA must validate the InternalTraceInfo (see
             section 7.8.3.5 for details on validation).  In addition,
             the PRMD will simply deliver messages routed to it from an
             ADMD, even if this results in routing a message from the
             ADMD to the PRMD to another ADMD (please see section 7.6.6).

             7.7.3.2   Loop Suppression within a PRMD

             a)   The only mechanism defined in the X.400 Recommendations
                  for suppressing loops is TraceInformation, which is
                  added on a per domain basis to detect and suppress
                  loops among domains.  Loops among MTAs within a domain
                  need to be detected and suppressed.  This implies that
                  each MTA must add trace information that is meaningful
                  within the domain.  The MOTIS solution of adding
                  InternalTraceInfo to the P1 Envelope of a message was
                  adopted.  The definition of InternalTraceInfo is given
                  in figure 7.9.  The InternalTraceInfo is added by each
                  MTA within a PRMD to handle a message, and it is
                  examined in the same way as TraceInformation to detect
                  and suppress loops.

              ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
              3       InternalTraceInfo ::= [APPLICATION 30]              3    
              3          IMPLICIT SEQUENCE OF                             3 
              3          SEQUENCE {                                       3 
              3             MTAName,                                      3    
              3             MTASuppliedInfo }                             3 
              3                                                           3    
              3       MTAName ::= PrintableString                         3    
              3                                                           3
              @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                  Figure 7.9  Definition of InternalTraceInfo

                  If the MTAName and password of X.411 are used for
                  validation,  then it is recommended that the MTAName
                  used for validation also  be used in the
                  InternalTraceInfo.  However, there is a complication:
                  in X.411, MTAName is an IA5String, and the MTAname
                  defined by MOTIS is a PrintableString.  Efforts will be
                  made to change the MOTIS definition from
                  PrintableString to IA5String.

             b)   Three actions are defined in MTASuppliedInfo: relayed,
                  rerouted, and recipientReassignment as shown in figure
                  7.10.  The recipientReassignment action is not
                  supported in these agreements.  The ability to generate
                  it is not required, and if it is present on an incoming
                  message, the action field will be ignored.

              ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
              3 MTASuppliedInfo ::= SET {                                  3   
              3   arrival [0] IMPLICIT Time,                               3
              3   deferred [1] IMPLICIT Time OPTIONAL,                     3
              3   action [2] IMPLICIT INTEGER                              3
              3      { relayed(0), rerouted(1), recipientReassignment(2) } 3
              3   previous MTAName OPTIONAL }                              3
              @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                Figure 7.10  Defined Actions in MTASuppliedInfo

             7.7.3.3   Routing Within a PRMD

             a)   Routing within a PRMD is complicated by the lack of a
                  directory standard.  In particular, it constrains
                  intra-domain routing decisions to be based on some
                  combination of the intra-domain attributes of the O/R
                  Name, Organization Name Organizational Units, and
                  Personal Name.  In order to enhance interworking and to
                  reduce the difficulty of configuring intra-domain
                  connections, it is useful to restrict the ways in which
                  these may be used in making routing decisions.

             b)   However, it is recognized that vendors may wish to
                  provide MTAs with varying degrees of routing capability
                  within a PRMD as a temporary expedient until
                  appropriate standards for automated construction of
                  directories and routing tables are available.  This
                  section assigns class numbers to certain levels of
                  routing capability and discusses the consequences of
                  using MTAs which fall into each class.  The
                  classification scheme will allow some diversity in
                  allocating O/R Name space and in configuring
                  intra-domain routes.

             c)   When other methods are recommended by standards bodies,
                  the classification scheme described here will become
                  obsolete.  Large-scale, multi-vendor PRMDs may not be
                  practical in the absence of standardized methods.

                  7.7.3.3.1 Class Designations

                  When it is clear that a message is to be delivered
                  within a domain, the Country Name, ADMD Name, and PRMD
                  Name have already served their purpose in determining
                  the next MTA in the route to the recipient.  The
                  remaining fields that might be used on making routing
                  decisions within the PRMD are the Organization Name,
                  Organizational Units, and Personal Name.

                  MTAs are classified by their ability to discriminate
                  between O/R names when making routing decisions within
                  a PRMD.  Conformant MTAs will be classified as shown in
                  table 7.17.

                  Table 7.17  Conformant MTA Classifications

            ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
            3                                      Class 1  Class 2  Class 3 3
            3                                                                3
            3  Organization Name                      H        H        H    3
            3  SEQUENCE OF Organizational Unit        X        H        H    3
            3  Personal Name                          X        X        H    3
            @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY


                  a)   An 'H' means that the MTA must be able to base its
                       intra-domain routing decisions on the given
                       component of the O/R Name.  In particular, both
                       Class 2 and Class 3 MTAs must be able to
                       discriminate on all the members in a supplied
                       sequence of OrganizationalUnits.  A Class 3 MTA
                       must be able to discriminate on all of the
                       elements in a PersonalName.

                       An 'X' means that the MTA need not have the
                       ability to discriminate on the given component.

                  b)   There is a hierarchy in support of components. 
                       The ability to discriminate on a given component
                       does not imply the requirement to do so: e.g., a
                       Class 3 MTA is not required to have tables for
                       every PersonalName in the domain.  Equally, an MTA
                       which can discriminate on OrganizationalUnits to
                       make routing decisions need not always use the
                       full sequence in an O/R Name if a partial sequence
                       provides enough information.

                  c)   The above classifications only apply to routing
                       decisions in selecting a next hop within a domain. 
                       All MTAs are entitled to examine the full O/R Name
                       when identifying their own directly served UAs.

                  d)   The routing table of a Class 1 MTA will be
                       relatively small, because intra-domain routing
                       decisions are based solely on OrganizationName. 
                       The routing table of a Class 2 MTA may be
                       substantially larger and more complex because of
                       its ability to discriminate on OrganizationalUnits
                       as well as OrganizationName to make routing
                       decisions.  The routing table of a Class 3 MTA may
                       be larger still, because its use of the components
                       of PersonalName in addition to the other
                       information.

                  7.7.3.3.2 Specification of MTA Classes

                  If an MTA implementation claims to follow the
                  implementation agreements, it must be either a Class 1,
                  Class 2, or a Class 3 MTA.  The class of an MTA
                  implementation should be specified so that PRMD
                  administrators can choose equipment properly.

                  7.7.3.3.3 Consequences of Using Certain Classes of MTAs

                  Definition:    An MTA which accepts submission requests
                                 and furnishes delivery indications to a
                                 UA is said to "directly serve" the UA.

                  a)   The presence in a domain of an MTA acting as a
                       Class 1 or Class 2 MTA imposes administrative
                       restrictions on the assignment of O/R Names to UAs
                       and in the configuration of routes within that
                       domain.

                       o    A Class 1 MTA may directly serve UAs from
                            several OrganizationNames. However, if a
                            Class 1 MTA directly serves a UA with a given
                            OrganizationName, no other MTA in the domain
                            may directly serve a user with the same
                            OrganizationName.  This means that if all
                            MTAs in a domain are Class 1, then all UAs
                            with a given OrganizationName must be
                            assigned to the same MTA.

                       o    A Class 2 MTA may directly serve UAs from any
                            combination of OrganizationName and sequence
                            of OrganizationalUnits.  However, if a Class
                            2 MTA directly serves a UA with a given
                            combination, no other MTA in the domain may
                            directly serve a user with the same
                            combination.  This means that if all MTAs in
                            a domain are Class 2, then all UAs with a
                            given OrganizationName and sequence of
                            OrganizationalUnits must be assigned to the
                            same MTA.

                       o    A domain consisting entirely of Class 3 MTAs
                            is free of all the above restrictions.

                  b)   If Class 1 or Class 2 MTAs are used to perform
                       relaying within a PRMD containing MTAs of other
                       classes, care must be exercised in determining the
                       topology of the domain to avoid leaving certain
                       UAs inacessible from certain MTAs within the
                       domain.  The example below shows one of the
                       configurations that should be avoided.  The
                       example is intended to stimulate careful
                       examination of the relationship between network
                       and organizational topologies.

                                                                   
         ZDDDDDDDDDDDDDDD?         ZDDDDDDDDDD?         ZDDDDDDDDDDDDDDD?
         3     MTA A     3         3   MTA B  3         3     MTA C     3      
         3    serving    CDD ... DD4          CDD ... DD4    serving    3
         3Organization X 3         3 (Class 1)3         3Organization X 3
         @DDDDDDDDDDDDDDDY         @DDDDDDDDDDY         @DDDDDDDDDDDDDDDY

            Figure 7.11  Example of a confirguration to be avoided


                  In Figure 7.11, B will route all messages for
                  Organization X to either A or C because B is a Class 1
                  MTA.  The administrator who created this configuration
                  probably wanted B to route some messages for
                  Organization X to A, and some to C.  However, B does
                  not have the capability for this because it is only a
                  Class 1 MTA.  The configuration in Figure 7.11 can be
                  corrected by replacing B with a Class 2 or Class 3 MTA.

             7.7.3.4   Uniqueness of MPDUidentifiers Within a PRMD

             When generating an IA5String in an MPDUIdentifier, each MTA
             in a domain must ensure that the string is unique within the
             domain.  This shall be done by providing an MTA designator
             with a length of 12 octets which is unique within the
             domain, to be concatenated to a per message string with
             maximum length of 20 octets.

             Two pieces of information, the MTA name and MTA designator,
             need to be registered within a PRMD to guarantee uniqueness. 
             This registration facility need not be automated.  If the
             MTA name is less than or equal to 12 characters, it is
             recommended that it also be used as the MTA designator.

        7.7.4     Service Elements and Optional User Facilities

        A PRMD made up of MTAs which support varying sets of service
        elements in addition to those required in these agreements may
        appear to provide inconsistent service for these elements.  For
        example, if one MTA supports deferred delivery and another MTA
        does not, then deferred delivery can be used by some, but not
        all, users in the PRMD.  Similarly, if one MTA supports return of
        contents and another does not, then a user outside of the PRMD 
        will receive returned contents for messages sent to one user, but
        not for messages sent to another user.  Note that this same
        inconsistency occurs when sending to two PRMDs which support
        different additional optional elements.

        7.7.5     X.400 Protocol Definitions

        This section describes additions and modifications to section
        7.5.3 which are required for implementation of a relaying PRMD or
        an MTA within a PRMD.

             7.7.5.1   Protocol Classification

             a)   The classification scheme given in section 7.5.3.1
                  applies to elements passing from one PRMD to another. 
                  For both relaying PRMDs, and MTAs in a PRMD, the same
                  classification scheme will be used, but within a PRMD
                  the classification applies to elements passing from one
                  MTA to another.

             b)   In addition to the classifications given in section
                  7.5.3.1, a classification of Prohibited has been used.

                                      PROHIBITED = P

                  This element shall not be used.  Presence of this
                  element is a protocol violation.

             7.7.5.2   P1 Protocol Elements

             Table 7.18 contains protocol elements and their classes.  An
             * signifies that the classification of the protocol element
             has not changed from Table 7.8.

                        Table 7.18 P1 Protocol Elements                 
                                                                       
ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Element                         Class     Restrictions and Comments         3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                            3
3UMPDUEnvelope                                                               3
3  MPDUIdentifier                  M*      This field needs to be unique     3
3                                          within a PRMD.  See sections      3
3                                          7.7.3.4 for the method of         3
3                                          ensuring uniqueness.              3
3                                                                            3
3  originator                      M*      It is recommended that all        3
3                                          components of the originator's    3
3                                          ORName be included to help ensure 3
3                                          that reports can be returned.     3
3                                                                            3
3  TraceInformation                M*      The first MTA in the domain to    3
3                                          receive the message adds the      3
3                                          TraceInformation.  Subsequent     3
3                                          MTAs can update the               3
3                                          TraceInformation in the event of  3
3                                          conversion or deferred delivery.  3
3                                          When a message is generated, the  3
3                                          originating MTA adds the          3
3                                          TraceInformation.                 3
3                                                                            3
3  InternalTraceInfo               M/P     This element is mandatory for     3
3                                          envelopes transferred between     3
3                                          MTAs within a PRMD, and           3
3                                          prohibited in messages            3
3                                          transferred outside the domain.   3
3                                          Elements are always added to the  3
3                                          end of the sequence.  (See Note 1)3
3                                                                            3
3InternalTraceInfo                 M       MTANames within a PRMD must be    3
3  MTAName                                 unique.  See section 7.7.3.4 for  3
3                                          the method of assuring uniqueness 3
3                                          Maximum length = 32 characters.   3
3                                                                            3
3  MTASuppliedInfo                 M                                         3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                      (Continued on next page.)


                  Table 7.18  P1 Protocol Elements, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Element                         Class     Restrictions and Comments         3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                            3
3                                                                            3
3MTASuppliedInfo                                                             3
3  arrival                         M                                         3
3  deferred                        X       This field must be generated by   3
3                                          MTAs which perform deferred       3
3                                          delivery.                         3
3                                                                            3
3  action                          M       See section 7.7.3.2 for           3
3                                          restrictions on values of this    3
3                                          field.                            3
3                                                                            3
3  previous                        X       This field must be generated by   3
3                                          MTAs which perform rerouting.     3
3                                                                            3
3DeliveryReportEnvelope                                                      3
3  TraceInformation                M*      The first MTA in the domain to    3
3                                          receive the report adds the       3
3                                          TraceInformation.  When a report  3
3                                          is generated, the originating MTA 3
3                                          adds the TraceInformation.        3
3                                                                            3
3  InternalTraceInfo               M/P     This field is mandatory for       3
3                                          envelopes transferred between     3
3                                          MTAs within a PRMD, and           3
3                                          prohibited in messages            3
3                                          transferred outside the domain.   3
3                                          (See Note 1)                      3
3DeliveryReportContent                                                       3
3  intermediate InternalTraceInfo  P       If it were possible to include    3
3                                          this field in the delivery report 3
3                                          content, an audit and confirmed   3
3                                          report could be provided to       3
3                                          detect problems within a PRMD.    3
3                                          Efforts are being made to add     3
3                                          this field to the MOTIS           3
3                                          definition.                       3
3                                                                            3
3DeliveredInfo                                                               3
3  typeOFUA                        R*      It is the responsibility of the   3
3                                          MTA generating the report to      3
3                                          generate this element.            3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY
                                                      (Continued on next page.)


                  Table 7.18  P1 Protocol Elements, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3Element                         Class     Restrictions and Comments         3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3                                                                            3
3ProbeEnvelope                                                               3
3  TraceInformation                M*      The first MTA in the domain to    3
3                                          receive the probe adds the        3
3                                          TraceInformation.  When a probe   3
3                                          is generated, the originating MTA 3
3                                          adds the TraceInformation.        3
3                                                                            3
3  InternalTraceInfo               M/P     This field is mandatory for       3
3                                          envelopes transferred between     3
3                                          MTAs within a PRMD, and           3
3                                          prohibited in messages            3
3                                          transferred outside the domain.   3
3                                          (See Note 1)                      3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

        Note 1: The M classification is only applicable if an
        implementation is claiming conformance according to section
        7.10.2, point (g) 4th bullet.

             7.7.5.3   Reliable Transfer Server (RTS)

             In the pUserData of PConnect, the value of
             applicationProtocol should be 1.  This value was chosen
             because the agreements on intra-domain connections are not
             strictly P1, nor are they MOTIS.  Philosophically, it would
             be good to choose a new application protocol identifier for
             these agreements, but this introduces too many practical
             problems.  Since these agreements are closer to P1 than to
             MOTIS, the value of 1 will be used.  This will not cause
             interworking problems between domains, because the only
             deviation from P1 is the InternalTraceInfo, which will not
             be present in messages transferred outside of a domain.

   7.8  ERROR HANDLING

   This section describes appropriate actions to be taken upon receipt of
   protocol elements which are not supported in this profile, malformed
   MPDUs, unrecognized O/R Name  forms, content errors, errors in
   reports, and unexpected values for protocol elements.

        7.8.1     MPDU Encoding

        The MPDU should have a context-specific tag of 0, 1, or 2.  If it
        does not have one of these tags, it is not possible to figure out
        who originated the message.  Therefore, the way this error is
        reported is a local matter.


        7.8.2     Contents

        Once delivery to the UA has occurred, it is not possible to
        report errors in P2 information to the originator.  In addition,
        it seems unreasonable to insist that the MTA that delivers a
        message ensure that the P2 content of the message is acceptable. 
        As a result, the handling of content errors is a local matter.

        7.8.3     Envelope

        This section describes the handling of errors in message
        envelopes.  Some of the error conditions described below may be
        detected in a recipient's O/R Name.  This may limit the reporting
        MTA's ability to generate a nondelivery notification that
        accurately reflects the erroneous O/R Name in the
        ReportedRecipientInfo.  This handling of this situation is a
        local matter.

             7.8.3.1   Pragmatic Constraint Violations

             In all cases of pragmatic constraint violation, a
             nondelivery report should be generated with a ReasonCode of
             unableToTransfer, and a DiagnosticCode of
             pragmaticConstraintViolation.

             7.8.3.2   Protocol Violations

             a)   If all required protocol elements are not present, a
                  nondelivery report with a ReasonCode of
                  unableToTransfer and a DiagnosticCode of
                  protocolViolation should be generated.

             b)   If a protocol element is expected to be of one type,
                  but is encoded as another, then a nondelivery report
                  with a ReasonCode of unableToTransfer and a
                  DiagnosticCode of invalidParameters should be
                  generated.

             7.8.3.3   O/R Names

             a)   The domain that has responsibility for delivering a
                  message should also have the responsibility to send the
                  nondelivery notification if the message cannot be
                  delivered.  Therefore, each MTA should only validate
                  the O/R Names of recipients with responsibility flags
                  set to TRUE.  In addition, a nondelivery notification
                  can only be sent if the originator's O/R Name is valid.

             b)   If any element in the O/R Name is unrecognized or if
                  the CountryName, AdministrationDomainName, and one of
                  PrivateDomainName and OrganizationName (and, for ADMDs,
                  PersonalName and OrganizationalUnit) are not all
                  present, then a nondelivery report should be generated
                  with a ReasonCode of unableToTransfer, and a
                  DiagnosticCode of unrecognizedORName.  If the message
                  can be delivered even though the ORName is invalid,
                  delivery is a local matter.  Note, however, that if the
                  message is delivered, the invalid ORName might be
                  propagated through the X.400 system (e.g., by
                  forwarding).

             c)   If the O/R Name has all of the appropriate protocol
                  elements and the message still cannot be delivered to
                  the recipient, the following DiagnosticCodes may appear
                  in the nondelivery report: unrecognizedORName,
                  ambiguousORName, and uaUnavailable.

             7.8.3.4   TraceInformation

             a)   Since non-relaying domains need not do loop
                  suppression, domains with responsibility for delivering
                  the message need not be concerned about the semantics
                  of the TraceInformation, that is, arrival time and
                  converted EncodedInformationTypes can be provided to
                  the UA without inspection by the MTAs of the domain as
                  long as the TraceInformation is properly encoded
                  according to X.409.

             b)   When a message is accepted for relay, the relaying
                  domain must check that a TraceInformation SEQUENCE has
                  been added by the domain that last handled the message. 
                  If the appropriate TraceInformation was not added, this
                  should be treated as a protocolViolation (section
                  7.8.3.2).

             c)   In addition, the relaying domain must check that the
                  information was added in the sequence defined by the
                  rules for adding TraceInformation in the CCITT X.400
                  Implementor's Guide.  If the sequence is invalid,then a
                  nondelivery report should be generated with a
                  ReasonCode of unableToTransfer and a diagnosticCode of
                  invalidParameters.

             Note: It would be desirable for the CCITT to add a
             diagnostic code of invalidTraceInformation to allow a more
             meaningful description of this problem.  A request for this
             new diagnostic code will be submitted.

             7.8.3.5   InternalTraceInfo

             This section applies only to MTAs which follow the
             agreements of section 7.7.

             a)   When a message is accepted for relay from another MTA
                  in the domain, the relaying MTA must check that an
                  InternalTraceInfo SEQUENCE has been added by the MTA
                  that last handled the message.  If the appropriate
                  InternalTraceInfo was not added, this should be treated
                  as a protocolViolation (section 7.8.3.2).

             b)   In addition, the relaying MTA must check that the
                  information was added in the sequence defined by the
                  rules for adding TraceInformation in the CCITT X.400
                  Implementor's Guide.  If the sequence is invalid, then
                  a nondelivery report should be generated with a
                  ReasonCode of unableToTransfer and a diagnosticCode of
                  invalidParameters.

             Note:It would be desirable for the CCITT to add a diagnostic
             code of invalidTraceInformation to allow for a more
             meaningful description of this problem.  A request for this
             new diagnostic code will be submitted.

             7.8.3.6   Unsupported X.400 Protocol Elements

             The protocol elements defined in X.400 but unsupported by
             this profile are:  the deferredDelivery and
             PerDomainBilateralInfo parameters of the UMPDUEnvelope, the
             ExplicitConversion parameter of RecipientInfo, and the
             alternateRecipientAllowed and contentReturnRequest bits of
             the PerMessageFlag.  Appropriate actions are described below
             for domains that do not support the protocol elements.

                  7.8.3.6.1 deferredDelivery

                  The delivering domain shall do one of the following:

                  o    deliver at once,
                  o    hold for deferred delivery,
                  o    return a nondelivery notification with a
                       ReasonCode of unableToTransfer and a
                       DiagnosticCode of noBilateralAgreement.

                  7.8.3.6.2 PerDomainBilateralInfo

                  If a delivering domain receives this element, the
                  element can be ignored.

                  7.8.3.6.3 ExplicitConversion

                  If ExplicitConversion is requested the message should
                  be delivered if possible.  That is, if the UA is
                  registered to accept the EncodedInformationTypes of the
                  message, then the message should be delivered even
                  though the requested conversion could not be performed
                  along the route.  If delivery is not possible, then a
                  nondelivery report should be generated with a
                  ReasonCode of conversionNotPerformed with no
                  DiagnosticCode.

                  7.8.3.6.4 alternateRecipientAllowed

                  If a delivering domain receives this element the
                  element can be ignored.

                  7.8.3.6.5 contentReturnRequest

                  If a delivering domain receives this element, the
                  element can be ignored.

             7.8.3.7   Unexpected Values for INTEGER Protocol Elements

             There are three INTEGERs in the P1 Envelope.  Appropriate
             actions are described below for domains receiving unexpected
             values for Priority, ExplicitConversion, and ContentType.

                  7.8.3.7.1 Priority

                  Additional values for Priority have been suggested by
                  at least one group of implementors as upward compatible
                  changes to the X.400 Recommendations.  Therefore, if a
                  PRMD receives an unexpected value for Priority, and
                  this value is greater than one byte in length, a
                  nondelivery report should be generated with a
                  ReasonCode of unableToTransfer and DiagnosticCode of
                  invalidParameters.  If the value is less than or equal
                  to one byte, the PRMD can either generate a nondelivery
                  report as previously specified or interpret the
                  Priority as normal and deliver or relay the message.

                  7.8.3.7.2 ExplicitConversion

                  When an unexpected value is received for
                  ExplicitConversion, it should be handled as in section
                  7.8.3.6.3.

                  7.8.3.7.3 ContentType

                  If the ContentType is not supported by the delivering
                  MTA, then a nondelivery report should be generated with
                  a ReasonCode of unableToTransfer, and a DiagnosticCode
                  of contentTypeNotSupported.

             7.8.3.8   Additional Elements

             In the absence of multilateral agreements to the contrary,
             receipt of privately tagged elements and protocol elements
             in addition to those defined in X.400 will result in a
             nondelivery report with a ReasonCode of unableToTransfer and
             a DiagnosticCode of invalidParameters.

             The exceptions to this are the MOTIS elements.  The
             treatment of MPDU's containing these MOTIS extensions is
             described in Section 7.6.11.

        7.8.4     Reports

        There is no mechanism for returning a delivery or status report
        due to errors in the report itself.  Therefore the handling of
        errors in reports is a local matter.

   7.9  MHS USE OF DIRECTORY SERVICES

        7.9.1     Directory Service Elements

        a)   Recommendation X.400 recognizes the need of MHS users for a
             number of directory service elements.  Directory service
             elements are intended to assist users and their UAs in
             obtaining information to be used in submitting messages for
             delivery by the MTS.  The MTS may also use directory service
             elements to obtain information to be used in routing
             messages.  Some functional requirements of directories have
             been identified and are listed below.

             o    Verify the existence of an O/R name.

             o    Return the O/R address that corresponds to the O/R name
                  presented.

             o    Determine whether the O/R name presented denotes a user
                  or a distribution list.

             o    Return a list of the members of a distribution list.

             o    When given a partial name, return a list of O/R name
                  possibilities.

             o    Allow users to scan directory entries.

             o    Allow users to scan directory entries selectively.

             o    Return the capabilities of the entity referred to by
                  the O/R name.

             o    Provide maintenance functions to keep the directory
                  up-to-date.

        b)   In addition to functionality, a number of operational
             aspects must be considered.  These include
             user-friendliness, flexibility, availability, expandability,
             and reliability.

        c)   Currently, these aspects of directory service elements and
             procedures are under study by both the CCITT and the ISO. 
             Both organizations are committed to the development of a
             single Directory Service specification for use by MHS and
             all other OSI based applications.

             Given the incomplete nature of the ongoing activities within
             the CCITT and the ISO, no implementation details will be
             provided now for MHS use of Directory Services. 
             Implementation agreements for MHS Use of Directory Services
             will be issued when current activities within the CCITT and
             the ISO are stable.

        7.9.2     Use of Names and Addresses

        a)   It is recognized that these agreements enable a wide variety
             of naming and addressing attributes (see section 7.5.3.5
             ORName Protocol Elements) wherein each PRMD may adopt
             particular routing schemes within its domain.

        b)   With the exception of the intra-domain connection
             agreements:

             These agreements make no attempt to recommend a standard
             practice for electronic mail addressing.

        c)   Inter-PRMD addressing may be secured according to practices
             outside the scope of these agreements, such as:

                  o  manual directories
                  o  on-line directories
                  o  ORName address specifications
                  o  ORName address translation.

        d)   Further, each PRMD may adopt naming and addressing schemes
             wherein the user view may take a form entirely different
             from the attributes reflected in table 7.9.  And, each PRMD
             may have one user view for the originator form and another
             for the recipient form, and perhaps other forms of user
             addressing.  In some cases (e.g., receipt notification)
             these user forms must be preserved within the constraints of
             these implementation agreements.  However, mapping between
             one PRMD user form to another PRMD user form, via the X.400
             ORName attributes of these agreements, is outside the scope
             of these agreements.

   7.10 CONFORMANCE

        7.10.1    Introduction

        In order to ensure that products conform to these implementation
        agreements, it is necessary to define the types and degrees of
        conformance testing that products must pass before they may be
        classified as conformant.  This section defines the conformance
        requirements and provides guidelines for the interpretation of
        the results from this type of testing.

        This section is incomplete and will be enhanced in future
        versions of this Agreement.  Later versions will reflect the
        problems of conformance testing and will outline specific
        practices and recommendations to aid the development of
        conformance tests and procedures.

        7.10.2    Definition of Conformance

        For this section, the term conformance is defined by the
        following:

        a)   The tests indicated for this section are intended to
             establish a high degree of confidence in a statement that
             the implementation under test (IUT) conforms (or does not
             conform) to the agreements of this section.

        b)   Conformance to a service element means that the information
             associated with the service element is made accessible to
             the user (person or process) whenever this agreement says
             that this information should be available.

             Accessible means that information must be provided
             describing how a user (person or process):

             o    causes appropriate information to be displayed, or
             o    causes appropriate information to be obtained.

        c)   Conformance to P1, P2, and RTS as part of an X.400 OSI
             application requires that only the external behavior of that
             OSI system adheres to the relevant protocol standards.

             In order to achieve conformance to this section, it is not
             required  that the inter-layer interfaces be available for
             testing purposes.

        d)   Conformance to the protocols requires:

             o    that MPDUs correspond to instances of syntactically
                  correct data units,

             o    MPDUs in which the data present in the fields and the
                  presence (or absence) of those fields is valid in type
                  and semantics as defined in X.400, as qualified by this
                  profile,

             o    correct sequences of protocol data units in responses
                  (resulting from protocol procedures).

        e)   Statements regarding the conformance of any one
             implementation to this profile are not complete unless a
             Protocol Implementation Conformance Statement (PICS) is
             supplied.

        f)   The term "Implementation Under Test" (IUT) is
             interchangeable with the term "system" in the definition of
             conformance, and may refer to:

             o    a domain, which may be one or more MTA's with
                  co-located or remote UA's,

             o    a single instance of an MTA and co-located UA with
                  X.400 (P1, P2, RTS and session) software,

             o    a relaying product with P1, RTS and session software,

             o    a gateway product.

        g)   Claiming Implementation Conformance

             o    An implementation which claims to be conformant as an
                  ADMD must adhere to the agreements in sections 7.5 and
                  7.6.

             o    An implementation which claims to be conformant as a
                  PRMD must adhere to the agreements in section 7.5.

             o    An implementation which claims to be conformant as a
                  relaying PRMD must adhere to the agreements in section
                  7.5 and the appropriate sections of 7.7.

             o    An implementation which claims to be conformant to the
                  intra-domain connection agreements must adhere to the
                  agreements in section 7.5 and the appropriate sections
                  of 7.7.

        7.10.3    Conformance Requirements

             7.10.3.1  Introduction

             Conformance to this specification requires that all the
             services listed as supported in sections 7.5, 7.6, and if
             appropriate, 7.7 of these agreements are supported in the
             manner defined, in either the CCITT X.400 Recommendations or
             these agreements.  It is not necessary to implement the
             recommended practices of section 7.12, Appendix B, in order
             to conform to these agreements.

             It is the intention to adopt, where and when appropriate the
             testing methodology and/or the abstract test scenarios
             currently being defined by the CCITT X.400 Conformance
             Group.  However, it is recognized that formal CCITT
             Recommendations relating to X.400 Conformance Testing will
             not be available until 1988.  It is also recognized that
             aspects of these agreements are outside the scope of the
             CCITT, and that other organizations will have to provide
             conformance tests in these cases.

             7.10.3.2  Initial Conformance

             This section is intended to provide guidelines to vendors
             who envisage having X.400 products available prior to any
             formal mechanism, or "Conformance Test Center" being made
             accessible that would allow for conformance to this product
             specification to be tested.

             It is feasible that vendors and carriers will want to enter
             bilateral test agreements that will allow for initial trials
             to be carried out for the purposes of testing initial
             interworking capabilities.  It is equally feasible that for
             the purposes of testing interoperability, only a subset of
             this specification will initially be tested.

             Note: By claiming conformance to this subset of information
             the vendor or carrier CANNOT claim conformance to this
             entire specification.

             There are two aspects to the requirements, interworking and
             service, as described in the following sections.

                  7.10.3.2.1     Interworking

                  The interworking requirements for conformance implies
                  that tests be done to check for the syntax and
                  semantics of protocol data elements for a system as
                  defined by the classification scheme of sections
                  7.5.2.1.1 and 7.7.5.2.  For a relay system, the correct
                  protocol elements should be relayed as appropriate. 
                  For a recipient system, a message with correct protocol
                  elements must not be rejected where appropriate.

                  7.10.3.2.2     Service

                  For information available to the recipients via the
                  IPMessage Heading and Body, the following should be
                  made accessible:

                  o    IPMessage ID - only the PrintableString portion of
                       the IPMessageId needs to be accessible.
                  o    subject,
                  o    primaryRecipients,
                  o    copyRecipients,
                  o    blindcopyRecipients,
                  o    authorizingUsers,
                  o    originator,
                  o    inReplyTo,
                  o    replyToUsers,
                  o    importance,
                  o    sensitivity,
                  o    IA5Text Bodypart.

7.11    APPENDIX A:    INTERPRETATION OF X.400 SERVICE ELEMENTS

The work on service element definitions is limited to those that are
defined as 'supported' in section 7.5 of this specification.  Furthermore
it is not the intent of this section to define how information should be
made available or presented to a MHS user, nor is it intended to define
how individual vendors should design their products.  In addition,
statements on conformance to a specific service element and the
allocation of error codes that are generated as a result of violations of
the service should be defined in the sections on conformance and errors
as part of the main product specification.  The main objective is to
provide clarification, where required, on the functions of a service
element, and in particular what the original intent of the
Recommendations were.

SERVICE ELEMENTS

The following Service Elements defined in X.400 have been examined and
require further text to be added to their definitions to represent the
proposed implementation of these service elements by the X.400 SIG.

The service element clarifications are to be taken in the context of this
profile.

Service elements not referenced in this section are as defined in X.400.

PROBE

A PRMD need not generate probes.

If a probe is addressed to and received by a PRMD, the PRMD must respond
with a Delivery Report as appropriate at the time the probe was
processed.

DEFERRED DELIVERY

In the absence of bilateral agreements to the contrary, Deferred Delivery
and Deferred Delivery Cancellation are local matters (i.e., confined to
the originating domain) and need not be provided.

The extension of Deferred Delivery beyond the boundaries of the
initiating domain is via bilateral agreement as specified in Section
3.4.2.1 of X.411.

Content Type Indication

It is required that both an originating and recipient domain be able to
support P2 content type.  The ability for domains to be able to exchange
content types other than P2 will depend on the existence of bilateral or
multi-lateral agreements.


Original Encoded Information Types Indication

It is required that both an originating and recipient domain be able to
support IA5 text.  Support for other encoded information types, for the
purposes of message transfer between domains, will depend on the
existence of bilateral or multi-lateral agreements.

The use of the 'unspecified' form of encoded information type should only
be used when the UMPDU content represents an SR-UAPDU or contains an
auto-forwarded IM-UAPDU.

The original encoded information type of a message is not meaningful
unless a message is converted en route to the recipient.  These
agreements support only IA5 text, which should not undergo conversion. 
The original encoded information types should be made accessible to the
recipient for upward compatibility with the use of non-IA5 text message
body parts.

Registered Encoded Information Types

A UMPDU with an 'unspecified' value for Original Encoded Information Type
shall be delivered to the UA.

Delivery Notification

The UAContentID may be used by the recipient of the delivery notification
for correlation purposes.

Disclosure of Other Recipients

This service is not made available by originating MTAE's to UAE's, but
must be supported by relaying and recipient MTAE's.

By supporting the disclosure of other recipients the message recipient
can be informed of the O/R names of the other recipient(s) of the
message, as defined in the P1 envelope, in addition to the O/R
Descriptors within the P2 header.

These agreements do not support initiation of disclosure of other
recipients, but the information associated with it should be made
accessible to the recipient for upward compatibility with support for the
initiation of this service element.

Typed Body

As defined in X.400 with the addition of the Private Body Types that are
to be supported.  At present there is no mechanism provided within X.420
that would allow you to respond to reception of an unsupported body type.

Action taken in this situation is a local matter.


Blind Copy Recipient Indication

It should be considered that the recipient's UA acts on behalf of the
recipient, and therefore may choose to disclose all BCC recipients to
each other.  Therefore it is the responsibility of the originating domain
to submit two or more messages, depending on whether or not each BCC
should be disclosed to each other BCC.

Auto Forwarded Indication

A UA may choose not to forward a message that was previously
auto-forwarded. In addition there is no requirement for an IPM UA that
does not support non-receipt or receipt notification to respond with a
non-receipt notification when a message is auto-forwarded.
 
Primary and Copy Recipients Indication

It is required that at least one primary recipient be specified; however,
for a forwarded message this need not be present.  The recipient UA
should be prepared to accept no primary and copy recipients to enable
future interworking with Teletex, Fax, etc.
 
Sensitivity Indication

A message originator should make no assumptions as to the semantic
interpretation by the recipients UA regarding classifications of
sensitivity. For example, a personal message may be printed on a shared
printer.

Reply Request Indication

In requesting this service an originator may additionally supply a date
by which the reply should be sent and a list of the intended recipients
of the reply. If no such list is provided then the initiator of the reply
sends the reply to the originator of the message and any recipients the
reply initiator wishes to include. The replytoUsers and the replyBy date
may be specified without any explicit reply being requested. This may be
interpreted by the recipient as an implicit reply request. Note that for
an auto-forwarded message an explicit or implicit reply request may not
be meaningful.

Body Part Encryption

The original encoded information type indication includes the encoded
information type(s) of message body parts prior to encryption by the
originating domain.  The ability for the recipient domain to decode an
encrypted body part is a local matter.  Successful use of this facility
can only be guaranteed if there exists bilateral agreements to support
the exchange of encrypted body parts.


Forwarded IP message Indication

The following use of the original encoded information type in the context
of forwarded messages is clarified:

   o    If forwarding a private message body part the originator of the
        forwarded message shall set the original encoded information
        types in the P1 envelope to undefined for that body part.

   o    The encoded information types of the message being forwarded
        should be reflected in the new original encoded information types
        being generated.

   o    See Appendix 7B on recommended practices for the use of the
        delivery information as part of Forwarded IP-message.

Multipart Body

It is the intent of multipart bodies to allow for the useful and
meaningful structuring of a message that is constructed using differing
body part types.  For example, it is not recommended that a message made
up of only IA5 text should be represented as a number of IA5 body parts,
each one representing a paragraph of text.

7.12   APPENDIX B:    RECOMMENDED X.400 PRACTICES

It is not necessary to follow the recommended practices when claiming
conformance to these agreements.

        7.12.1    RECOMMENDED PRACTICES IN P2

        1.   ORDescriptor

             Vendors following the NBS/OSI Workshop guidelines shall,
             whenever possible, generate the ORName portion of an
             ORDescriptor in ALL IPM heading fields.

        2.   ForwardedIPMessage BodyParts

             ForwardedIPMessage BodyParts should be nested no deeper than
             eight.  There is no restriction on the number of
             ForwardedIPMessage BodyParts at any given depth.

        3.   DeliveryInformation

             It is strongly recommended that DeliveryInformation be
             supplied in both forwarded and autoforwarded message body
             parts. DeliveryInformation is useful when a message has
             multiple forwarded message body parts because without it,
             the EncodedInformationType(s) of the component forwarded
             messages cannot be deduced easily.  DeliveryInformation is
             useful for autoforwarded messages because the
             EncodedInformationType of an autoforwarded message is
             "unspecified" and the EncodedInformationType(s) of the
             message cannot be determined easily without it. Absence of
             the EncodedInformationType(s) makes it difficult for a UA to
             easily determine whether the message can be rendered.

        7.12.2    RECOMMENDED PRACTICES IN RTS

        1.   In the case where S-U-ABORT indicates a temporaryProblem,
             reestablishment of the session should not be attempted for a
             "sensible" time period (typically not less than five
             minutes).

             In instances where this delay is not required or necessary,
             report a localSystemProblem.

        2.   S-U-EXCEPTION-REPORT reason codes can be interpreted as
             follows:

             o    receiving ability jeopardized (value 1)
                  Possible meaning: The receiving RTS knows of an
                  impending system shutdown.

             o    local ss-User error (value 5)
                  Possible meaning:  The receiving RTS needs to
                  resynchronize the session dialogue.

             o    irrecoverable procedure error (value 6)
                  Possible meaning:  The receiving RTS has had to delete
                  a partially received APDU, even though some minor
                  synchronization points have been confirmed.

             o    non specific error (value 0)
                  Possible meaning:  The receiving RTS cannot handle the
                  APDU (for example, because it was too large) and wishes
                  to inform the sending RTS not to try again.

             o    sequence error (value 3):
                  Possible meaning: The S-ACTIVITY-RESUME request
                  specified a minor synchronization point serial  number
                  which does not match the checkpoint data.

        3.   For purposes of identifying an MTA during an RTS Open, OSI
             addressing information should be used.  This addressing
             information is conveyed by lower layer protocols and is
             reflected by the calling and called SSAP parameters of the
             S-CONNECT primitives.

             MTA validation and identification are related, but separate,
             functions.  The mTAName and password protocol elements of
             the RTS user data should be used for validation, rather that
             identification, of an MTA.  The RTS initiator and responder
             may independently require each other to supply mTAName and
             password.

             The CallingSSUserReference parameter of the S-CONNECT
             primitives should only have meaning to the entity that
             encoded it and should not be used to identify an MTA.


        7.12.3    RECOMMENDED PRACTICES FOR ORName

        Table 7.9 stipulates that the StandardAttributeList must contain
        either PrivateDomainName or OrganizationName.  It is recommended
        that, for both originator and recipients in a private domain, the
        PrivateDomainName field be used.

        It is recommended that there should be a DomainDefinedAttribute
        to be used in addressing UAs in existing mail systems, in order
        to curtail the proliferation of different types of
        DomainDefinedAttributes used for the same purpose.  The syntax of
        this DomainDefinedAttribute conforms to the CCITT Pragmatic
        Constraints, and thus has a maximum value length of 128 octets
        and a type length of 8 octets, each of type Printable String. 
        Only one occurrence is allowed.

        This DomainDefinedAttribute has the type name "ID" (in
        uppercase).  It contains the unique identifier of the UA used in
        addressing within the domain.  This DomainDefinedAttribute is to
        be exclusively used for routing within the destination domain
        (i.e., once routed to that domain via the mandatory components of
        the StandardAttributeList); any other components of the
        StandardAttributeList may be provided.  If they conflict delivery
        is not made. 

        The contents of this parameter need not be validated in the
        originating domain or any relaying domain, but simply transferred
        intact to the next MTA or domain.

        Class 2 and class 3 MTAs in a PRMD should allow administrators to
        decide the number of OrganizationalUnits that should appear in
        user names, instead of imposing a software controlled limit which
        is less than four.  This is desirable because when two different
        vendors impose different limits on the number of
        OrganizationalUnits in a name, it becomes difficult for the
        administrator to choose a sensible naming scheme.

        There are existing mail systems that include a small set of non-
        Printable String characters in their identifiers.  For these
        systems to communicate with X.400 messaging systems, either for
        pass-through service or delivery to X.400 users, gateways will be
        employed to encode these special characters into a sequence of
        Printable String characters.  This  conversion should be
        performed by the gateway according to a common scheme and before
        insertion in the ID DDA, which is intended to carry electronic
        mail identifiers.  X.400 User Agents may also wish to perform
        such conversions.

        It is recommended that the following symmetrical encoding and
        decoding algorithm for non-Printable String characters be
        employed by gateways.  The encoding algorithm maps an ID from an
        ASCII representation to a PrintableString representation.  Any
        non-printable string characters not specified in the table are
        covered by the category "other" in the table below.
        The principal conversion table for the mapping is as follows:

                 Table 7B.1  Printable string to ASCII mapping

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3  ASCII Character     Printable String Character                            3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3  % (percent)              (p)                                              3
3  @ (at sign)              (a)                                              3
3  ! (exclamation)          (b)                                              3
3  " (quote mark)           (q)                                              3
3  _ (underline)            (u)                                              3
3  ( (left paren.)          (l)                                              3
3  ) (right paren.)         (r)                                              3
3  other                    (3DIGIT)                                         3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

where 3DIGIT has the range 000 to 377 and is interpreted as the octal
encoding of an ASCII character.

To encode an ASCII representation to a PrintableString, the table and the
following algorithm should be used:

   IF current character is in the encoding set THEN
      encode the character according to the table above
   ELSE
      write the current character;
   continue reading;

To decode a PrintableString representation to an ASCII representation,
the table and the following algorithm should be used:

   IF current character is not "(" THEN
      write character
   ELSE
      {
      look ahead appropriate characters;
      IF composite characters are in the above table THEN
         decode per above table
      ELSE
         write current character;
      }
   continue reading;

        Class 2 and class 3 MTAs in a PRMD should allow administrators to
        decide the number of OrganizationalUnits that should appear in
        user names, instead of imposing a software controlled limit which
        is less than four.  This is desirable because when two different
        vendors impose different limits on the number of
        OrganizationalUnits in a name, it becomes difficult for the
        administrator to choose a sensible naming scheme.

        7.12.4    POSTAL ADDRESSING

        For domains wishing to support postal (or physical) delivery
        options, the following interim set of "nationally-defined" domain
        defined attributes are recommended.  The CCITT will define
        Standard Attributes in support of physical delivery in its 1988
        Recommendations; this is only an interim solution.

        CCITT will also be addressing the services associated with
        physical delivery. This interim solution does not address the
        end-to-end service aspects of physical delivery; in particular,
        the following IPM service elements do not currently extend
        outside of the X.400 environment:

             o    alternate Recipient Assignment
             o    PROBE
             o    Receipt Notification / Non-Receipt Notifications
             o    Grade of delivery

        "Delivery" means passing a message from the MTS to the physical
        delivery system (PDS), and not to the user (or user agent).

        The following three DDAs are recommended to be used to specify a
        postal (or physical) address:

        CNTRPC -  encodes the country and postal code for postal
                  delivery.  The DDA value is of the form
                  "Country?Postalcode"  (for example, "USA?22096").  The
                  country field is optional, the postal code is
                  optional; the separator ("?") is not.  If both country
                  and postal code are missing, this DDA should not be
                  specified.

        PDA 1 -   The country and postal code fields are free-form text.

        PDA 2 -   These two DDA (signifying Postal Delivery Address
                  strings 1 and  2) form a 256 character free-form
                  postal address.  Fields are separated by a question
                  mark ("?").  There is no implied  separator between
                  PDA1 and PDA2.  The meaning of the fields are defined
                  by each domain supporting the physical delivery
                  interface.  PDA1 contains the first 128 characters,
                  PDA2 the next 128 characters.  If the PDA string is
                  less than 128 characters, PDA2 is not used.

        For example, if the domain interprets the PDA fields as lines,
        the address

        Mr. John Smith
        Conway Steel
        123 Main Street
        Reston VA 22096

        would be encoded as follows:

        type = "PDA1"  value = "Mr. John Smith?Conway Steel?123 Main
        Street?Reston VA"
        CNTRPC = "?22096"


        7.12.5    EDI use of X.400

             7.12.5.1  Introduction and Scope

             This is a guideline for EDI data transfer in an X.400
             environment conforming to the NBS agreements.  These
             recommended practices outline procedures for use in
             transferring EDI transactions between trading partner
             applications in an attempt to facilitate actual X.400
             implementation by EDI users.

             The scope of this guideline is to describe specific
             recommendations for adopting X.400 as the data transfer
             mechanism between EDI applications.

             7.12.5.2  Model

             The MHS recommendations can accommodate EDI through the
             approach illustrated below.  Many Message Transfer (MT)
             service elements defined in the X.400 recommendations are
             particularly useful to the EDI application.

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3                                  X.400 Message (1 EDI interchange)    3
3                              ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?  3
3                              3                                     3  3
3                              3   ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?  3  3
3                              3   3                              3  3  3
3   Envelope   ------------------->3         P1 Control           3  3  3
3                              3   3         Information          3  3  3
3                              3   @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY  3  3
3                              3                                     3  3
3                              3                                     3  3
3                              3                                     3  3
3                              3   ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?  3  3
3                              3   3         One                  3  3  3
3   Content    ------------------->3         EDI                  3  3  3
3                              3   3         Interchange          3  3  3
3                              3   @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY  3  3
3                              3                                     3  3
3                              @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY  3
3 MHS Message                                                           3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

             This diagram depicts an EDI content (1 EDI interchange)
             enveloped by the P1 MHS envelope.  All the MT Services
             defined in the X.400 Recommendations may be used for EDI. 
             However, it is not required to support optional or non-
             essential services to exchange EDI data between EDI users. 
             When an EDI user submits an EDI Trade Document to the EDI
             User Agent, the EDI UA will submit the EDI content plus P1
             envelope to the Message Transfer System (MTS).


ZDDDDDDDDDDD?             ZDDDDDDDDDDDD?              ZDDDDDDDDDDD?
3           3             3    EDI     3              3    EDI    3
3   MTS     3<----------->3    UA      3<------------>3    User   3
3           3             3            3              3           3
@DDDDDDDDDDDY             @DDDDDDDDDDDDY              @DDDDDDDDDDDY


             The EDI UA must support the essential MT Services as defined
             in these Agreements; for example, as a minimum, to provide
             default values for services not elected by the EDI user,
             such as Grade of Delivery.

             Note: MT Services are not necessarily made available by the
             EDI UA to the EDI user.


             7.12.5.3  Protocol Elements Supported for EDI

             The following P1 protocol elements will be used to support
             EDI applications:

             Content Type
                  For EDI applications, the content type will be 0
                  (undefined content).

             Original Encoded Information Types
                  Any EIT defined in the X.400 Recommendations may be
                  used to specify the encoding of EDI content.  However,
                  for ANSI X12 EDI applications in particular, it is
                  expected that the "undefined" and "Ia5Text" EIT's will
                  normally be used, with "undefined" used to signify the
                  EBCDIC character set.


             7.12.5.4  Addressing and Routing

             It is anticipated that connection of some existing systems
             to an X.400 service for EDI purposes will be by other than
             X.400 protocols, at least in the short term.

             EDI messages entering the X.400 environment will therefore
             need to have X.400 O/R Names added to identify the
             origination and recipient trading partners, typically by
             means of local directory services in the origination domain
             which will map EDI identifiers/addresses into O/R Names. 
             Such O/R Names will contain Standard Attributes as defined
             in Table 7.9 and for recipient trading partners will at
             least identify the destination domain.

             In the case of trading partners outside the X.400
             environment, it is expected, however, that there will be
             cases where message delivery will require the provision of
             addressing information beyond that which can be carried in
             Standard Attributes.  In such cases, Domain Defined
             Attributes are recommended to be used.

             The syntax of this DDA is as defined in Table 7.9, with a
             single occurrence having the type name "EDI" (uppercase) and
             a value containing the identifier/address of the trading
             partner.  For ASC X12 purposes, specifically, this value
             will comprise the 2 digit interchange ID qualifier followed
             by the interchange ID (max 15 characters).  Routing on this
             DDA shall only occur, if at all, in the destination domain.

        7.12.6    USA Body Parts

        It is recommended that UAs can generate any USA Body Part, as
        defined in section 7.5.3.6.2, and that they can receive such body
        parts as well.  reception of USA Body Parts does not imply
        further processing by the UA, but merely that the body part is
        made available, with a indication of its registered body part
        identifier, to another process or deposition in a file. 
        Generation implies the reverse of this process.

7.13   APPENDIX C:    RENDITION OF IA5Text AND T61String CHARACTERS
 
        7.13.1    GENERATING AND IMAGING IA5Text

        The characters that may be used in an IA5String are the graphic
        characters (including Space), control characters and Delete of
        the IA5 character repertoire ISO 646.

        The graphic characters that may be used with a guaranteed
        rendition are those related with positions 2/0 to 2/2, 2/5 to
        3/15, 4/1 to 5/10, 5/15 and 6/1 to 7/10 in the basic 7-bit code
        table.

        The other graphic characters may be used but have no guaranteed
        rendition.

        The control characters that may be used but have no guaranteed
        effect are a subset consisting of the format effectors 0/10 (LF),
        0/12 (FF) and 0/13 (CR) provided they are used in one of the
        following combinations:

        CR LF          to start a new line
        CR FF          to start a new page (and line)
        LF .. LF       to show empty lines (always after one of the
                       preceding combinations).

        The other control characters or the above control characters in
        different combinations may be used but have no guaranteed effect.

        The character Delete may occur but has no guaranteed effect. The
        IA5String in a P2 IA5Text BodyPart represents a series of lines
        which may be divided into pages.  Each line should contain from 0
        to 80 graphic characters for guaranteed rendition.  Longer lines
        may be arbitrarily broken for rendition.  Note that X.408 states
        that for conversion from IA5Text to Teletex, the maximum line
        length is 77 characters.

        7.13.2    GENERATING AND IMAGING T61String

        For further study.

7.14   APPENDIX D:    DIFFERENCES IN INTERPRETATION DISCOVERED THROUGH
                       TESTING OF THE MHS FOR THE CeBit 87 DEMONSTRATION

Several interworking problems were discovered through multi-vendor
testing.  These problems, and recommendations for solutions to them are
discussed in this appendix.

        7.14.1    ENCODING OF RTS USER DATA

        The password is defined as an ANY in the X.400 Recommendations,
        and implementor's groups have decided to use an IA5String for
        this field.  There was some confusion about what the X.409
        encoding for this IA5String would be, and the correct encoding
        is:

        class:    context specific
        form:     constructor
        id code:  1
        length:   length of contents
        contents: (primitive encoding)
             IA5String:     16
             length:        length of contents
             contents:      the password string
        class:    context specific
        form:     constructor
        id code:  1
        length:   length of contents
        contents: (constructor encoding) left as an exercise for the
                  reader

        Implementations should be prepared to receive any X.409 type for
        the password because of its definition as an ANY.

        7.14.2    EXTRA SESSION FUNCTIONAL UNITS

        One vendor proposed more than the required set of functional
        units on opening the session connection, and the receiver
        rejected the connection.  All debate aside about whether the
        initiator should have proposed units outside of the required set,
        or whether the receiver should have rejected the connection, the
        set of functional units can be negotiated in a straightforward
        way.  The following is recommended.

        If the initiator proposes using more than the required set of
        functional units, the responder should specify the set of
        functional units that it would like to use (which should include
        the required set) in the open response.  The session
        implementations will automatically use the intersection of the
        units proposed by both sides.

        If the initiator proposes using less than the required set of
        functional units, the responder should reject the connection. 
        Unfortunately, there is not an appropriate RefuseReason for
        rejecting the connection, so instead of refusing the connection
        in the response to the S-CONNECT, the receiver should issue an S-
        U-ABORT with an AbortReason of protocolError.  Note that it is
        valid to issue an S-U-ABORT instead of responding to the S-
        CONNECT.  A problem report has been submitted to the CCITT
        requesting the addition of a RefuseReason for this situation.

        If the responder proposes using less than the required set of
        functional units, the session connection is established before
        the initiator can check for this.  If too few functional units
        have been proposed, the initiator should abort the connection
        using S-U-ABORT, with an abort reason of protocolError.

        7.14.3    MIXED CASE IN THE MTA NAME

        The MTA name is frequently exchanged over the telephone when two
        systems are being configured to communicate with one another.  In
        one such telephone exchange, the casing of the MTA name was not
        specified, the MTA name consisted of both upper and lower case
        letters, and one of the implementations compared MTA names for
        equality in a case sensitive manner.  Consequently, connections
        failed until the problem was detected and repaired.  It is
        recommended that the MTA name be compared for equality in a case
        insensitive manner, and that the password be compared for
        equality in a case sensitive manner.

        7.14.4    X.410 ACTIVITY IDENTIFIER

        The X.400 Implementor's Guide recommends that the activity
        identifier be X.409 encoded, but this is only a recommendation
        and not a requirement.  Consequently, receiving systems cannot
        assume that the activity identifier will be X.409 encoded.

        7.14.5    ENCODING OF PER RECIPIENT FLAG AND PER MESSAGE FLAG

        In the definition of the PerRecipientFlag in X.411, there is a
        statement that the last three bits are reserved, and should be
        set to zero.  It is unclear whether those bits are unused in the
        X.409 encoding.  Receivers should accept encodings with either
        zero or three unused bits.  A problem report has been submitted
        to the CCITT asking for clarification.

        Though there is not any statement in X.411 about the last four
        bits of the PerMessageFlag, some vendors have encoded this with
        zero unused bits, and some have encoded it with four unused bits. 
        The PerMessageFlag should be encoded with at least four unused
        bits.

        7.14.6    ENCODING OF EMPTY BITSTRINGS

        There are three valid encodings for an empty bitstring: a
        constructor of length zero, a constructor of indefinite length
        followed by the end-of-contents terminator, and a primitive of
        length one with a zero octet as the value.

        7.14.7    ADDITIONAL OCTETS FOR BITSTRINGS

        Nothing in X.409 constrains an implementation from sending two,
        three, four, or even more octets for a bitstring that fits into
        one octet, with the undefined bits set to zero.  Note that the
        number of excess octets is bounded by the pragmatic constraints
        guidelines of the CCITT X.400 Implementor's Guide for all of the
        bitstrings in P1.

        7.14.8    APPLICATION PROTOCOL IDENTIFIER

        If a value other that 1 is received in the applicationProtocol of
        the  pUserData in the PConnect, NBS implementations will reject
        the connection.  If CEN/CENELEC implementations receive a value
        other than 8883 for this field, they will reject the connection. 
        This is an unfortunate state of affairs, because if NBS
        implementations accept the value of 8883 without supporting the
        MOTIS service elements, they would be misrepresenting themselves. 
        To make matters worse, CEPT uses a value of 1, but relays MOTIS
        elements, which means that MOTIS elements will be relayed to
        implementations using a value of 1 to demonstrate that they do
        not support MOTIS.  Work is continuing to try to find a solution
        that will allow European implementations to interwork with U.S
        implementations.

        7.14.9    INITIAL SERIAL NUMBER IN S-CONNECT

        This should be implemented in accordance with section 3.5.1 E4 of
        the Implementors' Guide.

        7.14.10   CONNECTION DATA ON RTS RECOVERY

        It is clarified that the ConnectionData is identical in both the
        S-CONNECT.request and the S-CONNECT.response.  The value of the
        ConnectionData is the old Session Connection Identifier.

        7.14.11   ACTIVITY RESUME

        If an activity is being resumed on a new session connection, it
        is not clear from X.410 and X.225 whether all four of the called-
        ss-user reference, the calling-ss-user reference, the common
        reference, and the additional reference information should be
        specified in the S-ACTIVITY-RESUME, or whether one of the ss-
        user-references should be absent.  It is also unclear whether the
        called-ss-user reference should be identical to the calling-ss-
        user reference if both are present.  Consequently, receivers
        should be tolerant of this situation.  Appropriate problem
        reports will be submitted to the CCITT asking for clarification.

        7.14.12   OLD ACTIVITY IDENTIFIER

        The Old Activity Identifier in S-ACTIVITY-RESUME refers to the
        original activity identifier.

        7.14.13   NEGOTIATION DOWN TO TRANSPORT CLASS 0

        For European implementations, X.410 specifies that class 0
        transport must be supported.  However, it is permissible for an
        initiator to propose a higher class as the preferred class,
        provided that class 0 appears as the alternate class in the T-
        Connect PDU.  A responding implementation can choose to use
        either the preferred or alternate class, but again, must be able
        to use class 0.  In other words, for private to private
        connections in Europe, class 0 transport is required.

        This conflicts with the NBS agreements, since class 0 is only
        required if one of the partners in a connection is an ADMD.
7.15APPENDIX E:WORLDWIDE X.400 CONFORMANCE PROFILE MATRIX

Y CONFORMANCE (E)
implies a conformance problem for European products in the U.S.

Y CONFORMANCE (US)
implies a conformance problem for U.S. products in Europe.

   o    The A/311 profile is specified in Env 41 202, the A/3211 profile
        in Env 41 201

   o    No TTC protocol classification for RTS exists.

   o    The notation X/Y indicates "X" for PRMDs and "Y" for ADMDs, i.e.
        "M/G" would be Mandatory for PRMDs and Generatable for ADMDs.

                Table 7E.1  Protocol element comparison of RTS

ZDDDDDDDDDDDDDDDDDDDDDDDBDDDDDDDBDDDDDDDDDDBDDDDDDDDDBDDDDDDDDDDDDDDDDDDDDDDD?
3RTS element            3  NBS  3   A/311  3  A/3211 3  PROBLEM Y/N          3
CDDDDDDDDDDDDDDDDDDDDDDDEDDDDDDDEDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDD4
3PConnect               3   M   3    M     3    M    3  N                    3
3 DataTransferSyntax    3   M 0 3    M 0   3    M 0  3  N                    3
3PUserData              3   M   3    M     3    M    3  N                    3
3 checkpointSize        3   H   3    H     3    H    3  N                    3
3 windowSize            3   H   3    H     3    H    3  N                    3
3 dialogueMode          3   H   3    H     3    H    3  N                    3
3 connectdata           3   M   3    M     3    M    3  N                    3
3 applicationProtocol   3   G 1 3    H 1   3 R 8883  3  N                    3
3                       3 H 88833          3         3                       3
3 ConnectionData        3       3          3         3                       3
3  Open                 3   G   3    G     3    G    3  N                    3
3  Recover              3   G   3    H     3    G    3  N                    3
3                       3       3          3         3                       3
3 Open                  3       3          3         3                       3
3  RTSUserData          3   G   3    G     3    G    3  N                    3
3                       3       3          3         3                       3
3 Recover               3       3          3         3                       3
3  SessionConnectionID  3   G   3    G     3    G    3  N                    3
3                       3       3          3         3                       3
3RTSUserData            3       3          3         3                       3
3  MTAName              3   G   3    G     3    G    3  N                    3
3                       3       3          3         3                       3
3  Password             3   G   3    G     3    G    3  N                    3
3                       3       3          3         3                       3
3  null                 3   G   3    G     3    G    3  N                    3
3                       3       3          3         3                       3
3SessionConnectionID    3       3          3         3                       3
3 CallingUserReference  3   M   3    M     3    M    3  N                    3
3                       3       3          3         3                       3
3 CommonReference       3   M   3    M     3    M    3  N                    3
3 AdditionalRefInfo     3   H   3    H     3    H    3  N                    3
3                       3       3          3         3                       3
3PAccept                3   G   3    G     3    G    3  N                    3
3 DataTransferSyntax    3   M 0 3    M 0   3    M 0  3  N                    3
@DDDDDDDDDDDDDDDDDDDDDDDADDDDDDDADDDDDDDDDDADDDDDDDDDADDDDDDDDDDDDDDDDDDDDDDDY
                                                      (Continued on next page.)

           Table 7E.1  Protocol element comparison of RTS, continued

ZDDDDDDDDDDDDDDDDDDDDDDDBDDDDDDBDDDDDDDDDDDBDDDDDDDDDBDDDDDDDDDDDDDDDDDDDDDDD?
3RTS element            3 NBS  3  A/311    3 A/3211  3 PROBLEM (Y/N)         3
CDDDDDDDDDDDDDDDDDDDDDDDEDDDDDDEDDDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDD4
3                       3      3           3         3                       3
3PUserData              3  M   3    M      3    M    3 N                     3
3 CheckpointSize        3  H   3    H      3    H    3 N                     3
3 WindowSize            3  H   3    H      3    H    3 N                     3
3 ConnectionData        3  M   3    M      3    M    3 N                     3
3                       3      3           3         3                       3
3PRefuse                3  G   3    G      3    G    3 N                     3
3 RefuseReason          3  M   3    M      3    M    3 N                     3
3                       3      3           3         3                       3
3SSUserData             3  G   3    G      3    G    3 N                     3
3 (in S-TOKEN-PLEASE)   3      3           3         3                       3
3                       3      3           3         3                       3
3AbortInformation       3  G   3    G      3    G    3 N                     3
3 (in S-U-ABORT)        3      3           3         3                       3
3 AbortReason           3  H   3    H      3    H    3 N                     3
3 reflectedParameter    3  X   3    X      3    X    3 N                     3
@DDDDDDDDDDDDDDDDDDDDDDDADDDDDDADDDDDDDDDDDADDDDDDDDDADDDDDDDDDDDDDDDDDDDDDDDY


                       Table 7E.2  Protocol element comparison of P1

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDBDDDDDBDDDDDDDBDDDDDDBDDDDDDBDDDDDDDDDDDDDDDDDDDD?
3P1 Protocol                         3 NBS 3 A/311 3A/32113 TTC  3   PROBLEM (Y/N)    3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDEDDDDDEDDDDDDDEDDDDDDEDDDDDDEDDDDDDDDDDDDDDDDDDDD4
3                                    3     3       3      3      3                    3
3        ORname                      3     3       3      3      3                    3
3          StandardAttributeList     3  M  3   M   3   M  3  M   3   N See Note 4     3
3          DomainDefAttributeList    3  X  3   X   3   X  3  G   3   Y See Note 5     3
3                                    3     3       3      3      3                    3
3        StandardAttributeList       3     3       3      3      3                    3
3          CountryName               3  R  3   R   3   R  3  M   3   N                3
3                                    3     3ISO R  3   R  3      3   N                3
3                                    3     3X.121 H3   H  3      3  Y Conformance (E) 3
3                                    3     3Other X3   X  3      3  Y Prot Vio        3
3          AdministrationDomainName  3  R  3   R   3   G  3  M   3   N                3
3             ... if PrintableString 3     3   R   3   G  3      3   N                3
3             ... if numericString   3     3   H   3   H  3      3  Y Conformance (E) 3
3          X.121 Address             3  X  3  X/R  3   X  3      3Y Conf(US)See Note 13
3          Terminal ID               3  X  3  X/G  3   X  3      3Y Conf(US)See Note 13
3          PrivateDomainName         3  G  3   G   3   G  3  G   3   N                3
3                                    3     3       3      3      3                    3
3          OrganizationName          3  G  3   G   3   G  3  G   3   N                3
3          UniqueUAidentifier        3  X  3  X/G  3   X  3      3Y Conf(US)See Note 13
3          PersonalName              3  G  3   G   3   G  3  G   3   N                3
3          OrganizationalUnit        3  G  3   G   3   G  3  G   3   N                3
3                                    3     3       3      3      3                    3
3        DomainDefinedAttribute      3  X  3   X   3   X  3  G   3   N                3
3          Type                      3  M  3   M   3   M  3  M   3   N                3
3          Value                     3  M  3   M   3   M  3  M   3   N                3
3                                    3     3       3      3      3                    3
3        PersonalName                3     3       3      3      3                    3
3          Surname                   3  M  3   M   3   M  3  M   3   N                3
3          GivenName                 3  G  3   G   3   G  3  G   3   N                3
3          Initials                  3  G  3   G   3   G  3  G   3   N                3
3                                    3     3       3      3      3                    3
3          GenerationQualifier       3  G  3   X   3   X  3  X   3  Y Conformance (E) 3
3                                    3     3       3      3      3                    3
3        GlobalDomainIdentifier      3     3       3      3      3                    3
3          CountryName               3  M  3   M   3   M  3  M   3   N                3
3          AdministrationDomainName  3  M  3   M   3   G  3  M   3  Y Proto Vio       3
3          PrivateDomainIdentifier   3 R/H 3   H   3   R  3 M/X  3   N                3
3                                    3     3       3      3      3                    3
3        MPDU                        3     3       3      3      3                    3
3          UserMPDU                  3  G  3   G   3   G  3  G   3   Y TTC required   3
3                                    3     3       3      3      3     MPDU size is   3
3                                    3     3       3      3      3     32K            3
3          DeliveryReportMPDU        3  G  3   G   3   G  3  G   3   N                3
3                                    3     3       3      3      3                    3
3          ProbeMPDU                 3  H  3   H   3   H  3  H   3   N                3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDADDDDDADDDDDDDADDDDDDADDDDDDADDDDDDDDDDDDDDDDDDDDY
                                                                  (Continued on next page.)

                 Table 7E.2  Protocol element comparison of P1, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDBDDDDDBDDDDDDDBDDDDDDBDDDDDDBDDDDDDDDDDDDDDDDDDDD?
3P1 Protocol                         3 NBS 3 A/311 3A/32113 TTC  3   PROBLEM (Y/N)    3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDEDDDDDEDDDDDDDEDDDDDDEDDDDDDEDDDDDDDDDDDDDDDDDDDD4
3                                    3     3       3      3      3                    3
3        UserMPDU                    3     3       3      3      3                    3
3          UMPDUenvelope             3  M  3   M   3   M  3  M   3   N                3
3          UMPDUcontent              3  M  3   M   3   M  3  M   3   N                3
3                                    3     3       3      3      3                    3
3        UMPDUenvelope               3     3       3      3      3                    3
3          MPDUidentifier            3  M  3   M   3   M  3  M   3   N                3
3          originatorORname          3  M  3   M   3   M  3  M   3   N                3
3          originalEncodedTypes      3  G  3   H   3   H  3  G   3   Y Conformance (E)3
3                                    3     3       3      3      3                    3
3          ContentType               3  M  3   M   3   M  3  M   3   N                3
3          UAcontentID               3  H  3   H   3   H  3  H   3   N                3
3          Priority                  3  G  3   G   3   G  3  G   3   N                3
3          PerMessageFlag            3  G  3   G   3   G  3  G   3   N                3
3          DeferredDelivery          3  X  3   X   3   X  3  X   3   N                3
3          PerDomainBilatInfo        3  X  3   X   3   X  3  X   3   N                3
3          RecipientInfo             3  M  3   M   3   M  3  M   3   Y TTC MPDU 32K   3
3          TraceInformation          3  M  3   M   3   M  3  M   3   N                3
3MOTIS->   LatestDelivery            3     3       3   X  3      3   N                3
3MOTIS->   InternalTraceInfo         3 M/P 3       3   P  3      3   N                3
3        UMPDUcontent                3  M  3   M   3   M  3  M   3   N                3
3                                    3     3       3      3      3                    3
3        MPDUidentifier              3     3       3      3      3                    3
3          GlobalDomainIdent         3  M  3   M   3   M  3  M   3   N                3
3          IA5string                 3  M  3   M   3   M  3  M   3   N                3
3                                    3     3       3      3      3                    3
3        PerMessageFlag              3     3       3      3      3                    3
3          DiscloseRecipients        3  H  3G @ MTL3   H  3  H   3  Y Conformance (US)3
3                                    3     3H at UA3   ?  3      3  Y Conformance (US)3
3          ConversionProhibited      3  G  3   G   3   G  3  G   3   N                3
3          AlternatRecipAllowed      3  H  3G @ MTL3   H  3  X   3  Y Conformance (US)3
3                                    3     3H at UA3   ?  3      3  Y Conformance (US)3
3          ContentReturnRequest      3  X  3   X   3   X  3  X   3                    3
3MOTIS->   redirectionProhibited     3     3       3   X  3      3  N                 3
3                                    3     3       3      3      3                    3
3        PerDomainBilateralInfo      3     3       3      3      3                    3
3          CountryName               3  M  3   M   3   M  3  M   3   N                3
3          AdminDomainName           3  M  3   M   3   G  3  M   3  Y Prot Vio        3
3MOTIS->   PrivateDomainName         3     3       3   G  3      3   N                3
3          BilateralInfo             3  M  3   M   3   M  3  M   3   N                3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDADDDDDADDDDDDDADDDDDDADDDDDDADDDDDDDDDDDDDDDDDDDDY
                                                                  (Continued on next page.)

                 Table 7E.2  Protocol element comparison of P1, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDBDDDDDBDDDDDDDBDDDDDDBDDDDDDBDDDDDDDDDDDDDDDDDDDD?
3P1 Protocol                         3 NBS 3 A/311 3A/32113 TTC  3   PROBLEM (Y/N)    3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDEDDDDDEDDDDDDDEDDDDDDEDDDDDDEDDDDDDDDDDDDDDDDDDDD4
3        DeliveryReportContent       3     3       3      3      3                    3
3          original MPDUident        3  M  3   M   3   M  3  M   3   N                3
3          intermediate Trace        3 X/G 3   X   3   X  3  X   3  Y Conformance (E) 3
3          UAcontentID               3  G  3   G   3   G  3  G   3   N                3
3          ReportedRecipientInfo     3  M  3   M   3   M  3  M   3   Y TTC 256 max    3
3          returned                  3  H  3   H   3   X  3  X   3  Y Conformance (E) 3
3          billing information       3  X  3   X   3   X  3  X   3   N                3
3                                    3     3       3      3      3                    3
3        ReportedRecipientInfo       3     3       3      3      3                    3
3          recipient ORname          3  M  3   M   3   M  3  M   3   N                3
3          extensionsIdentifier      3  M  3   M   3   M  3  M   3   N                3
3          PerRecipientFlag          3  M  3   M   3   M  3  M   3   N                3
3          LastTraceInformation      3  M  3   M   3   M  3  M   3   N                3
3          intendedRecipient         3  H  3   H   3   H  3  H   3   N                3
3          SupplementaryInfo         3 X/H 3   X   3   X  3  X   3  Y Conformance (E) 3
3MOTIS->   ReassignmentInfo          3     3       3   X  3      3   N                3
3                                    3     3       3      3      3                    3
3MOTIS-> ReassignmentInfo            3     3       3      3      3                    3
3MOTIS->   intendedRecipient         3     3       3   M  3      3   N                3
3MOTIS->   reasonForReassignment     3     3       3   H  3      3   N                3
3                                    3     3       3      3      3                    3
3        LastTraceInformation        3     3       3      3      3                    3
3          arrival                   3  M  3   M   3   M  3  M   3   N                3
3          convertedEncInfoTypes     3  G  3   G   3   H  3  G   3  Y Conformance (E) 3
3          Report                    3  M  3   M   3   M  3  M   3   N                3
3                                    3     3       3      3      3                    3
3        Report                      3     3       3      3      3                    3
3          DeliveredInfo             3  G  3   G   3   G  3 D?   3   N See Note 6     3
3                                    3     3       3      3  CDM 3                    3
3          NonDeliveredInfo          3  G  3   G   3   G  3 DY   3   N                3
3                                    3     3       3      3      3                    3
3        DeliveredInfo               3     3       3      3      3                    3
3          delivery                  3  M  3   M   3   M  3  M   3   N                3
3          TypeofUA                  3 R/H 3   H   3   R  3 M/G  3   N                3
3                                    3     3       3      3      3                    3
3        NonDeliveredInfo            3     3       3      3      3                    3
3          ReasonCode                3  M  3   M   3   M  3  M   3   N                3
3          DiagnosticCode            3  H  3   H   3   H  3  H   3   N                3
3MOTIS->   UAprofileIdentifier       3     3       3   X  3      3   N                3
3                                    3     3       3      3      3                    3
3MOTIS-> UAprofileIdentifier         3     3       3      3      3                    3
3MOTIS->   ContentType               3     3       3   M  3      3   N                3
3MOTIS->   EncodedInfoTypes          3     3       3   M  3      3   N                3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDADDDDDADDDDDDDADDDDDDADDDDDDADDDDDDDDDDDDDDDDDDDDY
                                                                  (Continued on next page.)
                 Table 7E.2  Protocol element comparison of P1, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDBDDDDDBDDDDDDDBDDDDDDBDDDDDDBDDDDDDDDDDDDDDDDDDDD?
3P1 Protocol                         3 NBS 3 A/311 3A/32113 TTC  3   PROBLEM (Y/N)    3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDEDDDDDEDDDDDDDEDDDDDDEDDDDDDEDDDDDDDDDDDDDDDDDDDD4
3                                    3     3       3      3      3                    3
3        ProbeEnvelope               3     3       3      3      3                    3
3          probe                     3  M  3   M   3   M  3  M   3   N                3
3          originator                3  M  3   M   3   M  3  M   3   N                3
3          ContentType               3  M  3   M   3   M  3  M   3   N                3
3          UAcontentID               3  H  3   H   3   H  3  H   3   N                3
3          originalEncInfoTypes      3  G  3   H   3   H  3  G   3  Y Conformance (E) 3
3          TraceInformation          3  M  3   M   3   M  3  M   3   N                3
3          PerMessageFlag            3  G  3   G   3   G  3  G   3   N                3
3          ContentLength             3  H  3   H   3   H  3  H   3   N                3
3          PerDomainBilatInfo        3  X  3   X   3   X  3  X   3   N                3
3          RecipientInfo             3  M  3   M   3   M  3  M   3   Y TTC 256 max    3
3MOTIS->   InternalTraceInfo         3 M/P 3       3   P  3      3   N                3
3                                    3     3       3      3      3                    3
3        RecipientInfo               3     3       3      3      3                    3
3          RecipientORname           3  M  3   M   3   M  3  M   3    N               3
3          ExtensionIdentifier       3  M  3   M   3   M  3  M   3    N               3
3          PerRecipientFlag          3  M  3   M   3   M  3  M   3    N               3
3          ExplicitConversion        3  X  3   X   3   X  3  X   3    N               3
3MOTIS->   OriginatorReqAlternatRecip3     3       3   X  3      3    N               3
3MOTIS->   ReassignmentInfo          3     3       3   X  3      3    N               3
3                                    3     3       3      3      3                    3
3        PerRecipientFlag            3     3       3      3      3                    3
3          ResponsibilityFlag        3  M  3   M   3   M  3   M  3    N               3
3          ReportRequest             3  M  3   M   3   M  3   M  3    N               3
3          UserReportRequest         3  M  3   M   3   M  3   M  3    N               3
3                                    3     3       3      3      3                    3
3        TraceInformation            3     3       3      3      3                    3
3                                    3     3       3      3      3                    3
3          GlobalDomainIdent         3  M  3   M   3   M  3  M   3    N               3
3          DomainSuppliedInfo        3  M  3   M   3   M  3  M   3    N               3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDADDDDDADDDDDDDADDDDDDADDDDDDADDDDDDDDDDDDDDDDDDDDY
                                                                  (Continued on next page.)
                 Table 7E.2  Protocol element comparison of P1, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDBDDDDDBDDDDDDDBDDDDDDBDDDDDDBDDDDDDDDDDDDDDDDDDDD?
3P1 Protocol                         3 NBS 3 A/311 3A/32113 TTC  3   PROBLEM (Y/N)    3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDEDDDDDEDDDDDDDEDDDDDDEDDDDDDEDDDDDDDDDDDDDDDDDDDD4
3                                    3     3       3      3      3                    3
3        DomainSuppliedInfo          3     3       3      3      3                    3
3          arrival                   3  M  3   M   3   M  3  M   3    N               3
3          deferred                  3  X  3   X   3   X  3  X   3    N               3
3          action                    3  M  3   M   3   M  3  M   3    N               3
3            (0=relayed)             3  G  3   G   3   G  3      3    N Note:         3
3                                    3     3       3      3      3   Re-routing not   3
3                                    3     3       3      3      3   required.        3
3            (1=rerouted)            3  H  3   H   3   H  3      3    N               3
3MOTIS->     (2=recipientReassigned) 3     3       3   H  3      3    N               3
3          converted                 3  H  3   G   3   H  3  H   3   Y Conformance(US)3
3          previous                  3  H  3   G   3   G  3  X   3   Y Conformance(US)3
3                                    3     3       3      3      3   (Note: G is      3
3                                    3     3       3      3      3   inconsistent with3
3                                    3     3       3      3      3   action (relayed) 3
3                                    3     3       3      3      3   being "H".)      3
3                                    3     3       3      3      3                    3
3        ORname                      3     3       3      3      3                    3
3                                    3     3       3      3      3                    3
3        EncodedInformationTypes     3     3       3      3      3                    3
3          BitString                 3  M  3   M   3   M  3  M   3    N  See Note 3   3
3          G3NonBasicParameters      3  X  3   X   3   X  3  X   3    N               3
3          TeletexNonBasicParams     3  X  3   R   3   X  3  X   3   Y Conformance(US)3
3          PresentationAbilities     3  X  3   X   3   X  3  X   3    N               3
3                                    3     3       3      3      3                    3
3        DeliveryReportMPDU          3  G  3   G   3   M  3  G   3    N               3
3          DeliveryReportEnvelop     3  M  3   M   3   M  3  M   3    N               3
3          DeliveryReportContent     3  M  3   M   3   M  3  M   3    N               3
3                                    3     3       3      3      3                    3
3        DeliveryReportEnvelope      3     3       3      3      3                    3
3          report                    3  M  3   M   3   M  3  M   3    N               3
3          originator ORname         3  M  3   M   3   M  3  M   3    N               3
3          TraceInformation          3  M  3   M   3   M  3  M   3    N               3
3          InternalTraceInfo         3 M/P 3       3   P  3      3    N               3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDADDDDDADDDDDDDADDDDDDADDDDDDADDDDDDDDDDDDDDDDDDDDY
                                                                  (Continued on next page.)

                       Table 7E.3  Protocol element comparison of P2

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDBDDDDDBDDDDDDDBDDDDDDBDDDDDDBDDDDDDDDDDDDDDDDDDDD?
3P2 Protocol                         3 NBS 3 A/311 3A/32113 TTC  3   PROBLEM (Y/N)    3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDEDDDDDEDDDDDDDEDDDDDDEDDDDDDEDDDDDDDDDDDDDDDDDDDD4
3                                    3     3       3      3      3                    3
3        UAPDU                       3     3       3      3      3                    3
3          IM_UAPDU                  3  G  3   G   3  G   3  G   3   N                3
3          SR_UAPDU                  3  X  3   X   3  X   3  X   3   N                3
3                                    3     3       3      3      3                    3
3        IM_UAPDU                    3     3       3      3      3                    3
3          Heading                   3  M  3   M   3  M   3  M   3   N                3
3          Body                      3  M  3   M   3  M   3  M   3   N                3
3                                    3     3       3      3      3                    3
3        Heading                     3     3       3      3      3                    3
3          IPmessageID               3  M  3   M   3  M   3  M   3   N                3
3          Originator ORname         3  R  3   R   3  R   3 M/G  3   N                3
3          AuthorizingUsers          3  H  3   H   3  H   3  H   3   Y TTC 16 max     3
3          PrimaryRecipients         3  G  3   G   3  G   3  G   3   Y TTC 256 max    3
3          CopyRecipients            3  G  3   G   3  G   3  G   3   Y TTC 256 max    3
3          BlindCopyRecipients       3  H  3   H   3  H   3  H   3   Y TTC 256 max    3
3          InReplyTo                 3  G  3   G   3  G   3  G   3   N                3
3          Obsoletes                 3  H  3   H   3  H   3  H   3   Y TTC 8 max      3
3          CrossReferences           3  H  3   H   3  H   3  H   3   Y TTC 8 max      3
3          Subject                   3  G  3   G   3  G   3  G   3   N                3
3          ExpiryDate                3  H  3   H   3  H   3  H   3   N                3
3          ReplyBy                   3  H  3   H   3  H   3  H   3   N                3
3          ReplyToUsers              3  H  3   H   3  H   3  H   3   Y TTC 32 max     3
3          Importance                3  H  3   H   3  H   3  H   3   N                3
3          Sensitivity               3  H  3   H   3  H   3  H   3   N                3
3          Autoforwarded             3  H  3   H   3  H   3  H   3   N                3
3MOTIS->   CirculationList           3     3       3  X   3      3   N                3
3MOTIS->   ObsoletingTime            3     3       3  X   3      3   N                3
3                                    3     3       3      3      3                    3
3        IPmessageID                 3     3       3      3      3                    3
3          ORname                    3  H  3   H   3  H   3  H   3   N                3
3          PrintableString           3  M  3   M   3  M   3  M   3   N                3
3                                    3     3       3      3      3                    3
3        ORdescriptor                3     3       3      3      3                    3
3          ORname                    3  H  3   H   3  H   3 D?   3   N See Note 6     3
3                                    3     3       3      3  CDM 3                    3
3          FreeFormName              3  H  3   H   3  H   3 DY   3   N                3
3          TelephoneNumber           3  H  3   H   3  H   3  G   3   N                3
3                                    3     3       3      3      3                    3
3        Recipient                   3     3       3      3      3                    3
3          ORdescriptor              3  M  3   M   3  M   3  M   3   N                3
3          ReportRequest             3  X  3   X   3  X   3  X   3   N                3
3          ReplyRequest              3  H  3   H   3  H   3  H   3   N                3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDADDDDDADDDDDDDADDDDDDADDDDDDADDDDDDDDDDDDDDDDDDDDY
                                                                  (Continued on next page.)

                 Table 7E.3  Protocol element comparison of P2, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDBDDDDDBDDDDDDDBDDDDDDBDDDDDDBDDDDDDDDDDDDDDDDDDDD?
3P2 Protocol                         3 NBS 3 A/311 3A/32113 TTC  3   PROBLEM (Y/N)    3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDEDDDDDEDDDDDDDEDDDDDDEDDDDDDEDDDDDDDDDDDDDDDDDDDD4
3MOTIS-> CirculationList             3     3       3      3      3                    3
3MOTIS->   CirculationMember         3     3       3  X   3      3   N                3
3MOTIS->   checkmark                 3     3       3  M   3      3   N                3
3MOTIS->   membername                3     3       3  M   3      3   N                3
3                                    3     3       3      3      3                    3
3MOTIS-> OBsoletingTime              3     3       3      3      3                    3
3MOTIS->   Time                      3     3       3  H   3      3   N                3
3MOTIS->   IP_MessageID              3     3       3  H   3      3   N                3
3                                    3     3       3      3      3                    3
3        Body                        3     3       3      3      3                    3
3          BodyPart                  3  G  3   M   3  M   3  G   3  Y Conformance (US)3
3                                    3     3       3      3      3                    3
3        SR_UAPDU                    3     3       3      3      3                    3
3          NonReceipt                3  H  3   H   3  H   3 D?   3   N                3
3                                    3     3       3      3  CDM 3                    3
3          Receipt                   3  H  3   H   3  H   3 DY   3   N                3
3          Reported                  3  M  3   M   3  M   3  M   3   N                3
3          ActualRecipient           3  R  3   R   3  R   3  G   3   N                3
3          IntendedRecipient         3  H  3   H   3  H   3  H   3   N                3
3          Converted                 3  X  3   X   3  X   3  G   3   N                3
3MOTIS->   CirculationStatus         3     3       3  X   3      3   N                3
3                                    3     3       3      3      3                    3
3        NonReceiptInformation       3     3       3      3      3                    3
3          Reason                    3  M  3   M   3  M   3  M   3   N                3
3          NonReceiptQualifier       3  H  3   H   3  H   3  H   3   N                3
3          =expired (value)          3  0  3   0   3  0   3  0   3   N                3
3          =obsoleted (value)        3  1  3   1   3  1   3  1   3   N                3
3          =subscriptionTerminated   3  2  3   2   3  2   3  2   3   N                3
3MOTIS->   =timeobsoleted (value)    3     3       3  X   3      3   N                3
3          Comments                  3  H  3   H   3  H   3  X   3   N                3
3          returned                  3  H  3   X   3  X   3  X   3  Y Conformance (E) 3
3                                    3     3       3      3      3                    3
3        ReceiptInformation          3     3       3      3      3                    3
3          Receipt                   3  M  3   M   3  M   3  M   3   N                3
3          TypeOfReceipt             3  H  3   H   3  H   3  G   3   N                3
3          SupplementaryInfo         3  X  3   X   3  X   3  X   3   N                3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDADDDDDADDDDDDDADDDDDDADDDDDDADDDDDDDDDDDDDDDDDDDDY
                                                                  (Continued on next page.)

                 Table 7E.3  Protocol element comparison of P2, continued

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDBDDDDDBDDDDDDDBDDDDDDBDDDDDDBDDDDDDDDDDDDDDDDDDDD?
3P2 Protocol                         3 NBS 3 A/311 3A/32113 TTC  3   PROBLEM (Y/N)    3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDEDDDDDEDDDDDDDEDDDDDDEDDDDDDEDDDDDDDDDDDDDDDDDDDD4
3                                    3     3       3      3      3                    3
3        BODYPART SUPPORT            3     3       3      3      3                    3
3                                    3     3       3      3      3                    3
3        o IA5 Text                  3  G  3   G   3  G   3      3   N See Note 7     3
3        o TLX                       3  X  3   X   3  X   3      3   N                3
3        o Voice                     3  X  3   X   3  X   3      3   N                3
3        o G3FAX                     3  X  3   X   3  X   3      3   N                3
3        o TIFO                      3  X  3   X   3  X   3      3   N                3
3        o TTX                       3  X  3  X/H  3  X   3      3Y Conf(US)See Note 23
3        o VideoTex                  3  X  3   X   3  X   3      3   N                3
3        o NationallyDefined         3  X  3   X   3  X   3      3   N                3
3        o Encrypted                 3  X  3   X   3  X   3      3   N                3
3        o ForwardedIPmessage        3  H  3   H   3  H   3      3   N                3
3        o SFD                       3  X  3   X   3  X   3      3   N                3
3        o TIFI                      3  X  3   X   3  X   3      3   N                3
3                                    3     3       3      3      3                    3
3MOTIS-> o ODA                       3     3       3  X   3      3   N                3
3MOTIS-> o ISO6937 Text              3     3       3  H   3      3   N                3
3                                    3     3       3      3      3                    3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDADDDDDADDDDDDDADDDDDDADDDDDDADDDDDDDDDDDDDDDDDDDDY

Note 1: It should be noted that the A/311 profile states:  For routing
        all ADMDs should support all Form 1 Variants of O/R Name.  All
        PRMDs should support at least Form 1, Variant 1 form of OR Name.

Note 2: It should also be noted that the A/311 profile requires that all
        ADMDs should support the reception of Teletex body parts for
        delivery to their own UAEs.

Note 3: An A/3211 implementation may generate MOTIS encoded information
        types.  See 7.6.11. 

Note 4: Only Form 1 Variant 1 of O/Rname shown for TTC, but TTC defines
        other forms and variants.  Form 1 Variant 1 recommended for PRMDs
        and ADMDs, Form 1 Variant 2 also recommended for ADMDs.

Note 5: DDA's can be used to specify recipients in any Japanese domains
        other than TTC.  Assignment of DDAs for UAs within TTC domains is
        not recommended.

Note 6: One of [DeliveredInfo/NonDeliveredInfo] must be present.  TTC
        encodes this as shown.  Other profiles represent this by
        classifying both protocol elements as generatable.  A similar
        situation exists with the P2 ORdescriptor.

Note 7: TTC is expected to support IA5 for some international MHS
        communications.
  
7.16 APPENDIX F:    INTERWORKING WARNINGS

   ADMD name is to be encoded as a single space when configurations with
   no ADMD's are  present.  It should be noted that this may change in
   January 1988 so that the ADMD name is encoded as a zero length element
   in such cases.

   The NBS agreements allow implementation to generate MPDUs with no
   body parts.  Such MPDUs will be rejected by European-conformant
   systems.  (Note this situation may change in January 1988)

   In order to optimize the number of recipients you can read and reply
   to, it is advisable to be able to generate all standard O/R name
   attributes.


8. DIRECTORY SERVICES PROTOCOLS

   8.1  INTRODUCTION

   This is an Implementation Agreement developed by the Implementor's
   Workshop sponsored by the U.S. National Bureau of Standards to promote
   the useful exchange of data between devices manufactured by different
   vendors.  This agreement is based on and employs protocols developed
   in accord with the OSI Reference Model.  While this agreement
   introduces no new protocols, it eliminates ambiguities in
   interpretations.

   This is an Implementation Agreement for Directories based on the ISO
   documents cited in the Reference Section 11.1 (hereafter referenced as
   Directory documents).  Versions of this document will stay consistent
   with the latest drafts of those Directory Documents.  Figure 8.1
   displays the structure of this Implementation Agreement.  References
   to corresponding CCITT documents are included for information.

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
3    Directory Access Protocol     3    Directory System Protocol     3
3              (DAP)               3              (DSP)               3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDADDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3              Remote Operations Services and Protocols               3
3            (CCITT X.219 and X.229/ISO 9072/1 and 9072/2)            3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD4
3             Association Control Services and Protocols              3
3             (CCITT X.217 and X.227/ISO 8649 and 8650)               3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

         Figure 8.1  Structure of this Implementation Agreement


   The Directory User Agents (DUAs) and Directory System Agents (DSAs)
   provide access to the Directory on behalf of humans and applications
   such as Message Handling and File Transfer, Access, and Management. 
   See the Scope and Field of Application section for more information on
   the model used in Directories.

   This document covers both the Directory Access Protocol (DAP) and the
   Directory System Protocol(DSP) defined in the Directory documents.  A
   good working knowledge of the Directory documents is assumed by this
   chapter.  All terminology and abbreviations used but not defined in
   this text may be found in those documents.


   8.2  SCOPE AND FIELD OF APPLICATION

   Centralized and distributed directories can both be accommodated in
   this Agreement by the appropriate choice of protocols and pragmatic
   constraints from those specified.  Figure 8.2 illustrates a
   centralized directory and Figure 8.3 illustrates a distributed
   directory.

   This agreement does not cover interaction between co-located entities,
   such as a co-resident DUA and DSA.  It also does not specify the
   interface  between a user (person or application) and a DUA. 
   Bilateral agreements between a DUA and DSA or DSA and DSA may be
   implemented in addition to the requirements stated in this document. 
   Conformance to this agreement requires the ability to interact
   without the use of bilateral agreements other than those required in
   the Directory documents.

   The logical structure of the Directory Information Base (DIB) is
   described in the Directory documents.  The manner in which a local
   portion of the DIB is organized and accessed by its DSA is not in the
   scope of this agreement.


       ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
       3                                                           3
       3                                   00000000000000000000000 3
       3                                   0   The Directory     0 3
       3                                   0                     0 3
       3                                   0    ZDDDDDDDDDDD?    0 3
       3 ZDDDDDDDDDDD?     ZDDDDDDDDDD?    0    3           3    0 3
       3 3   USER    3<DDD>3   DUA    3<DDD0DDD>3           3    0 3
       3 @DDDDDDDDDDDY     @DDDDDDDDDDY    0    3    DSA    3    0 3
       3 ZDDDDDDDDDDD?     ZDDDDDDDDDD?    0    3           3    0 3
       3 3   USER    3<DDD>3   DUA    3<DDD0DDD>3           3    0 3
       3 @DDDDDDDDDDDY     @DDDDDDDDDDY    0    @DDDDDDDDDDDY    0 3
       3                                   0                     0 3
       3                                   0                     0 3
       3                                   00000000000000000000000 3
       @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY     
                                                                         
                 Figure 8.2  Centralized Directory Model

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD? 
3                                                                     3 
3                              ZDDDDDDD?                              3  
3                              3 User  3                              3 
3                              @DDDBDDDY                              3 
3                                  3                                  3 
3                              ZDDDADDD?                              3 
3                              3  DUA  3                              3 
3                              @DDDBDDDY                              3  
3                                  3                                  3  
3ZDDDDDD?  ZDDDDDDD?0000000000000000000000000000000                   3  
33 User CDD4  DUA  30The Directory 3              0                   3  
3@DDDDDDY  @DDDDDDDY0              3              0                   3  
3                   0          ZDDDADDD?          0                   3  
3                   0          3  DSA  3          0                   3  
3                   0          @DDDDDDDY          0                   3  
3                   0ZDDDDDDD?           ZDDDDDDD?0                   3  
3                   03  DSA  3           3  DSA  30                   3  
3                   0@DDDDDDDY           @DDDDDDDY0                   3  
3ZDDDDDD?  ZDDDDDDD?0          ZDDDDDDD?          0ZDDDDDDD?  ZDDDDDD?3  
33 User CDD4  DUA  30          3  DSA  3          03  DUA  CDD4 User 33  
3@DDDDDDY  @DDDDDDDY0          @DDDDDDDY          0@DDDDDDDY  @DDDDDDY3  
3                   0000000000000000000000000000000                   3  
3                                                                     3  
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY  

                 Figure 8.3  Distributed Directory Model


   8.3  STATUS   

   This version was completed on December 18, 1987.


   8.4  Use of Directories

   Given the rapid multiplication and expansion of OSI applications,
   telecommunication systems and services, there is growing need for
   users of, as well as the applications themselves, to communicate with
   each other.  In order to facilitate their communications, a Directory
   protocol, as referenced in these agreements, has been tailored to meet
   their respective needs.

   In one instance, Directories will be used as a service to provide
   humans, in an on-line fashion, rapid and easy retrieval of information
   useful for determining what telecommunications services are available,
   and/or how to access, and address their correspondents.  Further,
   service providers offering such a Public Directory may also use this
   service internally with other various telecommunications services
   (e.g., MHS) for the proper addressing of calls or messages.  Likewise,
   this does not preclude the usage of these agreements to similarly
   generate a privately operated Directory that supports both human and
   application information exchanges.

   In another instance, Directories, will be used as a service by
   computer applications without direct human involvement.  One important
   service is to provide Presentation Address resolution for named
   objects, on behalf of OSI applications.  The directory may be used by
   applications to search for objects (i.e., Application Entities),
   without direct human involvement, by the use of the "search" or
   "list" operations.

   To support the many possible usages, the Directory is a general
   purpose system.  It is capable of storing data of many different
   forms as attributes within entries, and is also capable of supporting
   simple or complex hierarchical structures, with variations in
   structure possibly occurring between one part of the Directory and
   another.

   Compliant DSA implementations should safeguard this generality, where
   possible, by placing the minimum of restrictions in "hard-wired"
   form.  The Directory permits the imposition of rules by means of the
   Directory Schema (Section 8.6 below);  but the Directory Schema
   itself should be capable of alteration by Directory management.


   8.5  Directory ASEs, Application Contexts, and Ports

   The following section is included for tutorial purposes.  The
   functionality of the Directory AEs (DUAs and DSAs) is defined by a set
   of ASEs, each Directory ASE specifying a set of Directory operations.

   The interaction between these AEs is described in terms of their use
   of ASEs.  This specific combination of a set of ASEs and the rules for
   their usage defines an application context. 

   Thus, each Directory application context defines the operations needed
   by two communicating Directory entities.

   Access to the services provided by an application context is through
   one or more directory ports.  The point of access is called an Access
   Point (see Figure 8.4).  Each access point corresponds to a
   particular combination of port types.

   The following ASEs are described in the Directory Document:

        o    Directory Read ASE
        o    Directory Chained Read ASE
        o    Directory Search ASE 
        o    Directory Chained Search ASE 
        o    Directory Modify ASE 
        o    Directory Chained Modify ASE    

   ROSE and ACSE also form part of the Directory Application Contexts. 

   The following Application Contexts are described in the Directory
   Document:

        o    Directory Access Application Context
        o    Directory System Application Context


   The following Ports are described in the Directory Document:

        o    Read Port 
        o    Modify Port 
        o    Search Port 
        o    Chained Read Port 
        o    Chained Search Port 
        o    Chained Modify Port

   The ports cited above are to be specified for a particular Access
   Point to the Directory as illustrated by Figure 8.4.
                                                            
      ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
      3               Access Point DDDDDDDDD?                    3
      3                                     3                    3
      3 ZDDDDDDDDDDDDDDDD?                  3ZDDDDDDDDDDDDDDD?   3
      3 3                3                  33               3   3
      3 3 Directory ZDDDDADDDDD?            33               3   3
      3 3 user      3          3            3    The        3   3
      3 3           3   DUA    CDDDDDDDDDDDDD4    Directory  3   3
      3 3           3          3             3               3   3
      3 3           @DDDDBDDDDDY             3               3   3
      3 3                3                   3               3   3
      3 @DDDDDDDDDDDDDDDDY                   @DDDDDDDDDDDDDDDY   3
      @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

                   Figure 8.4  Access to the Directory



   8.6  Schemas

   There are four (4) major topics that relate to schemas:

        8.6.1     Maintenance of Structures and Naming Rules

        DSAs shall be capable of supporting the object classes and the
        associated structure and naming rules defined in the Directory
        documents, part 7, annex B, in the sense that DITs may be
        constructed and within these rules shall be supported.


        8.6.2     Maintenance of object classes and subclasses

        DSAs shall be able to support the storage and use of the
        following object classes defined in the Directory documents part
        7, annex B:

                  top                      alias
                  country                  application entity
                  locality                 organizational-person
                  organization             residential-person
                  organizational unit      application-process
                  DSA

        Use of the modification and local extension mechanisms provided
        by registered and unregistered object classes is optional.


        8.6.3     Maintenance of Attribute Types

        DSAs shall be able to support the storage and use of attribute
        type information, as defined in Part 6, including their use in
        naming and access to entries;  they shall also support the
        definition of new attribute types, making use of pre-existing
        attribute syntaxes.


        8.6.4     Maintenance of Attribute Syntaxes

        Suggested methods for the interpretation of selected Attribute
        Syntaxes are defined in Appendix B.


   8.7  Classification of Support for Attribute Types

   This section classifies directory support for selected attribute type
   specified in the Directory documents.

   Classification of support for selected attribute types is either
   mandatory or optional.


        8.7.1     Mandatory Support

        The Directory must be able to support these Attribute Types:

             Aliased Object Name      Postal Address
             Business Category        Postal Code
             Common Name              Preferred Delivery Mode
             Country Name             Presentation Address
             Locality Name            Role Occupant
             ISDN Address             See Also
             Member                   Serial Number
             Object Class             State or Province Name
             Organization Name        Street Address
             Organizational Unit Name Supported Application Context
             Owner                    Surname 
             Post Office Box          Telephone Number
                                      Title
                                      User Password
                                      X.121 Address


        Note:     Support of these Attribute Types implies full support
                  of the relevant Attribute Syntaxes.


        8.7.2     Optional Support

        Directory support of these attribute types is considered
        optional:

             Authority Revocation List
             CA Certificate
             Certificate Revocation List
             Description 
             Destination Indicator 
             Facsimile Telephone Number
             Knowledge Information
             Non-Basic Parameters
             Physical Delivery Office Name
             Registered Address
             Search Guide
             Teletex Terminal Identifier 
             Telex Number
             User Certificate 



        Note:     DSAs should consider initial support of the Attribute
                  Syntax relevant to any Attribute Type for which future
                  support is planned, in addition to those required for
                  mandatory Attribute Types.


   8.8  Introduction to Pragmatic Constraints

   The following sections of this document define the pragmatic
   constraints to which a conformant implementation must adhere in
   addition to those specified in the Directory documents.  The pragmatic
   constraints are divided into two areas.  The first includes those
   aspects of pragmatic constraints which apply to the scope of service. 
   The second includes those aspects of pragmatic constraints which are
   specific to particular attribute types.


   8.9  General Constraints


        8.9.1     Character Sets

        It is a requirement to support all character sets and other name
        forms defined in the Directory Documents Part 6.  Those
        character sets include: 

             o    T.61
             o    PrintableString
             o    NumericString


        8.9.2     APDU Size Considerations

        In the process of chaining requests it is possible that a
        chaining DSA may receive invoke or return APDUs that exceed its
        capacity:

                                                               
         ZDDDDDDDDD?       2k      ZDDDDDDDDD?      2k        ZDDDDDDDDD?
         3         CDDDDDDDDDDDDDD>3         CDDDDDDDDDDDDDDD>3         3
         3   DUA   3               3   DSA   3                3   DSA   3
         3         3<DDDDDDDDDDDDDD4       ZDE<DDDDDDDDDDDDDDD4         3
         @DDDDDDDDDY      37K      @DDDDDDDEDY       33K      @DDDDDDDDDY
                  DSA may pass on              DSA may discard


                        Figure 8.5  APDU Exchange


        It is a minimum requirement that invoke and return result APDUs
        must be accepted unless they exceed 32767 octets in size;  in
        this case they may be discarded as illustrated in the right side
        of figure 8.5, and an "unwillingToPerform" error reporting
        service shall be used.


        8.9.3     Service Control (SC) Considerations

        This agreement recognizes that DUAs may automatically supply
        defaults for any SC parameter.  The choice of default values
        selected (if any) is seen to be a matter of local policy and
        consumer needs.


        8.9.4     Priority Service Control

        Priority is specified as a service control argument in the
        Directory documents.  The following statements represent a
        clarification of the semantics that may be used by a DSA in
        interpreting and operating on this parameter.

        The logical model in Figure 8.6 may be considered as an example
        by DSAs that implement this Service Control.

             o    The DSA maintains three logical queues corresponding to
                  the three priority levels.

             o    The DSA Scheduler is separate and distinct from any
                  scheduling function provided by the underlying
                  operating system or control program services.

             o    The DSA Scheduler presents jobs to the Underlying
                  Operating Services for execution and always presents
                  jobs of a higher priority before those of a lower
                  priority.

             o    The DSA Scheduler will not preempt a request once it
                  has been passed to the underlying operating system
                  service.

       ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
       3                                                           3
       3        ZDDDDDDDDDDDDDDDD?      ZDDDDDDDDDDDDD?            3
       3   ZDDD>3     High       CDDDDD>3                         3
       3   3    @DDDDDDDDDDDDDDDDY      3          ZDDDDDDDDDDD?   3
       3   3    ZDDDDDDDDDDDDDDDD?      3          3 DSA       3   3
       3   CDDD>3     Medium     CDDDDD>3          3 Scheduler 3   3
       3   3    @DDDDDDDDDDDDDDDDY      3          @DDBDDDDDDDDY   3
       3   3    ZDDDDDDDDDDDDDDDD?      3             3            3
       3   CDDD>3     Low        CDDDDD>3             3            3
       3   3    @DDDDDDDDDDDDDDDDY                                3
       3ZDDADDDDDDDDDDDDDDDD?                   ZDDDDDDDDDDDDDDD?  3
       33 Underlying        3                   3 Underlying OS 3  3
       33 Protocol Services 3                   3 Services      3  3
       3@DDDDDDDDDDDDDDDDDDDY                   @DDDDDDDDDDDDDDDY  3
       @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY

             Figure 8.6  Logical DSA Application Environment


   8.10 Constraints on Operations

   There are no overall constraints upon service arguments or results
   except those implied in section 8.9.2 of this document.


        8.10.1    Filters

        It is required that DSAs, at a minimum, support 8 nested
        "Filter" parameters, and a total limit of 32 Filter Items.  If
        these limits are exceeded, the recipient of that SearchArgument
        may return the ServiceProblem "unwillingToPerform".


        8.10.2    Errors

        There are no constraints upon any Error service except the APDU
        size limit as defined in section 8.9.2.

   8.11 Constraints on Attribute Types

   This section defines the pragmatic constraints specific to particular
   attribute types.


        8.11.1    Attribute Values

        This section describes the pragmatic constraints for attribute
        values.  Each constraint is given in terms of a Length
        Constraint.  The Length Constraint for a given attribute value is
        the number of units which a sending entity must not exceed and
        which a receiving entity must accept and process.  A sending
        entity need not be capable of sending attribute values as large
        as the Length Constraints.

        Use of Pragmatic Constraints for Strings

        The Length Constraint for strings is expressed as the number of
        allowable characters and the number of allowable octets.  When
        using the Printable String ASN.1 data type, the number of octets
        equals the number of characters.  When using the T.61 ASN.1 data
        type, the number of octets is twice the number of characters. 
        This is because some T.61 characters occupy two octets per
        character.

        Attribute Types

        Table 8.1 specifies the pragmatic constraints for selected
        attribute types specified in the Directory documents; many of
        these constraints also appear and are the same in the CCITT
        version of the Directory documents.

        Alphabets

        T.61 Strings used as attribute values shall only encode graphic
        characters and spaces.  (They must not contain formatting
        characters (such as subscript) or other control characters.

           Table 8.1  Pragmatic Constraints for Selected Attributes. 

 ZDDDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDBDDDDDDDDBDDDDDDDDDBDDDDDDDDDBDDDDDDDDDDDDDDD?
 3 Attribute Type   3   Content   3 Number 3  Number 3  Status 3  Notes        3
 3                  3             3 of     3  of     3         3               3
 3                  3             3 Print- 3  Allow- 3         3               3
 3                  3             3 able   3  able   3         3               3
 3                  3             3 Char-  3  Octets 3         3               3
 3                  3             3 acters 3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4 
 3 Object Class     3   Object    3        3   256   3         3               3
 3                  3   Identifier3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Common Name      3   T.61 or   3   64   3   128   3         3  X.500        3
 3                  3   Printable 3        3         3         3               3
 3                  3   String    3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4 
 3 Serial Number    3   Printable 3   64   3    64   3         3  X.500        3
 3                  3   String    3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4 
 3 Country Name     3   Printable 3        3         3         3  ISO 3166     3
 3                  3   String    3   2    3    2    3         3  String only  3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Locality         3   T.61 or   3  128   3   256   3         3  X.500        3
 3                  3   Printable 3        3         3         3               3
 3                  3   String    3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Postal           3   T.61 or   3 30 x 6 3  60 x 6 3         3  Note 4       3
 3 Address          3   Printable 3        3         3         3  X.500 & UPU  3
 3                  3   String    3        3         3         3               3
 3                  3             3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4 
 3 Postal Code      3   T.61 or   3   40   3    80   3         3  UPU          3
 3                  3   Printable 3        3         3         3  X.500        3
 3                  3   String    3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Organization     3   T.61 or   3   64   3   128   3         3  X.500        3
 3 Name             3   Printable 3        3         3         3               3
 3                  3   String    3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Organizational   3   T.61 or   3   64   3   128   3         3  X.500        3
 3 Unit Name        3   Printable 3        3         3         3               3
 3                  3   String    3        3         3         3               3
 @DDDDDDDDDDDDDDDDDDADDDDDDDDDDDDDADDDDDDDDADDDDDDDDDADDDDDDDDDADDDDDDDDDDDDDDDY

     Table 8.1  Pragmatic Constraints for Selected Attributes.  (continued)

 ZDDDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDBDDDDDDDDBDDDDDDDDDBDDDDDDDDDBDDDDDDDDDDDDDDD?
 3 Attribute Type   3   Content   3 Number 3  Number 3  Status 3  Notes        3
 3                  3             3 of     3  of     3         3               3
 3                  3             3 Print- 3  Allow- 3         3               3
 3                  3             3 able   3  able   3         3               3
 3                  3             3 Char-  3  Octets 3         3               3
 3                  3             3 acters 3         3         3               3 
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Title            3   T.61 or   3   64   3   128   3         3  X.500        3
 3                  3   Printable 3        3         3         3               3
 3                  3   String    3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Description      3   T.61 or   3 1024   3  2048   3         3  X.500 About  3
 3                  3   Printable 3        3         3         3  1 Screen full3
 3                  3   String    3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Search Guide     3             3        3         3         3  ffs          3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Business Category3   T.61 or   3   64   3   128   3         3               3
 3                  3   Printable 3        3         3         3               3
 3                  3   String    3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Facsimile Tele-  3   Facsimile 3        3   ffs   3         3  CCITT E.163  3
 3 phone Number     3   Telephone 3        3         3         3  X.500        3
 3                  3   Number    3        3         3         3  Includes G3  3
 3                  3             3        3         3         3  Non Basic    3
 3                  3             3        3         3         3  Parameters   3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 ISDN Address     3   Numeric   3  n/a   3  16+40  3         3  CCITT        3
 3                  3   String    3        3         3         3  E. 164 X.500 3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Presentation     3   Presen-   3  n/a   3   224   3         3Note 2,ISO 74983
 3 Address          3   tation    3        3         3         3X.500, & X.200 3
 3                  3   Address   3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Telephone        3   Printable 3   32   3    32   3         3  CCITT E.163  3
 3 Number           3   String    3        3         3         3  X.500        3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Teletex Terminal 3   Teletex   3        3    ffs  3         3  CCITT F.200  3
 3 Identifier       3   Terminal  3        3         3         3  X.500        3
 3                  3   Identifier3        3         3         3  Includes     3
 3                  3             3        3         3         3  Teletex Non  3
 3                  3             3        3         3         3  Basic        3
 3                  3             3        3         3         3  Parameters   3
 @DDDDDDDDDDDDDDDDDDADDDDDDDDDDDDDADDDDDDDDADDDDDDDDDADDDDDDDDDADDDDDDDDDDDDDDDY

      Table 8.1  Pragmatic Constraints For Selected Attributes. (continued)
 ZDDDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDBDDDDDDDDBDDDDDDDDDBDDDDDDDDDBDDDDDDDDDDDDDDD?
 3 Attribute Type   3   Content   3 Number 3  Number 3  Status 3  Notes        3
 3                  3             3 of     3  of     3         3               3
 3                  3             3 Print- 3  Allow- 3         3               3
 3                  3             3 able   3  able   3         3               3
 3                  3             3 Char-  3  Octets 3         3               3
 3                  3             3 acters 3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3                  3   Telex     3        3         3         3  CCITT X.500  3
 3 Telex Number     3   Number    3        3   ffs   3         3  X.121        3
 3                  3             3        3         3         3  Contains     3
 3                  3             3        3         3         3  telex-number,3
 3                  3             3        3         3         3  country code,3
 3                  3             3        3         3         3  answer back  3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 X.121 Address    3   Numeric   3   15   3   15    3         3  CCITT X.121  3
 3                  3             3        3         3         3  X.500        3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Member           3   Distin-   3        3         3         3  Note 3       3
 3                  3   guished   3        3         3         3               3
 3                  3   Name      3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Owner            3   Distin-   3        3         3         3  Note 3       3
 3                  3   guished   3        3         3         3               3
 3                  3   Name      3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Role             3   Distin-   3        3         3         3  Note 3       3
 3 Occupant         3   guished   3        3         3         3               3
 3                  3   Name      3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 See Also         3   Distin-   3        3         3         3  Note 3       3
 3                  3   guished   3        3         3         3               3
 3                  3   Name      3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 User             3   Octet     3  n/a   3   128   3         3X.500 Allow    3
 3 Password         3   String    3        3         3         3long passwords.3
 3                  3             3        3         3         3Machine        3
 3                  3             3        3         3         3Generated      3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Aliased Object   3   Distin-   3        3         3         3  Note 3       3
 3 Name             3   guished   3        3         3         3               3
 3                  3   Name      3        3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3 Knowledge        3   T.61 or   3  1024  3  2048   3         3  About 1      3
 3 Information      3   Printable 3        3         3         3  screen full. 3
 3                  3   String    3        3         3         3  ffs          3
 @DDDDDDDDDDDDDDDDDDADDDDDDDDDDDDDADDDDDDDDADDDDDDDDDADDDDDDDDDADDDDDDDDDDDDDDDY
      Table 8.1  Pragmatic Constraints For Selected Attributes. (continued)    
 ZDDDDDDDDDDDDDDDDDDBDDDDDDDDDDDDDBDDDDDDDDBDDDDDDDDDBDDDDDDDDDBDDDDDDDDDDDDDDD?
 3 Attribute Type   3   Content   3 Number 3  Number 3  Status 3  Notes        3
 3                  3             3 of     3  of     3         3               3
 3                  3             3 Print- 3  Allow- 3         3               3
 3                  3             3 able   3  able   3         3               3
 3                  3             3 Char-  3  Octets 3         3               3
 3                  3             3 acters 3         3         3               3
 CDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDEDDDDDDDDEDDDDDDDDDEDDDDDDDDDEDDDDDDDDDDDDDDD4
 3                  3             3        3         3         3               3
 3 Street Address   3   T.61 or   3        3         3         3UPU. Component 3
 3                  3   Printable 3        3         3         3of Postal      3
 3                  3   String    3        3         3         3Address        3
 @DDDDDDDDDDDDDDDDDDADDDDDDDDDDDDDADDDDDDDDADDDDDDDDDADDDDDDDDDADDDDDDDDDDDDDDDY


Notes:

   1.   The pragmatic constraints of these parameters are defined in
        other standards.  We will accommodate these values in our
        pragmatic constraints.

   2.   Presentation address is composed of "X" NSAP addresses, and
        three selectors, (20X + 32 + 16 + 16 ), e.g. if X = 1, this would
        be 84.  These numbers are based on the most recent implementor's
        agreements.  With 8 NSAP addresses this value is 224.

   3.   Pragmatic constraints are only applied to the individual
        components of DistinguishedName as defined in the Directory
        Documents Part 2.  Not all components of a DN will necessarily be
        understood by an implementation.

   4.   Implementors should be aware that constraints on Postal Address
        may not be sufficient for some markets.


   8.12 Conformance

   The following sections will describe various aspects of Directory
   conformance.  It should be noted that conformance to the various ASEs
   and conformance to the Authentication Framework are viewed as separate
   issues and are presented in that context.


        8.12.1    DUA Conformance

        Conformance requirements for DUAs are adequately specified in the
        Directory documents, Part 5, section 9.1.  It should be noted
        that DUA conformance can only be demonstrated by exercising the
        interface that it provides to its user.

        It is recognized that DUAs will be widely differing in nature:

        o    Some are intended to support human users, some application
             users     

        o    Particular DUAs may not support particular operations
             because the application that they support has no
             requirement;  others will be general purpose, and will
             support all operations.       

        o    Some DUAs will have a fixed view of the Directory content
             and structure, reflecting the usage of the Directory by a
             particular application;  others will have a more flexible
             view which can be adapted to new usages.     

        o    Some DUAs will provide automatic referral services with
             automatic establishment and release of associations;  others
             will place the burden on the user.       

        o    Some DUAs will provide a variety of authentication means; 
             others will support simple authentication only    

        o    Some DUAs will handle operations synchronously; others will
             have the capability of maintaining several identifiable
             dialogues with the Directory at one time.

        No general implementation agreements are spelled out in respect
        of these possibilities.


        8.12.2    DSA Conformance

        Basic conformance requirements for a DSA are defined in the
        Directory documents, Part 5, section 9.2.

        Centralized

        A centralized DSA is defined as one that contains its entire
        relevant DIT;  it follows that it will not make use of the DSP or
        generate referral responses.  Since this model only contains a
        single DSA it is not subject to DSA interworking issues and will
        always provide a consistent level of service and results.  A
        centralized DSA must be fully "protocol" conformant to the DAP.

        Cooperating

        In a distributed directory, responsibility for various portions
        of the DIT may be "distributed" among multiple DSAs.  On a per
        operation basis we define a DSA to be "holding" when it is
        responsible for the fragment of the DIB in which a given entry
        will appear if it exists;  we define a DSA to be "propagating"
        when it is unable to complete the name resolution process.  All
        DSAs must be capable of acting as a "holder" and a"propagator."


        8.12.3    Directory Systems Conformance Classes

        A DSA implementation shall satisfy the conformance requirements
        as defined in the Directory documents, part 5, section 9.2, and
        shall support the "Versions" argument of "Bind".

        Additionally, an implementation conformant to these agreements
        shall state which of the following conformance classes it
        implements:

        Conformance Class 0:  Centralized Directory

        A DSA implementation conformant to this class only supports the
        DirectoryAccessAC.  It must implement all operations in the Read
        and Modify ASEs.  Optionally, it may implement the operations in
        the Search ASE.

        A DSA that does not support the Search and List operations must
        reply to such operations with an unwillingToPerform service
        error.

        Conformance Class 1:  Distributed Directories

        A DSA implementation conformant to this class must implement all
        the operations in the ASEs that are part of the Application
        context for which it claims conformance.  It must support the
        DirectoryAccessAC  and it may optionally support the
        DirectorySystemAC.

        8.12.4    Authentication Conformance

        A Directory System may choose to implement various levels of
        authentication (Directory documents, Part 8).  We define the
        following four (4) levels of authentication in the DS:

        o    No authentication at all; (None)

        o    Identification of the remote peer entity only, without
             verification; (Weak)

        o    Simple authentication:  verified identification with or
             without a password.  Intended to make masquerading     
             difficult; and

        o    Strong authentication: identification with verification
             using cryptographic techniques intended to make
             masquerading, in practical terms, nearly impossible.

        The Authentication Framework document describes the specific goal
        of each authentication level;  we have listed several practical
        uses of the various levels:

        NONE      No authentication may be required for associations with
                  a DSA containing public information:  DSAs operating on
                  a private network in a controlled environment may
                  implicitly trust all connections and have no
                  requirement for authentication.

        WEAK      authentication may be desired to maintain access
                  statistics or in a private network where the initiator
                  is implicitly trusted and there is no need to incur
                  the additional overhead of more sophisticated
                  authentication methods.

        SIMPLE    authentication may be necessary in situations where
                  strong authentication is not practical, (i.e.:
                  international connections, no knowledge of algorithms
                  in use, etc).

        STRONG    authentication will be required for secure
                  environments.


        8.12.5    Authentication Conformance Classes

        We define the following two (2) conformance classes for the
        support of authentication:

             o    None, Weak,
             o    None, Weak, and Simple (unprotected)

        Consideration of protected simple and strong authentication is
        not part of this agreement.

   8.13 Distributed Operations

   The following requirements apply to DSAs supporting distributed
   operations:

   1.   DSAs must support the generation of referrals.

   2.   DSAs may additionally support chaining.  DSAs that only support
        chaining (i.e. no referrals) are not allowed.

   3.   DSAs supporting authentication (e.g. simple authentication by
        name and password) must be able to invoke DSP operations to carry
        out authentication by reference to other DSAs.  Thus all such
        DSAs  must support the DSP protocol.


        8.13.1    Referrals and Chaining

        It is recommended that a DSA which has chained a request act upon
        any referrals it receives rather that returning them to the
        requestor if the "PreferChaining" service control is present.


   8.14 Underlying Services


        8.14.1    ROSE

        It should be noted that support of "abandon" implies support of
        operation class 2.


        8.14.2    Session

        All directory implementations are required to support Session
        Version 2.  

   8.15 Access Control

   Guidelines relation to access control can be found in annex F of the
   Directory documents, part 2.

   8.16 Authentication

   Simple Authentication, as defined in Part 8 of the Directory
   documents, encompasses both Weak and Simple Authentication, as called
   for by section 8.12.  (This shall be taken to imply unprotected simple
   authentication.)

   A DSA that implements Simple Authentication as called for in section
   8.12, will check a user password, (if one is supplied) by means of a
   compare operation on the user's entry or otherwise; if no user
   password is supplied, the DSA will validate the presence of an entry
   for the user, by a read operation or otherwise; the authentication
   will fail if the password is incorrect, or if the user's entry does
   not exist.  DSP must be used when the user's entry is not a local
   entry; this form of authentication is therefore not normally
   appropriate for DAP only DSAs.

   A DSA that implements Weak Authentication will accept simple
   credentials without validating them.


   8.17 Test Considerations

   This section outlines some items that implementors may wish to
   consider in terms of testing expectations; additionally, future
   conformance testers may wish to consider these items when developing
   tests.

        8.17.1    Major elements of Architecture

        One important aspect of testing is to confirm the correct
        behavior of DSAs and DUAs in respect of major elements of the
        directory architecture.

        Such major elements include:

        o    Conformance Statement

        o    Distinguished names (e.g., name resolution, equivalence of
             various forms)

        o    Entries and Attributes (e.g., accessibility by operations,
             compliance with rules)

        o    Handling of distributed operations (e.g.,naming contexts
             and knowledge)

        o    Schemas

             -    Structure rules (e.g., storage and maintenance of
                  structure and of naming)

             -    Object classes and sub-classes (e.g., storage and
                  extension of rules for object attributes)

             -    Attribute types (e.g., storage and maintenance of
                  syntax classes and rules for multi or single valued
                  attributes)

             -    Attribute syntax (e.g. maintenance and support for
                  attribute value testing and matching, to specification
                  for a defined set of attribute types)

        o    Operations 

             -    all operations

             -    correct function

             -    correct result

             -    correct responses 

        o    Aliases (e.g., correct resolution, error responses)

        o    Authentication and Access Control (e.g., limitation of
             modify access)

        o    ROSE (e.g., correct handling of invokes, results, rejects,
             and invoke ids)

        o    ACSE (e.g., association establishment / refusal for invalid
             application contexts, etc.)


        8.17.2    Search Operation

        Testing of support for filter items should be reasonable.  It is
        not expected that DSAs will be able to handle worst case testing
        in this area.


   8.18 Errors

   This section provides clarification of the semantics of various
   operation errors and implementation guidelines on their usage.


        8.18.1    Permanent vs. Temporary Service Errors

        The usage of the Service Errors busy, unavailable and
        unwillingToPerform requires some clarification:

        The error busy is particularly transient.  It is returned when
        one or more of the Directory's internal resources are being used
        to their capacity and, hence, the requested operation cannot, for
        the moment, be performed.  The Directory should be able to
        recover from this type of resource depletion after a short while.

        The error unavailable is also temporary but somewhat less
        transient.  It indicates that the Directory (or some part of it)
        is currently unavailable and may continue to be unavailable for
        a reasonably long period of time.  for example, this error is
        returned when a given DSA is functionally disabled, or when a
        specific part of the DIB is undergoing reconfiguration.

        The error unwillingToPerform has a permanent connotation.  It
        indicates that the Directory cannot perform the requested
        operation because it would require resources beyond its capacity. 
        For example, this error may be returned by a DSA if, satisfying a
        requested would result in the generation of an APDU in excess of
        32767 octets.

   8.19 APPENDIX A     Definitions

   Any definitions not found in this appendix can be found in the
   Directory Documents.

        o    Holding

        o    Propagating

        o    Centralized 

        o    Cooperating

   8.20 APPENDIX B     Attributes and Object Classes

   The Contents of this section are incomplete.  Additional work
   describing algorithms related to schemas and special attribute types
   should be placed here.

   The attribute types defined in the Directory documents, Part 6, and
   listed in table 8.1 have requirements for underlying algorithms which
   relate: 

   1.   To the checking of attribute values from the viewpoint of
        syntactical correctness and compliance with pragmatic
        constraints.

   2.   To the comparison of attribute values for the purpose of
        comparison (for equality, for matching substrings, and as a
        preliminary for determining relative ordering)

   Sections B.1 and B.2 give brief characteristics of the checking and
   comparison algorithms, respectively.  These characteristics are not
   currently defined explicitly in the Directory documents.  Section B.3
   summarizes their applicability to the attribute syntaxes defined by
   the Directory documents.

   It should be noted that determining relative ordering requires the
   application of a further algorithm appropriate to the type of value
   which requires ordering.

   B.1  Checking Algorithms

   Note.  A particular attribute type in some cases defines more than one
   alternative attribute syntax.  In this case, an attribute value is
   satisfied if it satisfies at least one checking algorithm, as listed
   below; maximum and minimum sizes may be specified for the attribute-
   syntax or the attribute type.

   B.1.1     T.61 String Check

   Checks that the value has the type code for T.61 string, that it
   encodes a sequence of valid T.61 characters, and that it complies with
   a maximum character length, if this is specified.  Only graphic
   characters (including spaces) are permitted.

   B.1.2     Printable String Check

   Checks that the value has the type code for Printable String, and that
   it encodes as a sequence of valid printable string characters, and
   that it complies with a maximum character length, if this is
   specified.

   B.1.3     Numeric String Check

   Checks that the value has the type code for numeric string, that it
   encodes a sequence of valid numeric string characters, and that it
   complies with a maximum character length, if this is specified.

   B.1.4     Distinguished Name Check

   Checks that the value is a valid ASN.1 encoding for Distinguished
   name, and that for each known attribute type (i.e. that is registered
   in the DSA) each attribute value satisfies the appropriate checking
   algorithm.

   B.1.5     Object Identifier Check

   Checks that the type is correct.  It is further study whether the
   value itself can be validated further.

   B.1.6     Criteria Check

   Checks that the value is a valid ASN.1 encoding for Criteria.  It is
   for further study whether the value itself can be validated further.

   B.1.7     Presentation Address Check

   Checks that the value is a valid ASN.1 encoding for Presentation
   Address, and that each field is within the size limits appropriate to
   the field.

   B.1.8     Telephone Number Check

   For further study.

   B.1.9     Telex Number Check

   For further study.

   B.1.10    Facsimile Telephone Number Check

   Checks that the value of the first element is a valid telephone number
   (B.1.8), and that the second element is a valid ASN.1 encoding for 
   Facsimile G3 Non-Basic Parameters.

   B.1.11    Teletex Terminal Identifier Check

   Checks that the value of the first element is a valid Printable String
   (B.1.2), and that the second element is a valid ASN.1 encoding for
   Teletex Non-Basic Parameters.

   B.1.12    Integer Check

   Checks that the value has integer type, and lies between defined or
   default integer values.

   B.1.13    String List Check 

   Checks that each component is compliant using T.61 String Check or
   Printable String Check.

   B.1.14    Preferred Delivery Method Check

   For further study.

   B.1.15    Octet String Check

   No checking.

   B.1.16    Country Check

   Checks that the value is a 2-character string complaint with IS 3166
   codes only.

   B.2  Matching Algorithms

   Note:     Matching algorithms are conveniently defined in terms of a
             two step process.

   1.   Take the checked reference value and the value to be matched, and
        reduce them to a canonical (i.e. standard) form (normalization),
        if necessary.

   2.   Carry out the comparison in the specified way (e.g. equality,
        substrings or ordering)

   Important Note

   The brief descriptions below outline the first step.  The algorithms
   may be replaced, in a particular implementation, by equivalent
   procedures.

   B.2.1     String Match

   All the specific algorithms below carry out the following basic
   normalization:  remove leading and trailing spaces;  intermediate
   multiple spaces become single spaces.  For example
   "[sp]Time[sp][sp]Flies[sp][sp]" becomes "Time[sp]Flies".

   B.2.2     Case Ignore String Match

   The basic normalization just described is carried out;  in addition
   each lower case letter is converted to its upper case form.  The ASN.1
   value is compared octet by octet, disregarding type.  It is possible
   in this way to compare, for example, T.61 strings with Printable
   Strings.

   B.2.3     Case Exact String Match

   As above, but without the lower case to upper case conversion.

   B.2.4     ASN.1 Match

   The ASN.1 is converted to a standardized encoding forms, such as that
   given in Part 8 of the Directory documents, section 8.6.

   Two ASN.1 values may then be compared octet by octet, including the
   initial ASN.1 type.  No matching for substrings or order is possible.

   B.2.5     Distinguished Name Match

   As for ASN.1 match, except that for each AVA within the distinguished
   name, normalization takes place (possibly recursively) in accordance
   with the nature of the attribute type.

   B.2.6     Case Ignore  List Match

   Each component must match as for Case Ignore String Match.

   B.2.7     Criteria Match

   For further study.

   B.2.8     Telephone Number Match

   For further study.

   B.2.9     Telex Number Match

   For further study.

   B.3  Mapping of Attribute Syntaxes

   The following table maps the attribute syntaxes of Part 6 of the
   Directory documents, to the algorithms described in B.1 and B.2 :

  Syntax                       3Check                     3Match
DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDEDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD
                               3                          3
  undefined                    3None                      3None
  caseExactStringSyntax        3T.61 String Check or      3Case Exact String Match
                               3Printable String Check    3
  caseIgnoreStringSyntax       3T.61 String Check or      3Case Ignore String Match
                               3Printable String Check    3
  caseIgnoreListSyntax         3String List Check         3Case Ignore List Match
  numericStringSyntax          3Numeric String Check      3Case Exact String Match
  printableStringSyntax        3Printable String Check    3Case Exact String Match
  distinguishedNameSyntax      3Distinguished Name Check  3Distinguished Name Match
  objectIdentifierSyntax       3Object Identifier Check   3No normalization
  criteriaSyntax               3Criteria Check            3Criteria Match
  presentationAddressSyntax    3Presentation Address Check3Presentation Address Match
  telephoneNumberSyntax        3Telephone Number Check    3Telephone Number Match
  telexNumberSyntax            3Telex Number Check        3Telex Number Match
  countrySyntax                3Country Check             3Case Ignore String Match
  integerSyntax                3Integer Check             3No normalization
  octetStringSyntax            3Octet String Check        3No normalization
                               3                          3


   8.21 APPENDIX C     The Use of ROSE

   The use of ROSE by the BIND and UNBIND macros as described in the
   Directory documents, part 5, clause 8.2 will be used with no
   additional agreements.

   8.22 APPENDIX D     Guidelines

   The following guidelines were used to provide a general mechanism for
   arriving at pragmatic constraints within the Directory.  These are
   included for the reader's information.

   1.   Align with other activities

   2.   Catch outlandish behavior

             o    Infinite Loops

             o     Runaway Process

   3.   Conserve Resources and Promote Efficiency

             o    Memory
             o    CPU
             o    Bandwidth
             o    Effort

   4.   Compromise Arbitrary Opinions

   5.   Police Actions / Catch Violators

             o    Protect the Network

   6.   Facilitate Interworking

   7.   Syntax Interpretation

             o    Errors

   8.   Set practical limits for the purpose of testing
  8.23 APPENDIX EGlossary

   The following abbreviations may be useful; not all are used within
   these agreements.

   ACL            Access Control List
   ACSE           Association Control Service Element
   ADDMD          Administration Directory Management Domain
   AETitle        Application Entity Title
   APDU           Application Protocol Data Unit
   ASE            Application Service Element
   ASN.1          Abstract Syntax Notation - 1
   AVA            Attribute Value Assertion
   B-RM           Basic Reference Model
   CA             Certification Authority
   CCITT          Consultative Committee on International Telegraph &
                  Telephone
   CEN            Committee for European Normalization 
   CENELEC        Committee for European Normalization Electronique
   CEPT           Committee European Postal & Telephonique
   COS            Corporation for Open Systems
   DAP            Directory Access Protocol
   DIB            Directory Information Base
   DIT            Directory Information Tree
   DMD            Directory Management Domains
   DSA            Directory System Agent
   DSP            Directory System Protocol
   DUA            Directory User Agent
   EWOS           European Workshop for Open Systems
   FTAM           File Transfer, Access & Management
   INTAP          Interoperability Technical Association for Information
                  Processing, Japan
   ISDN           Integrated Services Digital Network
   ISO            International Organization for Standardization
   KT             Knowledge Tree
   LL             Lower layers of OSI model (layers 1-4)
   MAP            Manufacturing Automation Protocol
   MHS            Message Handling Systems
   NBS            National Bureau of Standards
   NSAP           Network Services Access Point
   OSI            Open Systems Interconnection
   PKCS           Public Key Crypto System
   POSI           Promotion for Open System Interconnection
   PRDMD          Private Directory Management Domain
   PSAP           Presentation Service Access Point
   RDN            Relative Distinguished Name
   ROSE           Remote Operations Service Element
   SIG            Special Interest Group
   SPAG           Standards Promotion & Application Group
   TOP            Technical and Office Protocols
   UL             Upper layers of OSI model (layers 5-7)
   UPU            Universal Postal Union

9. SECURITY

The Security Architecture specified in ISO 7498/Part 2 - Security
Architecture (as presented in ISO/TC 97/SC 21/N1528) shall be used as a
basis for further work in the Special Interest Group on Security.

The security services that are to be implemented first shall include
confidentiality, integrity, authentication and access control.  Non-
repudiation of the source shall also be included for consideration for
implementation.  These services are defined and discussed in more detail
in ISO 7498/Part 2 - Security Architecture.


   9.1  Definitions

   The following definitions, based on the definitions in ISO 7498/Part2,
   are to be used when interpreting Chapter 9.

        Access Control:               The provision of a security system
                                      that establishes and enforces which
                                      users or processes can get access
                                      to what data or processing
                                      facilities.

        Authentication 
        Information:                  Information used to establish the
                                      validity of a claimed identity.

        Authorization:                The granting of access rights.

        Confidentiality:              A security service that protects
                                      data from unauthorized disclosure.

        Connection:                   A state of communication that
                                      exists between two communicating
                                      entities by establishing an
                                      association between them, providing
                                      one or more data paths between them
                                      allowing sequential transfers of
                                      data, and then terminating the
                                      association.

        Connectionless:               A state of communication that
                                      provides transfer of data from one
                                      entity to another without a
                                      preestablished association.

        Data Integrity:               The property that data has not been
                                      altered or destroyed in an
                                      unauthorized manner.

        Data Origin 
        Authentication:               The corroboration that the source
                                      of data received is as claimed.

        Digital Signature:            Data that allows a recipient of
                                      information to verify the source
                                      and integrity of the information.

        Peer-entity 
        Authentication:               The corroboration that peer
                                      entities in an association are as
                                      claimed.

        Repudiation:                  Denial by one or both of the
                                      entities of an association of
                                      having participated in all or part
                                      of the association or
                                      communication of the association.

        Selective Field 
        Protection:                   The protection of specified fields
                                      of data in a communication.

        Traffic Analysis:             The inference of information from
                                      observation of traffic flow in
                                      communications (presence, absence,
                                      amount, direction and frequency).

        Traffic Flow
        Confidentiality:              A confidentiality service to
                                      protect against traffic analysis.
  

   9.2  Matrix of Security Services and OSI Layers

   The following matrix shows the layers of the OSI architecture at which
   certain security services are considered to be desirable.  The entries
   in the matrix are "H" for high level of desirability, "M" for medium
   desirability, and "L" for low level of desirability.  No entry in the
   matrix means that the service is not considered desirable.  This
   matrix was produced from a similar matrix in ISO 7498/Part 2 which
   showed the layers of the architecture that could be used to provide
   the security service.  The level of desirability was established by
   the members of the Special Interest Group in Security of the OSI
   Implementors Workshop.

   
   Note: The Matrix is a consensus of the opinions of the members as to
   where selected security services should be placed.  It should not be
   considered restrictive and interpreted as meaning that the security
   services cannot be placed elsewhere in the OSI architecture or have
   other implementation priorities. This will depend upon the differing
   security needs of specific applications.  Also, it should not be
   considered complete in that other security services may exist that
   should be incorporated in the architecture.



          Table 9.1  OSI Layers Desirable for Placing Security

ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDBDDDBDDDBDDDBDDDBDDDBDDDBDDD?
3                   SERVICE                    3 1 3 2 3 3 3 4 3 5 3 6 3 7 3
CDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDEDDDEDDDEDDDEDDDEDDDEDDDEDDD4
3                                              3   3   3   3   3   3   3   3
31.(a) Peer entity authentication              3   3   3 L 3 H 3   3   3 H 3
3  (b) Data origin authentication              3   3   3 L 3 L 3   3   3 H 3
3                                              3   3   3   3   3   3   3   3
32. Access Control Service                     3   Authorization Model 3   3
3                                              3   3   3   3   3   3   3   3
33.(a) Connection confidentiality              3 L 3 L 3 L 3 H 3   3 H 3 H 3
3  (b) Connectionless confidentiality          3   3 L 3 H 3 L 3   3 H 3 H 3
3  (c) Selective field confidentiality         3   3   3   3   3   3 H 3 H 3
3  (d) Traffic flow confidentiality            3 M 3   3 L 3   3   3   3 L 3
3                                              3   3   3   3   3   3   3   3
34.(a) Connection integrity with recovery      3   3   3   3 H 3   3   3 L 3
3  (b) Connection integrity without recovery   3   3   3 No Plan   3   3   3
3  (c) Selective field connection integrity    3   3   3 No Plan   3   3   3
3  (d) Connectionless integrity                3   3   3 H 3 L 3   3   3 L 3
3  (e) Selective field connectionless integrity3   3   3   3   3   3   3 H 3
3                                              3   3   3   3   3   3   3   3
35.(a) Non-repudiation:  originator            3   3   3   3   3   3   3 L 3
3  (b) Non-repudiation:  receiver              3   3   3   3   3   3   3 L 3
3                                              3   3   3   3   3   3   3   3
@DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDADDDADDDADDDADDDADDDADDDADDDY

Implementation priority:    H (high)  
                            M (medium) 
                            L (Low)

   Table 1  ISO 7498/Part 2:  Security Addendum -- NBS OSI Workshop
   Summary Of SIG-SEC Discussions of Security Service Placement, May,
   1987

   Notes: The following notes are for explanation of the above matrix and
   comments.

   A security system should be considered to be an integrated set of
   security services that are placed at selected OSI layers.  The
   services should be selected based on a risk analysis for the computer
   system being protected.  Security mechanisms must be then chosen that
   will provide the security services and incorporated in the software
   and hardware of the computer system and controlled by the OSI software
   and hardware at the selected layer(s).

   For example, authentication, access control, confidentiality and
   integrity are selected as the major security goals for an OSI system. 
   A connection oriented transport protocol is being implemented.  An
   example of the use of the Matrix could be in an electronic mail
   system, to illustrate this the following specific services and layers
   were chosen:

        Peer entity authentication:  Layer 4
        Data origin authentication:  Layer 7

        Access Control:  Layer 7

        Connection confidentiality:  Layer 4
        Selective field confidentiality:  Layer 7

        Connection integrity with recovery:  Layer 4
        Connectionless integrity:  Layer 7

   The layer 7 services were chosen to support the mail system that would
   protect the selective paragraphs of an electronic message as directed
   by the user.  A mail system is considered connectionless.  Access
   control is a function of only layer 7.

   The layer 4 services were chosen to provide a reliable transport
   service from the sender to the intended receive of the electronic
   message.  A full connection integrity and confidentiality service with
   peer entity authentication will assure that all information gets to
   the receiver correctly and confidentially.

   Note: The security protocols and mechanisms that provide these
   services are beyond the scope of this Chapter at this time.  The
   mechanisms and standards for their interoperability are presently
   being defined and will be added to this Chapter as they become
   available.

11.     REFERENCES

Selected references are grouped by organization publishing the documents
and by Reference Model layer to aid relating standards to the OSI Basic
Reference Model and to aid relating equivalent standards published by
different standards organizations.

10.     OBJECT IDENTIFIER: STRUCTURE AND ALLOCATION


   In order to complete a stable version of the NBS OSI Implementation
   Agreements, the following objects need to be administered by an ad
   hoc registration authority:

        Application Context Name
        Abstract Syntax Name
        Transfer Syntax Name
        Document Type Name
        Constraint Set Name
        File Model

   Since all objects to be administered by the NBS Workshop SIGs are
   identified by the ASN.1 type OBJECT IDENTIFIER, the following
   structure shall be used:

   Using the NameAndNumberForm (::= identifier (NumberForm) ) for an
   ObjIdComponent we have:

   ObjectIdentifierValue ::=     { identifier1 (NumberForm1) 
          identifier2 (NumberForm2)
          identifier3 (NumberForm3)
          identifier4 (NumberForm4)
          identifier5 (NumberForm5)
          identifier6 (NumberForm6) }

   The assignment of identifiers and NumberForms is as follows:


        identifier1                   NumberForm1

        iso                           1

        identifier2                   NumberForm2 

        identified-organization       3

        identifier3                   NumberForm3

        issuing-organization          9999

        identifier4                   NumberForm4

        organization-code             1

        identifier5                   NumberForm5

        application-context           1
        abstract-syntax               2
        file model                    3
        constraint-set                4
        document-type                 5
        transfer-syntax               6
        ftam-nil-ap-title             7


   Note 1:   The value of NumberForm3 is selected for use by implementors
             of these agreements: it has not been assigned by ISO or by
             any official Registration Authority.  It does correspond to
             an "ad hoc" issuing organization with an ICD of 9999, as
             specified by ISO 6523. We intend to use the procedure
             designated in D.7 of the Specification of ASN.1, ISO 8824
             once the appropriate Registration Authority has been
             established.  This mechanism is subject to change dependent
             upon ISO standards.

   Note 2:   Specific values for identifier6 and NumberForm6 are chosen
             as needed by the .  A table of the currently allocated
             values is given later.

   Note 3:   The NBS UL SIG will assign values for identifier5 and
             NumberForm5 as required by other SIGs.        

   Note 4:   Companies wishing to interoperate may designate themselves
             with an organization code other than 1 under
             { iso (1) identified-organization (3) -
             issuing-organization (9999) } for the purpose of defining
             private OBJECT IDENTIFIERs.

           Table 10.1  TABLE OF ALLOCATED OBJECT IDENTIFIERS

The values of the first 4 NumberForms are constant, so the following
value is defined for use in the table below.

        nbs-ad-hoc OBJECT IDENTIFIER ::= {1 3 9999 1}

Note that the only OBJECT IDENTIFIERS herein defined all begin with "nbs-
ad-hoc"; all other OBJECT IDENTIFIERS and their associated
ObjeceDescriptor's are reproduced here solely for the convenience of
implementors.  The standards defining these OBJECT IDENTIFIERSs and
ObjectDescriptor's take precedence over the values specified below.


Application Context
   
   "ISO FTAM"
        { iso (1) standard (0) 8571 application-context (1) iso-ftam (1)
        }

Abstract Syntax

   "FTAM PCI"
        { iso (1) standard (0) 8571 abstract-syntax (2) ftam-pci (1) }

   "FTAM FADU"
        { iso (1) standard (0) 8571 abstract-syntax (2) ftam-fadu (2) }

   "FTAM unstructured text abstract syntax"

        { iso (1) standard (0) 8571 abstract-syntax (2) unstructured-text
        (3) }

   "FTAM unstructured binary abstract syntax"

        { iso (1) standard (0) 8571 abstract-syntax (2) unstructured-
        binary (4) }

   "NBS abstract syntax AS1"

        { nbs-ad-hoc abstract-syntax (2) nbs-as1 (1) }

   "NBS file directory entry abstract syntax"

        { nbs-ad-hoc abstract-syntax (2) nbs-as2 (2) }

   "ISO 8650-ACSE1"

        { joint-iso-ccitt association-control (2) abstract-syntax (1)
        apdus (0) version1 (1) }

   "Directory Services"


File Model

   "FTAM hierarchical file model"
        { iso (1) standard (0) 8571 file-model (3) hierarchical (1) }


Constraint Set

   "FTAM unstructured constraint set"
        { iso (1) standard (0) 8571 constraint-set (4) unstructured (1) }

   "FTAM sequential flat constraint set"
        { iso (1) standard (0) 8571 constraint-set (4) sequential-flat
        (2) }
   "FTAM ordered flat constraint set"
        { iso (1) standard (0) 8571 constraint-set (4) ordered-flat (3) }

   "NBS ordered flat constraint set"
        { nbs-ad-hoc constraint-set (4) nbs_ordered-flat (3) }

Document Type

   "ISO FTAM unstructured text"
        { iso (1) standard (0) 8571 document-type (5) unstructured-text
        (1) }

   "ISO FTAM sequential text"
        { iso (1) standard (0) 8571 document-type (5) sequential-text (2)
        }

   "ISO FTAM unstructured binary"
        { iso (1) standard (0) 8571 document-type (5) unstructured-binary
        (3) }
   
   "NBS-6 FTAM sequential file"
        { nbs-ad-hoc document-type (5) sequential (6) }

   "NBS-7 FTAM random access file"
        { nbs-ad-hoc document-type (5) random-file (7) }

   "NBS-8 FTAM indexed file"
        { nbs-ad-hoc document-type (5) indexed-file (8) }

   "NBS-9 FTAM file directory file"
        { nbs-ad-hoc document-type (5) file-directory (9) }

Transfer Syntax

   " Basic Encoding of a single ASN.1 type"
        { joint-iso-ccitt (2) asn1 (1) basic-encoding (1) }


Miscellaneous

   "nil AP Title"
        { nbs-ad-hoc ftam-nil-ap-title (7) }


   10.1 Specific ASE Requirements for ACSE Presentation and Session

   The following list for each ASE the corresponding NBS SIGs
   requirements of and restrictions on ACSE, Presentation, and Session.

   All listed requirements and restrictions shall be included in an NBS
   conformant system and shall be implemented in accordance with these
   NBS Implementor's agreements.

   All OBJECT IDENTIFIERS are specified in terms of their associated
   ObjectDescriptor's.  See the chapter on OBJECT IDENTIFIERs for the
   values of the associated OBJECT IDENTIFIERs.


        10.1.1    FTAM


             10.1.1.1  Phase 2

                       ACSE Requirements:
                            all

                            Application Contexts:
                                 o    "ISO FTAM" - implies the use of the
                                      ACSE and the FTAM ASE.

                            Abstract Syntaxes:
                                 o    "ISO 8650-ACSE1"

                                      Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single ASN.1 type"

                       Presentation Requirements:

                            Presentation Functional Units:
                                 o    kernel

                            Presentation Contexts:
                                 o    At least 4 Presentation Contexts
                                      must be supported.

                            Abstract Syntaxes:

                                 o    "FTAM-PCI"

                                      Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single ASN.1 type:

                                 o    "FTAM-FADU"
                                      Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single ASN.1 type"


                                 o    "FTAM unstructured text abstract
                                      syntax"

                                      Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single ASN.1 type"

                                 o    "FTAM unstructured binary abstract
                                      syntax"

                                      Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single Asn.1 type"

                                 o    "NBS abstract syntax AS1"

                                      Associated Transfer Syntax:
                                           o    "Basic Encoding  of a
                                                single ASN.1 type"

                                 o    "NBS file directory entry abstract
                                      syntax"

                                      Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single Asn.1 type"

                                 o    "NBS file directory entry abstract
                                      syntax"

                                      Associated Transfer Syntax:
                                           o    "Basic Encoding of a
                                                single Asn.1 type"


                       Session Requirements:

                            Session Functional Units:
                                 o    kernel
                                 o    duplex

                            Version Number: 2

                            Maximum size of User Data parameter field:
                            10,240


                       Session Options:

                            Session Functional Units:
                                 o    resynchronize
                                           only a Resynchronize Type
                                           value of "abandon"

                                 o    minor synchronize
                                           Note:     The minor
                                                     synchronize
                                                     functional unit is
                                                     required whenever
                                                     the resynchronize
                                                     functional unit is
                                                     available.


        10.1.2    MHS


             10.1.2.1  Phase 1

                       Session Requirements:

                            Session Functional Units:
                                 o    kernel
                                 o    half-duplex
                                 o    exceptions
                                 o    activity management
                                 o    minor synchronize

                            Version Number: 1

                            Maximum size of User Data parameter field:
                            512

                            Session Notes:
                                 o    Restricted use is made by the RTS
                                      of the session services implied by
                                      the functional units selected. 
                                      Specifically,

                                      .    No use is made of S-TOKEN-
                                           GIVE, and
                                      .    S-PLEASE-TOKENS only asks for
                                           the data token.

                                 o    In the S-CONNECT SPDU, the Initial
                                      Serial Number should not be
                                      present.

                                 o    The format of the Connection
                                      Identifier in the S-CONNECT SPDU is
                                      described in Version 5 of the
                                      X.400-Series Implementors' Guide.

        10.1.3    DS


             10.1.3.1  Phase 1


                       ACSE Requirements:
                            all

                            Application Context:

                            Abstract Syntaxes:
                                 o    "ISO 8650-ACSE1"
                                           Associated Transfer Syntax:
                                                o    "Basic Encoding of a
                                                     single ASN.1 type"

                                 o    "Directory Services"
                                           Associated Transfer Syntax:
                                                o    "Basic Encoding of a
                                                     single ASN.1 type"

                       Presentation Requirements:

                            Presentation Functional Units:
                                 o    kernel

                            Presentation Contexts:
                                 o    At least 2 Presentation Contexts
                                      must be supported.

                       Session Requirements:

                            Session Functional Units
                                 o    kernel
                                 o    duplex

                            Version Number:2

                            Maximum size of User Data parameter field:
                            10,240


11.1    CCITT

Network Layer

CCITT Recommendation X.25 - 1980, Interface Between Data Terminal
Equipment (DTE) and Data Circuit-Terminating Equipment (DCE) for
Terminals Operating in the Packet Mode on Public Data Networks.

CCITT Recommendation X.25 - 1984, Interface Between Data Terminal
Equipment (DTE) and Data Circuit-Terminating Equipment (DCE) for
Terminals Operating in the Packet Mode on Public Data Networks.


Transport Layer
 
CCITT Recommendation X.214, (Red Book, 1984), Transport Service
Definition for Open Systems Interconnection for CCITT Applications.

CCITT Recommendation X.224, (Red Book, 1984), Transport Protocol Profile
for Open Systems Interconnection for CCITT Applications.


Session Layer

CCITT Recommendation X.215, (Red Book, 1984), Session Service Definition
for Open Systems Interconnection for CCITT Applications.

CCITT Recommendation X.225, (Red Book, 1984), Session Protocol Profile
for Open Systems Interconnection for CCITT Applications.


Presentation

CCITT Recommendation T.50, (Red Book, 1984), International Alphabet No.
5.


Application Layer -- MHS

CCITT Recommendation X.400, (Red Book, 1984), Message Handling Systems:
System Model-Service Elements.

CCITT Recommendation X.401, (Red Book, 1984), Message Handling Systems:
Basic Service Elements and Optional User Facilities.

CCITT Recommendation X.408, (Red Book, 1984), Message Handling Systems:
Encoded Information Type Conversion Rules.

CCITT Recommendation X.409, (Red Book, 1984), Message Handling Systems:
Presentation Transfer Syntax and Notation.

CCITT Recommendation X.410, (Red Book, 1984), Message Handling Systems:
Remote Operations and Reliable Transfer Server.

CCITT Recommendation X.411, (Red Book, 1984), Message Handling Systems:
Message Transfer Layer.

CCITT Recommendation X.420, (Red Book, 1984), Message
Handling Systems: Interpersonal Messaging User Agent Layer.

CCITT Recommendation X.430, (Red Book, 1984), Message Handling Systems:
Access Protocol for Teletex Terminals.



11.2    ISO

Status of ISO work can be determined by the reference number; working
drafts are referenced by committee and number; e.g., TC 97/SC 6 Nxxxx.
Standards are cited by either ISO xxxx or IS xxxx; DIS and DPs are cited
in similar form.  Note: ISO TC 97 is now called ISO/IEC JTC1.

Information Processing Systems - Open Systems Interconnection - Basic
Reference Model.  ISO/IS 7498.  First Edition - Oct. 15, 1984. Ref. No.
ISO 7498-1984(E).

OSI Basic Reference Model - Part 2:  Security Architecture.  ISO/DIS
7498-2 TC 97/SC 21/N1895. Project 97.21.18. May 1987.

OSI Basic Reference Model - Part 3:  Naming and Addressing. ISO/DIS 7498-
3, ISO/TC 97/ SC 21 N2141. May, 1987.

Data Interchange - Structure for the identification of organizations. 
ISO 6523.  1984-02-01.


Physical Layer

Information Processing Systems - Local Area Networks - Part 3:  Carrier
Sense Multiple Access with Collision Detection (CSMA/CD) and Physical
Layer Specification ISO/DIS 8802/3

Information Processing Systems - Local Area Networks - Part 4: 
Token-Passing Bus Access Method and Physical Layer Specification,
ISO/DIS 8802/4

Information Processing Systems - Local Area Networks - Part 5: Token-Ring
Access Method and Physical Layer Specification ISO/DIS 8802/5

ISO 8802-5 Final Text of ISO/DIS 8802-5: Info proc systems - Local Area
Nets -Part 5: Token ring access method and physical layer specification,
ISO/TC 97/SC 6 N4477,1987

Data Link Layer

Information Processing Systems - Local Area Networks - Part 2: Logical
Link Control ISO/DIS 8802/2 1985

ISO 8802-2 Text for ISO/DIS 8802-2.2, Logical Link Control, ISO/TC 97/SC
6 N4609, 1987

Information Processing Systems - Data Communications - High-Level Data
Link Control Procedures - Description of the X.25 LAPB-compatible DTE
Data Link Procedures, IS 7776.

Network Layer

Information Processing Systems - Open Systems Interconnection - Network
Service Definition, IS 8348.

Information Processing Systems - Open Systems Interconnection - Addendum
to the Network Service Definition Covering Connectionless Data
Transmission, IS 8348/AD1.

Information Processing Systems - Open Systems Interconnection - Addendum
to the Network Service Definition Covering Network Layer Addressing,
IS 8348/AD2.

Information Processing Systems - Open Systems Interconnection - Internal
Organization of the Network Layer, DIS 8648.

Information Processing Systems - Open Systems Interconnection - Protocol
for Providing the Connectionless Network Service, IS 8473.

Information Processing Systems - Open Systems Interconnection -Addendumto
IS 8473 - Provision of the Underlying Service Assumed by ISO 8473, ISO TC
97/SC 6 N 3453.

Information Processing Systems - Open Systems Interconnection, Working
Draft, End System to Intermediate System Routing Exchange Protocol for
use in Conjunction with ISO 8473  ISO/DIS 9542 TC 97/SC 6 N 4053.

Information Processing Systems - Open Systems Interconnection - Data
Communications - X.25 Packet Level Protocol for Data Terminal Equipment,
IS 8208.

Information Processing Systems - Open Systems Interconnection - Data
Communications - Use of X.25 to provide the OSI Connection-mode Network
Service DIS 8878


Transport Layer

Information Processing Systems - Open Systems Interconnection - Transport
Service Definition, IS 8072.

Information Processing Systems - Open Systems Interconnection - Transport
Protocol Specification, IS 8072, 1984.


Session Layer

Information Processing Systems - Open Systems Interconnection - Basic
Connection Oriented Session Service Definition, ISO 8326: 1987 (E).
 
Information Processing Systems - Open Systems Interconnection - Basic
Connection Oriented Session Protocol Specification, ISO 8327 8326: 1987
(E).

Information Processing Systems - OSI - Basic Oriented Session Service
Definition - DAD 2 to ISO 8326 to Incorporate Unlimited User Data,
ISO/IS 8326. Aug. 27, 1987.

Information Processing Systems - OSI - Basic Oriented Session Protocol
Specification - DAD 2 to ISO 8327 to Incorporate Unlimited User Data,
ISO/IS 8327. Aug. 27, 1987.

Information Processing Systems - Open Systems Interconnection - Basic
Connection Oriented Session Service Definition-AD 2 to ISO 8326 to
Incorporate Unlimited User Data, ISO/IEC JTC1/SC21 N2494.

Information Processing Systems - Open Systems Interconnection - Basic
Connection Oriented Session Protocol Specification - AD 2 to ISO 8327 to
Incorporate Unlimited User Data, ISO/IEC JTC1/SC21 N2495.


        Note:     The Session DAD2 Documents This Document, SC21 1987,
                  may also be obtained from:

                       Standards Resource Librarian
                       AT&T Bell Labs
                       IM304
                       Crawfords Corner Rd.
                       Holmdel, NJ
                       07733

Presentation Layer

Information Processing Systems - Open Systems Interconnection -
Connection-Oriented Presentation Service Definition, ISO 8822:  1987 (E),
(ISO/TC97/SC21 N 2335).  Note: until final text is available, reference
Proof G.

Information Processing Systems - Open Systems Interconnection -
Connection Oriented Presentation Protocol Specification, ISO 8823:  1987
(E), (ISO/TC97/SC21 N 2336).  Note: until final text is available,
reference Proof G.

Information Processing Systems - Open Systems Interconnection -
Specification of Abstract Syntax Notation One (ASN.1), ISO 8824:  1987
(E).

Information Processing Systems - Open Systems Interconnection -
Specification of Basic Encoding Rules for Abstract Syntax Notation
(ASN.1), ISO 8825:  1987 (E).

7-bit Coded Character Set for Information Processing Interchange, ISO
646.

Information Interchange - Representation of Local Time Differentials,
ISO 3307.


Application Layer

Information Processing Systems - Open Systems Interconnection -
Application Layer Structure, ISO/DP 9545, ISO/TC97/SC21/N1743.  July 24,
1987. Revised November 1987.

Application Layer -- FTAM

Information Processing Systems - Open Systems Interconnection - File
Transfer, Access and Management Part I: General Introduction, ISO 8571-1: 
1987 (E) (ISO/TC97/SC21 N 2331).

Information Processing Systems - Open Systems Interconnection - File
Transfer, Access and Management Part 2: Virtual Filestore Definition, ISO
8571-2:  1987 (E) (ISO/TC97/SC21 N 2332).

Information Processing Systems - Open Systems Interconnection - File
Transfer, Access and Management Part 3:  The File Service Definition, ISO
8571-3:  1987 (E) (ISO/TC97/SC21 N 2333).

Information Processing Systems - Open Systems Interconnection - File
Transfer, Access and Management Part 4: File Protocol Specification, ISO
8571-4:  1987 (E) (ISO/TC97/SC21 N 2334).

Application Layer -- ASE/ACSE

Information Processing Systems - Open Systems Interconnection - Service
Definition for the Association Control Service Element, ISO 8649:  1987
(E) (ISO/IEC JTC1/SC21 N2326) (ISO/TC97/SC21 N)

Information Processing Systems - Open Systems Interconnection - Protocol
Specification for the Association Control Service Element, ISO 8650: 
1987 (E) (ISO/IEC JTC1/SC21 N2327) (ISO/TC97/SC21 N)


Application Layer -- VTP

Information Processing Systems - Open Systems Interconnection - Virtual
Terminal Service - Basic Class, IS 9040.

Information Processing Systems - Open Systems Interconnection - Virtual
Terminal Protocol - Basic Class, IS 9041.

Application Process -- Office Document Interchange -- ODA/ODIF

Information Processing Systems - Text and Office Systems - Office
Document Architecture (ODA) and Interchange Format - Part 1; General
Information, DIS 8613/1.

Information Processing Systems - Text and Office Systems - Office
Document Architecture (ODA) and Interchange Format - Part 2; Document
Structures, DIS 8613/2.

Information Processing Systems - Text and Office Systems - Office
Document Architecture (ODA) and Interchange Format - Part 3; Document
Processing Reference Model, DIS 8613/3.

Information Processing Systems - Text and Office Systems - Office
Document Architecture (ODA) and Interchange Format - Part 4; Document
Profile, DIS 8613/4.

Information Processing Systems - Text and Office Systems - Office
Document Architecture (ODA) and Interchange Format - Part 5; Office
Document Interchange Format, DIS 8613/5.

Information Processing Systems - Text and Office Systems - Office
Document Architecture (ODA) and Interchange Format - Part 6; Character
Content Architecture, DIS 8613/6.

Information Processing Systems - Text and Office Systems - Office
Document Architecture (ODA) and Interchange Format - Part 7; Raster
Graphics Content Architecture, DP 8316/7.

Information Processing Systems - Text and Office Systems - Office
Document Architecture (ODA) and Interchange Format - Part 8; Geometric
Graphics Content Architecture, DP 8613/8.

Information Processing Systems - Text and Office Systems - Standard
Generalized Markup Language (SGML), IS 8879.

Application  Process -- Computer Graphics -- CGM/GKS

Information Processing Systems - Computer Graphics - Metafile (CGM) for
the Storage and Transfer of Picture Description Information, Part 1;
Functional Specification, IS 8632/1

Information Processing Systems - Computer Graphics - Metafile (CGM) for
the Storage and Transfer of Picture Description Information, Part 2;
Character Encoding, IS 8632/2

Information Processing Systems - Computer Graphics - Metafile (CGM) for
the Storage and Transfer of Picture Description Information, Part 3;
Binary Encoding, IS 8632/3.

Information Processing Systems - Computer Graphics - Metafile (CGM) for
the Storage and Transfer of Picture Description Information, Part 4;
Clear Text Encoding, IS 8632/4.

Information Processing Systems - Font and Character Information
Interchange, IS 9541.

Information Processing Systems - 8-Bit Single Byte Coded Graphic
Character Sets, Part 1; Latin Alphabet Part 1, IS 8859/1.

Information Processing Systems - Computer Graphics Functional
Specification of the Graphical Kernel System (GKS), IS 7942.

Information Processing Systems - Computer Graphics - Graphical Kernel
System for Three Dimensions (GKS-3D), Functional Description, DIS 8805.

Information Processing Systems - Computer Graphics - Programmers
Hierarchical Interactive Graphics System (PHIGS), DP 9592.

Information Processing Systems - Computer Graphics - Interfacing
Techniques for Dialogues with Graphical Devices (CGI),ISO TC 97/SC 21 N
1179.

Application Layer -- Directory Services

The Directory--Overview of Concepts, Models, and Services (CCITT
Recommendation X.500, ISO 9594)

The Directory--Information Framework (CCITT Recommendation X.501, ISO
9594)

The Directory--Access and System Services Definition (CCITT
Recommendation X.511, ISO 9594)

The Directory--Procedures For Distributed Operation (CCITT
Recommendation X.518, ISO 9594)

The Directory--Access and System Protocols Specification (CCITT
Recommendation X.519, ISO 9594)

The Directory--Selected Attribute Types (CCITT Recommendation X.520, ISO
9594)

The Directory--Selected Object Classes (CCITT Recommendation X.521, ISO
9594)
   
The Directory--Authentication Framework (CCITT Recommendation X.509, ISO
9594)

Remote Operations-Part 1: Model, Notation and Service Definition (CCITT
Recommendation X.219, ISO 9072 Version 5)

Remote Operations-Part 2: Protocol Specification (CCITT Recommendation
X.229, ISO 9072 Version 5)

Association Control-Service Definition (CCITT Recommendation X217, ISO
8649)

Association Control-Protocol Definition (CCITT Recommendation X.217, ISO
8650)

Note: ISO 9594, 9072 are preferred texts (over the CCITT counterparts)
and are to be taken as of Gloucester, Nov. 1987.

CCITT documents may be obtained from:
                 International Telecommunications Union
                       Place des Nations, CH 1211,
                          Geneva 20 SWITZERLAND

ISO documents may be obtained from:
                          Frances E. Schrotter
                                  ANSI
                       ISO TC 97/SC 6 Secretariat
                              l430 Broadway
                          New York, NY.  10018

11.3    IEEE

Physical Layer

IEEE Standard for Local Area Networks:  Carrier Sense Multiple Access
with Collision Detection (CSMA/CD) and Physical Layer Specification,
ANSI/IEEE Standard 802.3 1985, Institute of Electrical and Electronics
Engineers, 345 East 47th St., New York, NY. 10017, 1985.

IEEE Standard for Local Area Networks: Supplements to Carrier Sense
Multiple Access with Collision Detection (CSMA/CD) Access Method and
Physical Layer Specification ANSI.IEEE Standard 802.3a, b, c, e -1988

Supplement a, MAU and Baseband Medium Specification, Type 10BASE2
(Section 10)

Supplement a, Broadband MAU & Medium Specification, Type 10BROAD36
(Section 11)

Supplement c, Repeater Set and Repeater Unit Specification for Use with
10BASE5 and 10 BASE2 Networks


Supplement e, Physical Signaling, Medium Attachment, and Baseband Medium
Specification, Type 10BASE5

IEEE Standard for Local Area Networks:  Token-Passing Bus Access Method
and Physical Layer Specification, ANSI/IEEE Standard 802.4 - 1985, 802.4
Draft 1987, Institute of Electrical and Electronics Engineers, 345 East
47th St., New York, NY. 10017, 1985.

IEEE Standard for Local Area Networks:  Token-Ring Access Method,
ANSI/IEEE Standard 802.5-1985 1986, Institute of Electrical and
Electronics Engineers, 345 East 47th St., New York, NY. 10017, 1985.


Data Link Layer

IEEE Standard for Local Area Networks:  Logical Link Control, ANSI/IEEE
Standard 802.2 - 1985 1987, Institute of Electrical and Electronics
Engineers, 345 East 47th St., New York, NY. 10017, 1985.

11.4    NBS

Local Area Networks:  Baseband Carrier Sense Multiple Access with
Collision Detection Access Method and Physical Layer Profiles and Link
Layer Protocol, FIPS l07, NTIS, U.S. Department of Commerce, 5285 Port
Royal Road, Springfield, VA. 22l6l.

Interface Between Data Terminal Equipment (DTE) and
DataCircuit-Terminating Equipment (DCE) For Operation With
Packet-Switched Data Communications Networks, FIPS l00, NTIS, U.S.
Department of Commerce, 5285 Port Royal Road, Springfield, VA. 22l6l.

Implementation Agreements for Open Systems Interconnection Protocols: 
NBS Workshop for Implementors of Open Systems Interconnection, National
Bureau of Standards, NBSIR 86-3385-6, Robert Rosenthal, Editor, Revised
July 1987. 

Implementation Agreements Among Participants of OSINET, National Bureau
of Standards, Institute for Computer Sciences and Technology, NBSIR
86-3478, 1987.

U. S. Government Open Systems Interconnection Profile (GOSIP),
National Bureau of Standards, Institute for Computer Sciences and
Technology, 1987.

NBS documents may be obtained from:
                                  NTIS
                       U.S. Department of Commerce
                          5285 Port Royal Road
                         Springfield, VA. 22l6l.
                                   or
                      National Bureau of Standards
             Institute for Computer Sciences and Technology
                         Gaithersburg, MD. 20899


11.5    MAP

Manufacturing Automation Protocol, General Motors
Corporation,Manufacturing Engineering and Development, Advanced Product
and Manufacturing Engineering Staff (APMES), APMES A/MD-39, GM Technical
Center, Warren, MI. 48090-9040.


11.6    TOP

Technical and Office Protocols Specification Version 3.0, MAP/TOP Users
Group, Attention TOP 3.0 Document.  One SME Drive, P.O. Box 930, Dearborn
Mi. 48121.

11.7    CEN/CENELEC

FTAM Draft Functional Standard A/111 (prENV 41 204) Simple File Transfer-
Unstructrued, 1987-12-01.

ENV 41201 "Private Message Handling Systems"

ENV 41202 "Public Message Handling Systems"


11.8    SPAG

FTAM Draft Profile A/112 Positional File Transfer - Flat, 1987-120-7.

FTAM Draft Profile A/122 Positional File Access - Flat, 1987-12-07.

FTAM Draft Profile A/13 File Management, 1987-12-07.


                          READER RESPONSE FORM


Please retain my name for the next mailing of the NBS/OSI Implementors
Workshop.



   ZDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD?
   3                                                                 3
   3NAME                                                             3
   3                                                                 3
   3ADDRESS                                                          3
   3                                                                 3
   3                                                                 3
   3                                                                 3
   3                                                                 3
   3                                                                 3
   3PHONE NO.                                                        3
   3                                                                 3
   @DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDY




Mail this page to:     National Bureau of Standards 
                       NBS Workshop for Implementors of OSI
                       Bldg. 225/B-217 
                       Gaithersburg, MD  20899